## Slide 1
Overview of the CCSDS Optical Communications Interoperability Standards
June 2021
Bernard Edwards / NASA (CCSDS Optical Communications Working Group Chair)
Notes: 1
1
1

## Slide 2: Optical Communications International Standardization
Sharing optical communication ground stations or relay satellites among the international space agencies would allow the agencies to share the cost of the communications infrastructure.
  For example, due to cloud blockage, it is critical to have multiple ground stations in use during space-to-ground optical operations to provide high availability.
International cross support is being worked within the Interagency Operations Advisory Group (IOAG) and the Consultative Committee for Space Data Systems (CCSDS).
The goal is to develop optical communications cross support by various agencies as we have today in traditional Radio Frequency (RF) communications.
Traditional International
RF Cross Support

## Slide 3
Scope:
  Physical, coding, and synchronization layer recommendations for the interoperability of flight and ground optical communications terminals
  Recommendations for characterizing the atmosphere channel and for the concept of operations for space-to-ground links
Published Books:
  Blue Book: Optical Communications Physical Layer
    Covers the High Photon Efficiency Recommendations
  Blue Book: Optical Communications Coding and Synchronization
    Covers High Photon Efficiency
  Green Book: Atmospheric Characterization For Optical Communication Systems
  ESA/DLR Orange Book: Optical High Data Rate Communications – 1064 nm
Books awaiting official publication:
  Revision 1 of the Blue Book on Optical Communications Physical Layer
    Will add Optical On / Off Keying Recommendations
  Magenta Book: Atmospheric Characterization and Forecasting for Optical Link Operations
  NASA/CNES/JAXA/NICT Orange Book: Optical High Data Rate Communications – 1550 nm
CCSDS Optical Communications
Working Group

## Slide 4
Optical On / Off Keying (O3K) Coding and Synchronization Recommendations
Inclusion of the ITU Generic Framing Procedure (GFP) in the appropriate CCSDS Books
Adding Ranging and Time Transfer to High Photon Efficiency
Future Work of the Optical Communications Working Group

## Slide 5
CCSDS International Optical Communication Standards in Development
100 Gbps
10 Gbps
1
Gbps
100 Mbps
10 Mbps
102
103
104
105
106
107
108
1010
Km
Km
109
GEO
light second
light minute
light hour
LEO SATS
VENUS
MERCURY
MARS
NEAR-EARTH SATS
MOON
JUPITER
SATURN
URANUS
NEPTUNE
PLUTO
Lagrange
MOON
Lagrange
1 AU
(1/R2 Loss)
1 Gbps @
1 AU SCaN
Goal
Range of Communication Link (km)
LCRD
EDRS
JDRS
LOP-G
O2O
Next Gen IOC
DSOC design 20 cm 6 W Tx
DSOC
Psyche
Gen 2 DSOC
TBIRD Demo
CCSDS
High Data
Throughput
CCSDS
High Photon
Efficiency
Commercial
LEO
Crosslinks
Or Direct-to-Earth Using OOK
To Commercial OGS
CCSDS
Optical On-Off
Keying
100X
More Loss
so PPM
1,000,000X
More Loss so PPM, Large OGS
100X
More Loss so PSK

## Slide 6
Received Signal
Local Oscillator
Power Detection
10
1
0.1
Photons per bit
Coherent
Photon
Counting
Quantum
Limit
Optically
Preamplified
LO shot noise limited
ASE noise limited
“noiseless”
Unknown architecture
CCSDS
Optical On-Off
Keying
CCSDS
High Data
Throughput
CCSDS
High Photon
Efficiency PPM
Detection Sensitivity
in Optical Communications

## Slide 7: CCSDS Optical Signaling Today
HPE
O3K
HDR
Free-Space Optical Channel
CCSDS Transfer Frames
Optical coding and sync layers accept fixed-length frames rate-matched to optical channel

## Slide 8: Frame Transfer Services Provided by Current Optical Communications Recommendations
Optical Coding and Sync
Optical Physical Layer
TM
AOS
Fixed Length USLP
Ethernet / Other
Fixed-length transfer frames
Not supported
Optical communications signaling recommendations would be more widely applicable if they accepted variable-rate variable-length frames at the input to the coding and sync layer
Variable Length USLP

## Slide 9: Add Generic Framing Procedure (GFP)
Augment existing CCSDS optical coding and sync layers to provide fixed-rate octet transport service in addition to fixed-rate fixed-length frame transport service
Use Generic Framing Procedure (GFP, ITU-T G.7041/Y.1303) to adapt higher-layer frame formats to fixed-rate octet transport service
Rationale:
  Provides necessary means for transporting variable-length variable rate frames
  Widely adopted industry standard for terrestrial optical transport systems (SDH, OTN)
  Supports many common client interfaces and flexible enough to support other custom frame formats (e.g. CCSDS transport frames)
Data Link Layer Frames
Generic Framing Procedure
Optical Coding and Sync
Optical Physical Layer
Fixed/Variable Rate,
Fixed/Variable Length
Frames
Fixed Rate
Octet Stream

## Slide 10
A set of standards for space optical communications is being developed by CCSDS to enable interoperability. International standards will allow optical communications terminals built by one agency to use the infrastructure of another.
However, current CCSDS recommendations for optical signaling do not support transport of variable-length variable-rate frames.
  The CCSDS Optical Communications Working Group is investigating the incorporation of Generic Framing Procedure (ITU G.7041) for handling variable-length, variable-rate frame inputs (e.g. USLP, Ethernet) to the optical coding and sync layers.

## Slide 11
BACKUP

## Slide 12: Field Guide to CCSDS Book Colors
BLUE BOOKS
Recommended Standards
Normative and sufficiently detailed (and pre-tested) so they can be used to directly and independently implement interoperable systems (given that options are specified).
MAGENTA BOOKS
Recommended Practices
Normative, but at a level that is not directly implementable for interoperability. These are Reference Architectures, APIs, operational practices, etc.
GREEN BOOKS
Informative Documents
Not normative. These may be foundational for Blue/Magenta books, describing their applicability, overall archtecture, ops concept, etc.
RED BOOKS
Draft Standards/Practices
Drafts of future Blue/Magenta books that are in agency review. Use caution with these… they can change before release.
ORANGE BOOKS
Experimental
Normative, but may be very new technology that does not yet have consensus of enough agencies to standardize.
YELLOW BOOKS
Administrative
CCSDS Procedures, Proceedings, Test reports, etc.
SILVER BOOKS
Historical
Deprecated and retired documents that are kept available to support existing or legacy implementations. Implication is that other agencies may not cross-support.
PINK BOOKS/SHEETS
Draft Revisions For Review
Draft Revisions to Blue or Magenta books that are circulated for agency review.
Pink Books are reissues of the full book, Pink Sheets are change pages only.

## Slide 13
13
Mars
¸
Venus
Mercury
Sun
Uranus
Jupiter
Saturn
Titan
Pluto
Charon
Neptune
High Photon Efficiency
Optical Communications
Attributes:
Long distance
Photon-starved channel
Direct detection
Serially Concatenated Pulse Position Modulation

## Slide 14
  Signal Features
  Near-capacity channel coding
  Modular – asynchronous with upper layers
  Robust to atmospheric fading (interleaver)
  Robust to non-random data input
  Compatible with existing/emerging technology
  Flexible parameters:
  PPM order,
  Code rate,
  Slot width, ns
  Repeat factor,
Data rates between 16 kbps and 2.1 Gbps
Photon efficient: generally with 1 dB of capacity
High Photon Efficiency Signaling
For Optical Communications

## Slide 15: High Data Rate Throughput 1064 nm (ESA/DLR Orange Book)
This book is based on
  European Space Agency missions (EDRS series, Sentinel series)
  German Aerospace Agency (DLR) developments
  TESAT Spacecom LCT terminal (heritage extending back to 1997 for LEO-LEO and a 2nd generation for LEO-GEO links developed since 2006
Key technical features:
  1064 nm wavelength
  BPSK modulation
  1.8 Gbps user data rate
Notes: JAXA is interested, resources being identified. Possible issues getting resources allocated / schedule.

## Slide 16
Clouds are primary source of attenuation
Characterization and prediction of the atmospheric channel are critical to inform
space link handovers, select ground sites, and to maximize system availability
  CCSDS Books will:
  Provide a narrative on atmospherics and explain why it is critical to accurately characterize
  Explain how long-term statistics of atmospherics are used to choose an optimal network of geographically diverse ground sites
  Provide content on the required instruments and parameters to support long-term site characterization and real-time decision making

## Slide 17: High Data Throughput 1550 nm Orange Book Link Scenarios
Space
Air
Ground
Space
Relay
Optical or RF
Trunks
Crosslinks
Users
Optical
Direct-to-Earth
Link
Atmosphere
Optical Link
RF Link

## Slide 18: High Data Rate Throughput 1550 nm Architectural Considerations
Space Relay
  Edge-to-Edge FEC– Decoding performed at edge nodes where processing resources are available
    DVB-S2 and other capacity-approaching codes used
  Optical link from user to relay; optical or RF link from relay to ground
    Options for coding + interleaving for atmospheric channels
  Wide range of supported user rates (~10 Mbps to 10+ Gbps)
    Burst mode PSK modulation formats for large range of data rates
  Example missions: JDRS, LCRD
Direct-to-Earth
  High-rate (~> 100 Gbps) link for large volume, short duration data transfer
    Signaling similar to high-rate fiber telecom approaches
  Example missions: large data volume LEO DTE

## Slide 19: High Data Throughput 1550 nm Signaling Overview
FEC:
DVB-S2, RS, or G.975 I.3
Convolutional Channel Interleaver
Physical Layer Framing
Randomizer
Q-Repeat
To amplifier or
telescope
Modulation:
Burst-Mode PSK@1550nm
CCSDS Transfer Frames
Slicer
Frame Sync Marker
Attachment
Notes: JAXA is interested, resources being identified. Possible issues getting resources allocated / schedule.

## Slide 20: High Data Rate Throughput 1550 nm Relay Link Example
Space Pkt
AOS Frame
FEC/ILV/ Q-Repeat
Physical Link
User Platform
User Terminal
Phy Frame
Relay Platform
Relay Terminal 1
Phy Frame
Relay Terminal 2
Physical Link
Ground Relay
Service I/F
AOS Frame
Ground Network
Switch
Optical relay serves as a transparent link-layer bridge between User Platform and Ground Relay
Phy Frame
Random
Modulation
De-Random
De-Mod
Random
Modulation
FEC/DeILV/ De-Q-Rep.
Phy Frame
De-Random
De-Mod
Transparent Bridge
05/10/17
Notes: JAXA is interested, resources being identified. Possible issues getting resources allocated / schedule.

## Slide 21: Example: Using GFP with 1550 nm HDR Orange Book Recommendations
Attach Sync Marker
Slicer
CRC Attachment
Forward Error Correction
Channel Interleaver
…
Fixed-Length Fixed-Rate CCSDS Frames
Frame Transport Service
Bit Transport Service
Variable-Length Variable-Rate Frames
GFP
Same approach could be used to transport variable-length/variable-rate frames
over CCSDE HPE or O3K

## Slide 22: GFP Description