## Slide 1: NASA Universal Waste Management System and Toilet Integration Hardware Delivery and Planned Operation on ISS ICES Paper 2021-403
Melissa McKinley, James L. Broyan, Laura Shaw, Melissa Borrego, NASA Johnson Space Center
Donald L. Carter, NASA Marshall Space Flight Center
Jim Fuller, Collins Aerospace

## Slide 2
Universal Waste Management System (UWMS)
Universal Waste Management System
  ISS Unit – Toilet
  Orion Unit – Waste Management System (WMS)
Toilet for exploration missions
Reduction in mass and volume
  Toilet is 65% smaller and 40% lighter than current ISS toilet (WHC)
  WMS is 61% smaller than Shuttle Toilet
ISS Toilet
  Delivered June 2020
  Installed May 2021
Orion WMS
  Delivered December 2019
  Installed into Artemis-2 Vehicle March 2021
Orion UWMS installed in Artemis-2
ISS UWMS installed in Node 3, ISS

## Slide 3: Dual Fan Separator
Dual Fan Separator Design resulted in UWMS reduction in mass/volume
  Compact design eliminated a set of fan/controller hardware needed for separate functions which reduced mass and volume
    Combines previous toilet designs with separate fans for urine and feces collection into one unit
  Single shaft and motor with two fans for entrainment of the waste and separation of liquid/gas functions
  Removal of air key to successful recycling of urine on ISS
3
ISS UWMS Dual Fan Separator show in highlighted area

## Slide 4: Urine Pretreat Systems
4
ISS Unit – low pH and strong oxidizing chemicals used to prevent microbial and fungal growth
Dose pump dispenses metered volumes of concentrated pretreat and water for each urination
Conductivity Sensor measures solution to provide a warning of incorrect pretreat concentration to protect downstream recycling systems
Full mixing is part of the design to ensure entire urination volume is treated
Orion unit – Oxone tablets from Shuttle design, urine is vented with no recycling
UWMS with Dosing Assembly including Conductivity Sensor

## Slide 5: Updated Designs for Urine Funnel and Commode Seat
Urine Funnels
  NASA updated urine collection with a urine funnel design optimized for female crew.
  Size and shape of funnel intended to improve simultaneous operations (urination and defecation) for female crew
  Numerous Crew evaluation and feedback resulted in three designs
  On-orbit evaluation with Waste and Hygiene Compartment (WHC) influenced design changes
Commode Seat
  Seat size and shape optimized to work with the urine funnel and to improve placement of female crew
  Two sizes were flown for evaluation
5
Urine Funnels and Plug for Toilet

## Slide 6: On-orbit Installation Issues
UWMS ISS launched on NG-14 in 10/2020, installation started 12/2020
Issues with Dosing Assembly Seal Replacement
  Discovered Conductivity Sensor improperly machined fittings
  Installation would result in lack of two levels of containment for Tox 2 fluid, pretreat solution
Additional ground testing also showed issue with sensor operation
  Noted to be inaccurate and decayed overtime
Installation was paused for evaluation
Approval given for installation in May 2021 in a “use as-is” configuration to evaluate sensor operation and seal integrity
6
Improperly machined and damaged fitting on Conductivity Sensor Outlet
Orientation relative to mating cap

## Slide 7: Toilet Integration Hardware - Stall
Deployed in ISS, Node 3 - 2/2019
Provides privacy for existing WHC and adjacent space for Toilet
Port side removed pending installation of Toilet
Stall panels modular design provides flexibility to remove individual panels for maintenance activities
Stall knob repairs
  Design issue if over rotated could result in release of internal components
  Two knobs damaged due to over rotation
  Modifications made and repair kits flown
    Addition of fastener and anti-rotation ring
Crew made updates to on-orbit hardware
7
1. Starboard Stall deployed in Node 3 ISS; 2. View of knobs installed; 3. Design modifications to knob
1.
2.
3.

## Slide 8: Stall Mesh Screen
Toilet Stall covered by Mesh Screen
  Provides containment of any potential free fluid and particles while still allowing air flow
  Stainless steel mesh with hole opening size of 2.38 mm (.1 in)
Crew reported damage at interface points
  Snaps secure Mesh Screens to top Stall panels
Design updated to reinforce materials at the attachment points
Replacement Mesh Screens delivery in work.
8
Mesh Frames installed on top of Toilet Stall panels

## Slide 9: Toilet Installation, Activation and Next Steps
Installation completion targeting 6/8/21
Activation TBD
  Spares evaluation
  Evaluation of Conductivity Sensor Performance
Technology Demonstration planned 2021
  Provides details on consumables usage
  Ability of crew to perform simultaneous operations
  Overall information on use of a compact toilet in micro-gravity
Informs exploration missions including Orion program milestones
9