## Slide 1: Air-Cooled Temperature Swing Compression System Rebuild ICES Paper 2021-129
Marian Alcid and Kelby Gan (Presenters)
Tra-My Justine Richardson and Darrell Jan
Jonathan Castellanos

## Slide 2
Agenda
Background and overview of AC-TSAC
Hardware upgrades
Software and LabVIEW program updates
Proposed tests
Future work

## Slide 3
Air-Revitalization System Workflow
CO2 Removal Assembly
CO2 Compressor
CO2 Reduction
Assembly
Cabin Air
Air with reduced CO2 content
Low
Pressure
CO2
High pressure
CO2
Separator
CH4, H2O
CH4
Vent
H2O
Electrolyzer
Cabin
Cabin
O2
H2
Current SOA:
CDRA
Isobe, J., et al., Carbon Dioxide Removal Technologies for U.S. Space Vehicles: Past, Present, and Future. International Conference on Environmental Systems, 2016.
Cmarik, G., et al., 4-Bed CO2 Scrubber – From Design to Build. International Conference on Environmental Systems, 2020.
Next Gen:
4BCO2
Richardson, T-M, J., et al., A Trade-off Study of the Spacecraft Carbon Dioxide Management System using the Analytical Hierarchy Process. International Conference on Environmental Systems, 2018.
Mechanical Compressor + Accumulation Tanks
Richardson, T-M, J., et al., A Trade-off Study of the Spacecraft Carbon Dioxide Management System using the Analytical Hierarchy Process. International Conference on Environmental Systems, 2018.
AC-TSAC

## Slide 4
AC-TSAC Overview
Replacement for mechanical compressor
Solid-state compressor
  No rotating machinery
Zeolite adsorbent bed
Two canister beds operating in alternate cycles
  Constant output of high-pressure CO2
Richardson, T-M, J., et al., A Trade-off Study of the Spacecraft Carbon Dioxide Management System using the Analytical Hierarchy Process. International Conference on Environmental Systems, 2018.

## Slide 5
Full-Cycle Operation
BED A
BED B
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
PRODUCTION
ADSORPTION
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
COMPRESSION
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
O=C=O
COOLING
PRODUCTION
ADSORPTION
COOLING
O=C=O
O=C=O

## Slide 6
Rebuild
Old Rack
New Rack
New/Updated:
Aluminum frame
Front panel
  -Main power switch
  -Canister stage indicator lights
  Solenoid valves
  Vacuum pump
  Thermostats
  Pressure controller
  Pressure relief valves
Carried over:
MFCs
Pressure transducers
Blowers

## Slide 7
Hardware Upgrades
Previous sorbent retaining screen - large mesh size
Current sorbent retaining screen – 80 x 700 mesh (35 micron)

## Slide 8
Hardware Upgrades
Canister front panel
Canister back panel
Feedthroughs

## Slide 9
Controller and Electrical Panel

## Slide 10: AC-TSAC Software Overview
Bakeout Program
  Automated regeneration of sorbent
Data Logging Program
  Records system status and sensor data
Auto Cycle Program
  Main operating program for AC-TSAC
  Completely automated operation of the system
10

## Slide 11
Bakeout Program
Notes: Used for regenerating zeolite sorbent
  Sorbent exposed to atmosphere
  Coming out of long-term storage and inactivity
  Previous program required manual operation
Program features:
  Automated operation
  Controlled ramp rate (simple and advanced control)
  Holding temperature for a pre-determined length of time
  Independent bakeout of individual sorbent canister beds

## Slide 12
Bakeout Program Overview
Full regeneration required:
  Sorbent exposed to atmosphere
  Coming out of long-term storage and inactivity
Program features:
  Automated operation
    Previous bakeout operation was done manually by the user
  Controlled ramp rate (simple and advanced control)
  Holding temperature for a pre-determined length of time
  Independent bakeout of individual sorbent canister beds

## Slide 13
Bakeout Program
Notes: -Explain differences between simple and advanced ramp
-

## Slide 14
Data Logging Program
Notes: Records system status and sensor data during system operation
Updated Logging program to support new NI cRIO hardware
Program features:
  Easily add new sensors for recording
  Ability to save copies to multiple locations
  Save experiment notes with data
  Easily adjust record rate
  Automatically create new data log to reduce individual files’ size

## Slide 15
Data-Logging Program
Updated Logging program to support new NI cRIO hardware
Program features:
  Easily add new sensors for recording
  Ability to save copies to multiple locations
  Save experiment notes with data
  Easily adjust record rate
  Automatically create new data log to reduce individual files’ size

## Slide 16
Auto-Cycle Program
Notes: Main control program for solid-state CO2 compressor operation
Program updated for use with cRIO hardware and improved for usability and modularity
Program features:
  Completely automated operation
  Easily reprogrammable
  All temperatures, sensor readings all on one screen
  Pause and Idle operation for quick hardware maintenance
  Integrated Data Logging program

## Slide 17
Auto-Cycle Program
Notes: Main control program for solid-state CO2 compressor operation
Program updated for use with cRIO hardware and improved for usability and modularity
Program features:
  Completely automated operation
  Easily reprogrammable
  All temperatures, sensor readings all on one screen
  Pause and Idle operation for quick hardware maintenance
  Integrated Data Logging program

## Slide 18
Auto-Cycle Program
Main control program for solid-state CO2 compressor operation
Program updated for use with cRIO hardware and improved for usability and modularity
Program features:
  Completely automated operation
  Easily reprogrammable
  All temperatures, sensor readings all on one screen
  Pause and Idle operation for quick hardware maintenance
  Integrated Data Logging program

## Slide 19
Proposed Tests
144 minute half-cycle tests
  Based on CDRA operating cycle
  Inlet pressure: 200 torr
  Outlet flowrate: ~1600 sccm (4.1 kg CO2/day)
80 minute half-cycle tests
  Based on 4BCO2 operating cycle
Extended test runs (1+ week)
4BCO2-TSAC integration tests at MSFC

## Slide 20
Future Work
Operate AC-TSAC with other zeolites or novel sorbents
Heat pipes
Heater redesign
Canister redesign
Flight hardware design

## Slide 21
Acknowledgements
Allen Yau – NASA ARC (KBR)
Jason Samson – NASA ARC
Ryan Purdy – NASA ARC (Intern)
Tim Giesy – NASA MSFC
Greg Cmarik – NASA MSFC (ESSCA)
Jim Knox – NASA MSFC (ESSCA)
AES-LSS Management Team