## Slide 1: A Synthesis Plugin for Auralization of Rotor Self Noise
Siddhartha Krishnamurthy, NASA Langley Research Center
Aric R. Aumann, Analytical Services and Materials
Stephen A. Rizzi, NASA Langley Research Center
AIAA Aviation Forum, August 5, 2021
Copyright 2021 United States Government as represented by the Administrator of the National Aeronautics and Space Administration and Analytical Services and Materials. All Rights Reserved. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.

## Slide 2: Motivation
Need to understand community response to noise from future advanced air mobility vehicles
Play recorded or auralized sounds of these aircraft in NASA Langley Exterior Effects Room to test subjects
  Auralizations: sounds generated from numerical data
Exterior Effects Room, NASA Langley Research Center

## Slide 3: Rotor Blade Self Noise
Rotor self noise is a combination of the following noise sources:
More Information: T.F. Brook and S.D. Pope, “Airfoil self-noise and prediction,” NASA-RP-1218, Hampton, VA, 1989

## Slide 4: NASA Auralization Framework (NAF) Overview - Standard Use Case
Per Path
Update Scene
Find Paths
Path: Gain, Time Delay, Filters (GTF)
Synthesize Source Noise
Propagate
Output
Emission Angle
Path
Sample Buffer
GTF Series
Output Buffer
Loop
Direct Path
Reflected Path
Ground Observer
Acoustic Predictions
Auralization at Ground Observer

## Slide 5: Modulated Broadband Synthesis Plugin
Per Path
Update Scene
Find Paths
Path: Gain, Time Delay, Filters (GTF)
Synthesize Source Noise
Propagate
Output
Emission Angle
Path
Sample Buffer
GTF Series
Output Buffer
Loop
Modulated Broadband Synthesis Plugin
Self Noise Acoustic Predictions
The Modulated Broadband Synthesis Plugin was developed to synthesize broadband self noise
One set of acoustic predictions per rotor

## Slide 6: Broadband Self Noise Acoustic Predictions
Self noise acoustic predictions are sound pressure levels in each 1/3 octave band as a function of time over a single rotor revolution.

## Slide 7: Self Noise Flyover Sound Synthesis (Conceptual Overview)
Primary Steps:
  Extend self noise data over flyover duration by interpolating over emission angles from source to ground observer.
  Use extended self noise data to modulate a stochastic signal.
Paper explains how primary steps were adapted to work within the NAF.
Ground Observer
Synthesized Sound Near Rotor to Propagate to Ground Observer
Flyover Duration [s]
Flyover Duration [s]
[deg]
[deg]
Band Number
Pressure [Pa]
Sound Pressure Level Prediction Data Formed by Interpolating Over Single Rotor Revolution Data
Ground

## Slide 8: Quadrotor Flyover
Auralize straight and level flyover of NASA eVTOL quadrotor concept
1000 ft
46.3 m/s (90 KTAS)
Ground
Start Position
End Position
0.36 miles
(Not to Scale)
0.36 miles
7.15
Observer Flush with Ground

## Slide 9: Auralization Results
NAF Modulated Broadband Synthesis Plugin auralized full NASA eVTOL quadrotor flyover at ground observer.

## Slide 10: Summary
Self noise synthesis implemented into NAF Modulated Broadband Synthesis Plugin.
  Plugin available in NAF 1.2 public release.
Demonstrated use of plugin; paper describes plugin architecture in NAF.
Plugin accepts self noise acoustic predictions in the form of spectral time histories.
  New capability for NAF.
Plugin exercised by auralizing NASA eVTOL quadrotor concept vehicle.

## Slide 11: Acknowledgements and Thank You
  Sound files are available for download at:
  http://stabserv.larc.nasa.gov/flyover/
Email: siddhartha.krishnamurthy@nasa.gov
Modulated Broadband Synthesis Plugin developed with support from Transformational Tools & Technologies Project of the NASA Transformative Aeronautics Concepts Program.
Self noise synthesis conceptual development performed with support from the Revolutionary Vertical Lift Technology Project of the NASA Advanced Air Vehicles Program.

## Slide 12: Image References
Slide 2:
  AAM Concept art from: https://www.nasa.gov/sites/default/files/thumbnails/image/aam-design4-new-image-2-24-2021-3.jpg.
  Picture of Exterior Effects room provided by Steve Rizzi, NASA Langley Research Center.
Slide 3:
  Self noise sources provided by Nicole A. Pettingill, NASA Langley Research Center, but originally from T.F. Brook and S.D. Pope, “Airfoil self-noise and prediction,” NASA-RP-1218, Hampton, VA, 1989.
Slides 4 and 5:
  NAF flowchart and aircraft flyover animation taken from Aumann, Aric and Tuttle, Brian, “NASA Auralization Framework 1.2 Upcoming Release,” Spring 2021 Acoustics Technical Working Group VIRTUAL Meeting, April 13-14, 2021.
Slides 6-8:
  Quadrotor and rotor pictures from Silva, C., et al., “VTOL Urban Air Mobility Concept Vehicles for Technology Development.” Paper 3847. 2018 Aviation Technology, Integration, and Operations Conference, Atlanta, GA, 2018.
All other images generated by presenter (Siddhartha Krishnamurthy).