## Slide 1
NESC Sensors & Instrumentation Webinar - July 20, 2021
Open Circuit Resonant (SansEC) Sensor Technology Applications
George Szatkowski
NASA Langley Research Center

## Slide 2: Outline
Introduction to SansEC Sensors
  Description & Theory
  Computational Electromagnetic Modeling
  Sensor Fabrication
  Detectable Phenomena
Applications
  Composite Aircraft Smart Skin for Lightning Environments
  Wearables
Detectable Phenomena
Conclusions
Reference Publications

## Slide 3
SansEC
Sans Electric Connection
Electric
field
Introduction to SansEC Sensors
Wireless – No physical electrical connections
Passive – No battery required;
Non-Contact – EM Fields permeate out from sensor surface
Electromagnetic Resonator – naturally oscillates with greater amplitude at some frequencies based on Inductance (L), Capacitance (C) & Resistance (R) of the total circuit
Loop Antenna
SansEC Sensor
Closed Circuit Open Circuit

## Slide 4
Introduction to SansEC Sensors
1. SansEC Sensor - Conductive coil designed to resonate at desired frequencies
  The trace length, trace width and gap width influence the resonate frequencies.
2. Interrogator RF Source -Typically a Network Analyzer is used, but excitation could come from any stable ambient RF source.
3. Interrogator Receiver - Typically a Network Analyzer is used to measure the reflection coefficient. This is the near field configuration. Data can be collected in the far field by using an electric field antenna connected to a loop antenna.
4. Loop Antenna – Induces magnetic excitation on sensor to generate a signal response
  Loop antenna is aligned parallel to sensor trace.
5. Signal Analysis – Deterministic Quantification using Machine Learning
  Looks for relative change in resonant response
  to indicate change in device under test.
Network Analyzer
Loop Antenna
Sensor
Components of the Measurement System

## Slide 5
Introduction to SansEC Sensors
Signal Processing Data Features
For each Resonant Frequency, the following data features can be used in machine learning quantification from the reflection coefficient measurement.
Frequency
Amplitude
Phase
Q factor (3dB bandwidth)
Electrical Impedance
Derived Parameters (Inductance, Capacitance and Resistance)

## Slide 6
SansEC Sensor Theory
Equivalent Circuit Model
Lumped components in Antenna circuit will change resonance

## Slide 7
SansEC Sensor Theory
The SansEC sensor will have zero current at both ends of the resonant spiral. When excited by an oscillating electromagnetic field, the induced electromotive force (EMF) pushes the electrons carried by the conductor into the resonant state where the electrons move back and forth along the conductive trace.
Current Distribution
(zero current at ends)
Current Distribution
Charge Distribution
(blue: lowest currents to red: highest currents)

## Slide 8
Resonant Modes
SansEC Sensor Theory
(blue: lowest currents to red: highest currents)
Current distribution along trace length

## Slide 9
Computational Electromagnetic Modeling
Fiberglass substrate model with inner damage
Electric field distribution
No Damage (ɛr=3)
Electric field distribution
With Damage (ɛr=1)
No inner damage
With inner damage
Computed SansEC resonant response
Response Characteristics from Delamination in Composite

## Slide 10: Computational Electromagnetic Modeling
Response Characteristics of CFRP Damage
No Damage
Puncture
Delamination
Electric Field Visualizations
Void

## Slide 11
Computational Electromagnetic Modeling
Response Characteristics with changing Trace conductivities

## Slide 12
Sensors can be various shapes or sizes
The sensors free space resonate frequencies are determined by the overall length of the conductive trace along with the trace width and gap width.
.04 mm trace width from NanoJet printer
(second generation Aerosol 3D printing technology)
.15 mm trace width using conventional etching printed circuit board manufacturing techniques
SansEC Sensor Fabrication

## Slide 13
Triangular
Square
Hexagonal
Circular
5x5 Square Array
2x2 Square Array
SansEC Sensor Fabrication
Klick-n-Kut Cutter

## Slide 14
SansEC Sensor Fabrication
1MHz
100MHz
Skin Depth relative to Frequency
10 mm
The sensor trace thickness must be greater than the skin depth

## Slide 15: Applications – Composite Smart Skin
Composite aircraft require a thin layer of metal in the outer skin to protect avionics and airframe from lightning damage.
Post-flight ground inspection is conducted after a suspected lightning strike to identify continued air worthiness. (Visual inspections/Tap Test)
Demonstrated Lightning Strike Protection conductive layer can be replaced with resonant sensors to provide comparable lightning mitigation characteristics and damage detection.
Program research focused on using SansEC Sensors on Carbon Composites
Lightning Testbed
Lightning Strike Video

## Slide 16: Applications – Composite Smart Skin
Lorentz Force
Sensor will generate a Lorentz Force on incoming charged particle

## Slide 17: Applications – Composite Smart Skin
Operation on Carbon Fiber Composites requires a thin sheet of high permeability material to sustain the resonance.

## Slide 18: Universal Common Practice Guide for Lightning Damage Testing of Composites Panel Design
Layup: 16 ply tape with 2 ply fabric
[(SURF)(ECF)(0/90F)/45/90/-45/0/45/90/-45/0/0/-45/90/45/0/-45/90/45/(0/90F)]
Tape: Hexcel 8552/AS4 (HexPly 8552/AS4),
Fabric: Hexcel 8552/AS4 (HexPly 8552 / A193-PW, 3K-70-PW)
Lightning Protection: Dexmet 3CU7-100FA (3mil copper mesh)/ SansEC Smart Skin
Primer: 0.5-1.5 mils thickness
Top coat: 4 to 6 mils per Mil-F-18264 or equivalent.
Test Panel
Applications – Composite Smart Skin
Previous Program Research

## Slide 19
Pre-Strike Test Panel
Post-Strike Test Panel
Pre-Paint Test Panel
8 inch SansEC Array
  SansEC Fiberglass Reinforced Plastic LSP Test Panels
Applications – Composite Smart Skin
Previous Program Research

## Slide 20
Carbon Fiber Panel Lightning Direct Effects Testing
Two 100 kA Strikes
High Speed Video First Frame showing Lightning Strike Initial Attachment on Mesh Protected Carbon Panel
High Speed Video First Frame showing Lightning Strike Initial Attachment on SansEC Protected Carbon Panel
Applications – Composite Smart Skin
Previous Program Research

## Slide 21
Electrical Current on the 4 Edges of the Test Panel were Independently Monitored during Lightning Test
Current Data collected during 100KA Strike
Pearson Probes mounted on Test Bed
4 independent current monitors enable measurements on the 4 edges
Inductive effects from ground strap installation should be minimized
Applications – Composite Smart Skin
Previous Program Research

## Slide 22: Mechanical deflection is measured using optical sensors or digital image correlation cameras
Digital image
Correlation
cameras
Digital Image Correlation Video
Applications – Composite Smart Skin
Previous Program Research

## Slide 23
Backside Thermal Data was Acquired using FLIR Systems SC645 IR Camera
Backside IR image of 8” SansEC LSP on Fiberglass Substrate
Infrared (IR) Camera Setup
IR Camera
Previous Program Research
Applications – Composite Smart Skin

## Slide 24
Hotter temperatures in the IR image represent the location of lightning attachment or current propagation.
Lightning Attachment was observed to occur at high electric field locations.
Previous Program Research
Applications – Composite Smart Skin
Computed E Field
Backside IR Temperature
Post Strike Damage

## Slide 25: Universal Common Practice Guide for Lightning Damage Testing of Composites NDI Assessments
Pre-Test NDI: Inspect the cured panel with a through transmission ultrasonic (TTU)'C' scan inspection at 5 MHz. A defect is defined as an area with ultrasonic attenuation that is at least 6db larger than the attenuation of the adjacent areas without flaws greater than 0.50 inch in diameter. Multiple defects are allowed, up to three (3) per panel as long as they are at least 1.00 inch apart.
Post-Test NDI: Pulse-Echo Ultrasonic Assessment, X-ray Assessment (Optional)
  Areas with ultrasonic attenuation >6dB larger than adjacent areas without flaws or defects.
Destructive Damage Assessments
  Taper sand to remove damaged material, use P-E Ultrasonics to verify. Then count plies remaining.
Photos from NASA Document Number: DOC-128697
TTU Data
Damage Assessment
Lightning Experiments – Damage Assessment
Applications – Composite Smart Skin
Previous Program Research

## Slide 26
Section A-A
Front Trace
Substrate
Back Trace
Pitch Centerline
0.050 in.
0.100 in.
0.100 in.
0.03125 in.
Experimental Setup
Double sided SanEC Design for DBD Test
Previous IRAD Research
Dielectric Barrier Discharge (DBD) SansEC Sensor
Response at 2KHz
Response at 10KHz
Applications – High Efficiency Plasma Generator
DBD Sensor Mounted inside Ventilation Hood

## Slide 27
Applications - Wearables
Conductive Yarn Sensors Embedded in Textiles
Experimental Setup
Video showing instantaneous temperature change

## Slide 28
Applications - Wearables
Hand Gesture Measurements

## Slide 29
Detectable Phenomena
Habitat Environmental Conditions
  Temperature
  Humidity
  Pressure
Physiological Measurements
  Vital Signs
  Body Mechanics
  Intercranial Fluids
Structures & Materials
  Composite Damage
  Stress & Strains
  Flutter/Morphing
If the monitored phenomena undergoes a change in its electrical impedance, SansEC sensing can possibly detect it.
Chemistry
  PH Level
  Contaminations
  Water/Ice Detection
  Mineral Exploration
Autonomous Assembly
  Proximity
  Angular Rotation
  Fastener Torque
  Integrity Monitoring
Rocket/Jet Engines
  Fuel Cavitation
  Performance Monitoring
  Turbine Blade Monitoring

## Slide 30
Conclusions
Wireless
Passive
Non-Contact
Electromagnetic Resonators
SansEC Sensors
Used to detect change in a physical phenomena by measuring/monitoring electrical impedance
Measurement components include the sensor, interrogator, loop antenna and signal processing
The physics-based data features work well in machine learning algorithms for quantification

## Slide 31
Reference Publications
Szatkowski, G. N., et al, “Open Circuit Resonant (SansEC) Sensor Technology for Lightning Mitigation and Damage Detection and Diagnosis for Composite Aircraft Applications”, NASA TP 2014-218554 https://www.worldcat.org/title/open-circuit-resonant-sansec-sensor-technology-for-lightning-mitigation-and-damage-detection-and-diagnosis-for-composite-aircraft-applications/oclc/916508919
Woodard, S. E., et al, “SansEC sensing technology — A new tool for designing space systems and components”, IEEE 2011 Aerospace Conference https://ieeexplore.ieee.org/document/5747495
Wang, C., et al, “Open Circuit Resonant (SansEC) Sensor for Composite Damage Detection and Diagnosis in Aircraft Lightning Environments”, 4th AIAA Atmospheric and Space Environments Conference, June 25-28, 20012, New Orleans, LA https://ntrs.nasa.gov/archive/nasa/casi.ntrs.nasa.gov/20120011948.pdf
Delelegn, D. T. et al, “Data Driven Understanding of SansEC Sensor Using Random Forest”, NASA study https://tpsas.larc.nasa.gov/lf99_view.cfm?lf99_id=34315&lf99_action=view
Cluff , Kim, et al, “Passive Self Resonant Skin Patch Sensor to Monitor Intraventricular Volume using Electromagnetic Properties of Fluid Volume Changes” https://ieeexplore.ieee.org/document/8472269
Griffith, Jacob, et al, “Non-invasive Electromagnetic Skin Patch Sensor to Measure Intracranial Fluid-Volume Shifts” https://ieeexplore.ieee.org/document/7516261