## Slide 1: Introduction to Radiative Heating
Brett A. Cruden
AMA Inc. at NASA Ames Research Center
Ames/Langley Summer Seminar Series
July 6, 2021

## Slide 2: Radiation in Planetary Entry Aeroheating
Spacecraft kinetic energy is converted to thermal energy during atmospheric entry deceleration
Thermal energy must be absorbed/dissipated by thermal protection system (TPS)
Part of that thermal energy reaches spacecraft through convective and radiative heat transfer
  Radiative heating scales as rnV8, in blackbody limit
  Becomes relevant for large vehicles and/or high entry velocities
Recent studies have found exceptions to the above
  Radiative heating often larger on the backshell than convection
  Regimes of molecular radiation occur at intermediate velocities, may cause non-monotonic radiation wrt V
Phenomenological models of shock radiation are used in CFD simulation tools to assess impact of radiative heating
  Models are developed and validated through ground testing (and flight test data, if available)
Notes: Give motivation and objectives

## Slide 3: Radiation, in Mission Context
Radiation is significant form of heating for many missions
  Often dominant on backshell or at high velocity

## Slide 4: Basic Radiation Terminology
Radiative Heat Flux is equal to the:
  Irradiance, which is the integral of the:
    Radiance, which is the integral of the:
      Spectral Radiance, which is the integral of the:
        Volumetric Spectral Radiance
          kinda

## Slide 5: Volumetric Spectral Radiance
In the bow shock, a control volume radiates uniformly in all directions
The radiation has a spectral (wavelength dependent) signature
The surface “sees” the volume through its intersecting line of sight
The fundamental quantity then is the volumetric spectral radiance, el
  Power per Wavelength per Volume per Solid Angle (W/cm3-sr-mm)
  (Also known as an emission coefficient)
Vehicle
Bow Shock

## Slide 6: The Radiation is accumulated over a line of sight
A radiating Line of Sight passes through multiple control volumes, all of which absorb and radiate light. The surface sees the integral along this line of sight:
At equilibrium, the absorption coefficient is related to the emission coefficient by Planck’s function:
For optically thin cases (a small, L << B)

## Slide 7: Spectral Radiance to Radiance
Simply, the Radiance is the integral of the Spectral Radiance:
However, heat absorbed depends on the interaction of the material with the radiation:

## Slide 8: Radiation Comes From All Directions
The (spectral) irradiance to a surface is the integral of the normal component of (spectral) radiance:
Technically, the absorption/reflection coefficients are also functions of q
The integrations over wavelength and angle can (generally) be performed in any order
L
L
L
L
L
q
j

## Slide 9: Terminology
Quantity | Symbol | Units | Notes
Radiant energy | Qe | J | energy
Radiant flux | Φe | W | radiant energy per unit time, also called radiant power.
Spectral power | Φeλ | W⋅m−1 | radiant power per wavelength.
Radiant intensity | Ie | W⋅sr−1 | power per unit solid angle.
Spectral intensity | Ieλ | W⋅sr−1⋅m−1 | radiant intensity per wavelength.
Radiance | Le | W⋅sr−1⋅m−2 | power per unit solid angle per unit projected source area.
Spectral radiance | Leλ | W⋅sr−1⋅m−3 | Radiance per wavelength, commonly measured in W⋅sr−1⋅m−2⋅nm−1 May also be expressed in terms of wavenumber or frequency.
Irradiance | Ee | W⋅m−2 | power incident on a surface, also called radiant flux density.
Spectral irradiance | Eeλ | W⋅m−3 | Irradiance per wavelength commonly measured in W⋅m−2⋅nm−1 May also be expressed in terms of wavenumber or frequency
Radiant exitance /emittance | Me | W⋅m−2 | power emitted from a surface.
Radiosity | Je or Jeλ | W⋅m−2 | emitted plus reflected power leaving a surface.
Radiant exposure | He | J⋅m−2 | 
Radiant energy density | ωe | J⋅m−3 | 
Volumetric Radiance | e | W⋅sr−1⋅m−3 | power per unit solid angle per unit volume.
Volumetric Spectral Radiance | El | W⋅sr−1⋅m−4 | Volumetric Radiance per unit wavelength/frequency/wavenumber
Luminance | Lv | Cd/m2 | Radiance corrected for spectral response of the human eye
Luminous Power, Illuminance, Luminosity, etc. |  |  | Spectral Power, Irradiance, Radiosity, etc. corrected for response of the human eye
Adapted from http://en.wikipedia.org/wiki/Radiance

## Slide 10: Intensity
The radiance (W⋅sr−1⋅m−2) is sometimes called the Intensity
The irradiance (W⋅m−2) is sometimes also called the Intensity
There is also something called the radiant intensity (W⋅sr−1) that is different from intensity, but may also be called the Intensity
The spectral radiant intensity (W⋅sr−1⋅nm-1) is often called the spectral intensity or intensity
The spectral radiance (W⋅sr−1⋅m−2) is sometimes called the spectral intensity or intensity
The irradiance (W⋅m−2) is sometimes also called the spectral intensity or intensity
There are other quantities that might also be called intensity which are different from the above
Intensity is what people say when they don’t know or care what they are actually reporting

## Slide 11: Wavelength, the 5th Dimension
In the flowfield, the volumetric spectral radiance is a function of position and time (4 dimension)
Radiation consists of electromagnetic waves (i.e. light)
An electromagnetic wave is characterized by a wavelength
Waves of different wavelength don’t (in general) interact with each other, so must be solved independently. This adds another dimension to radiation solutions
The energy of the radiation is determined by its wavelength, which is also related to the frequency or the wavenumber
Waves also have a polarization, but we’ll ignore that (assume randomly distributed, or circular)
Wavelength, l
E = hc/l
n = c/l
= 1/l
Energy (eV)
Wavelength (nm)
Frequency (Hz)
Wavenumber (cm-1)

## Slide 12: Computing Emission Coefficients
Emission coefficients depend on the species present in the gas
Through the magic of quantum mechanics, each species has particular allowed energy states
Transitions between allowed energy states cause radiation
n1
n2
n5
n3
n4
n7
n6
Example: N atoms
Energy
hn @ 149 nm
hn @ 174 nm
hn @ 868 nm
hn @ 821 nm
per unit solid angle, sr-1
Energy of photon (J)
Einstein coefficient(s-1)
Density of upper state (cm-3)
Lineshape function (nm-1)

## Slide 13: Molecular emission coefficients
Molecules have more states
  Electronic states

## Slide 14: Molecular emission coefficients
Molecules have more states
  Electronic states
  Vibrational states

## Slide 15: Molecular emission coefficients
Molecules have more states
  Electronic states
  Vibrational states
  Rotational states

## Slide 16: Building a spectrum
Example: FIRE II (Air entry, 10.7 km/s)
Continuum radiation, e.g.:
N+ + e- → N + hn
hn = DE = Ee - DErxn
Electron (kinetic) energy is not quantized – emits as a continuum

## Slide 17: Building a Spectrum
FIRE II Test Case

## Slide 18: Building a Spectrum
FIRE II Test Case

## Slide 19: Solving state populations
The density of flowfield species (from CFD) need to be converted to the density of excited states
Boltzmann (thermal) distribution:
4-Temperature (Tt,Tr,Tv,Te) Boltzmann distribution
Non-Boltzmann (non-thermal) distribution
Typically, it is necessary to solve non-Boltzmann in electronic modes. Rotational, vibrational modes close to thermal
Collisional excitation (heavy/electron) Absorption/Stim.Emission Spont.Emission State-specific reactions

## Slide 20: State populations: Boltzmann Plot
Boltzmann plot
  Population/Degeneracy is log-linear w.r.t energy at Boltzmann
  For molecules, need to normalize by qvr(Tv,Tr)
  Slope equals 1/Te
Some states tend to equilibrate with electrons instead of the ground state (Saha)
For molecules, may equilibrate with atoms or other species

## Slide 21: Radiation concerns for Different Destinations
N2/O2/(Ar)
Lunar return and beyond
High (>10 km/s) velocities
Radiation from atoms, ions
CO2/N2/(Ar)
Velocities not very high (5-6 km/s)
Density is low
Radiation from CO2 is concern
CN and CO radiation at higher velocity
H2/He/(CH4)
Titan
N2/CH4
Velocities are low (~5 km/s)
But CN is strong radiator
CO2/N2
Very high velocities (11 km/s)
Atomic species and ions (esp. C)
Later trajectory: CN, CO VUV, CO2
Velocities are fast (25 km/s)
But temperature is low
Radiation is negligible
Faster (27 km/s)
Radiation small
Fast (32 km/s)
Radiation from
H, H2, continuum
Ludicrous (46 km/s)
Massive continuum radiation
Optically thick

## Slide 22: Evaluating the Angular Integral
The hard (accurate) way :
  Ray tracing
  Full angular integration
Brute force approaches:
  Evaluation of 100s-1000s of lines of sight
  Can be slow
Other approaches: Monte Carlo, Finite Volume
  Not covered this talk

## Slide 23: Tangent Slab Approximation
Assume 1-D Semi-infinite geometry:
Integral may now be expressed as a 1-D integral, or a summation of transcendental functions.
Only one Line of Sight required
Limits: E/L = p (optically thick) to 2p (optically thin)
Good on the forebody to ~10%. Worse on shoulder, bad on backshell
.
.
.

## Slide 24: Putting it all together: radiative codes
NASA has two codes
  NEQAIR (Ames Research Center)
  HARA (Langley Research Center)
JAXA, ESA, ROSCOSMOS have their own codes
Several academic codes exist with varying levels of fidelity/options
HARA is packaged with LAURA CFD code. US release only.
NEQAIR is available for US and foreign release. Has pretty wide use through the scientific and engineering community:
https://software.nasa.gov/software/ARC-15262-1B
Read Inputs
Calculate State
Populations
Calculate el, al
n=1
Calculate
n=nLOS
Calculate
Calculate State
Populations
Calculate el, al
Calculate
Calculate
Write Outputs
…
…
…
…
…
Non-Boltzman
Solve (fast)
Emission/
Absorption
Coefficients
(slow)
Radiative
Transport
(relatively
fast)
CFD Code
ns,
Tt,Tr,Tv,Te,Tel

## Slide 25: Conclusions
Regions of relevance for radiative heating
  Important at High velocity, high density
  More important on Large vehicles
  Often important on the backshell
  Sometimes radiation surprises us (e.g. Mars backshell heating by CO2)
Radiative Heat flux is an integral over solid angle, wavelength, linear distance
  The fundamental measure of radiation is the emission coefficient, or volumetric spectral radiance
Radiation depends on wavelength – so does your TPS and sensors
Some radiation terminology and concepts to remember:
  Optical thickness
  Relationship of absorption to emission (blackbody fn)
  Radiance vs. Irradiance and Intensity
  Tangent slab vs. 3D radiation
  Molecular vs. Atomic vs. Continuum Radiation
  Boltzmann/non-Boltzmann
  Line of Sight
  Emission and absorption coefficients
Advanced topics not covered
  Escape factor and non-local effect
  Radiation/flowfield coupling
  Line broadening
  Excited state chemistry
  Spectral parameters
  The Planck Function
  Relationship of Boltzmann distribution to Planck’s function
  QSS Approximation
  Wavelength Classifications (vacuum ultraviolet, mid-infrared)
  Radiative Transport Equation