## Slide 1: Toxic dispersion Modeling & analysis
Cameron Mitchell

## Slide 2: About me
University of Colorado – Boulder
Major: Aerospace Engineering
  Minor: Physics
Safety and Mission Assurance (SA-E3)
  Institutional Division
    Technical Integration Branch
1st tour
12 siblings

## Slide 3: Importance
Level Of Concern (LOC)
½ IDLH
Acute Exposure Guidelines-1 (AEGL-1)
PPE
PPE
Irreversible adverse effects
Post-spill
Post-spill
Noticeable discomfort
Reversible
Preclear
Death
Accidental Spill
Liquid evaporates
Vapor carried downwind
Fueling Operations
Severity of health effects by distance

## Slide 4
Characteristics
  Used in MARSS/ERDAS
    Used by the 45th Space Wing
  Experiments in 50’s and 60’s
    Gained diffusion data
  Empirical data based off pool type releases
Limitations
  Designed for continuous, ground level, point source cold spills
  Little data was collected during stable nighttime conditions
  Model physics do not include clouds, condensation, or precipitation
Model comparison –
Ocean breeze/dry gulch (OB/DG)

## Slide 5: Model Comparison – Areal Locations of Hazardous Atmospheres (ALOHA)
Characteristics
  Maintained by NOAA and used by Boeing
  Can model multiple scenarios and hazards
  Incorporates clouds, and humidity into model
  Gaussian distribution model
Limitations
  Minimum puddle depth
  Very low wind speeds (< 3mph) result in concentration being larger than ALOHA predicts
  Does not account for wind shifts
  Assumes terrain is flat

## Slide 6: Modeling scenario
A max credible spill at Commercial Crew and Cargo Processing Facility (C3PF)
  Cold spill
  Size: 1 gallon
  Surface Area: 8 ft2
  Temp Lapse Rate: 0 deg
  Wind: 7 mph
Compounds involved
Hydrazine
(N2H4) - Lower concentration causes irritation
Monomethylhydrazine (MMH)
Dinitrogen Tetroxide (N2O4)
Nitrogen Dioxide (NO2) - Lower density results in larger distance traveled
Irritation of eyes, nose, throat
Dizziness
Headaches
Nausea
Seizures
Coma
Death
Airway inflammation
Cough/wheezing
Reduced lung function
Death

## Slide 7: OB/DG results

## Slide 8: ALOHA results

## Slide 9: Model results – c3pf
OB/DG model provides much more conservative results
Larger variation of AEGL-1 due to ALOHA values for Hydrazine being extremely small
 | OB/DG | ALOHA | % Diff
Preclear distance [ft] | 349 | 297 | 17.51%
LOC distance [ft] | 793 | 669 | 18.54%
AEGL-1 distance [ft] | 1932 | 1356 | 42.48%

## Slide 10: Going Forward
Use LATRA3D program to create a 3rd model
  Compare/contrast with previous models
  Explore model credibility
Perform hot spill analysis on applicable models
Perform blast overpressure analysis on applicable models
Acknowledgements
Mentors
Explosive Safety Officer
Range Safety Analyst

## Slide 11: Questions?

## Slide 12: References
ALOHA. (n.d.). https://response.restoration.noaa.gov/oil-and-chemical-spills/chemical-spills/response-tools/aloha.html.
Armstrong, Amber. (2013, April 2). Fuel Storage Area Operational Downwind Pre-Clear/Clear Distances for Fuel/Oxidizer Operations [PowerPoint slides]. 45 SW/SELR
Balimtas, L. (2021, January 26). New Artemis-Inspired Virtual Meeting Backgrounds. NASA. https://www.nasa.gov/feature/join-the-artemis-generation-with-new-artemis-inspired-virtual-meeting-backgrounds.
Missile Systems Safety Engineer, & Taddie, P. O., Derivation of the OBDG Diffusion Equation Used in MARSS (n.d.).
OFFICE OF RESPONSE AND RESTORATION. (2021, July 13). ALOHA. https://response.restoration.noaa.gov/oil-and-chemical-spills/chemical-spills/aloha.
Weather and Range Services Locations. (2017, November 8). KSC.Nasa.Gov. https://kscpartnerships.ksc.nasa.gov/Partnering-Opportunities/Capabilities-and-Testing/Support-Services/Weather-and-Range-Technology/Weather-and-Range-Services-Location-Maps