## Slide 1
Intent Modeling and Intent Conflict Probability Calculation for Operations in Upper Class E Airspace*
ETM Workshop July 21~22, 2021
Presented by: Min Xue
xTM subproject Technical Lead
NASA Ames Research Center, Moffett Field, CA
* M. Xue, J. Jung, J. Homola, and H. Yoo, “Intent Modeling and Conflict Probability Calculation for Operations in Upper Class E Airspace”, AIAA Scitech Forum, January 3-7, 2022

## Slide 2: What is flight intent?
In early ATM studies[1][2]
  Flight intent was mostly defined in the form of a flight plan, such as Trajectory Change Points (TCPs).
  Trajectory prediction was separated from flight intent formulation.
  Flight intent and trajectory prediction were mainly developed for tactical situations.
In UTM[3], flight intent is submitted and shared in the form of an operation plan, which should “indicate the four-dimensional volume of airspace within which the operation is expected to occur”. Furthermore, “segmentation of the 4D volume is encouraged to promote the efficient use of airspace”.
[1] Zhao, Y., Haissig, C., and Hoffman, M. J., “Analysis of Pilot Intent Parameters in Air Traffic Management,” Proceedings of the American Control Conference, Philadelphia, PA, 1998.
[2] Ruigrok, R., and Valent Clari, M., “The Impact Of Aircraft Intent Information And Traffic Separation Assurance Responsibility on En-route Airspace Capacity,”2003 ATM R&D Seminar, Budapest, Hungary, 2003.
[3] UTM Concept of Operations v2.0, FAA, 2020.

## Slide 3: Existing intent models in UTM and needs of advanced models
Static/dynamic 4D volume
Segmented dynamic volume
Problems with larger-than-necessary 4D volumes:
Inefficient use of airspace
Gaming and unfair use of airspace due to the arbitrariness
Unnecessary flight detours, interactions, and negotiations
Not making full use of known information (vehicle performance, wind, modeling technology, etc.)
Challenge with integrated and scalable airspace operations

## Slide 4: A flight-plan-based probabilistic flight intent model
Goal:
  Minimize the 4D intent volume within which the operation is expected to occur
  Provide accurate intent conflict probability that Cooperative Operating Practices (COPs) can rely on
Inputs:
  4D Flight plan
  Wind information (nowcast, forecast, including uncertainty)
  Vehicle trajectory control performance
Output: probabilistic 4D flight intent volumes

## Slide 5
Probabilistic intent model : fixed wing aircraft
Wind vector
(mean)
Wind vector
(std.)
cross-track error
along-track error
Assumption:
wind follows a Normal distribution
Step 1: calculate the nominal 4D trajectory
Step 2: calculate the error ellipses along the nominal trajectory.
Along-track error
caused by airspeed and wind errors
Grows with time
Cross-track error
Constant, depending on the vehicle lateral control performance

## Slide 6
Probabilistic intent model : balloon
Wind vector
(mean)
Wind vector
(std.)
Assumption:
wind follows a Normal distribution
Step 1: calculate the nominal 4D trajectory caused by wind mean vector
Step 2: calculate the error ellipses along the nominal trajectory.
Along-track error
caused by airspeed and wind errors
Grows with time
Cross-track error

## Slide 7
Probabilistic intent model : balloon with a ”flight plan”
A balloon climbs to a specified altitude - a flight plan with vertical segments
Wind vector
(mean)
Wind vector
(std.)
Mean direction changes when altitude increases
Operational intent for a balloon climbing in a wind field changing with altitude

## Slide 8
Verification with simulations
Balloon free-floating at the origin (0,0)
A total of 5,000 Monte Carlo simulations
A wind field following a Normal distribution
  Mean wind vector: 20 kts NE wind
  Wind std: 5 kts
Fe3 traffic simulator[2] is used:
  Trajectory generated @ 2Hz
  A dynamic model for the balloon
Wind vector
(mean)
Wind vector
(std.)

## Slide 9: Incorporate uncertain flight plans and longer look-ahead times
Wind
Mean = 20kts
Std. = 5 kts
50%
25%
25%
Flight plans uncertainty in spatial dimensions
Flight plans uncertainty in time
Can be simply used for longer look-ahead times
starts 5 min earlier (20% likelihood)
starts on time (60% likelihood)
starts 5 min later (20% likelihood)
Global Hawk
@ 340 kts
Global Hawk
@ 340 kts
6-hour mission
Notes: Hwang

## Slide 10
Calculating Intent Conflict Probability

## Slide 11: Calculation of intent conflict probability: Paielli’s method
Error ellipse modeling
Combined error ellipse*
Transformed combined error ellipse*
Assumptions:
Relative velocity vector is constant
Combined error ellipse is constant
Instant prob.
Total prob.
* R. Paielli, et. al. “Conflict Probability Estimation For Free Flight”, pp.588-596, Vol. 20, AIAA JGCD, 1997.

## Slide 12: Calculation of intent conflict probability: Hwang’s method
* Hwang, I., and Seah, C. E., “Intent-Based Probabilistic Conflict Detection for the Next Generation Air Transportation System, ”Proceedings of the IEEE, Vol. 96, No. 12, 2008, pp. 2040–2059.
Notes: Hwang

## Slide 13: Comparison of methods
Mean = 20kts
Std. = 5 kts
Paielli’s method overestimates and doesn’t tell when the intent conflict will happen.
The “ellipse overlap” method is inaccurate and unreliable.
Notes: Hwang

## Slide 14: Sample scenario: a balloon and a Global Hawk
Wind
Mean = 20kts
Std. = 5 kts
45%
1.6%
0.2%
Global Hawk starting now
Global Hawk starting 30 minutes later
Global Hawk starting 60 minutes later
Notes: 4Hwang

## Slide 15: Probability with uncertain flight plans
Mean = 20kts
Std. = 5 kts
50%
25%
25%
starts 5 min earlier (20% likelihood)
starts on time (60% likelihood)
starts 5 min later (20% likelihood)
Notes: Hwang

## Slide 16: Summary
Proposed a flight-plan-based intent model that can:
  Minimize the 4D intent volume within which the operation is expected to occur
  Provide accurate intent conflict probability that COPs can rely on
  Provide time-efficient calculation of intent conflict probability
  Prevent gaming and promote equal and efficient use of airspace
  Support uncertain flight plans and strategic planning (longer look-ahead time)
  Accelerate integrated airspace operation
As a foundational component of UTM/xTM like system, operational intent will be discussed at tomorrow’s breakout session.