## Slide 1: Mission Engagement Forum
Tools and Techniques

## Slide 2
Section | Topic | Presenter
Introduction | Welcome and Introduction | Tom Gitlin
NSN Purpose, Mission, Goals, Objectives, and Organization | An Overview of the Near Space Network | Vir Thanvi
NSN System Engineering | NSN System Engineering Function and Goals | Carlos Gomez-Rosa
NSN Services | NSN Services | Jacob Burke
DTE Services | Direct-to-Earth Overview | Jacob Burke
Relay Services | Space Relay Overview | Ted Sobchak
Mission Planning | Mission Planning Process Description | Jacob Burke
NSN Capabilities and Tools | Major Analytical Tools Used by NSN | Jacob Burke
Conclusion | The Benefits of Working with NSN | Tom Gitlin
Agenda

## Slide 3: Welcome and Introduction
Tom Gitlin
Mission Engagement Manager

## Slide 4: Welcome and Introduction
Serving the Space Communications and Navigation (SCaN) program office, the Goddard-managed Commercialization, Innovation, and Synergies (CIS) office and the Near Space Network (NSN) are implementing the commercialization of direct-to-Earth communications.
We advocate and foster strategic and tactical engagement with service providers and user communities.
We fully recognize and appreciate that all our efforts are ultimately focused on user support.

## Slide 5: Organization and Processes
In anticipation of the commercialization efforts, the Exploration and Space Communications (ESC) projects division reorganized to be more effective in integrating commercial service providers for direct-to-Earth (DTE) services.
Many CIS and NSN activities are planned to ensure a vibrant, capable community of providers are employed to support future mission concepts from inception through the mission life.

## Slide 6: Mission Engagement Working Group
The Mission Engagement Working Group (MEWG) within CIS is the single-entry point through which potential service-seeking missions can partner with ESC to begin the mission service acquisition process.

## Slide 7: Today’s Topics
This discussion will introduce participants to CIS and the NSN, and describe the services that the NSN provides.
The discussion will begin with an overview of CIS and NSN and a description of responsibilities. Subject matter experts will present brief overviews of the Advanced Communications Capabilities for Exploration and Science Systems (ACCESS), DTE services, mission planning processes and the major analytical tools used by NSN to ensure reliable communications and navigation support.
Participants will be encouraged to ask questions and suggest topics for future Mission Engagement activities.

## Slide 8: CIS Functions
The Commercialization, Innovation, and Synergies (CIS) office identifies opportunities, nurtures diverse relationships, and implements collaborative solutions to enhance capabilities and technologies in support of exploration and space communications. The office is dedicated to increasing the industry base for the Near Space Network and has three outreach focus areas, including:
MISSION ENGAGEMENT
CIVIL AND DEFENSE SPACE PARTNERSHIPS
INDUSTRY ENGAGEMENT

## Slide 9: Overview of the Near Space Network
Vir Thanvi
NSN Project Manager

## Slide 10: Who We Are
The Near Space Network is a single interface for missions seeking robust communications and navigation services.
We are an end-to-end network that blends the capabilities of government and commercial link providers to support highly proficient, cost-effective solutions to near-Earth missions.
Commercial Crew Program
SpaceX DM-2
Commercial Crew Program
SpaceX DM-2
McMurdo Station, Antarctica

## Slide 11: Functional Statement
The NSN project provides the project management leadership and subject matter expertise required to formulate, implement, operate and maintain a data system capable of connecting national and international data link providers with NASA users and partners via a virtual network management capability and routinely synchronizing systems, processes, and techniques with those of the U.S. private sector in order to provide NASA, other government agencies and partners optimal communications and navigation mission services.
Commercial Crew Program
SpaceX DM-2
Commercial Crew Program
SpaceX DM-2
Santiago Satellite Station

## Slide 12: Who We Are
We have the expertise necessary to see missions through a variety of communications and navigation milestones.
We actively engage with commercial industry to garner new partnerships and grow the U.S. space communications marketplace.
Commercial Crew Program
SpaceX DM-2
Commercial Crew Program
SpaceX DM-2
Near Space Operations and Control Center (NSOCC)

## Slide 13: Our Domain
Near Space: the volume of space from the Earth’s surface to 2,000,000 kilometers
Earth Proximity Region: a subset of near space; the volume from Earth’s surface to GEO (36,000 km) and the initial focus of service commercialization
Deep Space: volume of space starting at 2,000,000 km from Earth’s surface and proceeding out into the solar system and beyond and supported by the Deep Space Network
Earth Proximity: GEO and Below
HEO
Lunar
L1
SEL1
L2
SEL2
Not Drawn to Scale
 | FY20 | FY25 Projections
Number of Earth Proximity Missions | 43 missions | 62 missions
Number of HEO Missions | 5 missions | 4 missions
Number of Lunar Missions | 3 missions | 5 missions
Number of SEL1/2 Missions | 2 missions | 3 missions
Frequency Bands | S, X, Ku, Ka | S, X, Ku, Ka, Optical (Infrared)
Data Rates (DTE) | Up to 3.5 Gbps | Up to 3.5 Gbps
Data Rates (Earth Relay) | Up to 1.2 Gbps | Up to 1.2 Gbps
Data Rates (Lunar Relay) | N/A | Up to 100 Mbps
Space Internetworking Services | N/A | Delay/Disruption Tolerant Networking (DTN)

## Slide 14: What We Do
The Near Space Network empowers diverse missions up to two million kilometers away with communications and navigation services.
We connect customer missions to essential communications and navigation services.
We alleviate the need for users to do in-depth background research on which services or service providers best fit their mission.
We provide trusted and time-tested expertise to missions as they formulate, design, launch, and operate their missions.
We utilize government and commercial assets to achieve user goals through the entire mission lifecycle.
Near Space Network
NASA Network Assets
Commercial 1 Network Assets
Commercial N Network Assets

## Slide 15: 2020 Snapshot
Commercial Crew Program
SpaceX DM-2
Commercial Crew Program
SpaceX DM-2
SpaceX DM-2 Mission
2
Million Direct-to-Earth
Service Minutes
10
Million Space Relay
Service Minutes
16
Launches
Supported

## Slide 16: Customer Journey
Operations (NSOCC)
    LEOP / Critical Ops / Nominal Ops
    Orchestrated Govt. And Commercial Services Ops
    Virtual Network Management
      Mission Planning and Scheduling
      Data Transport Mgmt., Monitor, Control
Onboarding Providers
Onboarding Missions
Engagement with Potential Missions
Mission Viability Assessment
Hand off to NSN
457 / NSN Project
450.1 / CIS Office
Studies (Analysis of Alternatives)
Pre-Phase A: Concept Studies
Phase A: Concept & Tech Dev
Phase B: Prelim Design & Tech Completion
Phase C: Final Design & Fab
Phase E: O&M
Phase D: Sys I&T Checkout
Phase F: Closeout
459 / ACCESS Project
Manage Operations & Maintenance & Sustainment of GOCO SR and DTE assets
Technology Infusion
Development of commercially unavailable capabilities
Commercial Service Providers
Manage Operations & Maintenance & Sustainment of Commercial Assets
Technology Infusion / Capability Enhancements
Formulation
Implementation
Studies (Analysis of Alternatives)
Pre-Phase A: Concept Studies
Phase A: Concept & Tech Dev
Phase B: Prelim Design & Tech Completion
Phase C: Final Design & Fab
Phase E: O&M
Phase D: Sys I&T Checkout
Phase F: Closeout

## Slide 17: NSN Systems Engineering
Carlos Gomez-Rosa
NSN Systems Engineer

## Slide 18: NSN Systems Engineering: Function & Goals
Team includes Advance Planning, Conventional Systems Engineering, Communications Link Analysis, Network Coverage, Loading, and Modeling Analysis.
Accomplishes objectives through cross-cutting collaborations with other network support elements, such as Spectrum Management, Mission Services Integration, and Network Operations (including the service providers).
Ensures future missions needs are understood, solutions are devised to support current and future requirements, needed capabilities have plans for implementation, mission integration and interfaces are optimized, and the network assets to provide Direct-to-Earth and Space Relay services are effectively and efficiently utilized.
Technical Management
System Design
Requirement Definition
Technical Solutions
Design Realization
Integration and Implementation
Product Realization
Verification and Validation
Requirement & Interface Management
Technical Data/Baseline Management
Notes: The Near Space Network has been established to realize the vision of serving the customer missions through a single focal point throughout the entire lifecycle.
The NSN Systems Engineering team encompasses Advance Planning, Conventional Systems Engineering (establishment of overarching and consolidated effective processes, products, and tools), Communications Link Analysis, as well as Network Coverage, Loading, and Modeling Analysis teams.
The Systems Engineering team accomplishes the objectives through cross-cutting collaborations with other network support elements, such as Spectrum Management, Mission Services Integration, and Network Operations (including the Service Providers).
While the NSN Operations and Operations Support Elements ensure that the customer missions continue to receive reliable and secure services, the NSN Systems Engineering team concurrently works to ensure that future missions needs are understood, solutions are devised to support current and future missions’ requirements, needed capabilities have plans for implementation, mission integration and interfaces are optimized, and the network assets to provide Direct-to-Earth and Space Relay services are effectively and efficiently utilized.

## Slide 19: High-Level NSN Concept
The Near Space Network plans to orchestrate the customer missions’ services fulfilment via orchestrations amongst service providers that are part of the network, utilizing a virtual network manager.
The concept is to enable streamlined interfaces for the missions, potentially alleviating the burden on the missions to establish multiple interfaces.
The Near Space Network System Engineering team, in collaboration with network elements, is working to ensure effective interface artifacts get established during mission services integration phases that the providers can utilize to provide proficient services.
Notes: The Near Space Network plans to orchestrate the customer missions’ services fulfilment via orchestrations amongst service providers that are part of the network, utilizing a virtual network manager.
The concept is to enable streamlined interfaces for the missions, potentially alleviating the burden on the missions to establish multiple interfaces.
NSN Systems Engineering team will manage requirements at overarching network level, driven by SCaN requirements. In addition, the team will also manage the requirements related to NexTEra system, that is envisioned to be the virtual network manager that would realize the vision of single focal point for missions.
The Near Space Network System Engineering team, in collaboration with network elements, is working to ensure effective interface artifacts get established during mission services integration phases that the providers can utilize to provide proficient services.
The NSN Systems Engineering team will continue to support mission engagement rhythm to ensure that customer missions are well informed and involved with any evolutions that occur within the network.

## Slide 20: NSN Services
Jacob Burke
Advanced Planning Manager

## Slide 21: SCaN Networks - General Operations Regions
(≤ 2,000,000 km)
Near Space Region
NSN
Deep Space Region
DSN
CisLunar
Not to Scale
GEO
L1
L2

## Slide 22: NSN Services
The NSN provides four customer services:
  Mission Integration: development of service agreements, definition of interfaces, documentation, support of reviews, etc
  Mission Planning and Scheduling: performing link and loading analyses, spectrum management, supporting service requests, and generating and implementing operational schedules
  User Mission Data Transfer: forwarding command data and returning telemetry
  Position Navigation and Timing (PNT): navigation information and tracking data measurements and messages
1
3
4
2

## Slide 23: NSN Services
The NSN’s Direct to Earth (DTE) Comm and Nav services are provided by a blend of government owned and commercial link provider (CLP) stations. New CLPs are being procured.
The NSN’s Space Relay (SR) services are currently provided by the government owned TDRS constellation. Commercial providers are envisioned to be added in the future.
DTE
SR

## Slide 24: Direct to Earth (DTE) Overview
Jacob Burke
Advanced Planning Manager

## Slide 25
NSN Direct-to-Earth
The NSN uses ground-based antennas to provide direct-to-Earth (DTE) tracking, telemetry, and command services to NASA missions operating in the near-Earth (≤2Mil km) region. The NSN’s resources continuously evolve to meet the needs of the missions it supports.
NSN DTE support is used for:
High data rate missions
LEO and Polar-orbiting missions
Missions beyond LEO out to Lunar and Lagrange point distances

## Slide 26: NSN Direct-to-Earth (DTE) Coverage

## Slide 27: NSN Space Relay (SR) Services with TDRS
The Near Space Network uses a constellation of government owned geosynchronous satellites called Tracking and Data Relay Satellites (TDRS) to provide space communications and navigation services below and even above geosynchronous orbit.

## Slide 28: Space Relay Overview
Ted Sobchak
ACCESS Project Manager

## Slide 29
NSN provides Space Relay services through government-owned, contractor-operated assets that that are operated, maintained, and sustained by NASA.
Bent pipe data communication system comprised of a constellation of geosynchronous Tracking and Data Relay Satellites (TDRS) and a network of geographically diverse ground terminals.
Provides more than eight million minutes of communications services per year.
Key customers include the Hubble Space Telescope, Global Precipitation Mission, Expendable Launch Vehicles, the International Space Station and its visiting vehicles.
What is the Space Relay?

## Slide 30
User signals are demodulated and processed on the ground, which has allowed for the implementation of new wave forms and coding techniques enabling higher data rates and new customer concepts of operation.
KEY SERVICE ATTRIBUTES
Global coverage from 3 geosynchronous regions
24x7 coverage of all missions below geosynchronous orbit
High power beams that track users and minimize user communication payload size
Doppler compensation and correction of signals
Requires only ground stations in the US and its possessions
Space Relay User Overview

## Slide 31
Space Relay Constellation

## Slide 32
A Global Ground Segment

## Slide 33: Mission Planning
Jacob Burke
Advanced Planning Manager

## Slide 34: Mission Service Integration Process

## Slide 35: NSN Mission Service Integration Process
Mission Integration
Advanced Planning
Service Request
MEWG Screens and Dispositions Request
Requirements defined in NSN Questionnaire
Initial Analyses
Mission receives funding
Update Analysis
NSN Cost Estimate & LOC (if required)
Testing
(Compat, Verification, Validation)
Requirements documented in NSN Questionnaire
NSN Documentation (SLA, RFICD, NRD, Test Plan, etc.)
Reviews
(Test Reviews, NRR, MORR)
LEOP Support
Operations Support
EOL / Disposal Support

## Slide 36: NSN Capabilities and Tools
Jacob Burke
Advanced Planning Manager

## Slide 37: NSN Advanced Planning Overview
NSN Advanced Planning
Advanced planning is the set of mission analysis activities the NSN performs while working with new mission customers in pre-formulation.
These are typically missions that have not yet been funded for formulation and implementation (e.g. not yet selected for implementation by an AO process).
Typical NSN Advanced Planning Process:
Service Request
MEWG Screens and Dispositions Request
Initial Customer Meeting
(as required)
NSN Questionnaire to be completed
Q&A on Questionnaire Inputs
Link and Feasibility Analyses
Internal Review of Analysis Results
Customer Mission Reviews the Analysis Results
NSN Cost Estimate (if required)
NSN Letter of Commitment
(if required)

## Slide 38: NSN Analyses in Advanced Planning
Definitions of NSN Analyses:
Electromagnetic (RF or Optical) Link Analysis – The Link Budget is the primary planning and design tool for communication and PNT signals.
  In the Link Analysis we are attempting to answer questions such as, does the link close, what is the signal power margin at link closure, what is the required spacecraft EIRP to close the link, what is the max distance of link closure, or what is the minimum elevation angle at link closure?
Coverage Analysis – A modeling analysis that determines what network resources, if any, have geometric line-of-sight visibility with the customer during the required service times. This would include any mission operational constraints but is irrespective of any constraints and/or commitments for the network resources. This analysis considers each network resource as a “dedicated” resource.
Networks Feasibility Analysis – A modeling analysis whose goal is the determination of the networks’ ability to provide services to the specific mission being examined. It includes analysis of both coverage and loading based on commitments already made to other customers. It would also include all mission constraints on service times due to findings from the Link Analysis. This analysis considers the networks resources as “shared” resources.
Loading Analysis – A modeling analysis whose goal is to evaluate the effects on the existing and projected network load and the network’s ability to meet customer commitments as overall network parameters change (such as architecture changes and availability of different stations). Loading analysis is not a part of the standard Mission analysis.
The terms “Loading” and “Feasibility” are sometimes used synonymously. However, it is important to understand their differences. “Feasibility” is focused on the ability of the network to meet a specific mission’s requirements. “Loading” refers to an assessment of the network’s ability to meet all of its customer commitments, as is performed annually for the PPBE cycle.

## Slide 39: Networks Feasibility Analysis (NFA) Process
The NSN Advanced Planning Process showing an iterative flow between requirements definition, planning, coverage analysis, link analysis, and network feasibility analysis (NFA).
Coverage Analysis
Link Analysis (RF or Optical)
Feasibility Analysis
Research and Planning of Non-Standard Services/Usage
Q&A for
Requirements
Definition
NSN Costing Of Solution (as necessary)
Formulate a Viable Support Concept
Valid and Agreeable Solution
Customer Disagrees with Solution
No Valid Solution
Iterate on Requirements and ConOps
No Standard NSN Solution
Non-simplistic Link Design
Simplistic Link Design and Clear Visibilities
Non-clear visibilities
Non-simplistic Link Design
Non-clear visibilities
Links and Coverage Understood
Iterate on Requirements and ConOps
Iterate on Solution ConOps
Clear Requirements
For US Gov’t AO, NASA AO, competitive RFP, or reimbursable missions, prepare a planning estimate
For all other NASA missions, give presentation of NFA results, recommendations, and critical decision items
Repeat some or all of the processes as required
  Most Directed missions have 10+ NFA’s
  Most AO missions have 2 – 3 NFA’s

## Slide 40: NFA Example Flow 1: Simplistic Problem
Coverage Analysis
Link Analysis (RF or Optical)
Feasibility Analysis
Research and Planning of Non-Standard Services/Usage
Q&A for
Requirements
Definition
NSN Costing Of Solution
(as necessary)
Formulate a Viable Support Concept
Valid and Agreeable Solution
Customer Disagrees with Solution
No Valid Solution
Iterate on Requirements and ConOps
Non-simplistic Link Design
Simplistic Link Design and Clear Visibilities
Non-clear visibilities
Non-simplistic Link Design
Non-clear visibilities
Links and Coverage Understood
Iterate on Requirements and ConOps
Iterate on Solution ConOps
Clear Requirements
The NSN Advanced Planning Process showing an iterative flow between requirements definition, planning, coverage analysis, link analysis, and network feasibility analysis (NFA).
No Standard NSN Solution

## Slide 41: NFA Example Flow 2: More Complex Problem
Coverage Analysis
Link Analysis (RF or Optical)
Feasibility Analysis
Research and Planning of Non-Standard Services/Usage
Q&A for
Requirements
Definition
NSN Costing Of Solution
(as necessary)
Formulate a Viable Support Concept
Valid and Agreeable Solution
Customer Disagrees with Solution
No Valid Solution
Iterate on Requirements and ConOps
Non-simplistic Link Design
Simplistic Link Design and Clear Visibilities
Non-clear visibilities
Non-simplistic Link Design
Non-clear visibilities
Links and Coverage Understood
Iterate on Requirements and ConOps
Iterate on Solution ConOps
Clear Requirements
The NSN Advanced Planning Process showing an iterative flow between requirements definition, planning, coverage analysis, link analysis, and network feasibility analysis (NFA).
No Standard NSN Solution

## Slide 42: NFA Example Flow 3: Iterations on Design Solution
Coverage Analysis
Link Analysis (RF or Optical)
Feasibility Analysis
Research and Planning of Non-Standard Services/Usage
Q&A for
Requirements
Definition
NSN Costing Of Solution
(as necessary)
Formulate a Viable Support Concept
Valid and Agreeable Solution
Customer Disagrees with Solution
No Valid Solution
Iterate on Requirements and ConOps
No Standard NSN Solution
Non-simplistic Link Design
Simplistic Link Design and Clear Visibilities
Non-clear visibilities
Non-simplistic Link Design
Non-clear visibilities
Links and Coverage Understood
Iterate on Requirements and ConOps
Iterate on Solution ConOps
Clear Requirements
The NSN Advanced Planning Process showing an iterative flow between requirements definition, planning, coverage analysis, link analysis, and network feasibility analysis (NFA).

## Slide 43: Key Information
What do we need to know to start developing the mission’s C&N design in the advanced planning process?
Mission Operational Parameters:
Operating regime (LEO, GEO, HEO, Lunar, Lagrangian, Ascent)
Orbit details
Design constraints (Budget, SWaP)
Operational constraints (Scheduling flexibility)
Mission Requirements:
Communications requirements:
  Data Volume
  Latency
  Duty Cycle (contact separation times)
Position, Navigation, and Timing (PNT) requirements
      Position, velocity, and timing (PVT) and convergence time requirements
      PVT messages required (content, duty cycle)
      Predictive capability (computation)

## Slide 44: Key Information
  For link analysis, we need:
  At a minimum, with NSN making assumptions:
  Service Type: Direct to Earth (DTE), Space Relay (SR) Single Access (SA), or SR Multiple Access (MA)
  Frequencies
  Spacecraft EIRP & G/T
  Max Slant Range (Or Max Altitude and Minimum Elevation Angle)
  Communications Scheme (Modulation, Coding, BER, polarization, some of which can be assumed by NSN)
  Data Rate (Can be calculated or can be deduced from Data Volume Per day and a Coverage Analysis)
  Ground Station selections (can be assumed or can come from Coverage Analysis)
    All Parameters: see back-up slides

## Slide 45: Key Information
  For coverage and feasibility analyses, we need:
      Mission Timeline (Launch Date, LEOP and Operations timeframes)
      Orbit Profile
        Keplerian Elements, a state vector, TLE, IIRV, or a mission provided Ephemeris file
        For a constellation we will need to understand the orbit phasing/spacing
      Interfaces (compatibilities, frequency bands, communications schemes, max rates, max distances, etc., some of which can be assumed in the advanced planning stage)
      Contact Time Requested (or a Data Volume Required and an associated Data Rate)
      Latency constraints
      Station masking and on-board spacecraft masking
      Ranging requirements (Ranging methodology and accuracy needed, and whether science data is to be included in the TLM return link)
      Any other mission constraints effecting available communication time periods, view angles, interference, etc.

## Slide 46: Tools Used in NSN Advanced Planning
Communications Link Analysis Tools
  The NSN has link analysis tools that can simulate and analyze communication systems and their components for both SR and DTE mission customer interfaces.
  The NSN uses its link analysis tools to perform quantitative assessments of mission signal and communications ConOps designs, to support mission and/or network architecture trade studies, and to address various communications problems for NSN missions and network resources. Analyses include:
    Link Budget Analysis
    Dynamic Interference Modeling & Analysis
    Antenna Radiation Pattern Analysis
    End-to-End Communications Analysis for signal processing
    Propagation Modeling
CLASS (Communications Link Analysis and Simulation System) is the current tool used for all link analyses and definitions of network interfaces in the mission RF Interface Control Document (RFICD) for all NASA missions using NSN services.

## Slide 47: Tools Used in NSN Advanced Planning
NPAS (Network Planning and Analysis System) is the current coverage and loading analysis tool used by the NSN
Coverage and Loading Analysis Tools
  The NSN has coverage and loading analysis tools that can forecast future network loading to assess mission satisfaction and network performance against known and projected mission service levels.
  While the operational network scheduler systems of the NSN are located at WSC, the NSN can closely replicate the operational scheduling results by incorporating:
    the mission interfaces (i.e. which station/antenna services the missions are compatible with),
    mission requirements (e.g. how many contacts per schedule interval, such as a day, and in what timeframes), and
    antenna constraints (e.g. locations, altitudes, elevation masks (including trees, buildings, mountains, etc.)), and
    the NSN scheduling priority lists for both DTE and SR mission customers.
  The NSN primarily utilizes priority-based, deterministic scheduling, but when necessary, it is able to utilize dynamic scheduling algorithms to deconflict mission schedules.

## Slide 48: Tools Used in NSN Advanced Planning
Modern Commercial tools such as STK and Matlab are utilized by both Link Analysis and the Network Loading teams, and seamless integrations are possible for automation and visualization of NSN analyses.
  Note: STK and MATLAB are licensed external software and are not owned/managed by NASA.
Flexibility of NSN tools: Additional users, network resources, new or advanced communications schemes, new scheduling algorithms and new technologies can be integrated easily into the current NSN toolset.
A trade study is under way to determine what tools best fit the NSN’s needs going into the future.
The NSN can draw on other tools within the SCaN Community as necessary.
  ESC and Code 500 have developed a number of other custom tools for various studies requested by SCaN and missions including a Network Architecture Analysis Tool and a Lunar Outpost Coverage Tool among others.
  SCaN HQ is currently leading the development of a commercial network assessment and design tool called Commercial Systems for Mission Operations Suitability (CoSMOS) which is being discussed for applicability to NSN.

## Slide 49: Conclusion
Tom Gitlin
Mission Engagement Manager

## Slide 50
WHY CHOOSE NSN?
We’re connected.
We are progressing direct-to-Earth commercialization efforts.
We are connecting experts from industry, academia, and government and international agencies to create a community of innovators.
We have a proven record of success with a variety of missions and service providers.
We provide a single-entry point for all Near Space Network missions.
Potential for more stable pricing, particularly for mission extension operations
High level of transparency regarding communication system operations, status, troubleshooting activities, and administrative communication
Notes: Direct-to-Earth commercialization efforts are in progress
  Our mission is to find commercial partners so you can achieve the communication and navigation goals of your mission
  We are creating relationships for the partnerships you will need
  We are developing a vast network of technology vetted by NASA subject matter experts
Proven record of success with dozens of missions and different service providers for missions scaling from tech demos to flagship campaigns
Extremely high reliability and low risk service provider

## Slide 51
We have decades of experience from mission concept definition through mission completion.
  Set the standard in communication link analysis
  Provide spectrum guidance
  Utilize predictive network capacity analytical tools
  Employ engineers experienced in latest flight hardware designs and capabilities
  Engage in-house subject matter experts
We provide reasonable mission lifecycle costs.
  Avoids the risk and expense of setting up a custom communications team for each mission
  Scaling improves lifecycle costs
WHY CHOOSE NSN?
We’re experienced.
Notes: We have decades of mission support experience from early mission concept definition all the way through mission completion
  Set the standard in communication link analysis
  Provide clear and comprehensive spectrum guidance
  Utilize predictive network capacity analytical tools to ensure high availability for your mission
  Employ engineers experienced in the latest flight hardware designs and capabilities
  Have a significant number of subject matter experts in house, with a large, diverse base to draw upon to resolve any challenges
We provide reasonable overall mission lifecycle costs
  Avoids the risk and expense of setting up a custom communications team for each mission
  Better life cycle costs due to scaling

## Slide 52
We are the trusted NASA services provider.
We are well-positioned to support LEO, MEO, GEO, HEO, LaGrange and Lunar missions.
  We are creating paths for exploring new capabilities to expand services.
  We establish processes to maintain and evolve the network with industry standardization and interoperability.
  We have comprehensive end-to-end data security measures and are compliant with the National Institute of Standards and Technology.
WHY CHOOSE NSN?
We’re capable.

## Slide 53: Back-up

## Slide 54: DTE Link Parameters Needed for Analysis

## Slide 55: SR Link Parameters Needed for Analysis

## Slide 56: NSN Questionnaire

## Slide 57: NSN Questionnaire (cont’d)

## Slide 58: NSN Questionnaire (cont’d)