## Slide 1: Modeling of Electrolyte Conductivity in a Solid State Cathode Structure
Malik Satterwhite-Austin
Vesselin Yamakov and Yi Lin
2021 Summer Student Research Symposium

## Slide 2: Background
SABERS – (Solid-state Architecture Batteries for Enhanced Rechargeability and Safety).
Solid-State battery:
  Non flammable solid materials inside of the battery.
Illustrated by: Dr. Rocco Viggiano, Dr. James Wu, and Dr. John Connell

## Slide 3: SESAM
Solid Electrolyte Sphere Approximation Model
Spherical particles are randomly placed inside the cathode
The cathode is then compressed to achieve the optimal density
Power output:
  Electron and Lithium-ion conductivity
Figure 1: 40 nm sized spheres randomly placed in a simulated cathode
Figure 2: The spheres in Figure 1 condensed to reach a higher density
Figure 3: The tested power output in the cathode.

## Slide 4: Why/Purpose
Create an improved cathode composition for an efficient solid-state battery
Study the conductivity, σ, of the cathode constructed of conductive and non-conductive randomly compacted spheres subject to Maxwells equation:
  σ/σo = ½(3p- 1);
  p = fraction of conductive spheres
  σo = conductivity at p=1

## Slide 5: Results
Chart: 10,000 spheres of D=40 nm, 66% density
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Sigma0 | 1 | 0.79396 | 0.61218 | 0.43611 | 0.28835 | 0.16027 | 0.065579 | 0.0099864 | 1.4338e-05 | 1.1278e-05
1/2(3(1-f)-1 | 1 | 0.85 | 0.7 | 0.55 | 0.4 | 0.25 | 0.1 | -0.05

## Slide 6: Maxwell’s formula for conductivity
Maxwells' formula presumes that equation 1/2(3p-1) (p= fraction of the conductive spheres) will approximately equate to the corresponding σ/σo point
The more insulating spheres added the less conductive the mixture becomes
Simulated data is consistent with the experimental data published by J.P. FITZPATRICK PHYSICS LETTERS 47A (1974) 207.

## Slide 7: Next Steps/Outlook/Future Work
With more time on this project, I would:
  Continue to study Maxwells equation using different sized spheres in my simulations.

## Slide 8: Acknowledgements
My Mentors: NASA Internship Team:
Dr. Yamakov Langley Research
Dr. Lin Center
My lab mates:
Brandon Walker, Elizabeth A Barrios, April Rains,
and Jystin Lewis

## Slide 9: Questions