## Slide 1: Conceptual Thermal Control System Design for a Lunar Surface Habitat Greg Schunk, Stephanie Babiak and Dawn Naville Thermal Analysis and Control Branch/MSFC Brian Evans Jacobs Space Exploration Group/ESSCA
Presented By Greg Schunk
Thermal & Fluids Analysis Workshop TFAWS 2021 August 24-26, 2021
Virtual Conference
TFAWS Active Thermal Paper Session

## Slide 2: Overview
The NextSTEP, Appendix A-Habitation BAA was released in April 2016, with a focus on developing deep space habitation concepts, engineering design and development, and risk reduction efforts leading to a habitation capability in cislunar space.
The objective of the NextSTEP solicitation is to identify habitation concepts that can support extensive human spaceflight missions in the Proving Ground (around and beyond cislunar space) while encouraging application to commercial habitation capabilities in low-Earth orbit.
Government sponsored Moon-to-Mars Surface Habitat (SH) conceptual design studies and trades have been undertaken to develop a Reference Architecture for the SH Thermal Control System (and other systems) to inform and exchange lessons learned, ground rules & assumptions and requirements with NextSTEP partner efforts.

## Slide 3: Lunar Surface Habitat Architecture Reference
Crew: | 2-4
Power: | 15 kW
Night Power: | 2 kW
Eclipse: | 100 hours
Pressure: | 10.2 psia
Lifetime: | 15 years
Mission Duration: | 30-60 days
Mass: | 12 mT
Habitable Volume: | 175 m3
Location: | Lunar South Pole

## Slide 4: Surface Habitat ATCS Description
The Surface Habitat (SH) Thermal Control System (TCS) is designed to reject 15 kWt of heat under nominal conditions at the Lunar South Pole with 48 m2 of radiator surface area (double sided). The two-sided deployable thermal radiators are derived from the International Space Station (ISS) design utilizing a honeycomb core.
The TCS has two loops with HFE 7200 as the working fluid externally and a 60/40 water/propylene glycol mixture as the internal fluid.
The internal TCS loop is subdivided to provide both low and moderate temperature service analogous to the ISS ATCS. The low temperature service is intended primarily for ECLSS (e.g. condensing heat exchanger) as well as any payloads that may require it.
Heritage hardware is utilized where possible.
ISS HRS Radiator
X-38 Sublimator

## Slide 5: Conceptual Surface Habitat Thermal Control System
Internal ATCS parsed into low and moderate temperature loops.
An external recuperator is added to thermally manage (i.e. minimize) parasitic heat loss during Survive-the-Night.
Thermal
Radiator
#1
Thermal
Radiator
#2
LTL
Interface
Heat
Exchanger
MTL
Interface
Heat
Exchanger
Sublimator
Cond
Hx
Low Temp
Loads
Moderate Temp
Loads
Internal Pump
Package
External Pump
Package
External
Cold-Plates
From Airlock
To Airlock
Mixing
Valve
Mixing
Valve
Mixing
Valve
HFE 7200
Propylene Glycol/Water
Vent
Regenerative
Heat
Exchanger
Recuperator

## Slide 6: Surface Habitat TCS Resource Estimates
Primary drivers for mass and power are the thermal radiators and circulating fluid pump packages. Internal volume for TCS < 1 m3.
MLI included for reference but is generally considered part of the SH inflatable structure. Outer beta cloth covering not included but surface optical properties are a factor in thermal heat leak in to and out of the habitat.

## Slide 7: Surface Habitat Thermal Radiator Design
Based on ISS deployable radiator design with modifications.
ISS design may not be retractable in lunar gravitational field without modification.
Coolant tube diameter layout and geometry modified to support single phase HFE 7200 instead of freezable Ammonia.
Aluminum face-sheet thickness increased from 0.010” to 0.015” for performance improvement.
Four panels per side (~3 x 2m) needed for total area of 48 m2 in SH application.
Aluminum Face-sheet (0.015”)
Aluminum
Honeycomb
Inconel/Stainless Steel Tube
Conductive Bracket/Saddle
Bracket Assembly
Cross Section
~1.00’’
Test Orientation
ISS Deployed

## Slide 8: Thermal Radiator Panel Design
Manifold
Out
In
2m
3m
8”
8”
At 8” spacing with a nominal fluid temperature of 283K and 0.015” aluminum face-sheets, the predicted temperature profile is shown with an estimated fin efficiency of 85.5%.
Fluid enters the radiator via a manifold that splits the flow into 15 tubes. A balance between the spacing of the tubes and radiator fin efficiency is desired.

## Slide 9: Surface Habitat Heat Rejection and Growth Scenarios
Number of Radiator Panels Required vs Heat Rejection
Radiator Temperature 283K, 85% Efficiency
4-4
3-3-3
5-5
4-3-4
4-4-4
Baseline
8 Panel (4-4)
9 Panel
(3-3-3)
10 Panel
(5-5)
11 Panel
(4-3-4)
Results are for Primary Landing Site, a Lunar Ground Temperature 217K (-70oF) and Worst Case Orientation.

## Slide 10: Surface Habitat Survive-the-Night
A 100-hour eclipse is possible at the Lunar South Pole. Additional heat will be needed to maintain the SH inflatable volume and thermal radiators above minimum temperature limits during the dormant Survive-the-Night scenario.
Survive-the-Night may vary in duration and with partial illumination.
To maintain the SH at minimum temperature would require 1550 watts to offset the heat leak through the inflatable volume.
The radiator fluid (HFE 7200) has a lower working temperature limit of -100oC (-148oF) and a freezing point of -137oC (-215oF).
To maintain the radiators just above the working or freezing temperature limits would require nearly continuous heat of at least 3840 or 1353 watts, respectively.
For the fluid working limit, the un-mitigated (i.e. no counter-measures) total energy required would be 540 kWh for the 100 hour Survive-the-Night scenario.
Mitigation strategies to reduce the power requirement, including energy storage, preconditioning the SH (warm) and stowing or reconfiguring the radiators, are under consideration

## Slide 11: Simulation for Survive-the-Night Heat Load (3.7 kWt)
Re-generative fuel cell sized to provide 2.5 kWe which results in 1.2 kWt waste heat introduced into the external loop via cold plate mounting.
LTL I/F HX
MTL I/F HX
1100 kg/hr
2487 kg/hr
Regen
HX
Moderate
Temperature
Loads
Low
Temperature
Loads
20%
62oF (290K)
42oF (279K)
11oF (262K)
Radiator
52oF
(284K)
62oF
(290K)
50oF
(283K)
17oF
(265K)
Bypass=84%
=0.85
=0.85
=0.83
1000 W
1500 W
Q=3.7 kW
64oF
(291K)
14oF (263K)
19oF
(266K)
20oF
(267K)
Bypass=96%
Bypass=0%
HFE 7200
(173K)
-143oF
(176K)
-152oF
(171K)
1200 W
Fuel Cell
Pump
Mixing Valve
Shutoff Valve
Heat Load
Cold Plate

## Slide 12: Mitigation Strategy: Retractable Radiators
α=150°
α=0°
α=30°
α=60°
a
Stowing the thermal radiators for Survive-the-Night could greatly reduce energy storage requirements. Heat leak from the Surface Habitat is fixed.

## Slide 13: Mitigation Strategy: Habitat Temperature
In addition to the heat loss from the radiators, approximately 1550 watts of make-up heat would be needed to maintain the SH habitable volume above 68oF.
The heat required is proportional to the habitat internal temperature as shown.
Allowing the un-crewed habitat temperature to sink below respirable atmosphere limits could save on the total energy required (and ostensibly returned before crew arrives).
Pre-heating the habitat to store energy may also mitigate the energy required. For the nominal case, the energy required would be 155 kWh.
For both the thermal radiators and habitat, the total required stored energy would be ~550 kWh if no measures to reduce the heat loss are taken.

## Slide 14: Mitigation Strategy: Lower Emittance Covering
Baseline design utilizes beta cloth for the outer covering of the inflatable structure. Beta cloth has an infrared emittance of 0.9 (along with a solar absorptance 0.4).
Reducing the emittance could significantly reduce heat leak during survive-the-night periods.
Some margin to reduce the emittance exists as the surface habitat has a net heat loss during daylight operations. Prefer not to have a net heat gain during operational periods because of extra load for the TCS.
The potential energy savings is on the order of 50 kWh.
Beta Cloth e=0.90
New Material e=0.70
Savings
50 kWh

## Slide 15: Thermal/Power Growth Sensitivity
Normalized Thermal Radiator and
Photovoltaic Panel Mass vs Electrical Power
Radiator
Photovoltaic

## Slide 16: Survive the Night Considerations for Growth
Chart: Number of Thermal Radiator Panels (-)
| 8 | 9 | 10 | 11 | 12
 | 75.4891 | 80.3746 | 89.1361 | 93.8853 | 100.6522
 | 679.4015 | 723.3711 | 802.2245 | 844.9679 | 905.8698
Thermal Energy needed to
Maintain Habitat
Total Re-generable Fuel Cell Mass Needed to Thermally maintain Habitat*
Parasitic Thermal Radiator Loss
Habitat Heat Leakage
2H2O  O2 + 2H2
Hardware Mass
Thermal can utilize both electrical energy and waste heat from fuel cells. Fuel cells nominally produce 400 kWe/kg with 243 kWt/kg of waste heat at 62.2% efficiency.
*Ian Jakupca, NASA Glenn Research Center, Overview of Regenerative Fuel Cell Technologies for Space Applications, 29 July 2020

## Slide 17: Overall Thermal/Power Growth Sensitivity
Regenerative Fuel Cell (Fixed Hardware Only)
Photovoltaic Mass
Thermal Radiator Mass
Total Radiator/Photovoltaic/Fuel Cell
Mass vs Electrical Power
Regenerative fuel cell represents energy needed to support a 100 hour Survive-the-Night Scenario for a given thermal radiator size.
Habitat heat leak does not vary with electrical power sizing and is approximately a constant 1550 watts during the eclipse.
Electrical power and thermal heat rejection correlate 1:1 in the Survive-the-Night scenario.
Additional EPS mass may be required to scale up peripheral components for increased power requirements.
Thermal Control System needs additional pump power to support increased power levels (included).

## Slide 18: Summary
A TCS Reference Architecture for a 30 day Surface Habitat mission to the Lunar South Pole is presented.
TCS and energy storage needs may be minimized through Survive-the-Night mitigation strategies.
Additional thermal radiator capacity is needed to accommodate EPS growth. With the current TCS deployable radiator design, approximately 500 kg per 10 kWe is needed for the radiator panels.
  Some additional TCS pump power will also be required to accommodate larger heat dissipation.
Fixed re-generable fuel cell mass impacts for Survive-the-Night appear to be slight with increasing radiator size. The amount of water or oxygen/hydrogen required for Survive-the-Night energy storage will grow with increased radiator size (approximately 240 kg per 10 kWe).
Future plans are to continue refinement of the SH ATCS concept with detailed thermal modeling to provide performance predictions and support trade studies.