## Slide 1: Emerging Spaceborne Technologies for Oil Spill Detection
Ben Poulter
NASA Goddard Space Flight Center, Earth Sciences Division
AP Press; https://www.smithsonianmag.com/smart-news/keystone-pipeline-leak-was-twice-big-previously-thought-180968722/

## Slide 2: Informing climate policy with scientific monitoring from space
Transient Climate Response to Cumulative Emissions
NASA’s 2017 Decadal Survey
IPCC AR6 WGI SPM

## Slide 4
EARTH SYSTEM
OBSERVATORY
Water and Energy in the Atmosphere
Particles in the
Atmosphere
Large-scale Mass
Redistribution
AEROSOLS
CLOUDS, CONVECTION
AND PRECIPITATION
MASS CHANGE
SURFACE BIOLOGY
AND GEOLOGY
SURFACE DEFORMATION
AND CHANGE
Earth Surface & Ecosystems
Earth Surface Dynamics

## Slide 5
Sentinel 1 (SAR C)
Applying Spaceborne Assets to Pipeline Leaks:
Offshore detection
Offshore oil spill detection is fairly mature using synthetic aperture radar (SAR)
Dark patches versus speckled background – enable classification
Numerous false positives w ice and natural features (kelp, cloud shadow, pollen, plankton etc.)
AP Video; https://fox8.com/news/watch-video-shows-massive-underwater-fire-in-gulf-of-mexico-after-pipeline-ruptures/
Chaturvedi et al., 2020
Gulf of Mexico ‘eye of fire’

## Slide 6
Applying Spaceborne Assets to Pipeline Leaks:
Onshore detection
The challenge:
Massive infrastructure > 500,000 miles
Leaky, since 2002: +7000 liquid leaks (+2000 gas)
Observing requirements:
Sensitivity
  Spectral features
  Spatial resolution
Wall-to-wall coverage
Frequent revisit
  Tasking/pointing
  Cloud/smoke/snow avoidance or removal
Mature detection algorithms
  Incl. flow quantification
Low latency / delivery time
GAO & USDOT

## Slide 7
Applying Spaceborne Assets to Pipeline Leaks:
Onshore gas detection
Cusworth et al. 2021
Strong spectral absorption features in SWIR by CH4 and CO2
Detection of gas blowouts and leaks (CH4 and CO2) has advanced rapidly
Multiple national (JAXA, ESA, NASA) & commercial satellites (GHGSat) used for GHG retrievals
Estimate of fluxes possible using mass balance approach

## Slide 8
Direct detection:
Hydrocarbon contamination in soil shows strong spectral features at 1720-1760 nm and ~2300 nm (e.g., Achard et al., 2021)
Indirect detection:
Vegetation health, or greenness, is reduced with hydrocarbon exposure (Adamu et al., 2018)
Applying Spaceborne Assets to Pipeline Leaks:
1. Sensitivity – spectral features
Andreoli et al., 2007
Adamu et al., 2018

## Slide 9
Applying Spaceborne Assets to Pipeline Leaks
1. Sensitivity: spatial resolution
Yokoya et a., 2017 (IEEE)
https://www.dlr.de/content/en/images/2018/2/desis-hyperspectral-earth-observation-instrument-on-the-iss_30167.html
https://www.asi.it/en/earth-science/prisma/

## Slide 10
Applying Spaceborne Assets to Pipeline Leaks
2. Wall to wall coverage
NASA ARC

## Slide 11
Applying Spaceborne Assets to Pipeline Leaks
3. Frequent revisit
Li et al., 2020
September 16, 2021 launch of Landsat 9
S2A+B
L8+9
S2A+B
L8+9
NASA SBG
5-day hyperspectral revisit (by late 2020s)

## Slide 12
Approaches (using optical data)
Spectral indices, spectral matching, spectral unmixing, vegetation health, cloud+smoke removal
Issues
False positives from vegetation and soil (wet), or shaded slopes,
Needs
Flow rates (rate of spread, depth)
Applying Spaceborne Assets to Pipeline Leaks:
4. Detectability and classification
Dubucq et al., 2019

## Slide 13
Applying Spaceborne Assets to Pipeline Leaks
5. Data latency
https://www.nasa.gov/directorates/heo/scan/services/networks/nen
Near Earth Network & expanding downlink option (Ka band)
“Application Ready” data
Onboard payload module
Satellite retrievals
Science data system
User
(<24 hours)

## Slide 14
Opportunities to expand onshore leak detection methods using hyperspectral instruments
  New missions & pathfinders
    NASA SBG, ESA CHIME, ASI PRISMA, DESIS, HISUI,
  Advances in algorithms using machine learning, deep learning, AI
  Calibration and validation needs
    Spectral libraries (hydrocarbon/soil mixtures, stressed vegetation indices)
    Historical ground data needed for testing existing imagery archives
Applying Spaceborne Assets to Pipeline Leaks:
Outlook and opportunity
Andreoli et al., 2007
NASA SBG