## Slide 1
GFSSP Software Demo
André LeClair & Alok Majumdar
Propulsion Systems Department
NASA/Marshall Space Flight Center
andre.c.leclair@nasa.gov
alok.k.majumdar@nasa.gov
Virtual Thermal & Fluids Analysis Workshop
August 24-26, 2021

## Slide 2: Outline
Introduction & Overview
Mathematical Formulation
Resistance Options
Fluid Options
Demonstration Models

## Slide 3: Background
GFSSP stands for Generalized Fluid System Simulation Program
It is a general-purpose computer program to compute pressure, temperature and flow distribution in a flow network
It was primarily developed to analyze
  Internal Flow Analysis of a Turbopump
  Transient Flow Analysis of a Propulsion System
GFSSP development started in 1994 to provide a generalized and easy to use flow analysis tool
Selected for NASA Software of the Year award in 2001

## Slide 4: Availability
GFSSP is free for NASA civil servants and on-site contractors. Contact:
  andre.c.leclair@nasa.gov
  alok.k.majumdar@nasa.gov
GFSSP is also free for other civil servants and for contractors with federal contracts
  Request at software.nasa.gov
An Educational Version, without user subroutine capability, is available for universities
More information is available at the website:
  www.nasa.gov/gfssp

## Slide 5
NETWORK FLOW OR
NAVIER-STOKES ANALYSIS (1/2)
Computational Fluid Dynamics
(CFD)
Navier Stokes Analysis
(NSA)
Network Flow Analysis
(NFA)
Finite Difference
Finite Element
Finite Volume
Finite Volume
Finite Difference
GFSSP

## Slide 6
NETWORK FLOW OR
NAVIER-STOKES ANALYSIS (2/2)
Navier Stokes Analysis
Suitable for detailed flow analysis within a component
Requires fine grid resolution to accurately model transport processes
Used after preliminary design
Network Flow Analysis
Suitable for flow analysis of a system consisting of several components
Uses empirical laws of transport process
Used during preliminary design

## Slide 7: Network Definition
Fluid Nodes: mass and energy equations are solved for pressures and enthalpies
Fluid Branches: momentum equation is solved for flowrates
Fluid-to-Solid Conductors: Convection
Solid Nodes: Solve solid energy equation for wall temperatures
Fluid Boundary Nodes Set boundary P/T
Solid-to-Solid Conductors Conduction

## Slide 8
Units External (input/output) Internal (inside GFSSP)
  Length - in, ft, m, cm - feet
  Area - in2, ft2, m2, cm2 - feet2
  Pressure - psia, kPa - psf
  Temperature - °F, °R, °C, K - °R
  Mass injection - lbm/s, kg/s - lbm/s
  Heat Source - Btu/s, W - Btu/s
Sign Convention
  Mass input to node = positive
  Mass output from node = negative
  Heat input to node = positive
  Heat output from node = negative
UNITS AND SIGN CONVENTIONS

## Slide 9: MATHEMATICAL FORMULATION
Principal Variables
  Unknown Variables Available Equations to Solve
  1. Pressure 1. Mass Conservation Equation
  2. Flowrate 2. Momentum Conservation Equation
  3. Fluid Temperature 3. Energy Conservation Equation of Fluid
  4. Solid Temperature 4. Energy Conservation Equation of Solid
  5. Species Concentration 5. Conservation Equations for Mass Fraction of Species
  6. Mass 6. Thermodynamic Equation of State

## Slide 10
MASS CONSERVATION EQUATION
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
k = 2
Fluid
Mixture
Fluid
Mixture
Node
i
GOVERNING EQUATIONS
Note : Pressure does not appear explicitly in Mass Conservation Equation although it is earmarked for calculating pressures

## Slide 11
MOMENTUM CONSERVATION EQUATION
i
j
g
q
w
r
i
r
j
.
m
ij
Axis of Rotation
Branch
Node
Node
GOVERNING EQUATIONS
Represents Newton’s Second Law of Motion
Mass X Acceleration = Forces
Unsteady
Longitudinal Inertia
Transverse Inertia
Pressure
Gravity
Friction
Centrifugal
Shear Stress
Moving Boundary
Normal Stress
External Force

## Slide 12
ENERGY CONSERVATION EQUATION
k = 2
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
Fluid
Mixture
Fluid
Mixture
Node
i
GOVERNING EQUATIONS
  Energy Conservation Equation can be written in Enthalpy or Entropy
Enthalpy Equation
Rate of Increase of Internal Energy =
Enthalpy Inflow - Enthalpy Outflow + Heat Source
Based on Upwind Scheme

## Slide 13
Successive Substitution Form
Solid Node
Ambient Node
Fluid Node
GOVERNING EQUATIONS
SOLID ENERGY CONSERVATION EQUATION

## Slide 14
PROGRAM STRUCTURE

## Slide 15
1. Pipe Flow
2. Flow Through a Restriction
3. Non-Circular Duct
4. Pipe Flow with Entrance
& Exit Losses
5. Thin, Sharp Orifice
6. Thick Orifice
7. Square Reduction
8. Square Expansion
9. Rotating Annular
Duct
RESISTANCE OPTIONS

## Slide 16
RESISTANCE OPTIONS
10. Rotating Radial Duct
11. Labyrinth Seal
12. Face Seal
13. Common Fittings
& Valves
14. Pump Characteristics
15. Pump Power
16. Valve with Given Cv
17. Viscojet
P
18. Control Valve

## Slide 17
RESISTANCE OPTIONS
U
19. User Defined
20. Heat Exchanger Core
21. Parallel Tube
22. Compressible Orifice
23. Labyrinth Seal (Egli Correlation
24. Fixed Flowrate
25. Cartesian Grid

## Slide 18
FLUID OPTIONS
ID Number | SOURCE / FLUID | ID Number | SOURCE / FLUID | ID Number | SOURCE / FLUID
1 | GASP He | 51 | GASPAK He | 69 | GASPAK Kr
2 | GASP CH4 | 52 | GASPAK CH4 | 70 | GASPAK Propane
3 | GASP Ne | 53 | GASPAK Ne | 71 | GASPAK Xe
4 | GASP N2 | 54 | GASPAK N2 | 72 | GASPAK R-11
5 | GASP CO | 55 | GASPAK CO | 73 | GASPAK R-12
6 | GASP O2 | 56 | GASPAK O2 | 74 | GASPAK R-22
7 | GASP Ar | 57 | GASPAK Ar | 75 | GASPAK R-32
8 | GASP CO2 | 58 | GASPAK CO2 | 76 | GASPAK R-123
9 | GASP F2 | 59 | GASPAK H2 (para) | 77 | GASPAK R-124
10 | GASP H2 (para) | 60 | GASPAK H2 (normal) | 78 | GASPAK R-125
11 | WASP H2O | 61 | GASPAK H2O | 79 | GASPAK R-134A
12 | RP-1 Tables | 62 | GASPAK RP-1 (liq) | 80 | GASPAK R-152A
 |  | 63 | GASPAK Isobutane | 81 | GASPAK N2F3
33 | Ideal Gas | 64 | GASPAK Butane | 82 | GASPAK NH3
 |  | 65 | GASPAK Deuterium | 84 | GASPAK H2O2
37 | User Fluid 1 | 66 | GASPAK Ethane | 86 | GASPAK Air
38 | User Fluid 2 | 67 | GASPAK Ethylene |  | 
39 | User Fluid 3 | 68 | GASPAK H2S |  | 

## Slide 19: Demonstration Models

## Slide 20: 1. Blow Down of Pressurized Tank

## Slide 21: 1. Blow Down of Pressurized Tank
Analytical Solution:

## Slide 22: 2. Waterhammer
400 ft
D = 0.25 inch
Liquid Oxygen at 500 psia and 200 R
Flowrate = 0.1 lb/s
Valve closes in 100 milliseconds
450 psia

## Slide 23: 2. Waterhammer
GFSSP results compared to Method of Characteristics

## Slide 24
3. Sudden Valve Opening / Priming
Top: Schematic of the Pipeline System with ball-valve location.
Side: Ball-Valve Opening History
Parameters: a = Lg/LT
PR = pR/p0

## Slide 25
3. Sudden Valve Opening

## Slide 26
4. Transfer Line Chilldown
NBS Chilldown Experiment

## Slide 27
5. Tank Pressurization
Change in ullage and propellant volume.
Change in gravitational head in the tank.
Heat transfer from pressurant to propellant.
Heat transfer from pressurant to the tank wall.
Heat conduction between the pressurant exposed tank surface and the propellant exposed tank surface.
Mass transfer between the pressurant and propellant.

## Slide 28: Questions?
For more information:
  www.nasa.gov/gfssp
Or contact:
  alok.k.majumdar@nasa.gov
  andre.c.leclair@nasa.gov