## Slide 1: A Multi-Disciplinary Analysis Framework for the Design of Small Launch Vehicles
Presenter: Dr. Bradford Robertson

## Slide 2: Small Launch Vehicles
As spacecraft become smaller and less expensive, the need for small launch vehicles increases[14]
  Launching small payloads with medium/large vehicles results in disproportionately large and unnecessary costs
Number and rate of launches of small payloads expected to increase[14]
Small launch vehicles have low costs and short lead time[11], [12]
Ability to conduct research in areas inaccessible by satellites (sounding rockets)
Small launch vehicles do not require full launch pads[13]
  Ground launch: temporary launch sites
  Air launch
  Weather balloon launch
Introduction
Design Environment
Sample Problem
Results
Conclusion

## Slide 3: Framework
Construct a flexible environment for physics-based launch vehicle (LV) sizing utilizing multi-disciplinary analysis (MDA)
Disciplines are synthesized and their respective tools can be integrated to size a launch vehicle
In order to analyze the DOE options, a set of analysis capabilities are necessary
  These are defined by what is needed to correctly predict the behavior of the LV
The main part of the LV is the motor
  Mass Properties
  Propulsion Profile
To figure out the achievable acceleration
  Drag of the LV
  Overall Mass
Calculating the best path to orbit
Introduction
Design Environment
Sample Problem
Results
Conclusion
Propulsion
Aerodynamics
Structures
Trajectory
Introduction
Sample Problem
Discipline 1
Discipline 2
Discipline 3
Discipline 4

## Slide 4: Propulsion: Solid Motor Analysis Code (SMAC) [1]
SMAC is a preliminary design tool for solid rocket motors
Its capabilities include
  Mass estimation through regressions
  Geometric burn simulation
  Ballistic analysis
  Prediction of thrust performance
Introduction
Design Environment
Sample Problem
Results
Conclusion
Introduction
Sample Problem
Burn Progression Through Time
Propellant Properties
Grain Geometries
Nozzle Design
Operational Characteristics
Materials
Performance
Weight Regressions
P(t), T(t), (t)
Burn time
Nozzle Size
SMAC

## Slide 5: Structures: Launch Vehicle Structural Analysis (LVSA)
Focuses on structural dynamic analysis with sizing capability
Assumes axisymmetric structures
No longer relying on CAD descriptions of structure
Covers most launch vehicles: missiles, core/boosters, etc.
Allows for analytical representations
Core functionality is describing vehicle
  Geometric description
  Profile definition
  Component definition
  Assembly definition/layout
  Load initialization
Introduction
Design Environment
Sample Problem
Results
Conclusion
Introduction
Sample Problem

## Slide 6: SMAC/LVSA Loop
The DOE-provided variable is the diameter of the stage
  Need to know allowable space for the fuel
Between SMAC and LVSA there is a loop that converges on radius of the fuel grain ()
  SMAC determines insulation thickness ()
  LVSA determines casing thickness ()
After for a stage is within allowable tolerance between the runs that stage is considered to have converged
  Process results if a converged for each stage
Introduction
Design Environment
Sample Problem
Results
Conclusion
Introduction
Sample Problem
SMAC
LVSA
4
8
Convergence Loop

## Slide 7: Aerodynamics and Trajectory
Missile DATCOM is an aerodynamic design tool that was created for preliminary missile design
  The code is flexible enough to be used to analyze small launch vehicles[2],[3]
  Ability to incorporate fins and wings if required
POST2 enables trajectory analysis of vehicles operating near one attracting body
  Attempts to target the desired orbit
  Optimizes Payload Mass
Introduction
Design Environment
Sample Problem
Results
Conclusion
Introduction
Sample Problem

## Slide 8: Integration
Introduction
Design Environment
Sample Problem
Results
Conclusion
Introduction
Sample Problem
Missile DATCOM
POST
10
7
9
1
2
3
Inputs
SMAC
LVSA
4
5
8
6
Convergence Loop

## Slide 9: Sample Problem
Goal: Exercise the MDO environment for an SLV sample problem
Steps taken to achieve this:
  Develop a methodology to support SLV design
  Demonstrate methodology for a design analysis
Requirements for sample problem
  Target orbit:
    Inclination: 47 deg
    3636.6 by 3651.4 nautical mile orbit
    Launched from Wallops Launch Facility
  Design Constraints:
    Four Stage
    All solid rocket motors
    Axisymmetric body
    Uniform diameter
Design Environment
Introduction
Sample Problem
Results
Conclusion
Results
Sample Problem
Introduction

## Slide 10: DOE Setup
Design Environment
Introduction
Sample Problem
Results
Conclusion
Results
Sample Problem
Introduction
I.
II.
III.
IV.
D
D
Continuous and Discrete variables
DOE |  |  |  | 
Per Stage (x4) | Stage 1 | Stage 2 | Stage 3 | Stage 4
Stage Length | 8 - 10 ft | 4 - 6 ft | 2 - 4 ft | 0.5 - 2 ft
Outer Fuel Diameter | 0.05 - 0.1 | 0.1 - 0.15 | 0.1 - 0.15 | 0.1 - 0.15
MEOP target | 1000 - 1500 | 1000 - 1200 | 500 - 700 | 500 - 700
Inner Fuel Diameter | 0.05 - 0.07 | 0.07 - 0.1 | 0.07 - 0.1 | 0.07 - 0.1
Nozzle Length | 0.2 - 0.8 ft | 0.2 - 0.8 ft | 0.2 - 0.6 ft | 0.1 - 0.3 ft
Grain Type | bates, finocyl, star | bates, finocyl, starocyl, star | bates, finocyl, starocyl, star | bates, finocyl, starocyl, star
Propellant | TP-H-1148 | TP-H-1202, TP-H-3340, TP-H-1148 | TP-H-1202, TP-H-3340, TP-H-1148 | TP-H-1202, TP-H-3340, TP-H-1148
With of Fuel Fin | 0.03 - 0.05 | 0.05 - 0.07 | 0.05 - 0.07 | 0.05 - 0.07
Fuel Star Points | 2,3,4 | 2,3,4 | 2,3,4 | 2,3,4
Overall |  |  |  | 
Launch Vehicle Diameter | 1.5 - 2 ft |  |  | 
Nose Shape Parameter | 0.2 - 0.4 |  |  | 

## Slide 11: Results
Using a value function
  Min LV Mass
  Max Payload Mass
There is no single architecture that could be considered “the best”
The results show that there is a trade off to be made, with the solution space forming a Pareto Frontier
The space can also be discretized based on SLV Diameter forming 3 clear bands
  Based on this decisions can be made on what diameter ranges should be further exploded based on the designers desired payload and SLV mass
Design Environment
Introduction
Introduction
Design Environment
Sample Problem

## Slide 12: Case: SLV 4855
Design Environment
Introduction
Introduction
Design Environment
Sample Problem
TP-H-1148
TP-H-1202
TP-H-1148
TP-H-1202
DOE |  |  |  | 
Variable Name | Stage 1 | Stage 2 | Stage 3 | Stage 4
Stage Length (ft) | 9 | 6 | 3.23 | 1.15
Outer Fuel Diameter (% of total) | 0.098 | 0.15 | 0.13 | 0.11
MEOP target (psi) | 1174.5 | 1017 | 548.8 | 511.15
Inner Fuel Diameter (% of total) | 0.059 | 0.094 | 0.096 | 0.087
Nozzle Length (ft) | 0.59 | 0.23 | 0.52 | 0.19
Grain Type | Star | Starocyl | Finocyl | Star
Propellant | TP-H-1148 | TP-H-1202 | TP-H-1148 | TP-H-1202
With of Fuel Fin (%of total) | 0.03 | 0.06 | 0.054 | 0.051
Fuel Star Points | 4 | 3 | 2 | 2
Overall |  |  |  | 
Launch Vehicle Diameter | 1.7 ft |  |  | 
Nose Shape Parameter | 0.23 |  |  | 
 | Dry Mass (lb) | Fuel Mass (lb) | Payload Mass (lb)
Stage 1 | 425 | 1916 | 38.73
Stage 2 | 210 | 1286 | 
Stage 3 | 95 | 601 | 
Stage 4 | 36 | 232 | 
Total | 766 | 4035 | 38.73

## Slide 13: Case: SLV 4855
Design Environment
Introduction
Introduction
Design Environment
Sample Problem

## Slide 14: Summary
There are numerous possible design alternatives for an SLV
  Without exploring the design space, it is impossible to say just how optimal the solution is
  It is also infeasible to perform a detailed design for each option
Our methodology leads to a manageable exploration of the design space
  As part of the methodology, an analysis tool was developed that integrates physics-based tools for:
    Propulsion (SMAC)
    Aerodynamics (Missile DATCOM)
    Structures (LVSA)
    Trajectory (POST2)
Introduction
Design Environment
Sample Problem
Results
Conclusion
Created a methodology capable of analyzing/reducing the design space
The output of our sample problem leads to a selection of Pareto optimal designs that can be graduated to subsequent design cycles for further analysis

## Slide 15: Citation
Ritter, Paul Andreas, "Optimization and Design for Heavy Lift Launch Vehicles. " Master's Thesis, University of Tennessee, 2012. https://trace.tennessee.edu/utk_gradthes/1197
Bushnell, P. S., Jr, Busse, J.R.,Kraft, G.E Leffler,M.T., “A compendium of NASA Aerobee sounding rocket launchings for 1966” NASA Goddard Space Flight Center Greenbelt, July 1, 1967
Bodies of Revolution having Minimum Drag at High Supersonic Airspeeds; Eggers Jr, A. J.; Resnikoff, Meyer M.; Dennis, David H.; NACA Technical Report 1306, 1957.
4. Zapata, Edgar, "Nano-Launcher Technologies, Approaches, and Life Cycle Assessment" NASA Kennedy Space Center Cocoa Beach, October 16, 2014
NASA Technical Reports Server (NTRS). (n.d.). Retrieved September 11, 2020, from https://ntrs.nasa.gov/search.jsp?R=20150004148 2019-08-31T11:16:10 00:0
Jones, Jonathen E., Kibbey Timothy P., Cobb, C. Brent, Harris, Lawanna L., “Enabling Dedicated, Affordable Space Access Through Aggressive Technology Maturation”, Conference: Space Propulsion 2014, May 10,2014
Bhat, B. N. (2018). Aerospace Materials and Applications. Reston, VA: American Institute of Aeronautics and Astronautics.
Matt Bille, Robyn Kane, “Practical Microsat launch Systems: Economics and Technology”, Conference: Small Satellite Conference, 2013
https://bisresearch.com/industry-report/global-small-launch-vehicle-market.html
Orbital ATK., Minotaur IV User Guide., 2015.
NASA Sounding Rocket Program. NASA. 24 July 2006. Retrieved 10 October 2006.
What is a Sounding Rocket?. Research Aircraft. NASA. Retrieved 10 October 2006.
General Description of Sounding Rockets. Johns Hopkins University Sounding Rocket Program. Retrieved 10 October 2006.
National Research Council. 2000. The Role of Small Satellites in NASA and NOAA Earth Observation Programs. Washington, DC: The National Academies Press. https://doi.org/10.17226/9819.
Foust, J., “Ten companies bid for NASA small launch vehicle contract,” SpaceNews Available: https://spacenews.com/ten-companies-bid-for-nasa-small-launch-vehicle-contract/.