## Slide 1: Space Communications & Navigation
Lunar Communications & Navigation Interoperability Standards Engineering Interchange Meeting
September 15, 2021
WE WILL BEGIN SHORTLY

## Slide 2: Agenda
Introduction: Andrew Petro
LunaNet & Interoperability Document Overview: Dave Israel
Discussion, Questions, & Feedback
If you have questions or comments during the session:
  Submit in the chat
  Submit anonymously at https://www.menti.com/f9m6fdcqdd

## Slide 3: References
NASA Lunar Interoperability Specification: https://go.nasa.gov/3BQrCOk
2020 Request for Information Lunar Communications Relay and Navigation Services: https://bit.ly/3EkILle
SpaceOps 2021 LunaNet Architecture and Concept of Operations: https://go.nasa.gov/3nuBklx
The Future Lunar Communications Architecture (IOAG Report): https://bit.ly/3CeHBWy
International Communication System Interoperability Standards (ICSIS) Rev A: https://bit.ly/3hzsG1k
Recommendations on the Selection of End-to-end Space Internetworking Protocol: https://bit.ly/3k7zcOI

## Slide 4: Introduction
Andrew Petro Space Communications and Navigation Human Exploration and Operations NASA Headquarters, Washington D.C.
September 15, 2021

## Slide 5
Upgraded DSN and other assets, including commercial stations
Framework of standards for open, interoperable networks,
data, PNT & other services
Diverse, evolving constellation with multiple users and providers
Additional relay capability
Far Side
Missions
Other Robotic Missions
Artemis Surface Missions
Communication and navigation infrastructure lowers the barriers to entry for new missions and capabilities and supports expanding robotic and human activities on the Moon.
Surface Communications and Navigation Assets
Overview of Early Lunar Communications Architecture
SOUTH
POLE
Orbital Relays
LINKING LUNAR USERS TO EARTH & TO EACH OTHER
Gateway
Earth Stations
Orbiting Spacecraft
Users
LunaNet

## Slide 6: Lunar Communications & Navigation Evolution
Now to 2024
NEEDS
• Far side science mission
• South Pole human exploration
• PNT services
IMPLEMENTATION
• Existing ground networks
• Initial relay capabilities
• LunaNet compatibility
2024 to 2028
NEEDS
• Global coverage
• Longer, more complex
missions, greater mobility
IMPLEMENTATION
• Comprehensive relay network
• Surface comm & nav assets
• Full LunaNet services
2028 and Beyond
NEEDS
• Sustained surface and orbital presence
IMPLEMENTATION
• Evolution of infrastructure
• Infusion of new technology

## Slide 7: A Few Key Points
Our purpose today is to introduce a draft of the Interoperability Standards and Conceptual Framework and begin the dialogue with potential commercial service providers.
  Questions
  Feedback on the content
  Request for working group participants
These standards are not intended to be owned and controlled by NASA alone.
We are planning interaction with international partner agencies and expect more input from NASA and other U.S. government agencies.
We intend to be consistent with applicable existing standards, as much as possible.
We want to be inclusive of all potential providers and users but complete a useful product in a reasonable time.

## Slide 8: Integration of Feedback & Completion of Baseline Document
Introductory Meetings with industry, space agencies, other U.S. government agencies: September 2021
Working Groups, facilitated by NASA, to include members from private companies, national space agencies, and other U.S. government agencies
    Communications Services Working Group: focus on Initial Operations Capabilities (IOC)
    PNT Services Working Group: focus on IOC
    Enhanced Operations Capabilities (EOC) Working Group
Complete Baseline Document (IOC Sections): by end of January 2022
Complete Baseline Document (EOC Sections): by end of June 2022

## Slide 9: LunaNet Overview and Interoperability Document Walkthrough
Dave Israel Architect Exploration and Space Communications Projects Division Goddard Space Flight Center dave.israel@nasa.gov
September 15, 2021

## Slide 10: LunaNet Services
Position, Navigation, & Timing Services
Precise position, velocity, and time for autonomous navigation and collision avoidance
Fusion of multiple data types including radiometrics, optimetrics, celestial navigation, optical nav, terrain relative nav, and Global Navigation Satellite System (GNSS)
Broadcast service supplies time transfer and metric tracking to synchronize users
Detection and Information Services
Alerts for events such as space weather, collision avoidance, and surface impact predictions sent to all LunaNet subscribers
Mission sensors, for space weather and other measurements, distribute information services to other users via LunaNet information services
LunaSAR: Distress detection and notification services
Networked Communication Services
Critical data transmitted in real time
Data aggregated and transmitted in store-and-forward mode from orbiting and surface relays
Data exchanged among lunar users with no need for transfer to and from Earth
Data sent on demand by user or scheduled to better manage Earth stations loading & spectrum use
Science Services
Use radio frequency (RF) & optical assets (part of) as scientific instruments
Supports Radio & Radar Sciences, Radio Astronomy / Very Long Baseline Interferometry (VLBI), and other space sciences

## Slide 11: LunaNet Segments

## Slide 12: LunaNet Standard Services and Interfaces

## Slide 13: LunaNet Service Provider Interfaces

## Slide 14: Spacelink Interfaces and Frequency Bands

## Slide 15: LunaNet Communications Services
User Applications Simplified Protocol Stack
LunaNet Applications Simplified Protocol Stack

## Slide 16: LunaNet PNT Services

## Slide 17: Augmented Forward Signal

## Slide 18: LunaSAR Data Path ConOps

## Slide 19: Document Walkthrough

## Slide 20: Questions or Comments?

## Slide 21: References
NASA Lunar Interoperability Specification: https://go.nasa.gov/3BQrCOk
2020 Request for Information Lunar Communications Relay and Navigation Services: https://bit.ly/3EkILle
SpaceOps 2021 LunaNet Architecture and Concept of Operations: https://go.nasa.gov/3nuBklx
The Future Lunar Communications Architecture (IOAG Report): https://bit.ly/3CeHBWy
International Communication System Interoperability Standards (ICSIS) Rev A: https://bit.ly/3hzsG1k
Recommendations on the Selection of End-to-end Space Internetworking Protocol: https://bit.ly/3k7zcOI

## Slide 22: Thank You!
For any follow-up questions or comments, please email:
nasa-commercialsynergies@mail.nasa.gov