## Slide 1: HSRL-2 Status Update September 28, 2021
NASA LaRC HSRL-2 Team - Rich Ferrare, Chris Hostetler, John Hair, Sharon Burton, Marta Fenn, Dave Harper, Tony Cook, Amy Jo Scarino, Marian Clayton, Eduard Chemyakin, Joe Lee
Contributions from:
Sue van den Heever, Joe Schlosser, Snorre Stamnes, Bastiaan van Diedenhoven

## Slide 2: Summary of HSRL2 CAMP2Ex Products
Available Data Products
Aerosol Extensive Measurements (data(hdf5) and imagery(png) archived)
  Particulate backscatter profiles (355, 532, 1064 nm)
  Aerosol extinction profiles and AOT (355 and 532 nm)
Aerosol Intensive measurements (data(hdf5) and imagery(png) archived)
  Particle depolarization profiles (355, 532, 1064 nm)
  Extinction-to-backscatter ratio profiles (355 and 532 nm)
  Angstrom exponent profiles
    Extinction: 355-532
    Backscatter 355-532, 532-1064
Aerosol Type (data(hdf5) and imagery(png) archived)
Aerosol Optical Thickness (data(ICARTT) archived)
Mixed Layer Heights (data(ICARTT) archived)
Mean aerosol extinction and backscatter values within and above the Mixed Layer (data(ICARTT) archived)

## Slide 3
Aerosol
Backscatter (532 nm)
Mixed Layer Heights
Aerosol
Extinction (532 nm)
Aerosol Backscatter and Extinction Increase with Height in Mixed Layer associated with Increase in Relative Humidity (RH)
Dropsondes provide relative humidity profiles
Mixed Layer Height (Zi) derived from HSRL2 aerosol backscatter profiles
As RH increases with height within Mixed Layer, fine mode hygroscopic particles take on water, so aerosol backscatter and extinction increase.
These plots show behavior averaged over all of CAMP2Ex
Relative
Humidity
Water Vapor
Mixing Ratio
Dropsonde
Profiles
dropsonde
dropsonde
Relative Humidity
Normalized
Aerosol
Backscatter
Normalized
Aerosol
Extinction
Sept. 23, 2019
Sept. 23, 2019

## Slide 4: Multiwavelength Lidar Aerosol Microphysical Retrievals
3β
2α
Aerosol
Backscatter:
355 nm
532 nm
1064 nm
Aerosol
Extinction:
355 nm
532 nm
+
3+2 (i.e. 3 backscatter + 2 extinction) considered the minimum information content necessary for microphysical retrievals (Bockmann et al, 2005)
Information content and sensitivity studies suggest concentrations and effective radius can be retrieved well (Burton et al., 2016)
INVERSION
particle size distribution
size, refractive index, wavelength
lidar measurements
References
Müller et al, 1999, Applied Optics
Veselovskii et al. 2002, Applied Optics
Müller et al, 2014, AMT
Sawamura et al., 2017, ACP
Lidar microphysical retrievals of effective radius and concentrations compare well to airborne in situ measurements
TCAP (Müller et al., 2014, AMT)
DISCOVER-AQ (Sawamura et al., 2017, ACP)
Notes: PLACEHOLDER
Fix spacing
Consider using charts from Patricia’s instead
Add reference for Patricia’s paper also.

## Slide 5: HSRL2 Microphysical Retrievals – October 3, 2019
East of Manila
Larger particles
Lower SMF, Vol. Conc.
West of Manila
Smaller particles
Higher SMF, Vol. Conc.
Aerosol Backscatter (532 nm)
Fine Mode Effective Radius
Submicron Fraction
Fine Mode Volume Conc.
west
east
west
east
west
east
Manila
west
east
Preliminary

## Slide 6: Aerosol Fine Mode Effective Radii from HSRL2 and LARGE (ambient RH)
Joe Schlosser (U of A) computed fine mode effective radius (and other aerosol properties) at ambient RH using LARGE LAS aerosol measurements
Preliminary

## Slide 7: HSRL2 and RSP retrievals of column fine mode effective radius
Preliminary

## Slide 8: HSRL2 and RSP retrievals of column Submicron Fraction Extinction (AOD)
Preliminary

## Slide 9: HSRL2 Liquid Cloud Measurements (Ongoing Research)
Cloud Top Height:
  (1.25 m vertical resolution) based on backscatter gradient and absolute backscatter value – can provide cloud tops for tenuous clouds missed by radar
Cloud Lidar Ratio:
  HSRL technique provides unique method to normalize the measurements above the cloud (i.e. account for the attenuation above the cloud top)
  Observe variations in lidar ratio that are larger than those determined from the size parameters from polarimeter. There is interest into better understanding these differences and their variability. For example, do drizzling clouds reduce the lidar ratio?
CAMP2Ex offers opportunity to explore combined measurements from HSRL2, radar, and polarimeter

## Slide 10: Cloud Top Extinction Derived from HSRL2 measurements
Cloud Top Extinction - (mean and profile) – uses decay of signal within cloud to derive extinction. Integrated backscatter profile provides particulate transmission and extinction. Integrated depolarization profile provides multiple scattering fraction (Hu et al., 2006).
Particulate Transmission
Extinction (Profile)
Extinction (Mean)
Cloud Droplet Number Concentrations (CNDC): Cloud Top Extinction combined with scattering cross sections derived from polarimeter (or radar) size distributions

## Slide 11: Cloud Lidar Ratio Derived from HSRL2 measurements
CAMP2Ex provides opportunity to evaluate the lidar ratio at cloud top using detailed airborne remote sensing and in situ measurements.
What is the Lidar Ratio?
Lidar Ratio: Sc= extinction/backscatter
Note that backscatter here is the 180 degree backscatter
Why would we care about it?
Does not depend on number concentration, therefore it is an intensive parameter which provides information on the microphysics of the cloud
The lidar ratio is a function of the particle size distribution and the index of refraction of the cloud droplets
It can be directly compared to retrievals of the size distributions calculated from remote sensing and in situ measurements
Lidar Ratio is calculated from the layer integrated backscatter (γ’) within the cloud. Also requires AOD above the cloud.
Does drizzle impact lidar ratio? Radar profiles might help provide insight on this question.
Higher lidar ratios are present and are typically associated with mixed phase clouds. Are there other factors controlling higher lidar ratios?
Can the high vertical resolution profiles provide additional insight on these retrievals?