## Slide 1
Adapting Waste Processing for Space Applications
David Rinderknecht
NASA, Kennedy Space Center

## Slide 2: Why Trash is a Problem in Space
Represents mass with little to no benefit.
Mass requires fuel, not only for launch, but for transit injection and orbit insertion burns (multiplicative).
Occupies spacecraft volume.
Produces odor.
A Crew of 4 will produce 2122 kg/yr of complex waste.
NASA Image ID: iss063e066984
NASA Image ID: iss030e020707

## Slide 3
1 day
1.5 kg
5 ‘footballs’
7 days
10 kg
32 ‘footballs’
30 days
43.5 kg
138 ‘footballs’
One Astronaut’s Trash Production
550 days (Mars mission)
800 kg of waste
2536 ‘footballs’

## Slide 4: Current State of the Art (ISS)
Placed into plastic bags, wrapped with duct tape
Collected into crew stowage bags
Placed into available logistics module
Eventual de-orbit and burn-up on re-entry
Not practicable for Moon or Mars missions
  No atmosphere to burn up
  Planetary protection
  Mass budget
NASA Image IDs: iss017e015468/ARC-2008-ACD08-0218-00b9/sts073-356-018x

## Slide 5: Waste Processing Technology
Air Lock Ejection
Heat Melt Compactor
Trash to Gas (TtG)
  Combustion
  Incineration
  Oxidative Ozonation
  Steam Reforming
  Plasma (microwave, torch, gasification, pyrolysis)
  Pyrolysis
Incinerator/Gasifier
Advanced Organic Waste
Gasifier (AOWG)
Orbital Syngas Commodity
Augmentation Reactor (OSCAR)
Microwave Assisted
Pyrolysis (MAP)
Plasma Pyrolysis
Torrefaction Processing
Unit (TPU)
Plasma Gasification

## Slide 6: Space Mission Considerations
Limited Physical Footprint (Mass, Volume)
Limited power
Limited crew time
Space Environment (Gravity, Radiation)
Reliability and Maintainability
Safety
Conversion Reactor
Disposable or Reusable Products
Inputs?
Recycle
Minimal Sizing and Mass
Energy Recovery
Automation
Gravity independent unit operations (ex. Water Separation)
Testing campaigns
Commodity recycling
Waste

## Slide 7: Orbital Syngas Commodity Augmentation Reactor (OSCAR)
Goals:
Demonstrate combustion-based waste conversion in microgravity using waste representative of expected feedstock in space
Evaluate results to inform future design
Results:
Comparable conversion in microgravity/lab testing
Confidence for continued development
https://doi.org/10.2478/gsr-2021-0006

## Slide 8: A Mass Constrained Problem
Trash Receptacle
Feed Mechanism
Conversion Reactor
Effluent Treatment
Methanation (Sabatier)
Electrolysis
Solid Transport
Size Constrained
No Gravity
User Friendly
Containment
No Gravity
Solids removal
Tar/VOC destruction
Water Removal
Oxygen Recovery
2nd Reactor Pre-treat (Halides, Sulfur compounds, particulate etc)
CO2
CO
CH4
H2
H2O
O2
Water cleanup

## Slide 9: The Future of Waste Management in Space: Integration
https://arc.aiaa.org/doi/10.2514/6.2013-5326

## Slide 10: Acknowledgements
NASA Human Exploration and Operations Directorate: Advanced Exploration Systems Logistics Reduction program
Mike Ewert
Jim Broyan
KSC TtG/OSCAR Team
  Annie Meier
  Ray Pitts
  Joel Olson