## Slide 1: Engineering Directorate Materials & Processes Laboratory Capabilities
Blue Origin Engine TIM November 2021
H. DeWitt Burns
Deputy Director, Materials & Processes Laboratory

## Slide 2
NASA Marshall Space Flight Center
Materials & Processes Laboratory
M&P Technical Information System (MAPTIS)
Materials Usage Agreements (MUAs) & Materials Usage List (MIUL)
Small projects – ISS payloads, ECLSS
Physical Sciences Infomatics Database
Engineering Support Office
Lab Lead Engineers Office
Metallic Materials & Processes Division
Nonmetallic Materials & Advanced Manufacturing Division
Fracture Control and Damage Tolerance
Nondestructive Evaluation
Mechanical Testing / Hydrogen Test Facility
Tribology / Metrology
Chemistry & Contamination Control
• SLS Element Design Lead Engineers
• Human Landing System Lead
• Advanced Manufacturing Lead
• In-Space Manufacturing Lead
Space Environmental Effects
Ceramics & Ablatives
Polymeric Materials – Adhesives & Coatings
Additive Manufacturing & Digital Solutions
Advanced Composites Manufacturing
Materials Diagnostics & Failure Analysis
Materials Science & Metallurgy
Advanced Metals Processing & Technologies
Welding & Manufacturing
Materials Analysis & Test Division
Office Manager: Scott Tillery
scott.w.tillery@nasa.gov
office – 256-544-8651
cell - 256-783-6701
Office Manager: Teresa Miller
teresa.y.miller@nasa.gov
office – 256-544-7815
Division Chief: Dr. Sandeep Shah
sandeep.r.shah@nasa.gov
office – 256-544-0836
cell - 256-698-0096
Division Chief: Michael Frazier
(detailed to Chief Engineer’s Office)
michael.frazier@nasa.gov
office – 256-544-4968
cell - 256-603-0757
Division Chief: Freida Lowery
freida.s.lowery@nasa.gov
office – 256-544-2507
cell - 256-684-1883
Deputy: Shane Carpenter
shane.l.carpenter@nasa.gov
office – 256-544-4674
Deputy: Steven Phillips
steven.t.phillips@nasa.gov
office – 256-544-0626
Deputy: Carole Wagner (acting)
carole.y.wagner@nasa.gov
office – 256-544-2719
Notes: This chart shows our top level M&P organizational structure – we have over 300 personnel supporting M&P of which ~ ½ are CS
M&P Lab is made up of 2 Offices and 3 Divisions with each division containing 2 Branches
Points of contact for each are provided on the right side
Please do not hesitate to contact any of these individuals with questions

## Slide 3
M&P Laboratory partnerships utilize general and specialized capabilities to provide partners tailored solutions to materials, processing, manufacturing, and digital system application challenges.
Equipment
Digital Tools
CAPABILITIES
SLS
Lander & Surface Sys
In-Space
Prop
ECLSS/Habitat
Science
Today
Advanced Manufacturing
Tomorrow
SLS
ECLSS/Habitat
In-Space
Prop
Science
Advanced Manufacturing
Criticality
Uniqueness
Scale
Lander & Surface Sys
Scale
Uniqueness
Criticality
SMEs
Expertise
Facilities
Notes: Our lab utilizes both general and unique capabilities to provide solutions to M&P related challenges.
Components, sub systems and systems all require the proper application of materials and associated processes from development through qualification and flight to be successful.
Capabilities include 1 or more of the following - personnel expertise, equipment/instrumentation, digital tools in some cases and, facilities in some cases depending on the scale of the equipment
I am going to review some of our M&P capabilities with focus on past liquid propulsion needs
On the far right is a graphical representation of our work distribution in the recent past vs in the future with the size of the icon showing relative resource levels – SLS has been a big focus area during development but in the future as we move to an operation phase that support level will decrease and M&P’s participation in Habitats, Lunar Surface Systems, in space propulsion and advanced manufacturing will grow.
I have broken our capabilities into 5 topic areas:
  Materials
  Testing
  Process Development
  Advanced Manufacturing – For Space and In Space
  Digital Transformation
Additional info
Another important point - with the increased focus on model based engineering approaches – critical analysis tools have to be based on and validated with test and, more times than not, that includes some type of material performance consideration so I see our Lab being heavily involved in the migration to MBE
When selecting the capabilities to share - I also focused on criticality, uniqueness, scale and level of SME we have in the Lab

## Slide 4
Materials Capabilities
Materials Diagnostics and Failure Analysis
Sophisticated Metallurgical Analyses / Characterization
Fracture Control and Damage Tolerance – customized testing supporting analyses
High Temperature Materials
Corrosion
Materials and Processes Technical Information System (MAPTIS)
Mitigation for Materials Obsolescence
Development of Material Usage Agreements (MUAs), Material Usage List (MIUL)
Ionic Liquids Research
Materials Flight Experiments
Layered Pressure Vessel 2D Fracture Modeling
Microhardness Mapping of a Friction Stir Weld
(Blue = Low Hardness, Red = High Hardness)
https://maptis.nasa.gov
Grain Size Analysis in a Rolled Aluminum Plate (SEM/EBSD)
Notes: Our failure analysis team is called on from around the Agency and OGAs (FAA) to support various investigations – two photos on the right are graphical representations of some of the analyses we conduct
As far as agency expertise – the same holds true for fracture control / analyses and damage tolerance assessments – when required we design customized application specific test samples and test programs to address critical issues
The bottom right figure is part of an Agency wide layered pressure vessel program our experts led to analyze and evaluate the risk for Agency’s aging infrastructure.
Plasma Torch Test Bed for high temp TPS – thermal protection system – materials screening. We are involved in formulating and evaluating next generation SRM insulation materials through a sub scale motor program sponsored by SLS Booster
Our Lab is involved with the entire materials life cycle depicted in the lower left and we maintain the Agency’s M&P Tech Info Sys (MAPTIS) which is a database / repository of varied materials data
Our Lab has been extensively involved in materials flight experiments since the 80s – photo on the left middle is one of the 15 MISSE (Materials on ISS Exp) flight experiments used for evaluating new materials for space exposure performance. We compare on-orbit exposure results to our ground based testing to verify we are approximating space environment in the lab.
Materials Diagnostics and Failure Analysis
POC: Dr. Sid Gorti
The EM31 diagnostic laboratory has advanced capabilities which provide qualitative and quantitative data on materials characterizations such as microstructure, bulk chemical composition, surface composition, crystal structure, and atomic configuration are routinely determined and interpreted for any material - metallic or non-metallic. A comprehensive combination of modern analytical tools is utilized to provide complete understanding of additive manufactured parts, hence, that understanding can be extended to service performance.
All analytical tools and techniques, combined with hardware operations knowledge, especially in additive manufacturing, define the most efficient approach to documenting and resolving engineering hardware failures. EM31's goal is to understand the underlying contributing cause(s) of failure such that operational risk is minimized and system reliability is enhanced.
FRACTURE CONTROL AND ANALYSIS, DAMAGE TOLERANCE
POC: Joel Hobbs
The Damage Tolerance Team/EM21 is an Agency leader in fracture control and damage tolerance maintaining a team of experts and analysis tools. This team supports a variety of damage tolerance and fracture control related topics, including data evaluation and usage, analytical approaches, and fracture control approaches.
High temperature materials – refractories, Carbon Carbon, & CMCs
POC: Sarah Howse
EM41 has significant expertise in high temperature materials selection and characterization suitable for propulsion applications. Through our contract with Southern Research, we have easy access to high temperature mechanical and thermal testing. EM41 has provided key insight to Orion Launch Abort System, Interim Cryogenic Propulsion Stage, Exploration Upper Stage, and Air Force / DARPA Programs. Additionally, EM41 maintains awareness of SBIR programs in hypersonics and propulsion technology development.
TPS - Cryo-insulation, ablators, thermal blankets, optical property measurements
POC: John Bloyer The Thermal Protection System (TPS) Development Facility supports environmentally compliant TPS materials and processes development for current and future space programs. The TPS Development Facility is used to characterize materials and provide data on equipment and processing parameters to support large-scale TPS applications. The Facility provides the ability to apply primers, paints, and spray on foam insulation (SOFI) materials to large-scale test articles as well as flight hardware (e.g. OSA) in various orientations. Current and future environmental, health, and safety issues, as well as product performance issues, will drive a continual utilization of this facility to maintain adequate TPS materials and processes for space vehicle applications. Portable New Delivery System (PNDS) capability provides EM41 with a mobile capability for spray foam application for locations where environmental conditions can be accounted for. EM41 provides regular troubleshooting advice to the Core Stage and EUS prime contractors, as well as various industry partners.
MATERIALS SELECTION AND CONTROL, MUA/MIUL, DATA MANAGEMENT
POC: Teresa Miller
The Engineering Support Office (EM04) responsibilities include materials selection and control, engineering materials and physical sciences data management, and performing the Laboratory Lead function for payloads, ISS experiment facilities, and small projects. The Office is a resource for information on the wide range of material applications such as metals, non-metals, and composites for NASA, aerospace, defense and industry. This Office also provides materials and processes engineering support and is responsible for specifications, standards, drawing approvals, requirements definition, Materials Identification and Usage Lists (MIULs), and Materials & Processes (M&P) control plans, Materials Usage Agreements (MUAs) which includes serving as secretary and member of the Materials Application Evaluation Board (MAEB). The Office is chartered to maintain the Materials and Processes Technical Information System (MAPTIS) data base, an Agency resource for materials technical data.

## Slide 5
Test Capabilities
Hydrogen Test Facility (nationally unique)
Mechanical Testing
Tribology / Metrology
Impact Testing –
  launch and ascent debris
  weather encounter
  micrometeoroid and orbital debris
Space Environmental Effects (SEE) –
  high vacuum with thermal extremes,
  ionizing and non-ionizing radiation,
  plasma
  atomic oxygen
Lunar Surface Simulation -
  SEE coupled with regolith bed
    (~2 ft dia x 4 ft chamber)
  New full scale system level capability
    (20 ft dia x 28 ft chamber)
Investigative Chemistry & Planetary Protection
Lunar Env Test System
Notes: As far as Test capabilities
SEE – Agency unique materials exposure chambers allowing for simultaneous electron, proton and UV radiation exposure coupled with thermal vacuum conditions
The only agency asset capable of providing these space env exposure conditions over a lunar simulant bed – top right
LETS is a small test volume capable of conducting material and small component level tests.
Below LETS - Is a photo of a 20 ft dia x 28 ft long thermal vacuum chamber (V-20). We have recently received agency approval to convert this large thermal vacuum chamber into a lunar surface simulation chamber
We are partnering with test lab to add a simulant bed with capacity to test large/full scale lunar hardware components, subsystem and systems.
This will be one of only 2 chambers in the Agency for conducting large scale tests
Far right – another agency/nationally unique capability – hydrogen test facility with capability to test materials in cryogenic hydrogen at high pressures
Bottom center - MSFC is also one of the few NASA centers with tribological capability – study of lubrication and wear - that has applicability ranging from lunar surface system mechanism abrasion testing to liquid rocker engine turbopump bearings
The bottom left shows one of the numerous mechanical test machines which we use for standard ASTM testing as well as adaptation to customized testing I mentioned earlier
HYDROGEN TESTING
POC: Bryan Tucker
The Hydrogen Test Facility (HTF), a nationally unique NASA resource for mechanical testing of materials in hydrogen, has supported numerous engines programs such as HR-1 embrittlement testing, IN-100 embrittlement testing, and liquid hydrogen testing on Ti-6Al-4V. Tests performed on these alloys include smooth tensile, notched tensile, high-cycle fatigue, low-cycle fatigue, fatigue crack growth rate, and fracture toughness. Custom test systems are operated in 10 structurally reinforced test cells, using 14 test rigs, screening for property changes under different combinations of stress, pressure, and ambient to extreme temperatures. Testing can be performed in gaseous nitrogen, gaseous hydrogen, or gaseous helium at pressures up to 10,000 psi. Cryogenic tests are conducted in liquid hydrogen or liquid nitrogen. A new test system is currently being implemented to add gaseous methane environment to our capabilities.
MECHANICAL TESTING
POC: Bryan Tucker
Standard and non-standard testing of materials in various forms and environments – The team perform mechanical testing such as hardness, tensile, compression, shear, bending, fatigue, fracture toughness, creep, and other specialty tests such as torque-tension of threaded fasteners. Digital imaging correlation (DIC), a non-contact optical technique, is often used to monitor and measure three-dimensional full-field deformations and strains on a variety of specimens. They also conduct variable amplitude simulation testing to determine margin for flight environments. They have 25 test frames that can conduct uniaxial tests up to 265,000 pounds at temperatures ranging from –320oF to 1500oF using computerized data acquisition.
Liquid helium (LHe) testing – The Mechanical Test laboratory is developing a system to perform testing of materials in LHe (-452°F). The prototype system will utilize a 20-kip test frame, and upon successful completion, the lab will seek to acquire an additional test system with a 100-kip force capability.
TRIBOLOGY/METROLOGY
POC: Sara Rengifo
Analysis of turbopump rolling element bearings
The team can measure surface texture and damage/wear of race and ball surfaces before and after bearing use, using mechanical stylus and/or 3D optical profilers. They also perform circumferential trace measurements using a Talyrond TR595 UHPR to characterize manufacturing errors and details that cannot be found using typical stylus profilers. They perform acoustic emissions/vibration measurements to attempt to characterize damage/wear after use and bearing torque measurements to characterize differences between new and used bearings. Other capabilities are available to precisely measure ball and race diameters and to image surfaces at a wide range of length scales. They can also dynamically model bearings using the computer simulation software ADORE to understand the effects of material, geometry, speed, load, temperature, and cryogenic fluid type and flow rate on heat generation, contact stresses, contact angle, and predicted life.
Analysis of dimensions and surface texture of conventionally manufactured and additively manufactured (AM) surfaces
The team can characterize the unique surface texture and dimensional characteristics that result from the use of different AM materials and process parameters using various precision microscopes, white light interferometer, and laser confocal technologies. With these capabilities, the team can also characterize damage/changes to surfaces after use, after hot fire tests, etc.
Launch/ascent debris impact testing
POC: Mary Nehls The Thermal Vacuum Chamber provides ascent heating performance assessments, historically for foam insulation and various coatings. EM41 regularly partners with MSFC’s Test Lab to assess aerodynamic heating environments for launch vehicle TPS systems at the Hot Gas Test Facility. EM41 also possesses a suite of impact test capabilities utilized for launch debris, ascent debris and in flight weather impact testing (hail, rain, sand). The team also can conduct space environment MMOD-type impacts in conjunction with other SEE testing in low earth orbit. Customers include SLS and a variety of classified DOD customers.
Space Environmental Effects (SEE) testing
POC: Mary Nehls EM41’s Space Environmental Effects Team can conduct a wide variety of space environmental effects testing required for materials, components, and systems exposed in the space environment. Testing capabilities include charged particle, UV/NUV/VUV, atomic oxygen, plasma, and combined effects. Our SEE expertise also includes extensive flight experiment (MISSE, METIS) experience and associated historical databases as well as Planetary Protection (focused on propulsion elements). Customers include SLS, HLS, SpaceX, and DOD.

## Slide 6
Selected Process Development Capabilities
  Additive Manufacturing (AM) – Powder Bed Fusion/Selective Laser Melting, Large Scale Directed Energy Deposition, Refractory AM
  High Temperature Materials – Space Nuclear Propulsion Fuel Element Development
  Joining: welding (friction stir, laser, e-beam), brazing
  Alloy Development, Casting, Forming, Forging, Heat Treatment
  Composites (Automated Fiber Placement, Filament Winding, Tape Wrapping, Hand Layup)
  Thermal Protection Systems (TPS) – motor insulation, cryo-insulation, ablators, ceramics
  Adhesive Bonding
  Coatings
  3D Printable inks/materials for Electronics and Sensors
  Cleaning
  Non-destructive Evaluation (NDE)
Spark Plasma Sintering
Notes: M&P has agency leadership in AM – specifically PBF – we have focused on propulsion component fabrication with Inconel and GRCop alloys but have also printed aluminum, titanium and are currently working with HR-1, JBK, and refractory materials.
We also recently started work with Directed energy deposition (DED) which allows us to build larger parts as shown on the top right
Our scientists and engineers vary process parameters, analyze the effect on the resulting material \part quality then optimize the process to manufacture a part for test.
Bottom right shows a Space Nuclear Propulsion CERMET fuel element developed in our labs utilizing a spark plasma sintering process – we are very interested in high temperature materials and their application to nuclear propulsion for the future
The center photo is our Automated Fiber Placement machine used in process development for high strength composite development efforts
The Lab is also heavily involved in weld process development with extensive experience in AL -Li alloys used in launch vehicle tanks
CFM – Cryogenic Fluid Management – in space storage and transfer of propellants
Left middle photo is SHIIVER (Structural Heat Intercept Insulation Vibration Evaluation Rig) tank which we partnered w/ GRC to applying cryogenic foam insulation then machined to final outer mold line
Additive Manufacturing
POC: Brian West
The MSFC AM lab has been characterizing AM materials and processes for over 27 years. For the past 9 years the lab has focused heavily on laser powder bed fusion (L-PBF) systems (6 systems on site) for propulsion applications. Copper alloys, nickel superalloys, and hydrogen resistant alloys have been the most common materials characterized with properties traceable back to machine parameters and feedstock. Directed Energy Deposition (DED) and dual laser L-BPF technology have recently been added to the technology available in the MSFC lab. The knowledge base developed in the AM lab has been codified in the NASA AM standard NASA-STD-6030 and NASA-STD-6033. These documents govern how hardware built using AM will be certified for human rated spaceflight at NASA.
Propulsion Oriented Welding and Joining
POC: Dr. Jeff Sowards
The EM32 welding and manufacturing team has a long history of providing expertise to internal and external propulsion customers that support various NASA flight programs. The team provides welding consultations to propulsion vendors that need welding insight and expertise ranging from early research and development efforts to full-scale production. The team actively supports non- conformance resolution reviews, Root Cause and Corrective Action boards, and Critical Design Reviews. The team has expertise in traditional fusion, high energy density, and friction welding processes and provides hands-on process development, weldability testing, weld characterization, and weld analysis for a range of propulsion-centric alloys including refractory alloys. Areas of interest not only include welding of traditional forged and wrought product forms, but also of novel material forms developed from additive manufacturing processes.
Non-metallics – Composites
POC: Dr. Will Guin
MSFC’s EM42 is working to mature novel additive manufacturing and composites manufacturing technologies to increase scale, reduce cost, and improve performance for regeneratively-cooled thrust chamber assemblies (TCAs). In the course of this technology development effort, the team has developed composite overwrap techniques (using filament winding) for combustion chamber nozzles. Subscale articles have been manufactured and tested for 2k- and 7k-class rocket motors. Work is ongoing to scale these approaches to accommodate larger thrust chamber assemblies.
TPS - Cryo-insulation, ablators, thermal blankets, optical property measurements
POC: John Bloyer The Thermal Protection System (TPS) Development Facility supports environmentally compliant TPS materials and processes development for current and future space programs. The TPS Development Facility is used to characterize materials and provide data on equipment and processing parameters to support large-scale TPS applications. The Facility provides the ability to apply primers, paints, and spray on foam insulation (SOFI) materials to large-scale test articles as well as flight hardware (e.g. OSA) in various orientations. Current and future environmental, health, and safety issues, as well as product performance issues, will drive a continual utilization of this facility to maintain adequate TPS materials and processes for space vehicle applications. Portable New Delivery System (PNDS) capability provides EM41 with a mobile capability for spray foam application for locations where environmental conditions can be accounted for. EM41 provides regular troubleshooting advice to the Core Stage and EUS prime contractors, as well as various industry partners.
Non-metallics – seals, adhesives
POC: EM41 has the ability to develop and apply a wide range of coatings and adhesives for space applications. Specific examples include Electro-Static Dissipative (ESD) coatings to meet spacecraft hardware requirements; weather barrier coatings designed to protect cork-based thermal protection materials from severe heat, ultraviolent (UV) light, and moisture; and lightweight and low thermal conductivity coatings that provide excellent insulation capability for spacecraft applications. EM41 also supports adhesive material selection and bonding process development for highly unique space-related applications. EM41 has recently aided several NASA missions with adhesive selection & troubleshooting, including IXPE, NEA Scout, and ISS ECLSS.

## Slide 7
Selected “For Space” Advanced Manufacturing Capabilities
Welding
  Large scale FSW production
Additive Manufacturing
  Powder Bed Fusion / Selective Laser Melting
  Large scale DED - 6 ft dia x 10 ft
  Refractory AM
  Standards and certification (metal engine components)
  3D printable materials/inks for electronics and sensors
Modular / Flexible Tooling
Digital Transformation - Interest in AI / ML / MBE
Manufacturing Support
  Non-destructive Evaluation (NDE)
  Contamination Control and Cleaning
  Foreign Object Debris (FOD) Control
Combustion Chambers
Notes: For Space meaning technologies and manufacturing that support earth to orbit propulsion, launch vehicles and terrestrial applications supporting our missions
Looking for Advances in manufacturing technologies that lower product costs and delivery times resulting in lower cost to orbit
Top left - Large scale FSW production in south highbay of building 4755 – SLS – Orion SA and Launch Vehicle SA, one off development tanks and other hardware
Modular / Flexible Tooling – developed and patented by our engineers
  Tooling that is reconfigurable and reusable thus reducing time and costs associated with manufacturing large scale hardware.
  Revolutionary because it focuses on flexibility and interchangeable components rather than a tool that is application specific.
  Modular Tooling has saved millions of dollars and months of schedule for multiple projects.
Right side – shows Additively manufactured combustion chamber – some of GRCop which were incorporated into an engine which was successfully ground tested
Bottom middle to left show composited manufacturing automated fiber placement robot shown earlier and a cryogenic composite tank developed in partnership with Boeing undergoing thermography NDE inspection
Additional info -
Refractory AM - W/Mo that are basis of matrix for Nuclear propulsion engine fuel cell allowing for higher operational temperature
NDE
POC: Matt McDougal
The Non-Destructive Evaluation Team/EM21 has several inspection methods that could be helpful for engine inspections. The NDE Team has performed thermography and computed tomography (CT) on Carbon-Carbon nozzles and CT on some additively manufactured nozzles. We could supply NDE technique development, application and consultation for all standard methods (ultrasonics, radiography, penetrant, eddy current, magnetic particle) and some special methods (computed tomography, thermography, shearography, acoustic emission). This support could be provided in-house at MSFC and in some cases at remote sites.
FOD, Contamination Control, Cleaning
POC: Andrew Chaloupka
The Chemistry and Contamination Control Team (CCCT)/EM22 support for Engines can be broken down into three categories: FOD and Contamination Control program support, Additive Manufacturing (AM) powder analysis and powder removal/part cleaning methodology development.
The CCCT supports FOD and contamination control requirements definition, and control plan development and implementation during all phases of hardware development and manufacturing.
AM powder analysis consists of quantifying the physical and chemical properties of the various feedstock powders. The CCCT measures physical properties including particle size distribution, morphology, flowability, density, and angle of repose. Chemical analysis includes inductively coupled plasma spectroscopy (ICP) and elemental analysis to determine the metals and oxygen content. The data generated by powder analysis efforts have been used to determine receiving and acceptance parameters for new powder, verify that new powder meets powder spec, and to support reusability and recycling studies for powder.
The CCCT continues to support removing entrained powder from complex internal geometry. Prior work has included the use of compressed air, ultrasonic vibrations, and CO2 snow. Ongoing work includes chemical and electropolishing as well as the High Flow Differential (HFD) cleaning apparatus. Recent work on new cleaning methods has identified two promising new approaches to cleaning AM parts: vacuum cyclic nucleation and supercritical CO2. Both methods use the rapid phase change (and expansion) of the cleaning solvent from liquid to gas to physically remove trapped powder.

## Slide 8
Selected “In Space” Advanced Manufacturing Capabilities
In-Space Manufacturing
    On-orbit Servicing And Manufacturing (OSAM)
    Lunar surface excavation/construction
    In-Situ Resource Utilization (ISRU)
Joining / Welding
  Laser and e-beam welding – manufacturing and repair
Additive Manufacturing
  AM with In-Situ Resources-
  Standards and certification
  3D printed electronics
    & sensors
Digital Transformation
    Interest in AI / ML for
    remote operations
Manufacturing Support
  Non-destructive Evaluation
M&P capabilities will play a major role in maximizing component re-use, recycling and in-situ resource utilization.
Notes: In Space meaning technologies and manufacturing that are accomplished in space or on another body - supports minimizing resources launched from earth
We are involved with OSAM and lunar surface construction programs – first photo is a laser welding system – also looking into e-beam welding – both of these could be adapted to in space welding
NASA has had a 3D printer on ISS for years and we have been involved with evaluating materials – comparing properties with earth based prints.
The bottom left photo is the first plastic ratchet tool printed on orbit. Relative to minimizing feed stock for 3D printing - a refabricator (recycler) was developed and is now on ISS. We are evaluating reuse of waste plastics to supplement feedstock delivered from earth.
M&P has also partnered with Tia’s Dept/ES in electronics printing – we have developed specialized inks to support printing electronics and sensors some of which are being used for crew health monitoring
We are participating in lunar surface excavation and construction projects – evaluation of mechanisms used in abrasive lunar regolith/dust environment, also looking into utilizing Ionic Liquids which are a relatively new family of materials that are molten salts at room temperature. Our scientists have shown ILs can be used to extract water, O2, and metals from regolith to support ECLSS and propellant consumables collection as well as manufacturing of other components
Obviously – automation and remote operations are critical system features for future lunar operations so that leads me to my next chart -

## Slide 9
Selected Digital Transformation Capabilities
Digital Transformation - Interest in applications of
    Artificial Intelligence
    Machine Learning
    Model Based Engineering
    Autonomy & Remote Operations
    Digital Twin
Manufacturing Support
    Structured lights scanning
    Simulations for optimizing production flow and human factors
    Paperless production systems
Additive Manufacturing – In process monitoring and feedback
Processing
Properties & Performance
Hardness
Fatigue Life
Structure
CALPHAD
(Atomic)
Computational Modeling
Bridge Length Scales
FEA
(macro)
Laser
Beam Brazing
Braze Alloy Wettability Test
Chemical Segregation
Microstructure
Grain
Evolution (Meso)
Thermophysical
Properties
Notes: Digital transformation is a technology area of great interest and something we are focusing on
The application of Artificial Intelligence, machine learning and model based engineering to more efficiently implement advanced manufacturing technologies and processes will lower cost and reduce schedules.
One question we are trying to address is the quantity of data required to implement some of these techniques.
The figures on the top half of the chart show interactions across multiple aspects of a process development activity. To be able to characterize and understand the process to be able to predict post process part material properties and therefore performance is the goal.
We have implemented digital tools in M&P such as structured light for part scanning, electronic manufacturing planning and simulations for production flow and human factors evaluations.
Another area of great interest and current focus is in process monitoring of the additive manufacturing process. Since many of these parts are not inspectable once fabricated due to part thickness which translates to lack of NDE x-ray penetration we are looking to continuously monitor the manufacturing process real time to be able to identify potential problem areas resulting from any process parameter out of tolerance events that may occur. This monitoring would go a long way to qualification/certification of the part.
Additional info
Artificial Intelligence (AI) in manufacturing refers to software systems that can recognize, simulate, predict, and optimize situations, operating conditions, and material properties for human and machine action.
Machine Learning (generally seen as a subset of AI) refers to algorithms that use prior data to accurately identify current state and predict future state, with the goal of improving productivity, precision, and performance.
Networking creates digital connections among devices, machines, equipment, databases, computer programs, and users, to provide the connectedness needed to exchange information, make decisions, and take actions.
Predictive Modeling is the use of data, AI, machine learning, simulation, and digital twins to assess, predict, and anticipate process, product, and operational behaviors for control, design, optimization, health, and failure prevention and mitigation.
Network Effects produce increased benefits for network users as the number of connected user nodes increases by expanding the availability of information and knowledge accessible to all.
A Digital Twin is a virtual representation of a connected physical asset and encompasses its entire product lifecycle.

## Slide 10: Conclusion
MSFC Engineering has excellent, deep, and, in numerous places, unique technical capabilities.
We want to partner with you on implementing new and emerging technologies to lower manufacturing costs and thus, access to space.
We stand ready to assist academic institutions, other government agencies, and the commercial aerospace community in our region and around the country to deliver space fairing systems.
"If everyone is moving forward together, then success takes care of itself." --Henry Ford.
“When you need to innovate, you need collaboration.” – Marrisa Mayer
Please don’t hesitate to contact us as needed - mark.a.cooper@nasa.gov or dewitt.burns@nasa.gov