## Slide 1
Robert Stough
SLS Utilization Manager
Space launch System rideshare opportunities to cislunar space
18 November 2021

## Slide 2: The power of sls Foundation for a generation of deep space exploration
Maximum Thrust
9.5 M lbs
8.9 M lbs
8.9 M lbs
8.8 M lbs
** Not including Orion/Service Module volume
Low Earth Orbit (LEO) represents a typical 200 km circular orbit at 28.5 degrees inclination
Trans Lunar Injection (TLI) is a propulsive maneuver used to set a spacecraft on a trajectory that will cause it to arrive at the Moon. A spacecraft performs TLI to begin a lunar transfer from a low circular parking orbit around Earth.
The numbers depicted here indicate the mass capability at the Trans-Lunar Injection point.
SLS Block 2 Cargo
SLS Block 1B Cargo
SLS Block 1B Crew
SLS Block 1 Crew
SLS Block 2 Crew
9.5 M lbs
8.8 M lbs
SLS Block 1 Cargo
Payload Volume
34,910 ft3 (988 m3)
21,930 ft3 (621.1 m3)
10,100 ft3 (286 m3)**
10,100 ft3 (286 m3)**
8,118 ft3 (229.9 m3)
Payload to LEO
130 t (286.6k lbs)
105 t (231.4k lbs)
105 t (231.4k lbs)
95 t (209.4k lbs)
130 t (286.6k lbs)
95 t (209.4k lbs)
Payload to TLI/Moon
> 46 t (101.4k lbs)
42 t (92.5k lbs)
38 t (83.7k lbs)
> 27 t (59.5k lbs)
> 43 t (94.7k lbs)
> 27 t (59.5k lbs)
516 ft3 (14.6 m3)
Notes: The First 3 Artemis missions will use the block 1 configuration.

## Slide 3: STACKING THE ARTEMIS I VEHICLE

## Slide 4
10/7/2021
Notes: Version Control
MAP DATE: OCT 2021
POC
Aimee Crane
aimee.c.crane@nasa.gov

## Slide 5
SLS Block 1
Crew
Stages (Core)
Booster
Booster
Stages (Core)
Booster
Booster
Orion
Spacecraft
5m
Fairing
Primary
Payload
SLS Block 1
Cargo
CubeSats
Launch Vehicle Stage Adapter (LVSA)
Integrated Spacecraft/Payload
Element
(ISPE)
ISPE
Orion Stage Adapter (OSA)
Payload Adapter
BLOCK 1 PAYLOAD ACCOMMODATIONS
Interim Cryogenic Propulsion Stage (ICPS)
229 m3 available volume
Up to 17 places ≤ 12U
6U
14 kg
12U
20 kg
Notes: Available volume in 5 m fairing = 229 cubic meters

## Slide 6
10/7/2021
Notes: Version Control
MAP DATE: OCT 2021
POC
Aimee Crane
aimee.c.crane@nasa.gov

## Slide 7
10/7/2021
Notes: Version Control
MAP DATE: OCT 2021
POC
Aimee Crane
aimee.c.crane@nasa.gov

## Slide 8: BLOCK 1B/2 PAYLOAD ACCOMMODATIONS
Stages (EUS)
Stages (Core)
Booster
Booster
Stages (Core)
Booster
Booster
Co-Manifested Payload
Primary Payload
Stages (EUS)
CubeSats
Up to 7 places, ≤12U
Payload Adapter (PLA)
8.4m Fairing
SLS Block 1B
Crew
SLS Block 1B
Cargo
Orion
Spacecraft
CubeSats
Up to 21 places ≤12U
6U
12U
Universal Stage Adapter (USA) 286 m3, ≤10 t lbm
Fairing diameter x length | Available volume
8.4 m x 19.1 m | 621 m3
8.4m x 27.4 m | 988 m3
Ring-class smallsats
Notes: For Block 1B and Block 2 payloads, space is available in the Universal Stage Adapter in the crew configuration
Available volume in USA = 286 cubic meters
Available volume in 8.4 m x 19.1 m fairing = 621 cubic meters
Available volume in 8.4 m x 27.4 m fairing = 988 cubic meters
B1B can also potentially accommodate CubeSats, up to 27U, on a payload adapter
Possibly even ESPA-class payloads or a propulsive ESPA ring may be included in future missions
Vehicle planners are still keeping a 10 m-diameter payload fairing as an option. Lengths are the same as the 8.4 m fairing – 19.1 m and 27.4 m.

## Slide 9
10/7/2021
Notes: Version Control
MAP DATE: OCT 2021
POC
Aimee Crane
aimee.c.crane@nasa.gov

## Slide 10
10/7/2021
Notes: Version Control
MAP DATE: OCT 2021
POC
Aimee Crane
aimee.c.crane@nasa.gov

## Slide 11
SPACE LAUNCH SYSTEM ARTEMIS PROGRESS

## Slide 12
nasa.gov
images.nasa.gov
@NASA_SLS
NASASLS
youtube.com/nasa
@NASAArtemis
Notes: You can follow developments with SLS, Ground Systems, Orion – and the overall Artemis program by through our social media platforms.
We are proud of this community and honored to do the work we do.
And, we know, as they say, that we are standing on the shoulders of giants.
We don’t take that lightly – nor do we take this mission lightly.
We have delivered the rocket for Artemis I – and we are going.