## Slide 1
Power and Energy Technology for Lunar Surface Infrastructure
CLB.PNL-49: Infrastructure to Stay – Moon
AIAA ASCEND
16 November 2021

## Slide 2
CLB.PNL-49: 16 November 2021
NASA SpaceTech Strategic Thrusts/Outcomes

## Slide 3: POWER The key commodity needed to exploit the Lunar Surface
Illumination The scarce resource needed to produce power
Polar Illumination Limits
Intermittent with up to 100 hours darkness
Highly dependent on location/elevation
Equatorial Illumination Limits
Cyclical periods of 14 days illuminated, 14 days dark
Consistent
CLB.PNL-49: 16 November 2021

## Slide 4: Power demand will increase as surface exploitation grows from initial Artemis installations at the South Pole to intensive industrial and settlement development across the Lunar surface
Ultimate Artemis Polar power technology (2030+):
ISRU for O2/H2 is primary demand driver
  Crewed outpost
  Science exploration “survive the night”
Up to multi-MWe demand
Lower Latitude power technology (2040+?)
Earth-sourced generation assets “bootstrap” production of generation and storage assets from regolith
Up to GWe demand as science exploration and industrial/settlement activities expand
CLB.PNL-49: 16 November 2021

## Slide 5
Add 3 charts on site to show where solar arrays are
Add zoom for the fsp to base connection
5
Human Landing System
Lunar Terrain Vehicle
Foundation Surface
Habitat
Lab
O2-Regolith ISRU
H2/O2-Ice in PSR
Building Block Power Technology Options for Artemis South Pole “Base Camp” (2030+)
Generation: 40 kWe mobile fission power plant
Human Mobility
Platform
Generation: 50 kWe increment PV arrays (vertical or horizontal/reflector, > 200 V, > 200 We/kg BOL, < 10 % degradation over 10 years
Storage: 1 MWh increment RFC @ 10 kWe discharge with 50,000 hr/500 cycle durability
Distribution: Cables & Spools @ 10 kWe scale and 1000V with < 3% loss per km.
Distribution: Power Beaming @ 10 kWe scale < 80% loss over 5 km.
Storage: 50 kWh battery modules w/150 Wh/kg at 1 kW discharge over 500 cycles at 235 K
Generation: 500 We radioisotope power
Distribution & Management : Rad-hard power electronic circuits with 99% reliability over 10 years exposure
CLB.PNL-49: 16 November 2021

## Slide 6
Add 3 charts on site to show where solar arrays are
Add zoom for the fsp to base connection
6
Human Landing System
Lunar Terrain Vehicle
Surface
Habitat
Lab
Generation: 40 kWe mobile fission power plant
Human Mobility
Platform
  Landing pads and protective structures
  100’s to 1000’s metric tons of regolith-based feedstock for construction projects
  10’s to 100’s metric tons of metals, plastics, and binders
Polar Building Block Power Technologies Can Bootstrap Generation, Storage and Distribution at Lower Latitudes (2040+)
Storage: 1 MWh increment RFC @ 10 kWe discharge with 50,000 hr/500 cycle durability
Distribution: Cables & Spools @ 10 kWe scale and 1000V with < 3% loss per km.
Distribution: Power Beaming @ 10 kWe scale < 80% loss over 5 km.
Storage: 50 kWh battery modules w/150 Wh/kg at 1 kW discharge over 500 cycles at 235 K
Generation: 500 We radioisotope power
Distribution & Management : Rad-hard power electronic circuits with 99% reliability over 10 years exposure
Generation: 50 kWe increment PV arrays (vertical or horizontal/reflector, > 200 V, > 200 We/kg BOL, < 10 % degradation over 10 years
Mobile Fission Power drives equipment to print photovoltaic generation, electrochemical, storage, and thermal storage from regolith
CLB.PNL-49: 16 November 2021

## Slide 7: Power demand will increase as surface exploitation grows from initial Artemis installations at the South Pole to intensive industrial and settlement development across the Lunar surface
Ultimate Global Exploitation
CLB.PNL-49: 16 November 2021
Initial Polar Region Exploitation

## Slide 8: Path Forward
The immediate focus is on advancing TRL for power system components brought from Earth, defining the performance which surface system architects can assume when designing sustainable exploitation systems for the Moon and Mars.
  The future priority should be advancing the technology to manufacture power system components from in-situ Lunar resources. Such production bootstrapped with power systems brought from Earth.
CLB.PNL-49: 16 November 2021

## Slide 9
CLB.PNL-49: 16 November 2021