## Slide 1: Traffic Aware Strategic Aircrew Requests NASA Flight Deck Application for En Route Flight Optimization
TASAR Briefing
David Wing TASAR Principal Investigator NASA Langley Research Center
NASA / FAA Technical Interchange Meeting
November 30, 2021

## Slide 2: Traffic Aware Strategic Aircrew Requests (TASAR)
Onboard Route Optimizer
Electronic Flight Bag
Aircraft Sensors
Current Route
Aircraft State
Connected Internally
Enabling Strategic and Informed Route Optimization: Turning Data into Dollars
ADS-B Traffic
Connected Air-to-Air
Flight Re-optimized Saving Time & Fuel
Original route
Optimized
route
Connected to Ground Services
Weather
Airspace
Winds
$$ Operational Savings $$
TASAR provides immediate benefits while laying foundation for Digital Flight
More Likely Approved
Better Informed
Better Coordinated
Opportunities
Notes: “Strategic” meaning “well informed and purposeful”
Flow: data -> technology -> users -> benefits

## Slide 3: TASAR Technology: Traffic Aware Planner (TAP) Interactive Route Optimization App for Pilots
Powerful search algorithm finds non-obvious reroutes
Applies multiple degrees of freedom
Pilot-adjustable optimization objective
Leverages connectivity for operational savings
Adaptable to different aircraft and hardware architectures
Incorporates complex dynamic constraints
NASA Software of the Year
R&D 100 Award Winner*
* Internationally selected as one the 100 most technologically significant new products of the year
Recognition of unique capabilities, near-term benefits, and long-term revolutionary impact:
U.S. Patent, 8,977,482 Method and apparatus for generating flight-optimizing trajectories
U.S. Patent, 10,102,756 TAP User Interface
2016
2015
2018
2019

## Slide 4: NASA TASAR Project Accomplishments
Developed route-optimization application for the Connected EFB
Estimated DOC savings (time, fuel) via modeling
Developed software prototype
Analyzed safety, human factors, FAA authorization, and market needs
Conducted simulations and flight trials
Integrated into commercial aircraft
Conducted airline operational evaluation
Validated DOC savings and operational utility
Transferred technology to industry via commercial licenses
Concluded project at TRL 7
ATD-3
Project
CTD
Project
2012
2019
2015
2016
ATD Airspace Technology Demonstrations Project
CTD Concepts and Technology Development Project
DOC Direct Operating Cost
EFB Electronic Flight Bag
TRL Technology Readiness Level

## Slide 5: TASAR’s Rapid Advancement Timeline of Technology Maturity
High Fidelity
Simulations
Concept
Development
Community
Engagements
Software
Development
Concept Analyses
Flight Trials
Operational
Evaluation
Commercial
Evaluation
2012
2013
2014
2015
2016
2017
2018
2019
HITL 1
HITL 2
HITL 1
Partner Airline Adaptation Stage 1
Stage 2
Stage 3
FT 1
HITL 2
FT 2
FT 1
FT 2
FT 3
Airline Partnership Development
Implementation
Installed Testing
Op. Evaluation
Multiple Evaluation Licenses Issued
Mult. Comm. License Appl.
Concept Published
TASAR Patent
User Interface Patent
Benefits
Safety
FAA Approval Req’ts
Partner Benefits
S/W Certification
Enhancements
Airlines
Industry
FAA
Industry Forums
Eurocontrol
ATC
FAA NextGen
Webinar
RTCA
Industry

## Slide 6: Operational Evaluation of TASAR Conducted with Alaska Airlines
Partnered from 2015-2019
Collaborated with industry leaders
Equipped three aircraft for TASAR
Approved for revenue service operations
Conducted 90 valid flights for analysis
Validated cost savings and operational utility
Industry Collaborators
The use of trademarks or names of manufacturers in this presentation is for accurate reporting and does not constitute an official endorsement, either expressed or implied, of such products or manufacturers by the National Aeronautics and Space Administration.
© Alaska Airlines. Used with permission.

## Slide 7: TASAR Cost Savings and Operational Utility
Unrelated route changes that offset TAP gains
90 Evaluation Flights
July 2018 – April 2019
Mean Benefit
(All 90 Flights)
$97.00
Flight Duration | TAP Operator | Mean Benefit* | # Flights
All | Interns, NASA, Tech Pilots | $97 | 90
All | Tech Pilots | $204 | 22
*Mean benefit across all flights
Cost Savings Estimated at $100-$200/flight
Plan Validation
(But Counted as Zero)
Cumulative Small Gains
Home Runs
Operational Utility Validated by Alaska Airlines

## Slide 8: Home Runs Yield Significant Benefits By Themselves

## Slide 9: Cumulative Small Gains Accrue Benefits Through Minor Improvements

## Slide 10: Plan Validation Reduce Inefficient Deviations from Flight Plan

## Slide 11: Projected Annual Benefits
Airline | Estimated Aircraft that are Candidates to be Equipped with TASAR | Estimated Annual Cost Savings due to TASAR | Estimated Annual Emission Reductions due to TASAR
Alaska | 180 | $14.97M/year | 101.6 million lb CO2e
Allegiant Air | 37 | $1.41M/year | 10.51 million lb CO2e
American | 831 | $52.29M/year | 348.29 million lb CO2e
Delta | 466 | $23.61M/year | 166.11 million lb CO2e
Frontier | 62 | $4.38M/year | 31.94 million lb CO2e
JetBlue | 63 | $6.69M/year | 50.43 million lb CO2e
Southwest | 754 | $36.47M/year | 280.04 million lb CO2e
Spirit | 61 | $4.86M/year | 37.87 million lb CO2e
Sun Country | 30 | $1.41M/year | 9.83 million lb CO2e
United | 562 | $23.26M/year | 164.33 million lb CO2e
Total | 3,000+ | ~$170M/year | 1200.41 million lb CO2e
Pre-COVID-19 estimate
Applies Alaska’s achieved benefits (time and fuel savings by flight length)
Applies conservative benefits estimate ($97/flight)
Adjusts for fleet size, flight lengths, and direct operating costs (all public data)
Includes modern mainline jets; excludes regional and older jets
Includes domestic origin & destination only
Substantial savings are anticipated for U.S. airlines

## Slide 12: TASAR Project Final Status
NASA role is complete at TRL 7
  “System prototype demonstration in an operational environment”
  TAP prototype developed, tested, and matured
  Implemented on 3 distinct aircraft types (turboprop, bizjet, transport)
  Evaluated in airline revenue service
    Validated DOC savings in operational flights
    Demonstrated diverse operational utility to airline operations
    Inspired new ideas for expanded functionality and connectivity
Industry role is underway
  Commercialization in progress
  Multiple US airlines are evaluating TASAR for their fleets

## Slide 13: TASAR Growth Path
TASAR Evolution
Expanding Connectivity
Diversifying Input Data
Enhancing Functionality
Applying to Diverse Use Cases
Adapting to New Users
Advisory
Assistive
Responsible
Digital Flight
Flight Path Management (FPM) Automation Evolution
Notes: Expanding Connectivity
  FMS connectivity
  Dispatch connectivity
  ATC connectivity
Diversifying Input Data
  4D winds
  Onboard weather radar
  Turbulence
  Volcanic ash / icing
  Ionizing radiation
  FMS parameters
  Traffic intent
  Airspace structure
  Political boundaries
Enhancing Functionality
  Post-tactical optimization
  Ride quality optimization
  4D constraint adherence
  4D solutions
  New solution patterns
  Handoff monitoring
  Machine learning
Applying to Diverse Use Cases
  Minimizing refueling stops (range limited flights)
  Managing exposure to environment factors
  Optimally meeting time objectives (ATC and operator)
  Making complex requests via Data Comm
  Achieving specialized mission objectives
Adapting to New Airspace Users
Airlines (mainline, regional, fractional)
Corporate, general aviation
Military, UAS, UAM

## Slide 14: Traffic Aware Strategic Aircrew Requests NASA Flight Deck Application for En Route Flight Optimization
Questions?