## Slide 1
Adit S. Acharya1, K. Todd Lowe1, Wing F. Ng1, Paul M. Danehy2, Karl T. Edquist2,
Ross A. Burns2, Harry T. Pham2
1Virginia Tech, 2NASA Langley Research Center
2022 AIAA SciTech Forum, January 3-7 2022
Copyright © 2021 by Virginia Polytechnic Institute and State University and the U.S.A, as represented by the Administrator of the National Aeronautics and Space and Administration. All rights reserved.
Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Seeding Method for Velocimetry and Visualization of Supersonic Retropropulsion Nozzle Plumes
Funding from: NASA Aerosciences Evaluation and Test Capabilities (AETC) Portfolio

## Slide 2: Motivation
Growing interest in supersonic retropropulsion (SRP) for Martian vehicle descent1
  Current EDL systems not suitable for massive payloads
SRP: propulsive deceleration while still in supersonic flight
Figure 1: SRP flow features, adapted from Berry et al.2

## Slide 3: Motivation
SRP model wind tunnel studies are desirable
  Laser diagnostics such as particle image velocimetry can provide off-body measurements3
(requires seeding of tracer particles into flow)
BUT
if SRP nozzle expels dry air
tracer particle density is diminished
POOR MEASUREMENT QUALITY
observed in similar studies of SRB booster separation models4,5

## Slide 4: Concept
Goal: seed underexpanded nozzle flow with particles suitable for PIV
Solution: Venturi contraction to draw liquid into flow path; atomized by strong shear forces (presented at SciTech 20216)
Figure 2: Schematic of “Venturi seeder” with shock structure (red) and jet contact surfaces (brown)
1. Supply P0 and PS
2. Pressure drop forms at Venturi contraction
3. Seed liquid drawn into flow path
4. Seed liquid atomized by shear forces in nozzle
5. Particles ejected in jet

## Slide 5: Experimental Methods
Rig constructed with NPT + Swagelok fittings
Converging, sonic nozzle created by drilling into plug
7.87 mm exit dia.
15°half angle
15.7 area ratio
Figure 3: Picture of SRP nozzle rig
Seed line connected to pressure pot filled with DEHS oil

## Slide 6: Experimental Methods
Experiments aimed to ensure that:
Nozzle generated underexpanded jet
Particles in spray acceptable size for PIV measurements
PIV results matched expectations for nozzle plume
Shadowgraph imaging
TSI™ 3321 Aerodynamic Particle Sizer (APS)
2D PIV of axial and radial velocities
Measured with…
≤ 1 μm dia. for suitable response times in typical gas flows7

## Slide 7: Results: Shadowgraph
Rig supplied with P0 = 5.07 MPa
  Seed line shut off
  Significant losses, P1 = 0.79 MPa downstream of Venturi
Underexpanded plume observed
Figure 4: Shadowgraph image of dry SRP nozzle plume

## Slide 8: Results: Cases
Three cases of supply pressures used:
Case | P0 [MPa] | P1 [MPa] | Ps [MPa]
A | 4.44 | 0.67 | 0.67
B | 4.93 | 0.76 | 0.60
C | 6.17 | 0.93 | 0.93
Table 1: Absolute pressure settings for the three test cases
Used for TSI™ Particle Sizer and PIV experiments

## Slide 9: Results: Particle Sizer
Case | Particles Collected | Particle Concentration [#/cm3] | Median Diameter [μm] | Mean Diameter [μm] | % Particles < 1 μm Diameter
A | 4912 | 252.2 | 0.68 | 0.83 | 93.2
B | 5116 | 288.5 | 0.67 | 0.82 | 93.3
C | 6636 | 476.0 | 0.73 | 0.90 | 88.8
Table 2: Statistical data for diameters of particles collected by TSI™ spectrometer
Figure 5: Histograms of particle aerodynamic diameters

## Slide 10: Results: PIV
Figure 6: Raw instantaneous PIV images of seeded plumes for each of the three cases
Visible particle density variation near nozzle and across shock!

## Slide 11: Results: PIV
Figure 7: Sample instantaneous axial (above) and transverse (below) velocity contours and vectors for each of the three cases

## Slide 12: Results: PIV
Figure 8: Conditionally-averaged axial (above) and transverse (below) velocity contours and vectors for each of the three cases

## Slide 13: Results: Mach Disk Analysis
Mach disk location found from PIV; compared to relation from Crist8
Case | xO / De | xC / De
A | 1.45 | 1.53
B | 1.49 | 1.64
C | 1.73 | 1.84
Table 3: Mach disk standoff locations – observed (left) and computed (right) from Crist8
Aerodynamic response times of particles determined across normal shock
  Space-time transform + exponential decay fitting
Figure 9: Measured velocity across Mach disk and exponential decay model for Case A

## Slide 14: Results: PIV Particle Sizing
Aerodynamic response times converted to particle diameters using Stokes drag model7 and Melling rarefaction correction9
  These methods can result in >2x underprediction of particle size in compressible flow10
Case | τ [μs] | dp,S [μm] | dp,M [μm]
A | 0.604 | 0.449 | 0.266
B | 0.634 | 0.460 | 0.329
C | 0.537 | 0.423 | 0.337
Table 4: Particle response times and aerodynamic diameters using Stokes drag model (dp,S) and Melling correction (dp,M)
Figure 10: Particle sizes calculated from response times for eight PIV runs

## Slide 15: Conclusions
“Venturi seeder” shown to be acceptable for PIV in multiple ways
  TSI™ particle sizer reported at least 88.8% of particles ≤ 1 μm for three test cases
  Instantaneous raw PIV images showed suitable tracer particle distributions and concentrations
  Mean PIV velocity data revealed Mach disks, re-acceleration regions, etc. expected of underexpanded jet flow
Inexpensive, easy to implement in wind tunnels

## Slide 16: References
1Adler, M., Wright, M., Campbell, C., I., Engelund, W., Rivellini, T., “Entry, Descent, and Landing Roadmap: Technology Area 09”, National Aeronautics and Space Administration, 2012.
2Berry, S., Rhode, M., Edquist, K., Player, C., “Supersonic Retropropulsion Experimental Results from NASA Ames 9x7 Foot Supersonic Wind Tunnel”, Journal of Spacecraft and Rockets, Vol. 51, No. 3, 2014, pp. 724-734.
3Grant, I., “Particle Image Velocimetry: A Review”, Journal of Mechanical Engineering Science, Vol. 211, Part C, 1997.
4Lowe, K. T., Byun, G., Shea, S., Boyda, M., Winski, C., “Three-Velocity-Component Cross-Correlation Doppler Global Velocimetry for the Space Launch System Booster Separation Test in the NASA Langley Unitary Plan Wind Tunnel”, AIAA Aviation 2019 Forum, Dallas, Texas, 2019.
5Danehy, P., Wisser, B., Fahringer, T., Winski, C., Falman, B., Shea, S., Boyda, M., Lowe, K. T., “Laser Light Sheet Flow Visualization of the Space Launch System Booster Separation Test”, AIAA Aviation 2019 Forum, Dallas, Texas, 2019.
6Acharya, A. S., Lowe, K. T., Ng, W., Danehy, P., “Seeding Mechanism for High-Pressure Nozzles”, AIAA SciTech 2021 Forum, Virtual, 2021.
7Melling, A., “Tracer Particles and Seeding for Particle Image Velocimetry”, Measurement Science and Technology, Vol. 8, No. 12, 1997, pp. 1406-1416.
8Crist, S., Sherman, P., and Glass, D., “Study of Highly Underexpanded Sonic Jets”, AIAA Journal, Vol. 3, No. 6, 1965, pp. 68-71.
9Melling, A., “Seeding Gas Flows for Laser Anemometry”, AGARD Advanced Instrumentation for Aero Engine Components 1986.
10Williams, O., Nguyen, T., Schreyer, A.-M., Smits, A., “Particle response analysis for particle image velocimetry in supersonic flows”, Physics of Fluids, Vol. 27, No. 7, 2015.