## Slide 1
12/14/2021
Amin R. Nehrir
NASA Langley Research Center
PBL Incubation Study Team Report
Technology Survey Submissions
Techniques, Technologies and Sampling Strategies Toward a Global PBL Observing System
2021 AGU Fall Meeting
amin.r.nehrir@nasa.gov

## Slide 2: PBL types and flow down requirements

## Slide 3
Variable | Horizontal Resolution | Vertical Resolution | Temporal Resolution | Accuracy
Water Vapor | 0.1 –100 km | 0.1-1 km | Minutes- Monthly | 10%
Temperature |  |  |  | 1 K
PBL Height |  | N/A |  | 100 m

## Slide 4
Science Goals
G1 Convection & Extreme Weather
G2 Cloudy PBL
G3 PBL and Surface Interactions
G4 Mixing & Air Quality
Inclined
Polar
Suborbital
Shallow & Deep Convection
Surface Processes & Precipitation
PBL Thermo. &clouds
PBL Clouds, Surface Fluxes & Free Trop.
PBL Clouds & Mesoscale
PBL Thermo. & Surface Fluxes
Near Surface Water Vapor
Surface Heterogeneity
PBL Thermo. & Extremes
PBL Mixing & Transport
Convection & Mesoscale
Sub-daily variability
Climate-related processes
Science not achievable from space
Shallow & Deep Convection
Surface Processes & Precipitation
PBL Thermo. &clouds
PBL Clouds, Surface Fluxes & Free Trop.
PBL Clouds & Mesoscale
PBL Thermo. & Surface Fluxes
Near Surface Water Vapor
Surface Heterogeneity
PBL Thermo. & Extremes
Convection & Mesoscale
Shallow & Deep Convection
Surface Processes & Precipitation
PBL Thermo. &clouds
PBL Clouds, Surface Fluxes & Free Trop.
PBL Thermo. & Surface Fluxes
Near Surface Water Vapor
Surface Heterogeneity
PBL Thermo. & Extremes
PBL Mixing & Transport
PBL Param. & Modeling

## Slide 5
Measurement Techniques and Space-Based TRL
Active
Passive

## Slide 6
Hybrid Observing System to Bridge Scales

## Slide 7: Suborbital and Remote and In-Situ Sensing
Airborne and surface based remote sensing will be critical to bridge the observational gap not achievable from space
Many mature and emerging airborne technologies exist for process studies and technology demonstration for space
  Hyperspectral Infrared Sounder
  Microwave Sounder
  Water vapor DIAL
  Water vapor DAR (and T by proxy)
  HSRL/Backscatter lidar (aerosol/cloud/ocean)
  Raman Lidar (T,q, aerosol)
  Doppler Lidar (3-D winds)
  Imaging spectrometers (TPWV)
  Polarimeter (cloud properties)
  Broadband radiometer
Dedicated in situ aircraft is ideal for improved/coordinated sampling (e.g. ACTIVATE) sampling strategy
  Fast T,q, U,V
  Aerosol optical and microphysical properties
  Cloud optical and microphysics
  Cloud water
  Composition (atmospheric tracers and chemistry, AQ)
  Dropsonde
Surface Based Remote Sensing
  Lower Troposphere Observing System (LOTOS)
  Integrated Surface Flux System (ISFS)
  Integrated Sounding System (ISS)
  SMARTLabs Mobile Facility
  Saildrone
  Buoy – lidar, flux, radiometer…
  Tethered Balloon
  Networkable IR/MW sounders
  Networkable DIAL
  MPLNET, Unified Ceilometer Network

## Slide 8
IR/MW
Cubesats

## Slide 9: Hyperspectral Infrared Sounding
Program of Record
New Mission Concepts
Technology Advance
Adapted from Smith Sr. et al., 2009, AMT
Notes: IASI NG- launch in 2023 on Metop-SG-A
IASI-NG will have 16,923 spectral channels covering roughly the same bandwidth as IASI, providing twice the spectral resolution (0.25 cm-1 ) and hence higher vertical resolution resulting from narrower weighting functions (Crevoisier et al. 2014). A major advancement of IASI-NG over IASI is the 29 improvement in radiometric noise, leading to reduction in retrieved water vapor uncertainty by * 3–5%, although these improvements are realized between 800 and 200 hPa (Crevoisier et al. 2014). The vertical resolution and accuracy of IASI-NG water vapor retrievals below 800 hPa will remain approximately the same as IASI
Iron et al on averaging kernels

## Slide 10: Hyperspectral Infrared Sounding
Program of Record
New Mission Concepts
Technology Advance
x
Adapted from Smith Sr. et al., 2009, AMT
IASI-NG (2021)
IRS, GEO (2023)
GIIRS, GEO (2016)
Notes: IASI NG- launch in 2023 on Metop-SG-A
IASI-NG will have 16,923 spectral channels covering roughly the same bandwidth as IASI, providing twice the spectral resolution (0.25 cm-1 ) and hence higher vertical resolution resulting from narrower weighting functions (Crevoisier et al. 2014). A major advancement of IASI-NG over IASI is the 29 improvement in radiometric noise, leading to reduction in retrieved water vapor uncertainty by * 3–5%, although these improvements are realized between 800 and 200 hPa (Crevoisier et al. 2014). The vertical resolution and accuracy of IASI-NG water vapor retrievals below 800 hPa will remain approximately the same as IASI
Iron et al on averaging kernels

## Slide 11: Hyperspectral Infrared Sounding
AIRS averaging kernels and vertical resolution
Program of Record
New Mission Concepts
Technology Advance
Iron et al. 2018, AMT
Notes: IASI NG- launch in 2023 on Metop-SG-A
IASI-NG will have 16,923 spectral channels covering roughly the same bandwidth as IASI, providing twice the spectral resolution (0.25 cm-1 ) and hence higher vertical resolution resulting from narrower weighting functions (Crevoisier et al. 2014). A major advancement of IASI-NG over IASI is the 29 improvement in radiometric noise, leading to reduction in retrieved water vapor uncertainty by * 3–5%, although these improvements are realized between 800 and 200 hPa (Crevoisier et al. 2014). The vertical resolution and accuracy of IASI-NG water vapor retrievals below 800 hPa will remain approximately the same as IASI
Iron et al on averaging kernels

## Slide 12: Hyperspectral Infrared Sounding
AIRS averaging kernels and vertical resolution
IASI DOFS with improved Ne∆T
Program of Record
New Mission Concepts
Technology Advance
Iron et al. 2018, AMT
CIRAS (cubesat)
MISTiC (SmallSat)
Thompson et al. 2021, AMT
NIR Imaging Spectroscopy
Pagano et al., 2021 PBL DSI
Maschhoff et al., 2018, Remote Sensing
Gunapala et al. 2020, ESTF
RP-BIRD DFPA
Bendoym, ACT-17
Metamaterial Spectrometer
Notes: IASI NG- launch in 2023 on Metop-SG-A
IASI-NG will have 16,923 spectral channels covering roughly the same bandwidth as IASI, providing twice the spectral resolution (0.25 cm-1 ) and hence higher vertical resolution resulting from narrower weighting functions (Crevoisier et al. 2014). A major advancement of IASI-NG over IASI is the 29 improvement in radiometric noise, leading to reduction in retrieved water vapor uncertainty by * 3–5%, although these improvements are realized between 800 and 200 hPa (Crevoisier et al. 2014). The vertical resolution and accuracy of IASI-NG water vapor retrievals below 800 hPa will remain approximately the same as IASI
Iron et al on averaging kernels

## Slide 13: Hyperspectral Microwave Sounding
Program of Record
New Mission Concepts
Technology Advance
Blackwell

## Slide 14: Hyperspectral Microwave Sounding
Program of Record
New Mission Concepts
Technology Advance
Blackwell

## Slide 15: Hyperspectral Microwave Sounding
Program of Record
New Mission Concepts
Technology Advance
Blackwell
Reising et al. ESTF 21
Pett et al., 2021 PBL DSI
Gambacorta IIP-21
Gambini et al. 2021
Blackwell
IIIP-21

## Slide 16: Differential Absorption Lidar (DIAL) – NIR
Program of Record
New Mission Concepts
Technology Advance
High Altitude Lidar Observatory (HALO)

## Slide 17: Differential Absorption Lidar (DIAL) – NIR
Program of Record
New Mission Concepts
Technology Advance
High Altitude Lidar Observatory (HALO)

## Slide 18: Differential Absorption Lidar (DIAL) – NIR
Program of Record
New Mission Concepts
Technology Advance
∆x = 50 km
∆z = 1km
∆z = 315
Nehrir et al. 2021, ESTF
Nehrir IIP-19
High Altitude Lidar Observatory (HALO)

## Slide 19: Differential Absorption Radar (DAR) – G band
Program of Record
New Mission Concepts
Technology Advance
4.6”
Massively parallel transmitter
Lebsock et al., 2021 PBL DSI
Virginia Diode Inc.
~1.5”
Northrop Grumman
Roy et al. 2021, AMT
Vapor In Cloud Profiling Radar (VIPR)
Power Amplifier
Space-based DAR Simulations
Notes: a power-combined architecture using 170 GHz InP power amplifiers fabricated by Teledyne Inc. The size of the amplifier block (excluding the black heat sink) is 1.75” x 1.5” x 0.95”.

## Slide 20: GNSS Radio Occultation
Program of Record
New Mission Concepts
Technology Advance
COSMIC-2, Commercial, GRAS-2….
20 cm
Franklin et al., 2021 PBL DSI
Ao et al., 2021 PBL DSI
Wang et al., 2017 AMT
Turk et al., 2019 Rem. Sens.
Notes: Global Navigation Satellite System (GNSS) radio occultation (RO) measurements are promising in sensing the vertical structure of the Earth’s planetary boundary layer (PBL). However, large refractivity changes near the top of PBL can cause ducting and lead to a negative bias in the retrieved refractivity within the PBL (below ∼ 2 km).
Radio occultation was first used by NASA's Mariner 4 mission in 1965 when the spacecraft flew past Mars. As it passed behind the Red Planet from our perspective, scientists on Earth detected slight delays in its radio transmissions as they traveled through atmospheric gases. By measuring these radio signal delays, they were able to gain the first measurements of the Martian atmosphere and discover just how thin it was compared to Earth's.
By the 1980s, scientists had started to measure the slight delays in radio signals from Earth-orbiting navigation satellites to better understand our planet's atmosphere. Since then, many radio occultation instruments have been launched; Sentinel-6 Michael Freilich will join the six COSMIC-2 satellites as the most advanced GNSS-RO instruments among them.
"The Sentinel-6 instrument is essentially the same as COSMIC-2's. Compared to other radio occultation instruments, they have higher measurement precision and greater atmospheric penetration depth," said Chi Ao, the instrument scientist for GNSS-RO at JPL.
Due to the success of COSMIC-1, U.S. agencies and Taiwan decided to move forward with a follow-on Global Navigation Satellite System Radio Occultation (GNSS-RO) mission called FORMOSAT-7/COSMIC-2 (COSMIC-2). The six COSMIC-2 satellites launched successfully on June 25, 2019 into low-inclination orbits. U.S. agencies, led by the National Oceanic and Atmospheric Administration (NOAA) and Air Force (USAF) are partnering with Taiwan's National Space Organization (NSPO), UCAR, and others to execute the COSMIC-2 program. The GNSS-RO payload, named TGRS for Tri-GNSS Radio-occultation System, was developed by NASA's Jet Propulsion Laboratory and is tracking more than 4,000 high-quality profiles per day (across the 6 satellite constellation)
GRAS-2 (MetOp-SG)

## Slide 21: GNSS Radio Occultation
Program of Record
New Mission Concepts
Technology Advance
COSMIC-2, Commercial, GRAS-2….
20 cm
Ao et al., 2021 PBL DSI
Turk et al., 2019, Remote Sensing
Franklin et al., 2021 PBL DSI
Wang et al., 2017 AMT
Nehrir et al. 2017, Survey Geophysics
Notes: Global Navigation Satellite System (GNSS) radio occultation (RO) measurements are promising in sensing the vertical structure of the Earth’s planetary boundary layer (PBL). However, large refractivity changes near the top of PBL can cause ducting and lead to a negative bias in the retrieved refractivity within the PBL (below ∼ 2 km).
Radio occultation was first used by NASA's Mariner 4 mission in 1965 when the spacecraft flew past Mars. As it passed behind the Red Planet from our perspective, scientists on Earth detected slight delays in its radio transmissions as they traveled through atmospheric gases. By measuring these radio signal delays, they were able to gain the first measurements of the Martian atmosphere and discover just how thin it was compared to Earth's.
By the 1980s, scientists had started to measure the slight delays in radio signals from Earth-orbiting navigation satellites to better understand our planet's atmosphere. Since then, many radio occultation instruments have been launched; Sentinel-6 Michael Freilich will join the six COSMIC-2 satellites as the most advanced GNSS-RO instruments among them.
"The Sentinel-6 instrument is essentially the same as COSMIC-2's. Compared to other radio occultation instruments, they have higher measurement precision and greater atmospheric penetration depth," said Chi Ao, the instrument scientist for GNSS-RO at JPL.
Due to the success of COSMIC-1, U.S. agencies and Taiwan decided to move forward with a follow-on Global Navigation Satellite System Radio Occultation (GNSS-RO) mission called FORMOSAT-7/COSMIC-2 (COSMIC-2). The six COSMIC-2 satellites launched successfully on June 25, 2019 into low-inclination orbits. U.S. agencies, led by the National Oceanic and Atmospheric Administration (NOAA) and Air Force (USAF) are partnering with Taiwan's National Space Organization (NSPO), UCAR, and others to execute the COSMIC-2 program. The GNSS-RO payload, named TGRS for Tri-GNSS Radio-occultation System, was developed by NASA's Jet Propulsion Laboratory and is tracking more than 4,000 high-quality profiles per day (across the 6 satellite constellation)
GRAS-2 (MetOp-SG)

## Slide 22
IR/MW
Cubesats