## Slide 1: AIAA SciTech-2022 Nuclear Thermionic Avalanche Cell (NTAC) Augmented Nuclear Thermal Propulsion (NTP) & Nuclear Electric Propulsion (NEP)
Sang H. Choi
Dennis M. Bushnell
Robert W. Moses
NASA Langley Research Center
January 5, 2022
sang.h.choi@nasa.gov

## Slide 2: Nuclear Engine for Rocket Vehicle Application (NERVA) Engine
Image Credit NASA

## Slide 3: Maximum performance results of the Rover/NERVA programs
Parameter | Reactor (test date) | Peak performance achieved
Power | PHOEBUS 2A (July 1968) | 4100 MWt
Peak fuel temperature | PEEWEE (November 1968) | 2750 K
Specific impulse | PEEWEE (November 1968) | 848 s
Maximum restarts | XE’ (June 1969) | 28 times
Accumulated time at full power | NF-1 (June–July 1972) | 109 min
Continuous operation | NRX-A6 (December 1967) | 62 min
Binary alloy | Melting temperature (K)
NbC | 3873 ± 25 K
TaC | 4258 K
UC | 2803 K
ZrC | 3813 K
Alloys Considered for Reactor Chambers

## Slide 4: Comparison of rocket propulsion system characteristics
Theoretical
Specific
Impulse
440 s
980 s
2600 s
6700 s
1.33 Ms
Mass Ratio*,
Earth Escape
15
3.2
1.5
1.2
Energy Source
Chemical
Reaction
Nuclear
Fission
Reaction
LH2
Lox or LF2
LH2
Fusion
Materials
Nuclear
Fusion
Annihilation
Combustion Chamber
Reactor Core
Reaction Chamber
H2-solid core, 2800 K
H2-molten core, 5250 K
H2-gaseous core, 10000 K
H+ + e-
> 200000 K
*Ratio of take-off to final mass

## Slide 5: Nuclear Fission Patterns
Fission Released Energy | U-233 | U-235* | Pu-239 | Kinetic Range | Shielding
Fission Reaction |  |  |  |  | Iron & Concrete
Kinetic Energy of Fission Fragments, [MeV] | 168.2 | 169.1 | 175.8 | ~ m | Reactor Rod
Kinetic Energy of Prompt Neutrons, [MeV] | 4.9 | 4.8 | 5.9 | 1 cm ~ 10 cm | Moderator Reflector
Prompt -rays, [MeV] | 7.7 | 7.0 | 7.8 | > 1 m | Iron & Concrete
Decay Process of Fission Products |  |  |  |  | 
β – Decay, [MeV] | 5.2 | 6.5 | 5.3 | ~ mm | Fissile Fuel
Antineutrinos, [MeV] | 6.9 | 8.8 | 7.1 |  | none
Delayed  - rays | 5.0 | 6.3 | 5.2 | > 1 m | Iron & Concrete
Total Energy of Energetic β & , [MeV] | 17.9 | 19.8 | 18.3 |  | 
Total Recoverable Energy, [MeV] | 198 | 200.7 | 207 |  | 
Fission Released Energy | U-233 | U-235* | Pu-239 | Kinetic Range | Shielding
Fission Reaction |  |  |  |  | Iron & Concrete
Kinetic Energy of Fission Fragments, [MeV] | 168.2 | 169.1 | 175.8 | ~ m | Reactor Rod
Kinetic Energy of Prompt Neutrons, [MeV] | 4.9 | 4.8 | 5.9 | 1 cm ~ 10 cm | Moderator Reflector
Prompt -rays, [MeV] | 7.7 | 7.0 | 7.8 | > 1 m | Iron & Concrete
Decay Process of Fission Products |  |  |  |  | 
β – Decay, [MeV] | 5.2 | 6.5 | 5.3 | ~ mm | Fissile Fuel
Antineutrinos, [MeV] | 6.9 | 8.8 | 7.1 |  | none
Delayed  - rays | 5.0 | 6.3 | 5.2 | > 1 m | Iron & Concrete
Total Energy of Energetic β & , [MeV] | 17.9 | 19.8 | 18.3 |  | 
Total Recoverable Energy, [MeV] | 198 | 200.7 | 207 |  | 
*U-235 has 3 other fission patterns
Concrete - high density

## Slide 6: Principles and Concept
Fission Reaction Rate
where  - neutron flux [neutrons/cm2s]
 - microscopic cross section [barn, cm2]
N - atomic number density [atoms/cm3]
The reaction rate for various types of interactions includes the total t, the absorption a, the radiative capture c, and the fission f. The rate of energy release (power) due to the fission reaction is given by following equation:
P = RR  Er  V = Ф  Σf  Er  V = Ф  NU235  σf235  Er  V
where P – reactor power [MeV/s] Ф – neutron flux [neutrons/cm2∙s] σ – microscopic cross section [cm2] N – atomic number density [atoms/cm3] Er – the average recoverable energy per fission [MeV/fission] V – total volume of the core [m3]

## Slide 7: Nuclear Fission Reaction Rates for NTP and NEP
Neutron flux required to sustain nuclear fission reaction
for generation of fission power from HALEU
nuclear fuel (19.75% U-235 and 80.25% U-238) wrt. fuel
mass from 1 thru 10 tons
Power output from nuclear fission process requires a rate of
thermal neutron triggered nuclear fission reaction within HALEU
nuclear fuel (19.75% U-235 and 80.25% U-238)
HALEU: High-Assay Low-Enriched Uranium

## Slide 8
Gamma Ray Emission and Associated Power
Rate of gamma ray emission from nuclear fission reaction
of HALEU nuclear fuel (19.75% U-235 and 80.25% U-238)
wrt. fuel mass from 1 thru 10 tons
Photon power of gamma ray from nuclear fission reaction of
HALEU nuclear fuel (19.75% U-235 and 80.25% U-238).

## Slide 9
Propellant Flowrates and Isp for NTP
Flowrates of propellants (H2 and Ar) required to keep the reactor
temperature at 2800 oK based on reactor power output.
Specific impulse (Isp) of hydrogen and argon propellant at 2800 oK
reactor temperature.

## Slide 10
Prompt Gamma Ray Only
Prompt & Delayed Gamma Rays
Specific power of NTAC augmented NTP
Specific power of NTAC augmented NTP system considering
only prompt gamma rays based on nuclear reactor power output
from HALEU nuclear fuel (19.75% U-235 and 80.25% U-238)
for fuel mass from 1 thru 10 tons
Specific power of NTAC augmented NTP system considering
prompt and delayed gamma rays together based on nuclear reactor power output from HALEU nuclear fuel (19.75% U-235 and 80.25% U-238) for fuel mass from 1 thru 10 tons.

## Slide 11: Fission Reactor Parameters
Uranium Fuel: HALEU (19.75% of U-235)
Fuel Weight: Cases of 1 ton, 2 tons, 3 tons, 4 tons, 5 tons, 6 tons, 7 tons, 8 tons, 9 tons, and 10 tons
H2 & Ar Temperature: 2800 K
 | 500 MW | 600 MW | 700 MW | 800 MW | 900 MW | 1000 MW | 1500 MW | 2000 MW | 2500 MW | 3000 MW
H2 Flowrate | 9.83 | 11.79 | 13.76 | 15.72 | 17.69 | 19.66 | 29.48 | 39.31 | 49.14 | 58.97
Ve, m/s | 7577 | 7653 | 7714 | 7334 | 7394 | 7214 | 7426 | 7237 | 7189 | 7140
Isp, s | 773 | 781 | 787 | 748 | 754 | 736 | 758 | 738 | 734 | 729
Ar Flowrate | 20.60 | 41.21 | 61.81 | 82.42 | 103.02 | 123.63 | 144.23 | 164.84 | 185.44 | 206.04
Ve, m/s | 1432 | 1503 | 1535 | 1476 | 1497 | 1472 | 1487 | 1432 | 1408 | 1386
Isp, s | 166 | 166 | 167 | 164 | 164 | 163 | 164 | 163 | 162 | 162

## Slide 12: Ionization Fraction of H2 and Ar
=
Saha Equation of Ionization Fraction;
0.86 eV
0.86 eV
Ionization fraction of hydrogen. At 10000 oK,
80% of hydrogen can be ionized.
Ionization fraction of argon. At 10000 oK, Only 10% of argon
can be ionized even though argon has a large collision
cross-section.

## Slide 13
New Concepts of Nuclear Powered Rockets
Hybrid thruster of NTP and NEP
powered by NTAC
NTP combined with MPD thruster
powered by NTAC

## Slide 14
Inner Layer & Neutron Reflector
TRISO Pebble-bed: HALEU 19.5
Control Rods
Propellant from Pump
Exhaust Gas
Preheated Propellant
Heated
Propellant
Rocket Chamber
NTAC Cell
Structure
Neutron
Reflector
Reactor Core: HALEU 19.5
Control Rods
Propellant
from Pump
Exhaust Gas
Preheated Propellant
Heated
Propellant
Rocket Chamber
NTAC
NTP with Two Different Nuclear Reactor Cores
Reactor Core: TRISO Pebble-bed
Reactor Core: Pellet-stacked rods

## Slide 15
Pump
Propellant Feed Line
Nuclear Reactor Core
Neutron Reflector
NTAC
Electric Thrusters
Nuclear Thermal Thruster
Preheated Propellant Line
Hybrid Thruster of NTP and NEP powered by NTAC

## Slide 16

①
Propellant Feed Line
Pre-heated Propellant
Turbo Pump
Pellet or Pebble Nuclear Reactor
Neutron Reflector
NTAC
Electric Thrusters
Power Feed Line
for Electric Thrusters
NTAC Augmented NEP

## Slide 17: Concluding Remarks
NTP and NEP can be paired with NTAC to create additional power
NTAC can add 10% more power to NTP and 30% more to NEP since NEP requires one more step-down power conversion from thermal to electric which ends up with 30% of thermal. NTAC can add electric power (10% of thermal) amounting of 30% level of NEP electric power.
Possibility of mixed mode of NTP and NEP with NTAC exists
Additional power by NTAC improves the overall specific power of a system