## Slide 1: AIAA SciTech2022 Lunar Volatiles Collector
Sang H. Choi
Robert W. Moses
NASA Langley Research Center
Hampton, Virginia
January 5, 2022

## Slide 2: Problem/Need – The Importance of the Idea
The capture, collection, and onsite supply of volatiles on the Moon, Mars, and asteroids are the key aspects of technology needed as a post process of H2O, H2, O2, or other gases for propellant and habitats. The capture of volatiles is extremely difficult at lunar vacuum (i.e., 10-12 torr on the moon). No existing equipment for volatile capture is available to date.
  The lunar volatile collector (LVC) concept based on Bessel Tube (BT) enables the capture and collection of volatiles at extremely low vacuum pressure using the unique principle of ring-field harmonic generator (which is typically used for heavy ion accelerator, i.e., Large Hadron Collider).
The Problem of Current Arts
  No current arts are available to capture and collect volatiles at extremely low vacuum. Any volatiles extracted at the vacuum pressure of 10-12 torr level can freely fly away with their initial kinetic energy in all directions. A special tool like BT is definitely required.
  NASA and the aerospace community lack resource acquisition tools technology, such as Bessel Tube, for volatile capture to support production of H2O and propellants (H2 and O2) or any other volatiles from regolith.
The Need
  BT is quite suitable for harvesting volatiles (H2O, O2, H2, or He-3) at extreme vacuum environment (10-12 torr).

## Slide 3: Space Environment of the Moon
Atmospheric Pressure: < 10-12 torr
Micro-meteorite Impact: Velocities to > 105 km/hr (28 km/sec)
Radiation: Galactic, Cosmic, Solar-ray particles
Proton- 3x108 cm-2∙s-1
Electrons- 105 ~ 107 cm-2∙s-1
Temperatures: Equator- -20oC ± 120oC
South Pole- Light -50oC ± 20oC
Dark -220oC ± 20oC

## Slide 4
70%
7.70At%
5.25, 4.48, 3.23 At%
60.71 Atomic %
17.36 At%
Oxide
Magnesium, Calcium, Iron
Silicon
Lunar Dust Composition
- Elemental Analysis
Solar Wind (0.5 ~ 10 keV av.) & Solar Flare (> 28 keV)
Proton: 3x108 cm-2∙s-1
Electron: 105 ~ 107 cm-2∙s-1
~ 1 pA/cm2
O ~ 6x104 cm-2∙s-1
Mukherjee, N.R., Earth, Moon, and Planets, Vol. 21, No. 3, 307-317, 1979.
Snowden et al., The Astrophysical Journal, 610:1182–1190, August 1, 2004.
Secondary
electrons
Metal
elements
Aluminum

## Slide 5: Chemical Bonding Energy
Single & Multiple Bonds | Bonding Energy (kJ/mol) | Bonding Energy (eV) | Bond Length (pm)
H―H | 432 | 4.49 | 74
C―H | 413 | 4.29 | 109
C―C, C═C, C≡C | 347/614/839 | 3.61/6.38/8.72 | 154/134/121
C―O | 358 | 3.72 | 143
C═O | 745 | 7.74 | 123
N―H | 391 | 4.06 | 101
N―N, N═N | 160/418 | 1.66 | 146/122
N―O | 201 | 4.35 | 144
O―H | 467 | 4.85 | 96
O―O | 204 | 2.12 | 148
O═O (O2) | 498 | 5.17 | 121
Si―O | 368 | 3.83 | 161
Al―O | 102 | 1.06 | 17
Energy needed to breakdown

## Slide 6: Helium-3 Mining
Fusion reactions involving Helium-3 |  |  | 
Reactants |  | Products | Q
First Generation Fuels |  |  | 
21H + 21H | → | 32He + 10n | 3.268 MeV
21H + 21H | → | 31H + 11p | 4.032 MeV
21H + 31H | → | 42He + 10n | 17.571 MeV
Second Generation Fuel |  |  | 
21H + 32He | → | 42He + 11p | 18.354 MeV
Third Generation Fuel |  |  | 
32He + 32He | → | 42He+ 211p | 12.86 MeV
Rationale
Helium-3
Neutrons 1
Protons 2
Parent Isotopes 3H (β-decay)
Isotope Mass 3.016 u
Half Life stable
Spin ½+
Availability 0.000137% in Atm
Helium-3 in regolith
Dangling bond – van der Waals
Electrostatic
Trapped
Resources
Earth Mantle ~ 106 tons
Ocean Floor 4000 tons
Lunar Regolith ~ 106 tons
Needs
U.S.A. 20 tons/yr ($60B worth)
Others together 80 tons/yr
Price: $3B/ton
Aspiration (Richard B. Bilder, Fordham International Law Journal, Vol. 33, Iss. 2, 2009)
U.S.A. One of the justifiable space expeditions (2015)
China Officially stated goal of Chinese lunar exploration program
Russia Helium-3 mining plan by Russia’s RKK Energia by 2020
Japan ???
India Officially, but no details

## Slide 7: Challenges for Lunar Volatile Collection (LVC)
LVC must work under Lunar’s extreme environmental conditions.
Capture capability of LVC must be assured with high rate for collecting atoms and molecules.
Guiding channel of collected volatiles must be integrated with storage containers to keep volatiles (H2O, H2, O2, He-3) selectively and separately.
Power (thermal and electrical) must be secured as an autonomous unit.

## Slide 8: Bessel Tube (BT) Concept for Volatile Collection
Electron Accelerating Cavity
Bessel Tube
Hypocycloidal field formation is described by the equipotential lines within which any particles ionized or with dipole moment are captured and accelerated along the drift axis by ring field. The ring electrodes are charged with high voltage sequentially with time interval to create ring field.
Cylindrical harmonic generator in a hypocycloidal mode used for accelerating electrons in electron Accelerator laboratory.
Particle capture by cylindrical harmonic generator in a hypocycloidal mode.

## Slide 9
Drift Axis
Hypocycloidal Formation of Equipotential
Narrow Field Channel
Wide Field Channel
Hypocycloidal Formation of Equipotential
Field in BT
Linear Array of Ring Electrodes
Ring Electrode
High Voltage
Lead Wire (V)
DG
DR
DG: Gap distance between the ring electrodes
DR: Diameter of ring electrodes

## Slide 10
V
V
V
V
V1
V2
V3
V4
V5
V6
V1
V2
V3
V4
V5
V6
Voltages are all equal (Vn=Vn-1) or in a gradient (Vn > Vn-1 or Vn < Vn-1)
−
−
−
−
−
−
−
−
−
−
−
−
Pulled
Pushed
Particle with
Dipole Moment
BT with Distributed Voltages

## Slide 11
Capturing Mode
Straightening Mode
Acceleration Mode
Acceleration Mode
Acceleration Mode
Ejection Mode
Particles converge into drift axis
by cylindrical harmonic field (CHF)
Particles converge further into
drift axis by CHF
Particles accelerate along with
drift axis by CHF
Particles accelerate along with
drift axis by CHF
Particles accelerate along with
drift axis by CHF
Particles are ejected out along with
drift axis by CHF
Ionized or Dipole
Particles
BT with Sequentially Applied Voltages

## Slide 12: Helium-3 Mining Technology
Regolith
Gobbler
Crack Feeder
EM Kicker with BT
Flight Distributer
Mass-Drop Collector
E-Beam/Thermal
Dissociation

## Slide 13: O2 Separation
E-Beam
Gun
O2
Metal Sludge
Regolith In:
Oxides
Heated Regolith Out
Cassegrain System
BT
Quadruple Pole
Driver
Array of Volatile
Storage

## Slide 14: Melting Time of 8-cm Thick Regolith
Courtesy of NASA KSC
Time to Sinter a 32 cm thick, 30 meter diameter landing pad using 0.3 m focal plane diameter:
• 120 days by a 10 meter aperture diameter
• 30 days by a 20 meter aperture diameter
• 13 days by a 30 meter aperture diameter
• 8 days by a 40 meter aperture diameter
Chart: Primary Aperture Diameter, m
| 40 | 30 | 20 | 10
0.1m | 1.8071 | 3.2126 | 7.2284 | 28.9135
0.2m | 7.2284 | 12.8505 | 28.9135 | 115.6541
0.3m | 16.2639 | 28.9135 | 65.0554 | 260.2217
0.5m | 45.1774 | 80.3153 | 180.7095 | 722.8381
Focal Plane Diameter
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
sec
m
m
m
m

## Slide 15: Summary: Volatile harvesting from lunar regolith by BT
Description and Objectives Description: The invented BT (LAR-19538-1) is a unique device to capture and accelerate gaseous particles through drift axis of circularly harmonic field or ring-field generator. Circularly harmonic field establishes the cylindrical harmonic condition on the axially symmetric electric polar arrangement. The axially symmetric electric polar arrangement is used at the electron accelerator to create the drift axis of E-field equipotential in a cylindrical harmonic. The capture and collection of gas molecules under the extreme vacuum condition (i.e., 10-12 torr on the Moon) are extremely difficult. No equipment is available to date. The proposed BT is able to capture and collect the volatiles (H2O, He-3, and/or other gaseous molecules) for enabling lunar onsite supply. The captured gaseous elements are then accelerated and eventually stored selectively into a bottle by induction field at the other end of BT. Objectives: To develop BT array to effectively capture and collect gaseous molecules, such as H2O, He-3, or other gaseous molecules, for potential onsite supply. | State of the Art The Bessel Tube is totally a new invented device technology. There are NO comparable or better technologies available to date. Reference current SOA, (solely NASA Langley invented technology) S.H. Choi, H.S. Choi, R.W. Moses, and K. Kim, “Bessel Tube for Driving Gaseous Molecules and Nanoparticles into Linear Motion”, NASA Case No. LAR 19538-1, e-NTR #: 1539786201, Oct. 17, 2018. “Where are we now?” A preliminary design of BT was done.
Customers/Infusion, Alignment: Customers/Infusion Current - Lunar and Mars exploration under ISRU Potential Vacuum pump application with BT for extreme vacuum pump (< 10-8 torr) Partners Existing Collaborator – None Potential – Vacuum pump manufacturers | Technical Approach Technical development perspective how the mission or project will be approached. Process of design and fab for laboratory model and test performance in high vacuum (TRL 4) Fabrication of BT array with differential field controller of electric potential on each ring-field coil (TRL 6) Validation of BT array performance (TRL 7) On-going effort by the proposal team. Design study of the components of BT. Technology involved and how it will be used to solve the problem. An array of multiple ring-field generators for differential field generation “to-be-developed” subsystems: Subsystem requires a storage bottle of collected volatiles by BT. Maturity of component technologies: TRL 7, Suitability for the mission: very high Interface requirements Power modulation on each ring-field coil.