## Slide 1
Shock tube radiation measurement in expanding air flows
Augustin Tibère-Inglesse1
Khalil Benssassi2, Aaron Brandis2, Brett Cruden2
1 NASA Postdoctoral Program Fellow at NASA Ames Research Center
2AMA Inc at NASA Ames Research Center, Mountain View
AIAA SciTech meeting, 3-7 January 2021

## Slide 2: Outline
1) Introduction
  2) CFD simulations of EAST expansion cone
  3) Experimental data
  4) Conclusions

## Slide 3: Atmospheric entry phase: radiative heating
N2
N2
N2
N2
N+
Radiative heat fluxes
200% uncertainties
V ~ 11 km/s
T ~ 200 K
P ~ 10-5 atm
V ~ 100 m/s
T ~ 11000 K
P ~ 0.5 atm
Afterbody
= 2/3 of the surface
q ~ 20 W/cm2
q ~ 100 W/cm2
Shock
O2
O
e-
e-
High uncertainties on afterbody radiation because of nonequilibrium and lack of validation data
C. O. Johnston and A. M. Brandis, JSR 2015
Equilibrium
Nonequilibrium

## Slide 4: Experimental setup of EAST
Driver
Buffer (opt)
Driven
Cone
4 spectrometers
(VUV, Blue, Red, IR)
Last PCB before
cone entrance
PCB
Pitot rake
Velocity estimated using PCB measurements in the tube and extrapolating to the cone
Test conditions
  Test gas is Air at 0.2 Torr (60 km equivalent altitude)
  Target velocities at cone entrance are 10 and 11 km/s
Optional Configuration – He or He/Ar Buffer at 50 Torr
Diaphragm Configurations
  Thin Aluminum – Breaks randomly, burst at 130 psi
  Scored Stainless Steel – Breaks on petals, burst is estimated at 6000-12000 psi
Driver options - 30’’ Cylindrical or 11” Conical
Notes: Drop configurations

## Slide 5: 2D-axisymmetric simulations
Time step not constant
Notes: Primary shock -> flow establishment behind -> flow expanding in the nozzle
Impact of the window: oblique shock

## Slide 6: Goal: studying expanding flows
Camera range
Shock front
Compressing flow
Expanding flow
Line of sight: compressing + expanding flow
Camera range covers compressing and expanding flows
Expanding region starts ~6.5 cm from shock front
After 6.5 cm, the measured radiation is a combination of radiation coming from both expanding and compressing flows
Can we validate aerothermal mission design tools for wake flows with EAST cone measurements?
Flow

## Slide 7: Radiation from recombining region?
Accumulated radiance from 200 to 500 nm
Volumetric radiance
Line of sight
0
Total radiance (measured by optical setup)
0 %
10 %
25 %
45 %
70 %
85 %
Expanding region
Compression/expanding interface at ~6.5cm from shock front → 9 us minimum test time (vCFD=7 km/s)
Radiation from recombining region dominant ~10.5 cm from shock front → test time of ~15 us needed
“double” peak observed because of shock curvature
of total radiation

## Slide 8: Test 63 summary
37 shots, >50% with useable spectra
  5 without Velocity/Time of Arrival data
Test times from 3.5 to 10.5 us
“Good” (complete dataset + high test times) data for at least 4 shots, from 9.64 to 11.11 km/s
Data presented | Velocity (cone entrance) | Velocity (camera location)
CFD | 10.2 | 6.5 (with window)
 |  | 7.0 (w/o window)
Shot 8 | 10.2 | 8.85
Shot 21 | 9.64 | 8.54
Notes: Replace table with plots shot # vs test times or test time vs velocity
Shot 21

## Slide 9: Spectra
Typical shots:
Strongly contaminated
Test time:
3 to 10 us
Faint atomic line from impurities
Ca+
Fe → steel diaphragm

## Slide 10: Number densities
Shot 22 test time easily determined by the arrival of Fe lines and decrease of N2
No Fe lines on Shot 22, and no strong decrease of N2, larger test time?
Strongly contaminated
Weakly contaminated
Notes: Use same colors for species

## Slide 11: Comparison radiance CFD/experiments
Radiance underpredicted in the UV
Ratio of peaks intensity relatively well predicted with window
Distance between peaks not well predicted with the window, better agreement without the window
Radiance (normalized)
Data presented | Velocity (cone entrance) | Velocity (camera location)
CFD | 10.2 | 6.5 (with window)
 |  | 7.0 (w/o window)
Shot 8 | 10.2 | 8.85
Shot 21 | 9.64 | 8.54

## Slide 12: Conclusions
Test 63 campaign is done: good data measured for 10 and 11 km/s shock speeds
  Test times need to be higher than 15 us. May have been achieved for 3 or 4 shots
  30’’ driver and buffer tends to increase test times → use of both should be investigated in the future
Regions of shock identified
  Compressive flow in the cone: freestream gas in the cone is compressed by the shock
  Expansion region about 6.5 cm behind: Shocked gas from the tube expands in the cone
Double peak in intensity attributed to nonequilibrium regions on centerline and near wall
  Ratio of intensities relatively well predicted by CFD with window
  Peaks separation relatively well predicted by CFD without window
Simulations testing different kinetic model for N2 will be performed in the future

## Slide 13: Backup
Backup pitot pressures test time

## Slide 14: Unsteady 1D simulation & 2D-axisymmetric (COOLFluid)
One-dimensional, Δx = 10-4 m
Wall condition is used at the end of the driver tube.
Test gas: Air -11 species-, driver gas: 99% He, 1% N2.
Thermal and chemical non-equilibrium : Park’s two-temperatures model
Notes: Drop? Talk in next one

## Slide 15: Improving test times
30’’ driver and buffer seems to improve test times
Test times on shots 16, 21 and 25 may be underestimated
30’’ driver with buffer worth investigating
11’’ conical driver
11’’ conical driver
30’’ driver
Test driver diaphragm with
lower/higher burst pressure
High pressure driver
Buffer
(He or He/Ar)
Lighter buffer diaphragm
Higher Ar concentration

## Slide 16: Spectra
Shot 21:
Image taken 12 us after Blue
Ca+
Driver gas may arrive much later increasing the test time (from 15 to 22 us)
No Fe contamination
Cu
Notes: Drop for video

## Slide 17: Comparison with Shot 21
Ratio of peaks better predicted with window, and distance without
Intensity still underpredicted by a factor ~2
Radiance (normalized)

## Slide 18: Radiation from recombining region?
Relativelly good agreement
  Total radiation slightly underpredicted
  N2 radiation relatively well predicted but N2+B underpredicted
Accumulated radiance from 200 to 500 nm
Volumetric radiance
Good agreement overall
~50% from expanding region
Shock front (centerline)
Expansion region
Compression/expansion interface
N2+ radiation well predicted
N2 underestimated, maybe because of recombination
N+ continuum overestimated in fit
Shock front (wall)

## Slide 19: Temperatures
Compression region:
  Shock front overpredicted with the fit but good agreement with the mean
  Good agreement after the shock front
Expansion region:
  Tv: good agreement
  T: ~20% disagreement but strongly impacted by multi-dimensions effects

## Slide 20: Temperatures: CFD vs experiments
Measurements are line of sight integrated : shock is not 1D
Compare fit temperatures to predicted (max and mean):
Tr relatively well predicted after ~2cm

## Slide 21: Outline
1) Introduction
  2) Radiance
  3) Spectra
    4) Temperature and densities
      5) Conclusions

## Slide 22: Radiative species
Densities relatively well predicted near shock front
Higher discrepancies after the peak intensity
N2 underpredicted later on (recombination?)

## Slide 23: Radiance comparison with/without impurities
CN radiation alone does not explain the discrepancies
Without impurities
Without impurities and N+ continuum

## Slide 24: Radiance comparison without impurities (Shot 21)
Differences are less, maybe due to lower velocity
Relatively good agreement after ~8cm