## Slide 1: LTV Proposed Acceleration Requirements
K. Dolick1, N. Newby2, T. Reiber2, J. Somers3, D. Adelstein4, L. Stone4
1GCS, Houston, TX
2KBR, Houston, TX
3NASA Johnson Space Center, Houston TX
4NASA Ames Research Center, Mountain View, CA

## Slide 2
Background, Tasks & Deliverables
NASA is preparing for future Artemis missions that will return humans to the lunar surface
A Lunar Transport Vehicle (LTV) is planned to enhance exploration capabilities
We have been tasked to develop preliminary standards (with accompanying rationale) for LTV on acceleration, jerk, vibration, comfort and blunt trauma
A TIM was held to review/update the LTV draft requirements
  External SME Participants:
    Suzanne Smith, USAF – Vibration & Comfort
    Greg Goetchius, Joby Aviation – Vibration & Comfort
    John Bolte, Ohio State University – Blunt Trauma
Final requirement set delivered to NASA June 2021
2
Concept image of Artemis LTV – Source: nasa.gov
Applied Injury Biomechanics

## Slide 3
Considerations & General Assumptions
Unpressurized crewed rover
Crew will be wearing an EVA spacesuit
Intra-suit restraints vs no intra-suit restraints
Performance & Crew Health limits
Occupant centric requirements
3
EMU Suit & Components – Source: nasa.gov
Applied Injury Biomechanics

## Slide 4
Basis for Requirements
Acceleration requirements tailored from the SLS Emergency Egress System requirements
  Based on ASTM F2291 standard for amusement park ride design
Jerk requirements tailored from the SLS Emergency Egress System requirements
  Based on ASTM F2291 standard for amusement park ride design
Vibration health and comfort requirements tailored from NASA-STD-3001, ISO 2631-1, MIL-STD-1472H, and MIL-STD-1472G
Blunt trauma requirements based on Anthropometry & Biomechanics Facility (ABF) human volunteer testing data
4
Applied Injury Biomechanics

## Slide 5
LTV Sustained Translational Acceleration Requirements
5
Applied Injury Biomechanics
The LTV system shall limit the magnitude of crew exposure to sustained (>0.5 seconds) translational acceleration by staying below the limits in Table 1, which specify the ±Gx, ±Gy , and ±Gz translational acceleration limits appropriate for specific restraint conditions.
Table 1: Lunar Transport Vehicle Sustained Translation Acceleration Limits

## Slide 6
Thank you!
Email:
kevin.r.dolick@nasa.gov
Applied Injury Biomechanics

## Slide 7
Backup Slides
Applied Injury Biomechanics

## Slide 8
Jerk Requirements
8
Applied Injury Biomechanics
The LTV system shall limit the crew exposure to translational jerk by staying below the limits in Table 2, which specify the ±Gx, ±Gy , and ±Gz translational jerk limits appropriate for specific restraint conditions.
Table 2: Lunar Transport Vehicle Translation Jerk Limits

## Slide 9
Vibration Requirements Derived from ISO2631-1, MIL-STD-1472H, & MIL-STD-1472G
9
The LTV system shall limit the crew exposure to vibration such that the frequency-weighted acceleration between 0.5 and 80Hz, vectorially summed for the body x, y, and z axes does not exceed the limiting values in Table 3, which specify the allowable accumulated dosage over any 24hr interval for either seated or standing crew and all specified restraint conditions.
Zone | A | B | C
Acceleration Limit (ISO-weighted RMS) | 3.0m/s2 | 0.5m/s2 | 0.315m/s2
Allowable accumulated duration, t (dosage per 24hr interval) | 1s < t < 17s | 17s < t < 6hr | 6hr < t < 24hr
Table 3: Lunar Transport Vehicle Vibration Limits (Seated or Standing Vehicle Occupants)
Applied Injury Biomechanics

## Slide 10
Blunt Trauma Requirements
Additional blunt trauma metrics were obtained from Dr. John Bolte during the TIM process as they pertained to superficial boney points of interest
  Given that the lowest fracture threshold of identified superficial boney locations of concern is the clavicle (36 lbf to fracture), a threshold of 18 lbf shall be applied to all boney locations of concerns to mitigate the risk of fracture or other trauma
  SME opinion is that 50% of the fracture threshold would potentially result in soft tissue or bone bruising
Applied Injury Biomechanics

## Slide 11
Blunt Trauma Requirements
The LTV system shall limit the crew exposure to blunt trauma forces by staying below 18 lbf across bony locations of concern outlined in Figure 3.
Figure 3: Anthropometric Locations for Blunt Trauma Limits & Boney Locations of Concern
Applied Injury Biomechanics