## Slide 1
Flight Path Management (FPM) and Digital Flight (DF)
  Briefing to SC-147, 2022 Feb 08

## Slide 2: Flight Path Management (FPM) in Context
Flight Path Management
Achieve mission objectives through flight path creation, monitoring, and revision
Account for constraints in the operating environment
AFCM FPM
Flight Path Management
Tactical Operations
Suspend mission objectives until safety is restored
Respond to urgent, unforeseen hazards
AFCM HPA
Hazard Perception & Avoidance
Vehicle Control
Accurately fly the mission plan
Safely fly an established flight path and land the vehicle
Communicate performance constraints to FPM, Mission Management
AFCM AHO
Aircraft Handling & Operations
Mission Management
Establish mission objectives and associated information requirements
Monitor, decide, revise the mission parameters as needed
AFCM IPR
Integrated Pilot Requirements
AFCM ARA: Assurance of Responsible Automation
Develop guidance for achieving requisite assurance levels for responsible automation under AAM operational paradigm
AAM Advanced Air Mobility
AFCM Automated Flight & Contingency Management
Functional
Project

## Slide 3: FPM Automation Goals and Objectives
FPM Automation Goals
  Ensure that a safe and operationally acceptable flight path is available to the vehicle operator through the life of the flight
  Achieve mission objectives within established mission parameters
  Remain adaptable to evolving mission objectives, constraints, and external stimuli
Challenge: No certified FPM automation system or industry standards currently exist.
  Question: At what point do FPM automation standards become necessary?
  Consider: When the operating rules dictate that FPM automation functions are safety-critical*
Feasible – Conforms to aircraft performance and range; Complies with airspace structure, rules, and constraints
Deconflicted – Avoids unsafe proximity to known traffic, terrain, obstacles, weather, and airspace hazards
Coordinated – Follows cooperative rules and procedures to harmonize with other airspace users
Flexible – Provides adequate degrees of freedom to enable future flight path changes
Optimal – Achieves business objectives and preferences of the pilot and fleet operator
FPM Objectives: Create | Monitor | Evaluate | Revise Flight Path to be:
*Conflict Management

## Slide 4: Mode of Operation Enabled by Digital Technology
Decision-Maker
Operating Environment
Visual Flight
Pilot
Instrument Flight
ATC
Pilot
Proposed: Digital Flight
Operator
Automation
Self-managed by cooperative procedures and rules
Distributed decision-making without centralized coordinator
Pilot is the separator
Flexible
Scalable
Sharing of intent (i.e., flight plan)
Centralized strategic and tactical conflict management
ATC is the separator
(providing instructions to the pilot)
Predictable
Accessible
Self-managed by cooperative operating practices
Traffic awareness, including intent
Connectivity to centralized information services for shared situation awareness
Highly-automated separation through flight path management automation
Operator is the separator
(relying upon automation services)

## Slide 5: National Airspace System (NAS) User Constituencies Unified Mechanism for All Operators to Achieve Their Aviation Visions
Regional Air Mobility
“Community-friendly regional travel”
General Aviation
“Simplified Vehicle Operations”
Urban Air Mobility
“High density/complexity urban operations”
High Altitude Operators
“Cooperative separation”
Regional UAS
“Seamless integration in the NAS”
Airline / Business Aviation
“Reduced operating costs”
Small UAS
“Beyond visual line of sight”
Opportunity for Operational Convergence and Harmonization
through Common Capability of Digital Flight (DF)
  DF could increase scale of access to non-towered airports
  DF could reduce lost link contingency impacts and maximize NAS access
  DF could enable expansion beyond capacity-limited corridors
  DF could optimize flexible operations in Upper Class E airspace
  DF could reduce pilot training costs while increasing safety and access
  DF could enable access above 400 ft and beyond visual line-of-sight
  DF could increase flexibility to optimize under dynamic conditions

## Slide 6: FPM Interactions with UAM Operational Elements
Other Operators / Services
Common Operating Picture
Provider of Services to Operator
Community Based Rules
Ownship Aircraft
Avionics Data
Vehicle Control
Hazard Perception & Avoidance
Operating Environment
Vehicle to Vehicle
Onboard Sensors
Supplemental Data Service Provider
Operator
Fleet Operator
Pilot in Command
Settings, Conflict Alerts & Path Change Selections
Traffic
Weather Hazards
Airspace Restrictions
Atmosphere
Override
Path Changes
Active Data
Mission Parameters
& Analysis
Coordination
Supplemental Data
Cross Checks
FPM Automation
Agile response
Performance-based outcomes:
Feasible | Deconflicted | Coordinated Flexible | Optimal Flight Paths
FPM Operates at the Intersection
Operator Mission objectives
Airspace / community Constraints & coordination
Operating environment Dynamic conditions
Ownship aircraft Capabilities

## Slide 7: Autonomous Operations Planner (AOP)
Supporting NASA autonomy R&D for 20+ years
Platform for assessing FPM system requirements
Advanced algorithms for complex FPM operations
Human Testing for Pilot Procedures
Derivative Evaluation for Commercial Use
Batch Testing for Distributed Scalability
Integrated Testing for Mixed Operations
Initial Implementation for Autonomy Research in Commercial Transport Operations (2001-2019)
Strategic FPM Functionality
Tactical FPM Functionality
Strategic / Tactical Integration
Adapting AOP to AAM / UAM (Current)
  Predicts trajectories w/ bounded uncertainty
  Detects conflicts w/ traffic & area hazards
  Resolves conflicts strategically & tactically
  Prioritizes safety and coordination
  Complies with arrival time constraints
  Supports conflict-free maneuvering
  Optimizes for time, fuel, and cost index ($)
1
2
4
3
5
UAM Implementation for UML-4 Research (2019 start)
-NEW-
AOP Functional Capabilities
AFCM Reference Automation System for FPM Research

## Slide 8: AFCM FPM Integration & Testing
Tactical Operations (HPA)
Flight Path Mgmt (FPM)
Batch
HITL
V&V
FY21 FY22 FY23
IAS-1 Flight Test
HITL / Tech Integration
IAS-2 Flight Test / Sys. Integration
Mission Mgmt (IPR)
Flight-Evaluated Prototypes
Design Guidelines / Best Practices
Input to Standards Development
Suggested Means of Compliance
AFCM Guidance to Industry
FY23
FY24
FY25
Vehicle Control (AHA)
HITL Human-in-the-Loop Simulation
IAS Integration of Automated Systems Flight Test