## Slide 1: Digital Lunar Exploration Sites (DLES)
Presenter: Cory Foreman
Authors:
Sam Lawrence, Ph.D., Edwin Z. {Zack} Crues, Ph.D., Andrew Britton, Paul Bielski, Jonathan Schlueter, Amy Jagge, Chris Raymond, Nick Davis, Cory Foreman
10 March 2022
Presentation to the IEEE Conference, Big Sky, MT 2022

## Slide 2: Overview
Introduction
The Need for DLES
Building DLES
DLES Products
DLES In Use
Future Work
Conclusions
Questions

## Slide 3: Introduction
Apollo 17:
  Last time humans set foot on the moon
  December 1972 – almost 50 years ago!
  Made significant use of modeling and simulation
  Provided a wealth of data about the lunar surface
    https://apolloinrealtime.org
Artemis:
  Return Date: mid-2020s
  Will rely heavily on simulation
  Better data describing lunar surface
  Developing Digital Lunar Exploration Sites (DLES) products
AS17-140-21391.jpg

## Slide 4: The Need For DLES
The Artemis program is currently focusing on exploration sites at the Lunar South Pole (LSP).
  Rugged, mountainous, and cratered terrain.
  Low Sun and Earth angles.
  Lighting conditions will be challenging.
Limited information at the LSP
  No system has soft-landed at the LSP.
  Apollo missions focused on equatorial regions
  We do have significant imagery, terrain elevation, and resource information from remote observations.

## Slide 5: Building DLES
NASA collaboration between planetary science and space systems simulation
  Astromaterials Research and Exploration Sciences (ARES) Team (JSC)
  NASA Exploration Systems Simulations (NExSyS) Team (JSC)
  Engineering Simulation and Graphics Lab (ESGL) (JSC)
  NASA Planetary Geology, Geophysics and Geochemistry Laboratory (GSFC)
Data sources
Data processing
Data generation
Infrastructure

## Slide 6: Building DLES: Data Sources
Lunar Reconnaissance Orbiter (LRO)
  Launch Date: June 18, 2009
  Lunar Orbiter Laser Altimeter (LOLA)
    Able to generate 5 meter per pixel (mpp) Digital Elevation Models (DEM)
  2x LRO Camera Narrow Angle Cameras (NAC)
    Able to generate 1-4mpp surface imagery
      Depends upon altitude
    Stereo images can be processed to generate higher resolution DEM
Filename | Resolution | Description
Site01-Site04_merge-fillseam-crop.tif | 5 mpp | Blended and mosaicked DEM defining an area of roughly 25km x 25km around Connecting Ridge and Shackleton Rim
Site07_final_adj_5mpp_surf-reproj_scaled.tif | 5 mpp | DEM defining an area of 16km x 16km around Site 007. Reprojected pixel units to m from km
Site11_final_adj_5mpp_surf-reproj_scaled.tif | 5 mpp | DEM defining an area of 16km x 16km around Site 011. Reprojected pixel units to m from km
LDEM_875S_5M_geotiff.tif | 5 mpp | Regional LOLA DEM extending from -90° to -87.5° latitude
LRO_LOLA_DEM_SPole75_30m.tif | 30 mpp | Regional LOLA DEM extending for -90° to -75° latitude
NAC DTMs | 2 mpp | DTMs
SFS | 1 mpp | NASA Ames product from Beyer et al.

## Slide 7: Building DLES: Data Processing
Artifacts
  Orbital errors
  Spurious noise points
  DEM data can be processed, reducing artifacts around regions of interest
Gaps
  Occur at seams between or overlapping DEM data
  Must be properly stitched together
Resolution Changes

## Slide 8: Building DLES: Data Generation
Truth data provides good base
Not able to capture smaller surface details
Artificial Features:
  Rocks and Craters are used to enhance surface level detail
  Built on top of 5mpp truth data
  Populations are believed to be statistically representative
  Information is stored in the Persistent Object Database (PODB)

## Slide 9: Building DLES: Infrastructure
Persistent Object Database (PODB)
  Tracks information of persistent objects on the surface of the MOON
    Position, Orientation, and Metadata
  Web interface and API
  Rocks:
    Currently tracks: 1,483,507 rocks
    Data is stored such that retrieval of items in a region is very fast
    This feature is heavily used in simulations when scattering rocks
      Functions like a level of detail (LOD) system
      Only the rocks near the viewpoint are displayed in the rendering engine

## Slide 10: Building DLES: Infrastructure
Persistent Object Database (PODB)
  Craters:
    Currently Tracks: 128,559 craters
    Offline process, unlike rocks
    5mpp DEMs are upscaled to 20cmpp
    Craters are then inserted into the DEM
    Upscaled DEM can then be used like any other DEM
Upscaled 20cmpp DEM Hill-shade Image
300 m

## Slide 11: DLES Products
Truth Data DEMs:
  5mpp - 1mpp
Upscaled DEMs:
  20cm per pixel with craters inserted
FBX models:
  Generated from DEMs of region
Sub-resolution features via PODB:
  Craters
  Rocks
Unity FBX Rendering

## Slide 12: DLES Products: Validation
Validation Efforts:
  LRO imagery is replicated
  Side by side comparisons
Images:
  NAC M1224655261
    Date: 08-01-2016 1:46:34
  NAC M1195011983
    Date: 8-23-2015 23:31:55
EDGE
LROC
Unity
NAC M1224655261
NAC M1195011983

## Slide 13: DLES Products: Validation
EDGE
Apollo Image
Unreal Engine 5
Surface image comparisons
  Apollo 17: AS17-137-20874, Capture Date: Dec. 12th, 1972, 8:31:52 PM

## Slide 14: DLES In Use: Lunar Landing
Realtime Lander Simulations
  NASA Artemis Program:
    Human Landing Systems (HLS)

## Slide 15: DLES In Use: Lunar Surface Exploration
Realtime Rover Simulations
  NASA Artemis Program:
    EVA and Human Surface Mobility (EVAHSM)

## Slide 16: Future Work
Rover tracks
Footprints
Tools
Working with ARES
  1mpp & 2mpp DEMs
PODB Development
  Migrate to PostgreSQL / PostGIS
  Push for public release

## Slide 17: Future Work
Earthshine
  Roughly 50x more powerful than a full Moon on Earth
Sun Illumination
Earth Illumination
Combined-Colored
Combined

## Slide 18: Future Work
DLES Visualization Tool (DVT)
  3D site exploration tool
  Unity3D based tool
  Available on Windows, Mac, and Linux
  Date and planetary data based on JPL Spice package

## Slide 19: Conclusions
DLES provides a functional digital model of the Lunar South Pole region
  Elevation data
  Environmental lighting
Derived from the best available lunar data sources
Supports the ‘addition’ of higher resolution site detail
  Rock distributions
  Smaller craters
Supports the addition and management of ancillary data that needs to persist across simulation runs and analysis (PODB)
  Footprints
  Rover tracks
  Exploration artifacts
Upgradeable as new and improved data sets become available

## Slide 20: Questions?

## Slide 22: Backup

## Slide 23: Backup