## Slide 1: Updates in Upcoming V4.5 Data Releases
Jason Tackett, Brian Getzewich, Mark Vaughan,
Rob Ryan, James Lambeth, Kam-Pui Lee, Anne Garnier, & CALIPSO Data Management Team

## Slide 2: Overview of Updates in V4.5
Level 1
Low energy mitigation for calibration (532 nm day, 1064 nm)
Polarization gain ratio updates
1064 nm baseline shape correction
Level 2
Single-shot cloud clearing correction
Stratospheric aerosol subtyping
Smoke base extension
Optical depth over opaque water clouds added
(Hu et al., 2007 method)

## Slide 3: Overview of Updates in V4.5
Level 1
Low energy mitigation for calibration (532 nm day, 1064 nm)
Polarization gain ratio updates
1064 nm baseline shape correction
Level 2
Single-shot cloud clearing correction
Stratospheric aerosol subtyping
Smoke base extension
Optical depth over opaque water clouds added
(Hu et al., 2007 method)
= what we’ll discuss

## Slide 4
Level 1 Updates

## Slide 5: Level 1: Low Energy Mitigation for Calibration
Oct-Dec 2020
Frequency (%)
Laser shots with E532 < 10 mJ
Low energy shots impact 532 nm day and 1064 nm calibrations at SAA latitudes.
Causes low bias, increased variability, and increased uncertainty to calibration coefficients.
532 nm night calibration is unaffected.
Low bias
South Atlantic Anomaly (SAA)

## Slide 6: Level 1: Low Energy Mitigation for Calibration
New “Low Energy Mitigation” algorithm identifies and excludes profiles affected by low energy from calibration process for 532 nm day and 1064 nm.
Low bias is corrected
Uncertainty reduced

## Slide 7: Level 1: PGR Improvements
Polarization gain ratio – relative gain between || and ⊥ detectors
  Biases corrected in PGR calculation
  PGR now calculated separately for day and night.
day
night

## Slide 8
Level 2 Updates

## Slide 9: Level 2: Single-Shot Cloud-Clearing Correction
Version 4.2 Feature Classification (5-km resolution)
532 nm Attenuated Backscatter
Version 4.2 Aerosol Extinction
Clouds detected at single-shot resolution
Cloud contamination in retrieved aerosol extinction
Cloud deck and overlying dust layer detected as single layer; single-shot clouds not cleared
Saharan dust
Log (km-1)
aerosol
cloud

## Slide 10: Level 2: Single-Shot Cloud-Clearing Correction
Version 4.5 Feature Classification (5-km resolution)
532 nm Attenuated Backscatter
Version 4.5 Aerosol Extinction
Aerosol extinction no longer contains cloud contamination
Cloud deck now separated from overlying dust layer
Correction added in V4.5 to properly cloud-clear these situations
Saharan dust
Preliminary results
Preliminary results
Log (km-1)
aerosol
cloud

## Slide 11: Level 2: Stratospheric Aerosol Subtyping
Changes to stratospheric aerosol subtyping (ash, sulfate, smoke)
  Improved separation between volcanic ash and smoke from pyroCb
  Fewer “unclassified” layers due to weak backscatter
Ash
Dominant events
Smoke
Dominant events
Version 4.5
Version 4.2
Tackett et al., 2022 (in prep)

## Slide 12: Level 2: Smoke Base Extension
apparent gap
Version 4.2 Feature Classification
smoke
stratocumulus
Base altitudes of smoke layers over stratocumulus overestimated by in V4.2 (e.g., Rajapakshe et al., 2017).
532 nm attenuated backscatter
In V4.5, smoke layer bases are extended downward to cloud top (+60 m) if the base is within a certain distance to the cloud top and there is usable signal within the gap.
Benefit: improved smoke optical depths
1064 nm attenuated backscatter
smoke
stratocumulus
Version 4.5 Feature Classification
Smoke bases extended
aerosol
cloud

## Slide 13: Summary
Level 1
Low energy mitigation for calibration (532 nm day, 1064 nm)
Polarization gain ratio updates
1064 nm baseline shape correction
Level 2
Single-shot cloud clearing correction
Stratospheric aerosol subtyping
Smoke base extension
Optical depth over opaque water clouds added
(Hu et al., 2007 method)