## Slide 1: The Imaging X-ray Polarimetry Explorer (IXPE)
Martin C. Weisskopf
NASA Marshall Space Flight Center
Presentation at HEAD Meeting
March, 2022

## Slide 2: IXPE Mission Description
Launch December 9, 2021 on a Falcon 9 from KSC
600-km circular orbit at a nominal 0 inclination
2-year baseline mission, optional extension with GO program
Point and stare (with dither) at pre-selected targets
Malindi ground station - primary (Singapore - secondary)
Mission Operations Center (MOC) at the University of Colorado, Laboratory for Atmospheric and Space Physics (LASP)
Sciences Operations Center (SOC) at MSFC
Data archiving at NASA’s HEASARC
  During the first 3 months of the mission, including one month of orbital checkout, all IXPE data shall be made publicly available at the HEASARC within 30 days of the end of an observation, which is defined as when data for 90% of the scheduled observation time are received by the MOC.
  After the first 3 months of the mission, data shall be made available to the HEASARC within 1 week of the end of an observation, which is defined as when data for 90% of the scheduled observation time are received by the MOC.

## Slide 3: The IXPE Team
SAT currently comprises > 100 scientists from 12 countries

## Slide 4
Launch (December 9, 2021)
Equatorial Orbit
600 km altitude

## Slide 5
Release from the Falcon 9

## Slide 6
IXPE Deployed
5.2 m total length
4.0 m focal length
Forward Star Tracker
DU (1 of 3)
MMA (1 of 3)

## Slide 7: Shield and Collimator Suppress Background
X-ray
Shield
Shield
Detector unit
On-axis Target
Mirror Module Assembly
Off-axis background

## Slide 8: Optics Production Process
(+)
(+)
(-)
8. Separate shell from mandrel in chilled water
4. Polish mandrel to 0.3-0.4 nm RMS
7. Electroform Nickel/Cobalt shell onto mandrel
6. Passivate mandrel surface to reduce shell adhesion
3. Diamond turn mandrel to sub-micron figure accuracy
1. Machine mandrel from aluminum bar
5. Conduct metrology on the mandrel
2. Coat mandrel with electroless nickel (Ni-P)
Ni/Co electroformed IXPE mirror shell
Mirror-shell forming
Mandrel fabrication

## Slide 9: The Optics

## Slide 10: Calibration: MSFC Stray Light Test Facility

## Slide 11: Polarized Sources
3 Polarized Sources
  Crystal Box
    Holds all X-ray sources
    Holds crystals — needed for polarized source
Detector
~ 100 m
10 Pin Electrical Feedthrough CF 2.75
Glass View Port ISO 160K
Source
Turbo Pump CF 4.5
Non-Polarized Source
CF 4 5/8
Gas Gauge CF 2.75
Translation Stage Port ISO 200K
Detector Box/ Stray Light Facility
CF 8
CF 2.75
Translation-Rotation Stage
Crystal Box attached to SLTF Beamline
Interior of Crystal Box, showing stages and crystal being aligned on turret
Energy | X-ray Tube | Crystal | Polarization
2.7 keV | Rh | Ge(111) | > 99%
4.5 keV | Ti | Si(220) | > 99%
6.4 keV | Fe | Si(400) | > 99%

## Slide 12: Angular Resolution
MMA | #1 | #2 | #3
6.4 keV | 18.9″ | 24.8″ | 24.2″
4.5 keV | 18.9″ | 25.0″ | 26.9″
2.3 keV | 18.7″ | 24.5″ | 26.7″
Based upon X-ray calibration, analysis, and on-orbit performance the system-level performance is ≈ 30″ HPD
Values in the table are half-power diameters (HPDs) for the individual MMAs alone. These need to be adjusted for alignment errors, detector resolution, focus etc. to determine the on-orbit system-level resolution.

## Slide 13: Imaging polarimetry
IXPE 30″ half-power diameter on Chandra image

## Slide 14
Property | Value
Number of modules | 3
Mirror shells per module | 24
Inner, outer shell diameter | 162, 272 mm
Total shell length | 600 mm
Inner, outer shell thickness | 180, 250 µm
Shell material | Nickel cobalt alloy
Effective area per module | 163 cm2 (2.3 keV) ~ 192 cm2 (3-6 keV)
Angular resolution | ≤ 27 arcsec HPD
Detector limited FOV | 12.9 arcmin
Focal length | 4 m
Mass (3 assemblies) | 93.12 kg
Mirror Module Assembly Properties

## Slide 15: Polarization Detection Principle
The detection principle is based on the photoelectric effect

## Slide 16
The distribution of the photoelectron initial directions determines the degree of polarization and the position angle
, where
The Polarization-Sensitive Detectors

## Slide 17: The Detectors
The Detector Units (DUs) mounted to the spacecraft top deck at Ball

## Slide 18: Detector Properties
Parameter | Value
Sensitive area | 15 mm × 15 mm (13 x 13 arcmin)
Fill gas and composition | DME @ 0.8 atmosphere
Detector window | 50-µm thick beryllium
Absorption and drift region depth | 10 mm
GEM (gas electron multiplier) | copper-plated 50-µm liquid-crystal polymer
GEM hole pitch | 50 µm triangular lattice
Number ASIC readout pixels | 300 × 352
ASIC pixelated anode | Hexagonal @ 50-µm pitch
Spatial resolution (FWHM) | ≤ 123 µm (6.4 arcsec) @ 2 keV
Energy resolution (FWHM) | 0.57 keV @ 2 keV (∝ √E)
Useful energy range | 2 - 8 keV

## Slide 19
Filter Calibration Wheel Assembly
Filter and Calibration Wheel (FCW), providing open, attenuator, and closed positions, plus four 55Fe-powered calibration sources:
  Cal A – Bragg-reflected polarized 2.98-keV (Ag-L𝛼 fluorescence) and 5.89-keV (Mn-K𝛼) Cal B – unpolarized 5.89-keV spot Cal C – unpolarized 5.89-keV flood Cal D – unpolarized 1.74-keV (Si-K𝛼 fluorescence) flood

## Slide 20: The Minimum Detectable Polarization (MDP)
RS is the observed source counting rate
RB is the observed background counting rate
t is the integration time
M is the modulation factor, i.e. the amplitude of the variation of the ensemble of position angles for a 100% polarized source

## Slide 21
Modulation Function
M

## Slide 22
Response (3 Polarimeters)

## Slide 23: Analysis Based upon Neural Networks
Baseline moments analysis is a simple, effective, long-studied and well-understood method of extracting information from ionization tracks made by a photo-electron in the detector gas
Machine Learning (neural-network) techniques can extract more information from each track
  Improves position-angle (PA) measurements, especially at high energy
  Computes statistical and reconstruction errors for each event
  Mildly improves estimates of the energy and conversion point of each event

## Slide 24: First Year Observations
OBJECTIVE 1: Active Galactic Nuclei (AGN)
  Obtain polarimetry of three (3) AGN to look for a correlation of polarization direction with the orientation of the AGN radio structure. [15]
OBJECTIVE 2: Microquasars (μ-Quasars)
  Obtain spectral polarimetry of two (2) microquasars to constrain the value of the black-hole spin parameter, in combination with information on the radio structure. [2]
OBJECTIVE 3: Radio Pulsars and Pulsar-Wind Nebulae (PWNe)
  Obtain polarimetric imaging of one (1) Pulsar Wind Nebula (PWNe) to constrain the magnetic-field geometry of the nebula and the phase-dependent polarization of the pulsar. [3]
OBJECTIVE 4: Supernova Remnants (SNR)
  Obtain spectral polarimetric imaging of one (1) Supernova Remnant (SNR) to constrain the magnetic-field structure of the X-ray emitting regions. [3]
OBJECTIVE 5: Magnetars
  Obtain phase-dependent polarimetry of one (1) magnetar to constrain the effects of vacuum polarization (birefringence in a strong magnetic field). [2]
OBJECTIVE 6: Accreting X-ray Pulsars
  Obtain phase-dependent polarimetry of three (3) classical accreting X-ray pulsars (high-magnetic-field binaries) to constrain models and geometries for the pulsing emission. Obtain polarimetry of two (2) millisecond X-ray pulsars (low-magnetic-field binaries) to constrain the geometry of the accretion-disk system. [8]
IXPE Year-1 observing plan:
33 planned targets, plus 36 days for
~6 transients or other targets of opportunity

## Slide 25: Microquasars
Microquasars
  Perform X-ray spectral polarimetry on microquasars to use the position angle to help localize the emission site (accretion disk, corona, jet)
  For a micro-quasar in an accretion-dominated state, scattering polarizes the disk emission.
  Polarization rotation versus energy is greatest for emission from inner disk.
    Inner disk is hotter, producing higher energy X-rays.
  Disk orientation from other experiments used to constrain GRX1915+105 model.
    a = 0.50±0.04; 0.900±0.008; 0.99800±0.00003 (200-ks observation)

## Slide 26: Active Galaxies: CEN A
Active galaxies are powered by supermassive BHs with jets
  Radio polarization implies the magnetic field is aligned with jet
  Different electron-acceleration models predict different dependence in X-rays
Region | MDP99
Core | 1.4%
Knots C+F+G | 21%
ULXs | 25% 15%
ULX sources

## Slide 27: Magnetars: A Long-Searched Vacuum-Birefringence QED Effect
Pulsing neutron stars with magnetic fields up to 1015 Gauss
Non-linear QED predicts magnetized-vacuum birefringence
An effect predicted more than 80 years ago but never verified
NO QED
QED
Weisskopf, V.C. (1936) Uber die Elektrodynamik des Vakuums auf Grund der Quanten-theorie des Elektrons. Det Kgl Danske Viden Selskab Mat fys Medd XIV 6:1–36