## Slide 1: Automating Model Selection and Tuning for Multifidelity UQ (MFUQ)
James Warner1, Geoffrey Bomarito1, Gianluca Geraci2, Michael Eldred2, Marten Thompson1,3,
John Jakeman2, Patrick Leser1, Paul Leser1, Alex Gorodetsky4
MS77: Advanced Multilevel and Multifidelity UQ Strategies: Applications,
Generalized Model Hierarchies, and Data-Driven Approaches
SIAM Conference on Uncertainty Quantification
April 13th, 2022
NASA Langley Research Center, Hampton, VA
Sandia National Laboratories, Albuquerque, NM
University of Minnesota Twin Cities, Minneapolis, MN
University of Michigan, Ann Arbor, MI

## Slide 2: Motivation: Trajectory Guidance
Orders of magnitude improvement in landing precision required to enable human Mars missions
  Long-term goal: robust trajectory optimization under uncertainty
Mars landing precision over time

## Slide 3: Motivation: Trajectory Guidance
Heatshield
Payload
Current focus: uncertainty propagation for high-fidelity trajectory simulation
  High dimensional inputs – e.g., atmosphere conditions, vehicle state
  Multiple quantities of interest (QoIs) – e.g., landing location, flight time
  Model: Program to Optimize Simulated Trajectories II (POST2)
Monte Carlo (MC) simulation

## Slide 4: Motivation: Trajectory Guidance
Heatshield
Payload
Current focus: uncertainty propagation for high-fidelity trajectory simulation
  High dimensional inputs – e.g., atmosphere conditions, vehicle state
  Multiple quantities of interest (QoIs) – e.g., landing location, flight time
  Model: Program to Optimize Simulated Trajectories II (POST2)
High-fidelity (hi-fi) model
Low-fidelity (lo-fi) model
Medium-fidelity (med-fi) model
High-fidelity: timestep = 0.001
Low-fidelity: timestep = 0.1
Mid-fidelity: timestep = 0.01
MFUQ

## Slide 5: Motivation: Trajectory Guidance
Lo-Fi 1
Lo-Fi 2
Lo-Fi 3
Lo-Fi Correlation With Respect to Hi-Fi for Each Trajectory QoI
Heatshield
Payload
Current focus: uncertainty propagation for high-fidelity trajectory simulation
  High dimensional inputs – e.g., atmosphere conditions, vehicle state
  Multiple quantities of interest (QoIs) – e.g., landing location, flight time
  Model: Program to Optimize Simulated Trajectories II (POST2)
High-fidelity (hi-fi) model
Low-fidelity (lo-fi) model
Medium-fidelity (med-fi) model
[1] J. E. Warner et al. AIAA SciTech 2021.
Sub-optimal lo-fi models = sub-optimal MFUQ
Variance Reduction for Each Trajectory QoI
High-fidelity: timestep = 0.001
Low-fidelity: timestep = 0.1
Mid-fidelity: timestep = 0.01
AIAA SciTech 2021[1]:
MFUQ

## Slide 6: Outline: Model Tuning for MFUQ
Model tuning is important
How we can do it optimally (In Progress)
Application to trajectory simulation
  Optimal time step selection for lo-fi models
Heatshield
Payload
High-fidelity (hi-fi) model
Low-fidelity (lo-fi) model
Medium-fidelity (med-fi) model

## Slide 7: Approximate Control Variates (ACV)[1]
Multilevel Monte Carlo (MLMC)[2] and Multifidelity Monte Carlo (MFMC)[3] are instances of this estimator
New ACV estimators[1] based on independent sampling (ACV-IS), multifidelity sampling (ACV-MF) and their corresponding generalizations[4] (GIS, GMF)
Estimator is unbiased (wrt )
ACV estimator variance:
[1] Gorodetsky, A A., et al. Journal of Computational Physics (2020) [3] Peherstorfer, B, et al. SIAM Journal on Scientific Computing (2016)
[2] Giles, M B. Operations Research (2008) [4] Bomarito, G. F., et al. Journal of Computational Physics (2022)
: hi-fi model
: lo-fi models
MC estimator
: CV weights

## Slide 8: ACV-MF Estimator Variance
cov of lo-fi models w.r.t. hi-fi
cov of lo-fi models w.r.t. each other
Matrix representing ACV-MF sampling strategy
sampling ratios
argmin s.t.
Variance minimization for sample allocation:
Estimator cost
Computational budget

## Slide 9: ACV-MF Estimator Variance
cov of lofi models w.r.t. hifi
cov of lofi models w.r.t. each other
Introduce model tuning parameters
In general, these are not known a priori and must be estimated
Can reformulate generally in terms of only model correlations
Model costs are also a function of (potentially known)

## Slide 10: Optimization Approach*
Build global surrogate for from pilot samples
  : number of values of tuning parameters to investigate
  : number of pilot samples at each set of tuning parameters
  Local quadratic interpolant
Assume known relationship of model costs
Gradient based-optimization (SLSQP)
*work in progress
  Currently based on single iteration from pilot samples for all ,
argmin s.t.

## Slide 11: Analytical Example[1]
: model cost
: correlation between and
: correlation between and
Hi-fi and lo-fi models
Model costs:
, are constants
[1] Gorodetsky, A A., et al. Journal of Computational Physics (2020)
Goal: study the effect of hyperparameter, , for lo-fi model, , on estimator variance
Notes: W1 varies between cost of lowest fidelity model & high fidelity model
Mimics case where hyperparameter makes Q1 more correlated to HiFi but at price of exponentially increasing cost zzz

## Slide 12: Analytical Example[1]
Model tuning can greatly affect estimator variance
[1] Gorodetsky, A. A., et al. Journal of Computational Physics (2020)
: model cost
: correlation between and
: correlation between and

## Slide 13: Trajectory Simulation Example
Goal: Predict the flight time of an umbrella heatshield reentering the Earth’s atmosphere within computational budget
High-fidelity (: timestep = 0.001
Low-fidelity (): timestep = 0.25
Mid-fidelity (): timestep =
: model cost
: correlation between and
: correlation between and
Heatshield
Payload
Model Cost vs. Time Step
Model Correlation vs. Time Step

## Slide 14: Trajectory Simulation Example
Goal: Predict the flight time of an umbrella heatshield reentering the Earth’s atmosphere within computational budget
argmin s.t.
Determine mid-fidelity time step through joint optimization:
Compare correlation surrogate models with varying amounts of data
  =24,
  =24,
  =6,
  Reference case (Ref Surr) with all data: =24,
: model cost
: correlation between and
: correlation between and
Model Cost vs. Time Step
Model Correlation vs. Time Step

## Slide 15: Results: Most Accurate Surrogate
Optimal model tuning is achievable using surrogates for correlation
Estimator Variance vs. Time Step
Estimated Model Correlation vs. Time Step
  Optimization using , to build correlation surrogate models; 200 random trials

## Slide 16: Results: Sparser Grid
Smoothness is important for gradient-based optimization
Estimator Variance vs. Time Step
Estimated Model Correlation vs. Time Step
  Optimization using , to build correlation surrogate models; 200 random trials
Notes: Overfitting with local surrogate / interpolation

## Slide 17: Results: Fewer Pilot Samples
Statistical variability impacts optimization
: correlation between and
: correlation between and
Estimator Variance vs. Time Step
Estimated Model Correlation vs. Time Step
  Optimization using , to build correlation surrogate models; 200 random trials
Notes: Call out high statistical variability w/ fewer pilot samples; overlap between rho’s

## Slide 18: Results: Two Tunable Lo-Fi Models
Optimal ACV method (model graph) can be function of hyperparameters
High-fidelity (: timestep = 0.001
Low-fidelity (): timestep = 0.001 <=
Mid-fidelity (): timestep =
Optimal Estimator Variance vs. Time Step Sizes
Estimator variance was calculated directly for each ) pair using MFMC and ACV-MF and the optimal (minimum) value was plotted

## Slide 19: Conclusions
Model tuning can greatly affect estimator variance
Optimization requires estimation (or knowledge) of correlations/costs as a function of tuning parameters
Quality of the correlation surrogate is an important factor in tuning parameter optimization
Future Work:
  Automating sample allocation + model tuning optimization – implementation in Dakota
  Global optimization with adaptive surrogate refinement
  All-at-once optimization with model hierarchy

## Slide 20: Questions?
Email: james.e.warner@nasa.gov
Reference:
  G. F. Bomarito, G. Geraci, J. E. Warner, P. E. Leser, W. P. Leser, M. S. Eldred, J. D. Jakeman, A. A. Gorodetsky. Improving Multi-Model Trajectory Simulation Estimators using Model Selection and Tuning. 2022 AIAA Scitech Proceedings. January 2022. https://doi.org/10.2514/6.2022-1099.
Acknowledgement:
  NASA researchers supported by the Entry Systems Modeling (ESM) project