## Slide 1: A High-Performance Computing GNSS-aware Path Planning Algorithm for Safe Urban Flight Operations
Julian Gutierrez, Natasha Neogi, and Evan Dill, NASA Langley Research Center
David Kaeli, Northeastern University
AVIATION - July 2022

## Slide 2: Motivation
New complex operational paradigms: Advanced and Urban Air Mobility (AAM/UAM)
  Present regulatory authorities and the aviation community with several design-and-implementation challenges
We need to develop protocols that can integrate these operations without compromising safety or disrupting traditional airspace operations
  A shift toward a more predictive, autonomous, risk mitigation capability becomes critical to meet this challenge
We propose and evaluate a computationally-efficient path planning approach to perform pre-flight planning and autonomous in-flight re-routing to minimize exposures to GNSS hazards

## Slide 3: Outline
GNSS Prediction Framework
3D Path Planning
Setup
Results
Conclusions

## Slide 4: GNSS Prediction Framework
The quality of a GNSS based position solution is largely correlated to:
  the number of space vehicles (SVs) a receiver has within direct line of sight
  the geometry of the available SVs (dilution of precision (DOP) metric)
In low altitude flight operations, it is common to have objects (e.g., buildings, terrain, foliage) completely or partially obstruct the direct line of site between a receiver and GNSS SVs
Red: Blocked SV
Green: Available SV
Blue: Visible Horizon
Notes: Prior work focused on developing a GPS prediction framework that allow us to simulate the behavior of GPS satellites in the sky and how they project into 3D models of cities

## Slide 5: GNSS Prediction Framework
The quality of a GNSS based position solution is largely correlated to:
  the number of space vehicles (SVs) a receiver has within direct line of sight
  the geometry of the available SVs (dilution of precision (DOP) metric)
In low altitude flight operations, it is common to have objects (e.g., buildings, terrain, foliage) completely or partially obstruct the direct line of site between a receiver and GNSS SVs
Red: Blocked SV
Green: Available SV
Blue: Visible Horizon
We developed a prediction framework to simulate the availability of signals from GNSS satellites to estimate the quality of position calculations in urban areas
Notes: Prior work focused on developing a GPS prediction framework that allow us to simulate the behavior of GPS satellites in the sky and how they project into 3D models of cities

## Slide 6: GNSS Prediction Framework
Positional Error Covariance Matrix
  For any voxel 𝑣[𝑖][𝑗][𝑘] in a volume V:
  cov (D𝜌): diagonal matrix of User Ranging Errors (URE) values corresponding to the SVs in LOS to the given position 𝑣[𝑖] [𝑗] [𝑘] within the volume
  H: matrix which represents the unitary vectors pointing to each SV in LOS from the point 𝑣[𝑖][𝑗][𝑘]
Risk Factor
1.0 = BAD
0.0 = GOOD
Notes: From this framework, we can obtain a positional error covariance matrix:
URE represents the errors associated to signal characteristics, orbit estimation errors and receiver characteristics.
Cov (i, j, k) is a 4 × 4 matrix representing the error distribution along each dimension.
ER:
  ER = 1: voxel inaccessible (building is located in that location).
  ER = 0.99: voxel without sufficient number of satellites in LOS to compute Cov (i, j, k)
  ER = 0: voxel with more than 15 SV in LOS

## Slide 7: GNSS Prediction Framework
Positional Error Covariance Matrix
  For any voxel 𝑣[𝑖][𝑗][𝑘] in a volume V:
  cov (D𝜌): diagonal matrix of User Ranging Errors (URE) values corresponding to the SVs in LOS to the given position 𝑣[𝑖] [𝑗] [𝑘] within the volume
  H: matrix which represents the unitary vectors pointing to each SV in LOS from the point 𝑣[𝑖][𝑗][𝑘]
Risk Factor
1.0 = BAD
0.0 = GOOD
We use this data as the main input to the path planning algorithm to provide safe and reliable operation routes within urban scenarios
Notes: From this framework, we can obtain a positional error covariance matrix:
URE represents the errors associated to signal characteristics, orbit estimation errors and receiver characteristics.
Cov (i, j, k) is a 4 × 4 matrix representing the error distribution along each dimension.
ER:
  ER = 1: voxel inaccessible (building is located in that location).
  ER = 0.99: voxel without sufficient number of satellites in LOS to compute Cov (i, j, k)
  ER = 0: voxel with more than 15 SV in LOS

## Slide 8: 3D Path Planning
Goal: Get from one point to another optimizing for a specific target (distance, fuel, etc.)
When it comes to 3D path planning for safe flights, prior work focused on simple mechanics:
  Vertical take-off
  Horizontal fly
  Vertical landing
These propositions limited the systems capabilities to perform more advanced 3D maneuvers
Additionally, the selected plane for horizontal traversal might not be optimal once time fluctuations to the SV positions are considered, and there might not be an optimal solution that is solely plane based

## Slide 9: 3D Path Planning
Our approach is an adaptation of Bellman Ford
  Use a structured grid instead of a graph
  Target minimum aggregated risk (1) and distance (2)
    0-risk voxels present a problem
    To avoid infinite loops with 0-risk voxels, we consider the distance:
      Take the shortest path amongst the neighbors if the accumulated risk is the same (0-risk voxels)

## Slide 10: 3D Path Planning
Time Incorporation
  Fluctuations in the satellites position in the sky force us to update the input data
  Minimum update interval (MUI)
    minimum amount of time that can pass without updating the risk volume to reflect the new satellite locations as we traverse the path
  Events
    When a satellite crosses the mask angle boundary (in or out of the sky’s line of sight)
Checkpoints

## Slide 11: Setup
We selected GPS as the GNSS of interest
Flying emergency vehicle from Massachusetts General hospital to intersection in the Financial district in Boston, MA
Constant velocity of 5 m/s (keep things simple)
26 movements allowed
Euclidean distance between start and end points: 1248.8 m
Summarized by using independent function that verifies the risk value at each point along the path using a 1 s update interval

## Slide 12: Results
Performance Comparison
Chart: Minimum Update Interval [s]
| 1000 | 100 | 10 | 2 | 1
proposed | 261.083 | 244.853 | 239.329 | 239.326 | 239.325
proposed-fpac | 261.083 | 242.1 | 239.129 | 238.957 | 238.923
bf-phy | 596.677 | 596.677 | 596.677 | 596.677 | 596.677
simple | 278.211 | 278.211 | 278.211 | 278.211 | 278.211
Chart: Minimum Update Interval [s]
| 1000 | 100 | 10 | 2 | 1
proposed | 11.909 | 12.427 | 26.35 | 87.177 | 161.611
proposed-fpac | 11.622 | 18.263 | 110.946 | 607.641 | 1442.898
bf-phy | 23.12 | 23.12 | 23.12 | 23.12 | 23.12
simple | 0.006 | 0.006 | 0.006 | 0.006 | 0.006

## Slide 13: Results
Event-Driven Impact
Chart: Minimum Update Interval [s]
| 1000 | 100 | 10 | 2 | 1
OFF | 261.083 | 244.853 | 239.329 | 239.326 | 239.325
ON | 247.444 | 243.911 | 239.512 | 239.328 | 239.327
Chart: Minimum Update Interval [s]
| 1000 | 100 | 10 | 2 | 1
OFF | 261.083 | 242.1 | 239.129 | 238.957 | 238.923
ON | 249.895 | 243.222 | 239.064 | 238.957 | 238.923
Proposed
Proposed-fpac

## Slide 14: Results
Path Comparison

## Slide 15: Conclusions

## Slide 16: Conclusions
We could attenuate the risk related to the effects of the GPS satellite movements in time
  If we can predict the vehicles movement
Decreasing the MUI results in a lower accumulated risk while still achieving a reasonable execution time (for our proposed algorithm)
The execution time of the proposed-fpac version increases with short MUIs
  At 1-2 s MUIs, the execution time suffers drastically and becomes infeasible to use in-flight
Worse accumulated risk using a slower MUI can be mitigated by incorporating event-driven updates
Due to the HPC improvements, flight path segments can be rerun as needed to evaluate the current circumstances and adjust the path accordingly

## Slide 17: Thanks!
Any questions?

## Slide 18: Backup

## Slide 19: 3D Path Planning
Algorithm inputs
  Start point and end point
  Satellite propagations
    Used to generate the 3D risk volume
      Composed of 1x1x1 m voxels
Intermediate data
  Accumulated risk array
  Accumulated distance array
  Previous neighbor array
Algorithm output
  Final path between start point and end point

## Slide 20: 3D Path Planning
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Risk
∞ | ∞ | 0 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Risk
∞ | ∞ | 0 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Distance

## Slide 21: 3D Path Planning
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Risk
∞ | 0.1 | 0 | ∞ | ∞
∞ | ∞ | 0.6 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Risk
∞ | 1 | 0 | ∞ | ∞
∞ | ∞ | 1 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Distance

## Slide 22: 3D Path Planning
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Risk
0.1 | 0.1 | 0 | ∞ | ∞
∞ | 0.4 | 0.6 | ∞ | ∞
∞ | ∞ | 1.2 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
∞ | 2 | 1 | ∞ | ∞
∞ | ∞ | 2 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Distance

## Slide 23: 3D Path Planning
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.1 | 0.7 | ∞ | ∞
0.1 | 0.1 | 0.7 | ∞ | ∞
0.1 | 0.1 | 0.6 | 1.1 | 1.6
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
3 | 2 | 1 | ∞ | ∞
4 | 5 | 6 | ∞ | ∞
5 | 6 | 7 | ∞ | ∞
6 | 7 | 8 | 9 | 10
Accumulated Distance

## Slide 24: 3D Path Planning: incorporation of time
Update every second
  At a constant speed of 5 m/s, means update every 5 steps
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Risk
∞ | ∞ | 0 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Risk
∞ | ∞ | 0 | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
∞ | ∞ | ∞ | ∞ | ∞
Accumulated Distance

## Slide 25: 3D Path Planning: incorporation of time
Update every second
  At a constant speed of 5 m/s, means update every 5 steps
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.4 | 1.2 | ∞ | ∞
∞ | 0.4 | 1.8 | ∞ | ∞
∞ | ∞ | 2.3 | ∞ | ∞
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
3 | 2 | 1 | ∞ | ∞
4 | 3 | 2 | ∞ | ∞
∞ | 4 | 3 | ∞ | ∞
∞ | ∞ | 4 | ∞ | ∞
Accumulated Distance

## Slide 26: 3D Path Planning: incorporation of time
Update every second
  At a constant speed of 5 m/s, means update every 5 steps
0.1 | 0.2 | S | 1 | 1
0.1 | 0.4 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.2 | 0.1 | 0.6 | 0.6 | 0.6
Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.2 | 1.2 | ∞ | ∞
0.2 | 0.4 | 1.8 | ∞ | ∞
∞ | 0.5 | 2.3 | 2.9 | ∞
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
3 | 2 | 1 | ∞ | ∞
4 | 5 | 2 | ∞ | ∞
5 | 4 | 3 | ∞ | ∞
∞ | 5 | 4 | 5 | ∞
Accumulated Distance

## Slide 27: 3D Path Planning: incorporation of time
Update every second
  At a constant speed of 5 m/s, means update every 5 steps
0.1 | 0.2 | S | 1 | 1
0.1 | 0.4 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.2 | 0.1 | 0.6 | 0.6 | 0.6
Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.2 | 0.9 | ∞ | ∞
0.2 | 0.3 | 1.0 | ∞ | ∞
0.4 | 0.4 | 1.0 | 2.9 | 3.5
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
3 | 2 | 1 | ∞ | ∞
4 | 5 | 6 | ∞ | ∞
5 | 6 | 7 | ∞ | ∞
6 | 7 | 8 | 5 | 6
Accumulated Distance

## Slide 28: 3D Path Planning: incorporation of time
Update every second
  At a constant speed of 5 m/s, means update every 5 steps
0.1 | 0.2 | S | 1 | 1
0.1 | 0.4 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.2 | 0.1 | 0.6 | 0.6 | 0.6
Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.2 | 0.9 | ∞ | ∞
0.2 | 0.3 | 1.0 | ∞ | ∞
0.4 | 0.4 | 1.0 | 1.6 | 3.5
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
3 | 2 | 1 | ∞ | ∞
4 | 5 | 6 | ∞ | ∞
5 | 6 | 7 | ∞ | ∞
6 | 7 | 8 | 9 | 6
Accumulated Distance

## Slide 29: 3D Path Planning: incorporation of time
Update every second
  At a constant speed of 5 m/s, means update every 5 steps
0.2 | 0.3 | S | 1 | 1
0.2 | 0.5 | 0.8 | 1 | 1
0.2 | 0.2 | 0.8 | 1 | 1
0.2 | 0.2 | 0.8 | 1 | 1
0.3 | 0.2 | 0.7 | 0.7 | 0.7
Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.2 | 0.9 | ∞ | ∞
0.2 | 0.3 | 1.0 | ∞ | ∞
0.4 | 0.4 | 1.0 | 1.6 | 2.3
Accumulated Risk
2 | 1 | 0 | ∞ | ∞
3 | 2 | 1 | ∞ | ∞
4 | 5 | 6 | ∞ | ∞
5 | 6 | 7 | ∞ | ∞
6 | 7 | 8 | 9 | 10
Accumulated Distance

## Slide 30: 3D Path Planning
Comparison (time) (no time)
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.1 | 0.7 | ∞ | ∞
0.1 | 0.1 | 0.7 | ∞ | ∞
0.1 | 0.1 | 0.6 | 1.1 | 1.6
Accumulated Risk
0.1 | 0.1 | 0 | ∞ | ∞
0.1 | 0.4 | 0.6 | ∞ | ∞
0.1 | 0.2 | 0.9 | ∞ | ∞
0.2 | 0.3 | 1.0 | ∞ | ∞
0.4 | 0.4 | 1.0 | 1.6 | 2.3
Accumulated Risk
Notes: Without time it seems like our accumulated risk is lower, but there is a catch. This is not representative of the real results once we consider the time fluctuations

## Slide 31: 3D Path Planning
Comparison time (AR = 2.3) no time (AR = 1.6)
 |  | 0 |  | 
Accumulated Risk
 |  | 0 |  | 
Accumulated Risk
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Input Weights (0 s)

## Slide 32: 3D Path Planning
Comparison time (AR = 2.3) no time (AR = 1.6)
0.1 | 0.1 | 0 |  | 
0.1 |  |  |  | 
0.1 |  |  |  | 
Accumulated Risk
0.1 | 0.1 | 0 |  | 
0.1 |  |  |  | 
0.1 |  |  |  | 
Accumulated Risk
0.0 | 0.1 | S | 1 | 1
0.0 | 0.3 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.6 | 1 | 1
0.0 | 0.0 | 0.5 | 0.5 | 0.5
Input Weights (0 s)

## Slide 33: 3D Path Planning
Comparison time (AR = 2.3) no time (AR = 1.6)
0.1 | 0.1 | 0 |  | 
0.1 |  |  |  | 
0.1 |  |  |  | 
0.2 |  |  |  | 
0.4 | 0.5 | 1.1 | 1.7 | 
Accumulated Risk
0.1 | 0.1 | 0 |  | 
0.1 |  |  |  | 
0.1 |  |  |  | 
0.2 | 0.3 |  |  | 
 | 0.4 | 1.0 | 1.6 | 
Accumulated Risk
0.1 | 0.2 | S | 1 | 1
0.1 | 0.4 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.1 | 0.1 | 0.7 | 1 | 1
0.2 | 0.1 | 0.6 | 0.6 | 0.6
Input Weights (1 s)

## Slide 34: 3D Path Planning
Comparison time (AR = 2.3) no time (AR = 1.6)
0.1 | 0.1 | 0 |  | 
0.1 |  |  |  | 
0.1 |  |  |  | 
0.2 |  |  |  | 
0.4 | 0.5 | 1.1 | 1.7 | 2.4
Accumulated Risk
0.1 | 0.1 | 0 |  | 
0.1 |  |  |  | 
0.1 |  |  |  | 
0.2 | 0.3 |  |  | 
 | 0.4 | 1.0 | 1.6 | 2.3
Accumulated Risk
0.2 | 0.3 | S | 1 | 1
0.2 | 0.5 | 0.8 | 1 | 1
0.2 | 0.2 | 0.8 | 1 | 1
0.2 | 0.2 | 0.8 | 1 | 1
0.3 | 0.2 | 0.7 | 0.7 | 0.7
Input Weights (2 s)