## Slide 1: EDLA Considerations for Initial Human Missions to Mars
Douglas Trent, Ph.D.
Entry, Descent, Landing, and Ascent Lead, ESDMD Mars Architecture Team
Humans to Mars Summit, Washington, D.C.
May 19, 2022

## Slide 2
Distance
Time Away from Earth
Entry, Descent, Landing … and Ascent
2022 Humans to Mars Summit
Mars poses many unique problems for Human Spaceflight

## Slide 3
Failure
Success
3
7
Mars EDL, 1960 - 2000
Failure
Success
7
2
Mars EDL, 2000 - Present

## Slide 4
 | Viking 1&2 | Pathfinder | Spirit & Opportunity | Phoenix | Curiosity | InSight | Perseverance | 
Diameter (m) | 3.505 Rigid | 2.65 Rigid | 2.65 Rigid | 2.65 Rigid | 4.5 Rigid | 2.65 Rigid | 4.5 Rigid | 
Entry Mass (kg) | 930 | 585 | 840 | 602 | 3,151 | 606 | 3,369 | 
Landed Mass (kg) | 603 | 360 | 539 | 364 | 899 | 375 | 1,026 | 
Landing Altitude (km) | -3.5 | -1.5 | -1.5 | -3.5 | -4.4 | -2.6 | -2.5 | 
Peak Heat Rates (w/cm2) | 24 | 106 | 45 | 56 | 78 | 51.8 | 68 | 
Landing Ellipse (km) | 280 x 130 | 200 x 70 | 150 x 20 | 130 x 27 | 25 x 20 | 130 x 27 | 7.7 x 6.6 | 
Ballistic Guidance | Unguided | Unguided | Unguided | Unguided | Bank Angle Control | Unguided | Bank Angle Control | 
Technologies | Parachute + Retro-propulsion | Parachute + Airbags | Parachute + Airbags | Parachute + Retro-propulsion | Parachute + SkyCrane | Parachute + Retro-propulsion | Parachute + SkyCrane + TRN | 
2022 Humans to Mars Summit
Steady Progression of “in family” EDL
New Paradigm Needed for Human Class Landers
Mars EDL Progression
 | Human Class Lander (Government Reference)
 | 16-19 Inflatable
 | 47,000-65,000
 | 36,000-40,000
 | +2
 | 120 - 350
 | 0.1 x 0.1
 | Direct Force Control
 | HIAD + Supersonic Retro-propulsion + TRN

## Slide 5
2022 Humans to Mars Summit
Humans have ascended from only two celestial bodies to date
Earth
  Significant in-person ground support
  Generous delay/abort capability
Moon
  Vehicle is delivered with crew prepared for ascent
  Real-time ground support via coms
Mars
  Little to no margin for delays
  Little to no real-time ground support
  Vehicle likely arrives unprepared for launch
6 human launches
100’s human launches
0 human launches

## Slide 6
douglas.trent@nasa.gov
National Aeronautics and Space Administration