## Slide 1: Observations and Analysis from a Scaled, Supersonic Plume-Surface Interaction Experiment
Wesley A. Chambers1, Juan Sebastian Rubio2, Matt Gorman2,
Miguel X. Diaz-Lopez2, Rui Ni2, and Manish Mehta1
1NASA Marshall Space Flight Center
2Johns Hopkins University
NASA Exploration Science Forum
20 July 2022

## Slide 2
STS-134 (NASA/Jim Grossman)
Mars 2020 (NASA/JPL)
Apollo 11 (NASA)
Notes: Shuttle image source: NASA - Launch and Landing
Apollo video source: Apollo 11 45th Anniversary Resource Reel | NASA Image and Video Library (trimmed/compressed by the author)
M2020 landing video: NASA/JPL (trimmed/compressed by the author)

## Slide 3: NASA’s Plume-Surface Interaction Project
Modeling & Simulation
Plume flow in low-pressure environments
Mixed continuum/rarefied flow
Regolith particle phase modeling
Gas-particle interaction modeling
Testing
PSI testing using NASA vacuum facilities
Sub-scale, inert-gas PSI test (2021/2022)
Follow-on, flight-relevant test (Planned)
Instrumentation
mm-wave Doppler radar
Dust concentration monitor
Physics Focused Ground Test 1
Summer 2021
Half-space PSI experiment
Physics Focused Ground Test 2
Summer 2022
Plume impingement experiment

## Slide 4
FLIR Cameras (FC1, FC2, FC3)
VEO
(CC)
V2511
(EC2)
TMX
(EC1)
HS Vision
LED
Crater LEDs
Physics Focused Ground Test 1
MSFC Test Stand 300
Experiment Diagram (Top-Down View)

## Slide 5: PFGT1 Regolith Bin and Nozzle Setup
Side-Facing Diagram
Face-On Diagram with Example High-Speed Camera Fields of View

## Slide 6: PFGT1 High-Speed Cameras
Face-On Diagram with Example High-Speed Camera Fields of View
Crater Camera (CC)
Phantom VEO
5,000 Hz
Ejecta Camera 1 (EC1)
Phantom TMX
775,000 Hz
Ejecta Camera 2 (EC2)
Phantom V2511
25,000 Hz

## Slide 7
Regolith Simulants |  | Description
Mono-disperse silica sand | MDS | 150 micron (mean)
Bi-disperse sand mixture | BDS | 50 micron (mean) + mono-disperse
Tri-disperse sand mixture | TRI | Sieved BP-1 + bi-disperse
BP-1 | BP1 | Full range lunar simulant
Sieved BP-1 | IRR | 300 micron (mean)
Mono-disperse glass spheres | MGB | 150 micron (mean)
Parameter | min | max
Vacuum chamber pressure [Torr] | 0.02 | 4.5
Nozzle height/nozzle diameter [dimensionless] | 3 | 13
Nozzle mass flow rate [g/s] | 0.32 | 8.6
PFGT1 Parameters and Simulants
Run 49
BP-1 Lunar simulant

## Slide 8: Image Analysis Techniques
Run using silica sand; ;
Run using glass beads; ;
Crater Profile Recovery
Ejecta Particle Tracking

## Slide 9: (Preliminary) Crater Analysis Results

## Slide 10: (Preliminary) Crater Analysis Results

## Slide 11: (Preliminary) Crater Analysis Results

## Slide 12
Runs 14 & 17, ,
Run 14,
Run 17, (Mars atmosphere)
Difference in vacuum pressure

## Slide 13: Difference in mass flow rate
Runs 14 & 26, ,
Run 26,
Run 14,

## Slide 14
Runs 9 & 14, ,
Run 14,
Run 9,
Difference in nozzle height

## Slide 15: Summary/Forward Work
We have conducted Physics Focused Ground Test 1, a small-scale, inert gas, supersonic plume-surface interaction experiment
Significant variation in behaviors observed across parameter space
  Changes with vacuum pressure, mass flow rate, nozzle height
  Allows qualitative judgment about mitigation strategies
Analysis ongoing to measure crater profiles, track ejecta particles, and understand behaviors
Analysis products to be used for computational model validation