## Slide 1: Active Flow Control (AFC) on the Simplified High-Lift CRM: Lessons Learned
LaTunia Melton, Judith Hannon, Marlyn Andino, Mehti Koklu, Keith Paschal
Flow Physics and Control Branch (D303)
and
Veer Vatsa
Computational Aerosciences Branch (D302)

## Slide 2: Active Flow Control (AFC) on the Simplified High-Lift CRM: Lessons Learned
LaTunia Melton, Judith Hannon, Marlyn Andino, Mehti Koklu, Keith Paschal
Flow Physics and Control Branch (D303)
and
Veer Vatsa
Computational Aerosciences Branch (D302)
A Tribute to John Lin

## Slide 3: Outline
Motivation & Approach
CFD
Actuator Technology
Actuator Comparison (NPR , , Cp )
Other Data

## Slide 4
Motivation
3.3 count cruise drag reduction and 2.25% fuel savings motivate research
A high-lift wing using AFC to recover lift
AFC
Fairings for flap mechanism increase cruise drag
Conventional High-Lift
AFC-enabled Simplified High-Lift
Hartwich et al. NASA/CR 2016-219170

## Slide 5
Fabricate a relevant high-lift model that can be configured with either a single-element Fowler flap or an AFC-enabled simple-hinged flap.
Integrate efficient AFC actuation systems capable of recovering the lift of the conventional high-lift system.
Perform a wind tunnel test to compare the performance of the high-lift systems.
5
Single-element Fowler flap
AFC-enabled simple-hinged flap
AFC
Approach

## Slide 6: Simplified High-Lift (SHL) System Benefits
2.25% due to 3.3 count reduction of excrescence drag for twin-engine, long-range airplane from Boeing Systems Study (BAART Contract)
Fuel Savings per plane
  790 gallons of fuel per flight
  237,000 gallons of fuel per year
  $23.7 million saving during life cycle
    $5 per gallon
    20-year service life
Reduced emissions
Hartwich et al., NASA/CR-2016-21170

## Slide 7
High-Lift Version of Common Research Model (CRM-HL): Landing Configuration
CRM-HL landing configuration: dslat = 30°, Fowler dflap = 37°
Single-element Fowler Flap
10% scale model
Based on geometry of Lacy and Sclafani
AIAA Paper 2016-0308
Notes: Original nominal landing configuration prior to testing the CRM-HL model in the QinetiQ 5m tunnel. New nominal landing has a slightly different slat gap and overlap setting while maintaining slat deflection of 30 deg.
In the 2016 paper defined a nominal landing configuration that was intended to be reevaluated once wind tunnel data on the configuration had been aquired.
The biggest change is the more aggressive flap deflection. The inboard flap deflection is set at 40 deg and the outboard remains at 37deg. The deflection remain 30 deg but is changed based on how the angles rare defined.
Lacy and Clark June 2020 (https://doi.org/10.2514/6.2020-2771) Definition of Initial Landing and Takeoff Reference Configurations for the High Lift Common Research Model (CRM-HL).
Lacy and Clark call the CRM-HL model the CRM-HL geometry set.
CFD tool improvement and validation
Technology development
Wind tunnel data acquisition methodolgy development
Nacelle/pylon based on the high-speed geometry. Cowl separation numerically separated from wing stall. However, experimentally found to be too close. Should have modified the nacelle cowl because separation occurred at the same time for the nacelle cowl and the wing.

## Slide 8
High-Lift Version of Common Research Model (CRM-HL): Landing Configurations
CRM-HL landing configuration: dslat = 30°, Fowler dflap = 37° & SHL dflap = 50°/55°
AFC-enabled Simple-hinged Flap
10% scale model
Based on geometry of Lacy and Sclafani
AIAA Paper 2016-0308
Simplified high-lift version of the
CRM-HL (CRM-SHL-AFC)
Single-element Fowler Flap

## Slide 9: CRM-HL Lift Performance
Single-element Fowler flap
M∞ = 0.2
a (deg)

## Slide 10: Lift Performance – CRM-HL
Nacelle Chine Lift Effect
Koklu et al., https://doi.org/10.2514/1.J059869
M∞ = 0.2
a (deg)

## Slide 11: Comparison of CRM-HL and CRM-SHL (AFC off)
DCL ≅ 0.5
Simple-hinged flap
M∞ = 0.2
a (deg)
Experimental lift objective DCL ≅ 0.5
Matches CFD derived lift increment
Comparison of CRM-HL with nacelle chine to CRM-SHL provides CL target

## Slide 12: Outline
Motivation & Approach
CFD
Actuator Technology
Actuator Comparison (NPR , , Cp )
Other Data

## Slide 13: Pretest CFD: Background
Vatsa , Koklu, and Wygnanski, “Numerical Simulation of Fluid Actuators for Flow Control Applications”
AIAA Paper 2012-3239
Varied actuator geometry
Blocked feedback tube
Predicted
  Jet Spreading
  Jet Profile
  Jet Frequency
Sweeping Jet (SWJ) Actuator

## Slide 14: Pretest CFD: Background
Vatsa, Casalino, Lin, and Appelbaum
“Numerical Simulation of a High-Lift with Embedded Fluidic Actuators”
AIAA Paper 2014-2142
Vatsa, Duda, Fares, and Lin
“Numerical Simulation of a High-Lift Configuration Embedded with High Momentum Fluidic Actuators”
AIAA Paper 2016-3932
Baseline
Cm = 1.5%

## Slide 15: Pretest CFD: CRM-SHL-AFC
Vatsa, Duda, Lin, Melton, O’ Connell
“Numerical Simulation of a Simplified High-Lift CRM Configuration with Embedded Fluidic Actuators”
AIAA Paper 2018-2142
Pre-Test Lift Increment with SWJ Actuators
(lbm/sec)
M∞ = 0.2

## Slide 16: Outline
Motivation & Approach
CFD
Actuator Technology
Actuator Comparison (NPR , , Cp )
Other Data
“Need more Lift?
‘HELP’ is on
the way! ”
J. C. Lin 2019

## Slide 17
Double Row Sweeping Jet (DRSWJ) Actuator
Cartridge 1
Top view
Cartridge 1
Side view
Row 1, SWJ
Row 2, SWJ
  Modular interchangeable AFC cartridges on the flap shoulder:
  4 inboard & 6 outboard
Candidate actuators
  Double Row Sweeping Jet (DRSWJ)
  Alternating Pulsed Jet (APJ)
  High Efficiency Lower Power (HELP)
Notes: The double row sweeping jet actuator was our initial actuator geometry due to the following reasons:
Risk reduction experiments (low speed tunnels) showed that a single row of actuator could not provide enough control authority at high flap deflection angles (df=60 deg) on a generic wing at NPR values less than or equal to 3 to attach the separated flow field.
Publications showing that multiple rows of excitation were more effective than single row excitation

## Slide 18
Alternating Pulsed Jet (APJ) Actuator
Cartridge 1
Top view
Cartridge 1
Side view
Row 1, PJ
Row 2, PJ
  Modular interchangeable AFC cartridges on the flap shoulder:
  4 inboard & 6 outboard
Candidate actuators
  Double Row Sweeping Jet (DRSWJ)
  Alternating Pulsed Jet (APJ)
  High Efficiency Lower Power (HELP)
Notes: The alternation pulsed jet actuation new approach aimed at generating a generated fluidic fence that has been shown in the literature as an effective way of managing separate flows.

## Slide 19
High Efficiency Low Power (HELP) Actuator
Cartridge 1
Top view
Cartridge 1
Side view
Row 1, SWJ
Row 2, STJ
Steady, discrete jet (STJ) in Row 2
  Modular interchangeable AFC cartridges on the flap shoulder:
  4 inboard & 6 outboard
Candidate actuators
  Double Row Sweeping Jet (DRSWJ)
  Alternating Pulsed Jet (APJ)
  High Efficiency Lower Power (HELP)
Notes: HELP actuator developed as a way to introduce additional momentum into the flow field

## Slide 20: CRM-SHL-AFC Pre-test CFD Lift Predictions
Vasta et al., (https://doi.org/10.2514/1.C036233)
Pre-test simulations HELP actuators meet target, DRSWJ actuators increase lift
M∞ = 0.2, a = 8°
Notes: Prior to the the test CFD simulations were performed to develop a lift objective/target for the CRM high-lift system with a simple-hinged flap configuration. From the figure, we see that there is good agreement between the expt and computational lift objectives.
All candidate actuation approaches had one thing in common. They incorporated a sweeping jet actuator.
The other thing to note from the figure is that one actuator HELP actuator provides the necessary lift recovery with an NPR less than or equal to 3.

## Slide 21
Synergistic Benefit of HELP Dual Row Actuation
M∞ = 0.2
a (deg)
a (deg)
Notes: Prior experience in small scale experiment illustrated that a single row of excitation would not be enough to reattach the flow to the flap surface.

## Slide 22: Outline
Motivation & Approach
CFD
Actuator Technology
Actuator Comparison (NPR , , Cp )
Other Data

## Slide 23: AFC Scaling Parameters (NPR , Cq , Cp )
M∞ = 0.2, a ≅ 8°
/

## Slide 24: Outline
Motivation & Approach
CFD
Actuator Technology
Actuator Comparison (NPR , , Cp )
Other Data

## Slide 25: Flow Visualization: Infrared Images
Health Monitoring
Verify Actuators Working
NPR = 2.4, a = 9°, M∞ = 0.2
Lin, et al. AIAA Paper
2020-0783

## Slide 26
Above: Simulated surface streamline with from Vatsa et al. (AIAA 2019-3724)
Right: Surface oil flow visualization on inboard and outboard flaps of CRM-SHL-AFC
Evidences of 3D Periodic Flow on Flaps from CFD and Oil Flow Visualization
(HELP: C1-C10 & NPR = 2.4; M∞ = 0.2, a = 9 ⏤ equivalent to TWICS applied)
Inboard flap (C1-C4)
Outboard flap (C5-C8)
Outboard flap (C8-C10)
Attached flow
Corner vortex
Attached flow
Flow separation
C1
C5
C4
C3
C2
C5
C6
C7
C8
C8
C9
C10
Focal points
Flow separation
Attached flow
Flow separation
Attached flow
Attached flow

## Slide 27: Flow Visualization: Oil Flow
NPR = 2.4, a = 9°, M∞ = 0.2
M∞ = 0.0
Lin, et al. AIAA Paper
2020-0783

## Slide 28: Flow Visualization: Oil Flow
NPR = 2.4, a = 9°, M∞ = 0.2
Inboard Region of Outboard Flap
Outboard Region of Outboard Flap
Lin, et al. AIAA Paper
2020-0783

## Slide 29: Flow Visualization: Oil Flow
NPR = 2.4, a = 9°, M∞ = 0.2
Inboard Region of Outboard Flap
Outboard Region of Outboard Flap
Lin, et al. AIAA Paper
2020-0783

## Slide 30: Flow Visualization: Fluorescent Mini Tufts
NPR = 2.4, a = 9°, M∞ = 0.2
Inboard Region of Outboard Flap
Outboard Region of Outboard Flap
Lin, et al. AIAA Paper
2020-0783

## Slide 31: Flow Visualization: CFD
Vatsa, et al., AIAA Paper 2019-3724

## Slide 32: CRM-HL Flow Visualization : Fluorescent Minitufts
Koklu, et al., AIAA Journal, Vol. 59, No. 9
M∞ = 0.2, a = 16°
No Chine

## Slide 33: CRM-HL Flow Visualization : Fluorescent Minitufts
Koklu, et al., AIAA Journal, Vol. 59, No. 9
Chine On
M∞ = 0.2, a = 16°

## Slide 34: Photogrammetry Target Identification
#1
#3
#6
#10
#8

## Slide 35: CRM-SHL-AFC - Photogrammetry
#1
#3
#6
#10
#8
Uncorrected a
AFC with Cartridges 1 – 8
M∞ = 0.2

## Slide 36: CRM-SHL-AFC – CL Balance
#1
#3
#6
#10
#8
Uncorrected Data
M∞ = 0.2

## Slide 37: CRM-HL: Photogrammetry
M∞ = 0.2, a ≅ 19°

## Slide 38: CRM-HL: Photogrammetry
M∞ = 0.2
Target 1051

## Slide 39: Lessons Learned
Motivation & Approach
CFD – Use During Planning, Testing, & Analysis
Actuator Technology - Actuation Tailored to Application Required
Actuator Comparison (NPR , , Cp ) - Consider Power Requirements
Other Data – Health Monitoring, Verification, Enhance Understanding

## Slide 40
Questions ?

## Slide 41: Backup Slides

## Slide 42
HELP Actuator Frequency Characteristics
NPR
Row 1 SWJ Actuators
High Efficiency Low Power
(HELP) Actuator
Benchtop measurement with unsteady pressure probe
NPR = Pcav/P∞
Notes: The frequency vs NPR figure on the RHS illustrates the relationship between NPR or mass flow rate and jet oscillation frequency. The data were acquired during post-test benchtop measurement obtained of the outputs for the upstream row of sweeping jet actuators.
The results show that the actuator oscillation frequency varies from roughly 400 Hz to little more than 1.1 kHz.
The results also indicate that this cartridge is producing a fairly uniform output because of the similarity of the curves. Minor changes in frequency between the 8 actuators can be attributed to minor inconsistencies in the geometry.

## Slide 43
Sweeping Jet (SWJ) Actuator Frequency
Paschal et al., (https://doi.org/10.2514/6.2021-1647)
12 unsteady pressure transducers
Unsteady pressure sensors detect SWJ actuator frequency
M∞= 0.2, a = 8°
Notes: During a run with the AFC on, the unsteady pressure sensors in the row closest to the actuator exit sensed the the jet oscillation and the spectra shown on the LHS indicates that the oscillation frequency during wind on operations were similiar to those detected during benchtop testing.