## Slide 1: NASA Spacecraft Conjunction Assessment and Collision Avoidance Best Practices: The History, Evolution and Opportunities.
Dr. Alinda Mashiku
NASA CARA Deputy Manager
July 19th, 2022
COSPAR 2022
44th SCIENTIFIC ASSEMBLY
16-24th July 2022, Athens, Greece

## Slide 2: OUTLINE
Conjunction Assessment process summary
Current and growing Challenges
Opportunity: For a Resilient Space Environment
Conclusion and Summary

## Slide 3: NASA CARA Process
3
  The NASA Conjunction Assessment Risk Analysis (CARA) program has provided CA services to the Agency’s unmanned missions since 2004
    Largest single governmental organization that performs CA risk assessment (~70 S/C)
    Includes CA ops, SME support, and internationally-recognized R&D
    Well-honed relationship with DoD data providers, international partners, and commercial entities
  CARA provides CA support, risk analysis, and mitigation for all NASA non-human spaceflight (HSF) missions NASA requires CA for all operational missions regardless of orbit, maneuver capability, or size
Conjunction Identification
Analysis, Risk Characterization, HIE Identification & Notification
HIE analysis & Maneuver Planning
Maneuver Screening
Maneuver Execution
DECISION POINT:
Begin Maneuver Planning
DECISION POINT:
Maneuver Go / No-Go
High-Interest Event / Non-Routine
Routine
TCA- 7 Days
TCA- 5.5 Days
TCA- 3 Days
TCA- 2 Days
TCA- 1 Days
TCA

## Slide 4: Conjunction Assessment: Basic Definitions and Responsibilities
Conjunction Assessment (CA) is the process of identifying close approaches between two orbiting objects; sometimes called conjunction “screening”.
The 18th Space Control Squadron (18 SPCS) at Vandenberg SFB maintains the high accuracy catalog of space objects. Orbital Safety Analysts (OSAs) at VSFB screen protected assets against the catalog, perform tasking requests, and generate close approach data.
CA Risk Analysis is the process of assessing collision risk and assisting satellites in planning maneuvers to mitigate that risk, if warranted.
The NASA CARA program performs risk assessment for all NASA operational non-HSF satellites, and some partner missions.
Johnson Space Center Flight Operations Directorate performs risk assessment for all NASA HSF program assets and is the Owner/Operator (O/O) for maneuver decisions and execution.
Collision Avoidance is the process of executing mitigative action, typically in the form of an orbital maneuver, to reduce collision risk.
Each satellite O/O – mission management, flight dynamics, and flight operations – is responsible for making maneuver decisions and executing the maneuvers.
4
∆V
Primary S/C
Catalog Object i+2
Catalog Object i+1
Catalog
Object i
Primary S/C
Secondary Object
Secondary Object
Primary S/C
Maneuver
Conjunction Assessment
Risk
Analysis
Risk
Mitigation

## Slide 5: OUTLINE
Conjunction Assessment process summary
Current and growing Challenges
Opportunity: For a Resilient Space Environment
Conclusion and Summary

## Slide 6: Changing Space Environment
Conjunction Events:
Payloads (Non-Debris) > Debris
Number of unique events per month with an RIC
Screening Volume (0.5,5,5) km
Repeating Conjunctions btn a NASA S/C and two S/C

## Slide 7: Evolution and Challenges
CUBESATS
Increasingly varied technical capabilities
Small doesn’t mean safe
  Can create large debris clouds
Small satellites must be tracked in order to prevent collisions
Maneuverable satellites, even if small, must have maneuvers screened
  CA is not effective if screenings cannot be performed against intended trajectories
https://www.nasa.gov/sites/default/files/thumbnails/image/ocsd_02_v02.png
Lechtenberg, T. 2019a. “An Operational Algorithm for evaluating Satellite Collision Consequence.” 2019 AAS Astrodynamics Specialist Conference (Paper #19-669), Portland ME, August 2019.
OCSD NASA mission with water propulsion(1)
Fragmentation algorithms developed by the NASA ODPO to assess the debris production potential of any given conjunction.(2)
In short, small, less expensive satellites require the same CA as large satellites
Notes: Small satellites can destroy large satellites and create large debris clouds as effectively as existing orbital debris
  Small satellites are harder to track, and some have been smaller than US Space Force’s (USSF) regular tracking threshold
  Many small satellite operators do not compute ephemerides and rely on Two-Line Elements (TLEs), making Space Surveillance Network (SSN) tracking essential to their position determination

## Slide 8: Evolution and Challenges
COMMERCIAL and INTERNATIONAL GROWTH
Dramatic increase in owner/operators (O/O), orbital objects, and associated launches
Large constellations using novel techniques
  Autonomous maneuvering
  Multiple Rideshares (up to 60-100) with secondary deploys
More independent operators with varying expertise and capabilities
https://www.swp-berlin.org/publications/assets/Research_Paper/2021RP03/images/2021RP03_InternetFromSpace_003.png
Need a CA process that enables automation without sacrificing maneuver planning coordination that also facilitates rapid cataloging of multiple objects.
Notes: More independent operators with varying expertise and capabilities, some with invalid assumptions (including about Government-provided services)
Large constellations in progress (e.g., OneWeb, Starlink, Kuiper) using novel techniques
  Ex. 1,500 Starlink spacecraft in 540-550 km (circular) orbit
Challenge areas include:
  Launch injections of 60-100 payloads at once, without enough separation to be easily trackable
    Can take 7-14 days to catalogue
  Onboard autonomous maneuvering, including on-board Conjunction Assessment
  Maneuvering without CA screening of maneuver ephemeris, which can prevent other operators from having position knowledge
  No established community best practices

## Slide 9: Evolution and Challenges
The general consensus is that space is not only getting crowded but also operationally complex.
https://i.gifer.com/Gx1H.gif
So, what can we do about it?

## Slide 10: OUTLINE
Conjunction Assessment process summary
Current and growing Challenges
Opportunity: For a Resilient Space Environment
Conclusion and Summary

## Slide 11: Opportunity
Space Situational Awareness can play a role to enable greater international cooperation and collaboration as well as improving established international partnerships.
International regulatory bodies are essential and have their role, but can be complex to enforce
A robust Conjunction Assessment process is necessary for space resilience because:
  Risk is not just to the protected spacecraft but also to the space environment
  Loss of one CubeSat may be tolerable to the owner of a large constellation from a mission performance standpoint, but could put hundreds of pieces of debris in the environment used by another spacecraft
  Even if a small sat is non-maneuverable, the other object may be maneuverable and coordination with the other operator is thus warranted

## Slide 12: Best Practices for Space Operators
Space operators’ goal is mission success.
A compilation of lessons-learned and best practices has been accumulated and is worth considering in the quest for space resilience
Sources of existing best practices:
    Best practices for 18 SPCS support are available on SpaceTrack.org website
    Secure World Foundation published “Handbook for New Actors in Space”
    Best practices for satellite operations at Spacesafety.org
    CONFERS publishes best practices for Proximity ops
    The December 2020 publication of the NASA Spacecraft Conjunction Assessment and Collision Avoidance Best Practices Handbook contains analysis describing the technical/scientific foundations of best practices

## Slide 13: Best Practices: NASA Handbook
The Handbook serves two distinct audiences:
For NASA personnel
  Context and support to internal NASA policies
  and implementation requirements
For other space operators
  Understanding the technical basis used by NASA’s conjunction
  assessment processes
  In effect a primer to establishing a conjunction
  assessment capability
Supports NASA’s strategic goals:
SPD-3: National Space Traffic Management Policy guidance to develop best practices
Improves global awareness of responsible space activity
Mitigates the risk of on-orbit collisions
Maximizes space safety for all space operators

## Slide 14: Best Practices: NASA Handbook
Preface
Acknowledgements
Introduction
Roles and Responsibilities
History
Space Vehicle and Constellation Design
Pre-Launch Preparation and Early Launch Activities
On-Orbit Collision Avoidance
Contact Information
Appendix A: Acronyms
Appendix B: Glossary
Appendix C: Best Practices List
Appendix D: Best Practices for NASA Missions
Appendix E: Use of Analytic Theory Orbital Data in Conjunction Assessment
Appendix F: Expected CA Event Rates
Appendix G: Orbital Debris Density
Appendix H: Satellite Colocation Analysis
Appendix I: Satellite Covariance Realism Assessment Procedures
Appendix J: CARA Risk Assessment Tools Validation
Appendix K: R-15 Message
Appendix L: Commercial Data in NASA Conjunction Assessment
Appendix M: Use of the Probability of Collision (Pc) as the Risk Assessment Metric for Conjunction Assessment
Appendix N: Pc Calculation Approaches
Appendix O: Collision Consequence
Appendix P: Event Actionability
Appendix Q: List of Works Cited
Content developed from a US-based inter-agency working group
AVAILABLE HERE: https://www.nasa.gov/press-release/nasa-releases-best-practices-handbook-to-help-improve-space-safety

## Slide 15: Best Practices: NASA Handbook Overview
The Best Practices NASA Handbook recommendations, can be grouped into 3 major categories:
Suresh B.N., Sivan K. (2015) Mission Design. In: Integrated Design for Space Transportation System. Springer, New Delhi. https://doi.org/10.1007/978-81-322-2532-4_7
Parker Solar Probe Launch Preparations is a photograph by Nasa/kim Shiflett/science Photo Library which was uploaded on September 25th, 2019.
Rendition of SDC 2.0 system. Photo: SDA
Space Vehicle and Constellation Design
Pre-Launch Preparation and Early Launch Activities
On-orbit Collision Avoidance

## Slide 16: Best Practices: NASA Handbook Overview
The Best Practices NASA Handbook recommendations, can be grouped into 3 major categories:
Suresh B.N., Sivan K. (2015) Mission Design. In: Integrated Design for Space Transportation System. Springer, New Delhi. https://doi.org/10.1007/978-81-322-2532-4_7
Parker Solar Probe Launch Preparations is a photograph by Nasa/kim Shiflett/science Photo Library which was uploaded on September 25th, 2019.
Rendition of SDC 2.0 system. Photo: SDA
Space Vehicle and Constellation Design
Pre-Launch Preparation and Early Launch Activities
On-orbit Collision Avoidance

## Slide 17: Space Vehicle and Constellation Design: General Orbit Selection
Launch COLA Analysis
Ascent to/ Disposal from Operational Orbit
Spacecraft Colocation
700-900 km shell still dominated by debris
400-600 km shell has noticeable spike due to Starlink
Orbit Selection can reduce the number of conjunctions and preserve the space environment

## Slide 18
Technology advances make possible spacecraft that are too small to be tracked by the SSN
Un-trackable objects on orbit pose threat to flight safety
Basic actions to advance safety of flight:
  Ensure objects are large enough to be tracked passively on-orbit
  At injection, allow adequate separation from other deployed satellites and on-orbit objects to allow unique, unambiguous tracking
Potential workarounds include:
  Active tracking (e.g. beacon), though may not be sufficient after mission end (e.g., beacon becomes inactive)
  Laser reflectors, so long as tracking service operative and funded
  Providing O/O ephemerides of sufficient accuracy and realism to 18 SPCS
)
Space Vehicle and Constellation Design: Trackability
Notes:   SSN is the DOD USSF resource assigned to track all on-orbit objects
  Objects must be ~10 cm to be tracked reliably by more than one sensor
  CA can be performed only against objects in the catalog
https://www.space.com/satellite-megaconstellation-impact-astronomy-report.html (light pollution

## Slide 19: Space Vehicle and Constellation Design: Ephemeris generation and TLEs
Three main operational capabilities should be developed wrt CA:
  Predicted ephemeris capability
  Risk assessment capability
  Mitigation capability
An accurate predicted spacecraft ephemeris including any planned maneuvers is necessary for screening, risk assessment and mitigation.
TLEs (Two Line Elements) not intended for CA:
  Intended uses:
    Can provide position and velocity predictions
    with enough accuracy to allow reaquisition
    Can be mined for maneuver information about other objects
  Problems with use for CA:
    Available only for objects in public catalog, so screening against TLEs misses a large portion of the full catalogue
    No covariance information (crucial for Probability of Collision calculation)
    Accuracy is only on the order of 1-2km within a few days of the epoch of the element set – not sufficient for CA per 18 SPCS
https://www.satsig.net/satellite/tle-archive/tle-archive.htm
https://www.space-track.org/documentation#/user_agree

## Slide 20: Best Practices: NASA Handbook Overview
The Best Practices NASA Handbook recommendations, can be grouped into 3 major categories:
Suresh B.N., Sivan K. (2015) Mission Design. In: Integrated Design for Space Transportation System. Springer, New Delhi. https://doi.org/10.1007/978-81-322-2532-4_7
Parker Solar Probe Launch Preparations is a photograph by Nasa/kim Shiflett/science Photo Library which was uploaded on September 25th, 2019.
Rendition of SDC 2.0 system. Photo: SDA
Space Vehicle and Constellation Design
Pre-Launch Preparation and Early Launch Activities
On-orbit Collision Avoidance

## Slide 21: Pre-Launch Preparation and Early Launch Activities: CONOPS Discussions with 18th SPCS (Space Control Squadron)
Launch
  Delivery and deployment methodologies
  R-15 form (Ready minus 15 days Vehicle Information Message by Launch Vehicle Ops.)
  Launch provider relevant information and data (injection states, initial ephemeris)
On-Orbit Mission Phase (register S/C on Space-Track.org)
  Operational contact information
  Satellite construction and operation information
  Satellite orbit maintenance strategy
  Satellite flight control and navigation paradigm
Conjunction Assessment
  Free service from 18th SPCS; provides CDMs for conjunction assessment
  O/O needs a risk analysis and mitigation service
  Implement an SSA sharing agreement to receive advanced data support and services
Notes: Establish contact with USSPACECOM to describe and discuss all aspects of the launch including delivery and deployment methodologies.
Space the deployment of multiple spacecraft in a way that enhances the ability of USSPACECOM to quickly identify and differentiate the spacecraft using the SSN.

## Slide 22: Best Practices: NASA Handbook Overview
The Best Practices NASA Handbook recommendations, can be grouped into 3 major categories:
Suresh B.N., Sivan K. (2015) Mission Design. In: Integrated Design for Space Transportation System. Springer, New Delhi. https://doi.org/10.1007/978-81-322-2532-4_7
Parker Solar Probe Launch Preparations is a photograph by Nasa/kim Shiflett/science Photo Library which was uploaded on September 25th, 2019.
Rendition of SDC 2.0 system. Photo: SDA
Space Vehicle and Constellation Design
Pre-Launch Preparation and Early Launch Activities
On-orbit Collision Avoidance

## Slide 23: On-Orbit Collision Avoidance: Robust Risk Assessment and Mitigation
Risk assessment is the practice of determining which close approaches present a serious collision risk
  Precision state and covariance data are required
  Advanced probabilistic calculations and data analysis are performed
  Enables mitigation action decision
Ephemerides should be sent to 18 SPCS for screening
  Maneuverable payloads need to provide statement of predicted position that includes planned maneuvers—only way to perform useful CA screenings
  Providing of ephemerides is the only reliable way
  to communicate future positions to users of autonomous
  flight control and navigation
Risk Mitigation maneuvers always require screenings to avoid an inadvertent collision with other objects in the immediate future.
∆V
Secondary Object
Primary S/C
Maneuver

## Slide 24: On-Orbit Collision Avoidance: Safe Autonomous Maneuvering
Large constellations are achieving economy of scale through increased automation and autonomy of flight dynamics
Automated on-board maneuvering and CA practices may prevent CA screening of maneuvers and hence add flight safety risk – without coordination, there is no way to ensure safety
NASA missions employing autonomy required to ensure flight safety
  Ability to notify ground controllers of any autonomous maneuvers planned or taken, including characteristics of the maneuver.
  Ability for the ground controllers to pause or abort planned autonomous maneuvers.
  Accurate on-ground emulation capability that can reasonably predict the autonomous behavior and give advance notice of maneuver plans
Large constellations depend on automation to manage large scale
Credit: Next Big Future, Dec. 13,2018
Notes:   Maneuvers planned/executed only a few hours in advance—no time or mechanism for CA screenings
  Satellites cannot know maneuver intentions of non-constellation spacecraft
  Without coordination, there is no way to ensure safety
    Ex. If two satellites autonomously plan mitigations to avoid collisions with each other, result might be for both satellites to maneuver into each other

## Slide 25: OUTLINE
Conjunction Assessment process summary
Current and growing Challenges
Opportunity: For a Resilient Space Environment
Conclusion and Summary

## Slide 26: SUMMARY
NASA has been performing CA for the past 30 years, including HSF CA.
NASA plans to continue to evolve our CA process: improving operations, streamlining approaches, and collaborating with other operators to make the most of limited resources.
NASA continuing to update and refine Agency CA requirements
  Defines baseline CA requirements (e.g. compliance methods, thresholds, reporting)
  Defines acceptable minimum risk levels
  NID (NASA Interim Directive) 7120.132: Collision Avoidance for Space Environment Protection available at: https://nodis3.gsfc.nasa.gov/OPD_docs/NID_7120_132_.pdf
There are a lot of lessons learned to be shared and we welcome your feedback on general technical and handbook topics:
ca-handbook-feedback@nasa.onmicrosoft.com

## Slide 28: NASA Points of Contact
Feedback on general technical and handbook topics:
ca-handbook-feedback@nasa.onmicrosoft.com
Support to specific space flight missions:
  Human spaceflight (HSF) missions: JSC Flight Operations Directorate (FOD) jsc-dl-topo-iwg@mail.nasa.gov
  Non-HSF missions: Conjunction Assessment Risk Analysis (CARA) program cara-management@lists.nasa.gov
NID 7120.132: Collision Avoidance for Space Environment Protection https://nodis3.gsfc.nasa.gov/OPD_docs/NID_7120_132_.pdf
NASA Spacecraft Conjunction Assessment and Collision Avoidance Best Practices Handbook https://nodis3.gsfc.nasa.gov/OCE_docs/OCE_50.pdf
NASA OCE web site with FAQs and future content: https://www.nasa.gov/oce

## Slide 29: On-Orbit Collision Avoidance: Orbital Data for CA Screenings
CA screenings determine which space objects will have close approaches with a protected asset, several days in advance
  Often many close approaches, few result in safety of flight concerns
Risk assessment is not performed by US Space Force (USSF) 18th Space Control Squadron — they provide screenings only
Conjunction Data Messages (CDMs) are screening data to be analyzed for risk – they are not warnings that indicate an action is necessary
Meaningful risk assessment is not possible with TLEs, as there is no associated covariance