## Slide 1: Venus Science Enabled by Human Proximity Workshop Keck Institute for Space Studies Interplanetary Trajectories Perspective
Patrick R. Chai
Exploration System Development Mission Directorate
Mars Architecture Team

## Slide 2: Background
Mars “Opposition Class” missions have been of interest recently to enable shorter roundtrip missions to Mars; these mission can utilize Venus flybys to help reduce the total energy required
Compared to longer minimum energy “Conjunction Class” missions which utilize the planet’s natural motion around the Sun to minimize the roundtrip energy
ESDMD Mars Architecture Team (MAT) has been performing analysis to define the trade space and integrate with internal and external stakeholders to help identify potential options

## Slide 3: Deep Space Mission “Change of Reference”
Earth
Moon
Avg. Distance 384,000km
ISS: 420km
Earth is no longer the center of the reference frame
All scales and reference of existing human spaceflight are no longer representative
Apollo 13 Altitude Record: 400,000km
Earth
Mars
Average Distance 225,000,000km
Earth
Mars
Maximum Distance 400,000,000km
Venus
Average Distance 40,000,000km
Venus
Maximum Distance 260,000,000km
Roundtrip Distance Traveled will be Significantly More!

## Slide 4: Getting to Mars or Venus
Venus
Earth
Mars
Mercury
Sun
Interplanetary Transits are governed by heliocentric orbital dynamics
Relative Velocity between Planets & Spacecraft will dictate the energy required
Phasing is most important, must depart and arrive at the right time to minimize energy

## Slide 5: Example Mars + Venus Flyby Mission
2039 High Energy Roundtrip Mission to Mars with a Venus Flyby |  | 
From 400x400,000 km High Earth Orbit To: 1-Day Period Elliptical Mars Orbit |  | 
Earth Departure | 03/11/2039 | 
Mars Arrival | 01/29/2040 | 
Mars Departure | 03/20/2040 | 
Venus Flyby | 10/05/2040 | 
Earth Arrival | 03/18/2041 | 
Outbound | 324 | Days
Stay | 51 | 
Inbound | 363 | 
Total | 738 | 
Total ΔV | 8,867 | m/s
Outbound
Inbound
Stay

## Slide 6: Visualization of Mars with Venus Flyby

## Slide 7: Example Venus Flyby

## Slide 8: Example Direct Roundtrip Mission Comparisons
2039 Minmum Energy Roundtrip Mission to Mars |  | 
From 400x400,000 km High Earth Orbit To: 1-Day Period Elliptical Mars Orbit |  | 
Earth Departure | 09/20/2039 | 
Mars Arrival | 08/25/2040 | 
Mars Departure | 08/07/2041 | 
Earth Arrival | 05/29/2042 | 
Outbound | 340 | Days
Stay | 347 | 
Inbound | 296 | 
Total | 982 | 
Total ΔV | 2,952 | m/s
2039 Minimum Energy Roundtrip Mission to Venus |  | 
From 400x400,000 km High Earth Orbit To: 1-Day Period Elliptical Venus Orbit |  | 
Earth Departure | 07/20/2039 | 
Venus Arrival | 12/22/2039 | 
Venus Departure | 03/17/2041 | 
Earth Arrival | 08/04/2041 | 
Outbound | 155 | Days
Stay | 450 | 
Inbound | 140 | 
Total | 745 | 
Total ΔV | 2,218 | m/s

## Slide 9: Example Roundtrip Mission Comparisons
Outbound
Inbound
Stay
Outbound
Inbound
Stay
2039 Minimum Energy Roundtrip to Mars – 982 Day Roundtrip
2039 Minimum Energy Roundtrip to Venus – 745 Days Roundtrip

## Slide 10: The Energy cost
ΔV requirement translates to an exponential growth in mass
Figure shows the propellant mass required for a 100t and 200t spacecraft (including habitation) with chemical propulsion system
Minimum Energy Roundtrip mission ΔVs are in the 2-4 km/s range
Mars + Venus Flyby missions ΔVs are in the 7-10 km/s range
Chart: Propellant Mass vs Total ΔV
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
100t | 25.4333 | 57.335 | 97.3504 | 147.5431 | 210.5013 | 289.4719 | 388.5273 | 512.7757 | 668.6245 | 864.1108 | 1109.3156 | 1416.8839 | 1802.6768 | 2286.5895 | 2893.5769 | 3654.9409
200t | 50.8665 | 114.67 | 194.7009 | 295.0861 | 421.0027 | 578.9439 | 777.0546 | 1025.5515 | 1337.2491 | 1728.2216 | 2218.6311 | 2833.7677 | 3605.3536 | 4573.1789 | 5787.1537 | 7309.8819

## Slide 11: When does it make sense?
Venus flyby in the context of a Mars mission would help reduce the energy required for very short missions to Mars
But these missions are very high energy and require significant amount of mass to be launched and assembled in orbit
Chart: 2039 Roundtrip Missions to Mars
| 480.00000000109867 | 520.00000000074942 | 559.99999999974534 | 600.00000000005093 | 640.0000000003929 | 650.42805973444047 | 719.89401412014558 | 740
With Venus Flyby | 12.0695 | 10.5876 | 9.9741 | 9.6 | 9.0601 | 9.0085 | 8.9548 | 8.867
Without Venus Flyby | 11.9185 | 9.9 | 8.6597 | 7.0546 | 6.2 | 5.4 | 3.9424 | 3.0977 | 2.9539
Duration where Flybys Provide Energy Saving
Current ESDMD Mars Study Reference
Forcing Flybys for longer missions will be costly

## Slide 12: Summary
Conjunction (minimum energy) vs Opposition (high energy) has been a big part of the talking point, with opposition enabled by Venus flybys
Mars and Venus missions trade space is not bimodal, but rather a continuous space with regards to mission duration
Direct missions to Venus are somewhat comparable to Mars, but more analysis will be needed to understand the trade space
Venus flybys as part of a Mars mission are only worthwhile if total mission duration is suppressed, and will require significant technology investment and/or large number of launches to assemble the spacecraft