## Slide 1
LEIA: Lunar Explorer Instrument for space biology Applications
A. Mark Settles
Bioengineering Branch
NASA Ames Research Center
andrew.m.settles@nasa.gov
Sergio R. Santa Maria
KBR/FILMSS
NASA Ames Research Center
sergio.santamaria@nasa.gov
Image credit: NASA

## Slide 2
Image credit: NASA

## Slide 3
Radiation is a significant risk for organisms traveling in deep space
SPEs: sporadic, transient (mins to days); high proton flux (low-medium energy)
GCRs: high-energy protons and highly charged, energetic heavy particles
GCRs are not easy to shield
Deep space radiation levels are modulated by the 11-year solar cycle
Trapped particles
Galactic Cosmic Rays (GCRs)
Solar Particle
Events (SPEs)
Image credit: NASA

## Slide 4
Lunar surface radiation is a distinct environment from deep space
GCR
γ
Image credits: NASA
Hayn Crater
Lunar regolith absorbs galactic cosmic radiation (GCR) to produce secondary albedo neutrons
    High-energy, fast neutrons cause direct cellular damage
    Fast neutrons also produce ionizing radiation
    Estimates of surface neutron doses vary widely
    Effects of lunar surface radiation on bioprocessing are unknown

## Slide 5
Lunar Explorer Instrument for space biology Applications:
a South Pole Lunar surface investigation
Team: Dr. A. Mark Settles (PI), Dr. Sergio Santa Maria (Deputy PI), Dr. Donald M. Hassler (Co-I, SwRI), Brandon Maryatt (PM), Leandro James (SE)
Motivation.
What are the radiation health risks for crewed exploration of the lunar surface?
Will proposed mitigations for crew health using in-space biomanufacturing be effective beyond low Earth orbit?
Approach.
Engineer yeast strains to test growth and metabolism for sensitivity to radiation.
Measure biologically relevant radiation in transit and on the lunar surface.
Expected Outcomes and Impact.
Determine cellular sensitivity to the lunar environment.
Evaluate feasibility of bioproduction on the Moon.
Test genetic strategies to enhance cellular tolerance to the lunar environment.
Determine ground truth radiation risks for crew.
LEIA Instruments
For more information: https://www.nasa.gov/press-release/nasa-selects-new-instruments-for-priority-artemis-science-on-moon
Image credits: NASA

## Slide 6
Radiation causes cellular stress through DNA damage and Reactive Oxygen Species (ROS)
Consequences for biology:
DNA damage leads to mutations.
ROS damages all parts of the cell.
Cells shift energy from growth to repairing damage.
X-ray
Heavy ion
Protein & Ion Leaks
DNA Damage
Peroxidation of lipids
Repressed translation
Low ATP
Cell cycle arrest
Cellular Effects of ROS Damage

## Slide 7
C. richardii SporeSat-1 (2014 / 3U): ion channel sensors, µ-centrifuges
E. coli GeneSat-1 (2006 / 3U): gene expression
EcAMSat (2017 / 6U): antibiotic resistance
B. subtilis O/OREOS* (2010 / 3U): survival, metabolism
S. cerevisiae PharmaSat (2009 / 3U): drug dose response
BioSentinel (2022 / 6U): cell damage repair
*Organism/Organic Response to Orbital Stress
Biological space missions using CubeSats
Image credits: NASA

## Slide 8
BioSentinel: a CubeSat for deep space biological investigation
Propulsion system
Batteries
Attitude control subsystem
Star tracker cutout
Solar arrays
Solar array
gimbal
BioSensor payload
(~4U, 4.5 kg)
Low-gain antennas
Command & data handling EPS
Medium-gain antenna
LET radiation sensor
Iris
transponder

## Slide 9
BioSentinel biological payload is housed in the BioSensor
4U BioSensor
Microfluidic Card
Individual Cell Culture Well
For LEIA:
BioSensor will contain 16 microfluidic cards
Each card has 16 culture wells (256 wells total)
Pumps and valves control medium addition through 2 separate manifolds
Each well can record light absorbance data at 3 LED wavelengths
~5 cm
4 cm

## Slide 10
BioSensor optical detection system
Yeast growth with flight-like optical unit
3-color optical system at each well tracks
cell growth via infrared optical density
cell metabolic activity via alamarBlue dye color changes
LEDs:
570 nm - green, measures pink alamarBlue
630 nm - red, measures blue alamarBlue
850 nm - infrared, measures cell growth

## Slide 11
Specific Aims:
Aim 1. Determine cellular sensitivity to the lunar environment.
Direct comparison to BioSentinel mission
Aim 2. Test production of antioxidant carotenoids for use in crew dietary supplementation.
Comparison to BioNutrients mission
Aim 3. Engineer genes from tardigrades and yeast to test for enhanced tolerance to the lunar surface.
Aim 4. Measure biologically relevant radiation at the south pole landing site.
Central goal: Identify genetic factors impacting cellular response to lunar surface radiation and gravity.
Image credits: NASA

## Slide 12
Yeast will be engineered to be more sensitive to the mission environment
Chart: γ irradiated WT & DNA repair mutants
Strains developed for the BioSentinel mission have single and multiple DNA repair mutants.
These mutants show slower metabolic activation and higher sensitivity to exposure to gamma radiation.
Additional mutants will be generated to test multiple genes involved in ROS and DNA damage.

## Slide 13
Synthetic biology products are an engineered read-out of cellular metabolism.
Metabolic stress during the mission may be revealed in reduced production.
Swap out one of the BioSensor LEDs and replace with a 465 nm emission light.
Carotenoids absorb at this wavelength.
Mixed carotenoid and wild-type cells emulate reduced production with a linear relationship.
This spectroscopy approach allows a direct read-out of nutrient or protein production levels.
350
400
450
500
550
600
650
700
Relative Absorbance/Emission
Wavelength (nm)
Y55
Extract
465 nm
aB
570
630
Chart: Fraction Y55 Carotenoid:WT
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
465 nm | 1.2045 | 1.2358 | 1.2246 | 1.2959 | 1.283 | 1.316 | 1.3436 | 1.3759 | 1.3782 | 1.4657 | 1.4946
570 nm | 1.1248 | 1.1287 | 1.096 | 1.1357 | 1.095 | 1.0945 | 1.0898 | 1.108 | 1.1051 | 1.1532 | 1.1112

## Slide 14
Linear Energy Transfer (LET) spectrometer
Mini-Fast Neutron Detector (FND)
Mission | Project | Dose Type | % Fast Neutron
Chandrayaan-1 | RADOM | Effective | 2-20%
Lunar Prospector | LP | Effective | 16-18%
LRO | CRaTER | Absorbed | 0.7%
Chang’E 4 | LND | Absorbed | 23%
Lunar surface radiation is primarily extrapolated from lunar orbiter data.
There is not yet a consensus for the percentage of fast neutrons in total dose.
Direct measurement of charged particles and fast neutrons will provide ground truth data at a south polar landing site.

## Slide 15
LEIA expected outcomes
Determine cellular sensitivity to the lunar environment.
Evaluate feasibility of bioproduction on the Moon.
Test genetic strategies to enhance cellular tolerance to the lunar environment.
Determine ground truth radiation risks for crew.
Image credits: NASA

## Slide 16
Project team
A. Mark Settles (Principal Investigator)
Sergio Santa Maria (Deputy PI)
Donald M. Hassler (Co-I, SwRI)
Brandon Maryatt (PM)
Dave Pletcher (PM)
Science Team
Natalie Ball
Jared Broddrick
Jessica Chau
Natalya Dvorochkin
Jennifer Gil Acevedo
Diana Gentry
Aditya Hindupur
Jessica Lee
Lauren Liddell
Jack Miller
Cary Zeitlin
BioSensor Engineering Leads
Leandro James (Systems Engineering)
Earl Daley (Mechanical)
Shang Wu (Electrical)
Brandon Schmitt (Software)
Alex Szerszen (Thermal)
Mike Padgen (Fluidics)
Mini-FND Engineering (SwRI)
Traci Case (PM)
Bent Ehresmann
Kerry Neal
Brian Pyke
Michael Shoffner
Funding
NASA PRISM-2
NASA Space Biology

## Slide 17
References/Background
Ball N., Kagawa H., Hindupur A., Sims K., Hogan J., Levri J. (2020) BioNutrients-1: Development of an On-Demand Nutrient Production System for Long-Duration Missions. ICES-2020-119. https://ttu-ir.tdl.org/handle/2346/86343.
Ball N., Hindupur A., Kagawa H., Kostakis A., Gresser A.L., Levri J.A., Sims K., Sharif S., Villanueva A.G., Donovan F., Settles A.M., Hogan J. (2021) BioNutrients-2: Improvements to the BioNutrients-1 Nutrient Production System. ICES-2021-331. https://ttu-ir.tdl.org/handle/2346/87260.
Ricco, Antonio & Santa Maria, Sergio & Hanel, Robert & Bhattacharya, Sharmila. (2020). BioSentinel: A 6U Nanosatellite for Deep-Space Biological Science. IEEE Aerospace and Electronic Systems Magazine. 35. 6-18. doi:10.1109/MAES.2019.2953760.
Santa Maria, S.R., Marina, D.B., Massaro Tieze, S., Liddell, L. C., Bhattacharya, S. (2020) BioSentinel: Long-Term Saccharomyces cerevisiae Preservation for a Deep Space Biosensor Mission. Astrobiology doi:10.1089/ast.2019.2073.