## Slide 1: Return to the Moon with Artemis: Overview, Challenges, and the Future
Alicia Dwyer Cianciolo NASA Langley Research Center
Bryan Welch NASA Glenn Research Center
International Planetary Probe Workshop | Santa Clara, CA | September 2, 2022

## Slide 2
“Remain a global leader in science and engineering by pioneering space research and technology that propels exploration of the Moon, Mars, and beyond.”
“U.S. human and robotic space exploration missions will land the first woman and person of color on the Moon, advance a robust cislunar ecosystem, continue to leverage human presence in low-Earth orbit to enable people to live and work safely in space, and prepare for future missions to Mars and beyond.”
“The United States will Maintain its Leadership in Space Exploration and Space Science”
— The White House U.S Space Priorities Framework, Dec 2021
United States Space Priorities Framework
NASA 2022 Strategic Plan
2023 NASA Budget Request

## Slide 3: What is Artemis?
=
+
+
+
Extravehicular Activity and Human Surface Mobility Program (EHP)
+
Combines programs into missions

## Slide 4
+
https://appel.nasa.gov/2021/11/15/artemis-i-undergoing-final-rounds-of-testing/
1
2
3
4
5
6
7
Launch
Jettison Rocket Boosters
Main Engine Cut Off
Perigee Raise Maneuver
Earth Orbit
Trans Lunar Injection Burn
Interim Cryogenic Prop Stage Separation
Outbound Trajectory Correction Burn
Distant Retrograde Orbit (DRO)
Outbound Powered Flyby
Lunar Orbit Insertion
DRO Departure
Return Powered Flyby
Crew Module Separation
Entry Interface
Splashdown
8
11
10
15
16
12
13
17
9
Return Transit
14
https://appel.nasa.gov/wp-content/uploads/2021/11/artemis_1_map_october_2021.jpg

## Slide 5: Stargate access
+
+
Crew
1
2
3
4
5
6
7
Launch
Jettison Rocket Boosters
Main Engine Cut Off
Perigee Raise Maneuver
Apogee Raise burn to High Earth Orbit
Prox Ops Demonstration
Interim Cryogenic Prop Stage Separation
High Earth Orbit Checkout
Trans-Lunar Injection
Outbound Transit to the Moon
Lunar Flyby
Crew Module Separation
Entry Interface
Splashdown
8
10
13
14
11
15
9
Trans-Earth Return
12
https://www.nasa.gov/sites/default/files/thumbnails/image/artemis_2_map_october_2021.jpg
Proximity Operations Demonstration Sequence

## Slide 6: Stargate access
+
+
+
Crew +EHP
1
2
3
4
5
6
7
Launch
Jettison Rocket Boosters
Main Engine Cut Off
Enter Earth Orbit
Trans Lunar Injection Burn
Orion Outbound Transit to Moon
Orion Outbound Powered Flyby
NRHO Insertion Burn
Lunar Landing Preparation
Lander Undocking and Separation
Lander Enters Low Lunar Orbit
Lunar Surface Exploration
Orion Remains in NRHO
Lander Ascends to Low Lunar Orbit
Lander Performs Rendezvous and Docking
Crew Returns to Orion
Orion Performs Return Powered Flyby
Final Return Trajectory Correction Burn
Crew Module Separation
Entry Interface
Splashdown
8
9
10
11
12
13
17
18
19
20
14
15
16
21

## Slide 7
Propellant
aggregation
HLS Starship launch
Artemis III launch
Loiter in NRHO
Surface expedition
Crew returns in Orion
Earth Orbit
Near Rectilinear Halo Orbit (NRHO)
Fast trans-lunar injection (TLI)
Crew board Starship from Orion
Crew board Orion from Starship
Human Landing System (HLS) Starship
Artemis III Concept of Operations
Storage depot launch
HLS propellant fill
South Pole surface
expedition
(2 crew)
NASA has awarded SpaceX a contract to develop its HLS Starship for use on Artemis III

## Slide 8: Challenges of Landing at the Lunar South Pole

## Slide 10: Characteristics of the South Pole

## Slide 11: Characteristics of the South Pole
Earth is upside down and spins backwards
Same side of the moon always faces the Earth
Sun and Earth only rise above the horizon ~2 to 7 deg
Sun casts long shadows
Earth is in a 2-week cycle: visible two weeks, not visible two weeks
Terminator, where light meets darkness, is not smooth
Constantly changing lighting effects at the pole
Kaguya “Earth-Set” from the Lunar South Pole
Lunar South Pole terminator rotates around the pole.

## Slide 12: Characteristics of Near Rectilinear Halo Orbit
~6.5 day period
Visible from Earth 100%
Periapsis of ~1500 km and apoapsis nearly 70,000 km
Due to variations in Moon and NRHO, approach path varies orbit-to-orbit but has general left to right direction
Other Considerations:
  Assumes Gateway fixed NRHO, so can only descend to the surface once every 6.5 days (~55 opportunities to land per year)
  Earth/Moon orbital mechanics and SLS/Orion limitations reduce ability to get to NRHO to ~28 NRHO departure opportunities per year

## Slide 13: Key Artemis III Landing Requirements
Land within 6 deg latitude of the South Pole
Surface slope for landing (100m): <10 deg
Surface slope limit for EVA (2km): <20 deg
Direct with Earth (DWE) communication; assume no comm relay is available
Lighting
  Surface Lighting
  Approach lighting
Land within 100 m of a target
Objective: Identify locations that are viable for landing and meet all requirements and constraints

## Slide 14: 1. Land within 6 deg latitude of the pole
https://pgda.gsfc.nasa.gov/products/78
Earth
Poor DWE

## Slide 15: 2. Surface slope for landing: <10 deg
Slopes for landing must be less than 10 deg
Green areas show slopes less than 10 deg
White contours show regions of continuous 8 deg slope

## Slide 16: 3. Surface slope for EVA: <20 deg
Slopes for Extravehicular Activity (EVA) must be less than 20 deg
Black designates areas of slope > 20 deg
No EVAs can occur in black areas

## Slide 17
Artemis III will require Earth to be visible for communications
Black designates areas of slope > 20 deg
+
Earth visibility < 25%
Reduces areas suitable for landing.
4. Direct with Earth Communication

## Slide 18
Artemis III will require the surface to be lit for the duration of the surface stay
Black designates areas of slope > 20 deg
+
Earth visibility < 25%
+
Solar visibility less 5%
Reduces areas suitable for landing.
5a. Surface Lighting

## Slide 19
Illumination along the approach trajectory is beneficial.
The approach trajectory is different for each landing opportunity.
Notional range designated in red
  Peak lighting conditions are periodic and shift 2-3 weeks earlier each year, where by 2030, peak solar illumination occurs around the month of August
5b. Approach Lighting

## Slide 20
Human Landing Accuracy Requirements
100 m x 100 m
Past Robotic mission landing performance at Mars
Apollo 11 landing ellipse: 17 x 5 km
6. Land within 100m of a target
Gale Crater Mars

## Slide 21: Looking Forward

## Slide 22
+
+
+
Crew
1
2
3
4
5
6
7
Launch
Jettison Rocket Boosters
Main Engine Cut Off
Enter Earth Orbit
Trans Lunar Injection Burn
Orion Tugs I-HAB to Moon
Orion Outbound Transit to Moon
Orion Outbound Powered Flyby
I-HAB Arrives at Gateway
I-HAB Activation and Crew Ingress
Crew Returns to Orion
Orion Performs Return Powered Flyby
Final Return Trajectory Correction Burn
Crew Module Separation
Entry Interface
Splashdown
8
11
13
14
15
16
12
17
Gateway Orbit Insertion Burn
9
10