## Slide 1: Necessity for professionally trained CC technicians to support the James Webb Space Telescope integration, testing and launch campaign
Raymond LeVesque, presenter
KBR, Inc.
Colette D. Lepage, Azuka J. Harbor
Peraton, Greenbelt, MD, 20770
Kelly Henderson-Nelson, Jason E. Durner
KBR, Inc., Fulton, MD, 20759
Eve M. Wooldridge,
NASA Goddard Space Flight Center, Greenbelt, MD, 20771
Edwin Goldman
Prime Science and Technology,
Baltimore, MD, 21201

## Slide 2: Introduction
ESA/NASA/Don Pettit
Webb’s Contamination Challenges
The usual issues & more
Very low End-Of-Life (EOL) particulate and molecular limits
Specialized facilities scattered all over the planet
A long, arduous Integration & Test (I&T) campaign over 15+ years
(Credit: NASA/GSFC)

## Slide 3: Industry Standard Approach
Janitorial staff daily maintenance is key to good cleanroom operations
  Vacuum and mop floors (avoiding hardware)
  Empty trash cans
  Pull dirty tacky mats
  Clean return air registers
This allows discipline specialists to focus on their work, not the cleanroom
  Electrical I&T focuses on routing their cables, not whether the floor is dirty
  Mechanical I&T is less worried about using dirty tools
  Metrology can install their delicate mirrors and optics without concern that they will be at risk from the cleanroom environment
  Good outcomes arise from a team tasked to maintain facility cleanliness

## Slide 4: Simple questions yielded complex answers
What Happens When . . .
  Electrical I&T needs to route SpaceWire, a delicate specialized cable?
  Ground Support Equipment (GSE) arrives dripping with cutting fluid, metal cuttings, grease and peeling paint?
  Mechanical I&T needs to chase the threads on a mounting hole in a flight structure?
  Metrology brings in delicate, expensive laser trackers and mirrors that are visibly dusty?
  Delicate, one-of-a-kind flight hardware needs to be inspected and cleaned?

## Slide 5: A Cleanroom versus what lives there
Janitorial service staff are integral to a well-functioning cleanroom
  Keep the facility in good operational condition
Generally, janitorial staff lack training for sensitive hardware work
  Safe handling of specialized hardware, like SpaceWire cables
  Electrostatic Discharge (ESD) protocols
  Hands on cleaning knowledge for flight parts, laser trackers & so on
Webb bridged this gap with specially trained, dedicated contamination control technicians (CCTs)

## Slide 6: Specialized CC Technicians
Goddard Space Flight Center (GSFC) has a cadre of specially trained CCTs supporting programs in many cleanrooms on Center
While Webb hardware was at GSFC it used these specialized CCTs
When Webb left GSFC, some CCTs traveled with it; others were hired & carefully trained at each location along its journey to launch
Careful hiring and On-the-Job training were key to building effective CCT Teams for this sensitive observatory
“Familiarity breeds Respect” - Knowledge of the Project
  Invests crew members in mission success
  Equips them to better tackle what arises
  Enables them to be flexible and collaborate in solving problems

## Slide 7: Benefits of Specialized CCTs
Cleaning of the Webb transporter
  Dedicated Webb CCTs traveled to OH from AZ, TX, CA and MD
  This familiar, cohesive team made quick work of a huge task
  Quickly knew how to collaborate and resolve new, unexpected situations
  Understood how this would interact with the precious cargo that it would carry to the South American launch site
  Managed logistics for cleaning supplies
(Credit: NASA/GSFC)

## Slide 8: Benefits of Specialized CCTs, continued
Consistency, Efficiency
  Webb CCTs cleaned Transporter for entry to Webb cleanroom
  Webb CCTs cleaned Transporter for entry to launch site cleanroom
Risk Reduction
  Webb CCTs knew peculiar sensitivities of the Observatory
  CCTs and CC engineers (CCEs) worked as a cohesive team to surface, discuss and resolve contamination issues
(Credits: NASA/GSFC)

## Slide 9: The CCT training program
First Day on the Job
  Walkdown of the Webb cleanroom
  Cleanroom training specific to the facility
  High-level training of Webb’s mission and its unique systems
After some time working on the Floor
  Second review of Webb’s mission
  Particles: Light scattering and throughput loss
  Molecular: Altering absorptance, reflectance, emittance
  Thermal impacts, emphasizing hot and cold sides of Observatory
  Need to minimize heat transfer

## Slide 10: Most training was On-the-Job
Various hardware & equipment entered/exited cleanroom each day
Each piece arriving at CCT workstation was unique, incompatible with a “one size fits all” cleaning approach
As effective as On-the-Job training proved to be, CCEs supplemented it with training packets on various subjects, including
  Cleanroom garment gowning
  Cleaning
  Inspection
  Hardware triaging techniques
  Cleanroom design and operation
  Types and sources of contamination
  Identifying metal coatings

## Slide 11: Identifying metal coatings
Problematic
  Zinc
  Galvanized
  Cadmium
  Black oxide
  Tin
Cleaning cautions
  Dry film lube
Acceptable
  Stainless steel
  Aluminum
  Conversion Ctg.
  Anodize
(Credit: NASA/GSFC)

## Slide 12: Growing knowledge & capabilities
Solvent selection expedited cleaning operations, reduced problems
Flight hardware often arrived with cleaning guidance
GSE was a mixed bag, leaning on CCT, CCE experience
  Painted, other coated surfaces
  Multilayer Insulation, Tapes, Films
Webb CCEs, Lead CCTs learned their team’s strengths and provided options for new duties playing to these natural talents
  Enhanced the team’s capabilities
  Reduced some of the inherent tedium in the CCT role
  Prepared CCTs to better handle new situations, which were many as Webb made its way to launch

## Slide 13: Expanded Capabilities
CCTs were identified as being well suited to key added duties
  Image Analysis and Ellipsometry
  Hardware management and logistics/tracking
  Simultaneously supporting multiple I&T facilities
  Adapting Launch site laundry facilities
  SCAPE suit cleaning
(Photo credits: BBC, ESA/CNES/Arianespace/Optique video du CSG)
(Credit: ESA/CNES/Arianespace/Optique Vidéo du CSG)

## Slide 14: Concluding Remarks
Webb repeatedly showed the benefits of specially trained CCTs
CCTs aligned with CC protocols, req’ts & hardware sensitivities
  Fostered positive attitudes toward CC, earned trust & collaborated with other I&T disciplines
  Achieved an order of magnitude reduction in cleanroom fallout
  Augmented capabilities of many Webb partners
15+ years: The temperament, training & work ethic of Webb’s CCTs advanced work with ingenuity & integrity, ensuring every item on or near Webb was clean, providing additional margin on-orbit
The CCTs created a cooperative relationship with the I&T process that was an invaluable part of Webb’s spectacular success

## Slide 15: Acknowledgments
The authors gratefully acknowledge support from NASA Contract NNG15CR64C and
  NASA-GSFC Contamination Control Management
    Eve Wooldridge, Randy Hedgeland, and Tina Montt de Garcia
  NASA-GSFC OTIS Management
    Lee Feinberg, Mark Voyton, Juli Lander

## Slide 16: Thank you…
(Credit: NASA/GSFC)