## Slide 1: High Enthalpy Testing
Ernest Fretter
Thermophysics Facilities Branch
Brett A. Cruden*
Aerothermodynamics Branch
Entry Systems and Technology Division
NASA Ames Research Center, Silicon Valley
* AMA Contract No NNA15BB15C

## Slide 2: Arc Jets
Ernest Fretter
NASA Ames Research Center
IPPW Short Course
Aug. 7, 2022

## Slide 3: What is High Enthalpy?
General range from 1 to 100 MJ/kg at pressures from .01 to >100 bar
Depends on mission. Low for supersonic low altitude flight to highs for Mars Sample Return
MSR

## Slide 4: Ideal testing at High Enthalpy

## Slide 5: For TPS, What are the Test Objectives
  Comparative screening of candidate materials
  Evaluating performance over a range of conditions
  Develop data base for modeling
  Validating performance of material interfaces (gaps, steps, A to B, etc.)

## Slide 6: Techniques for Producing High Enthalpy Flows
Radiation (lasers, solar)
Furnaces & Combustion
Ballistic ranges (Low Enthalpy Testing topic)
Arc heaters
Shock tubes

## Slide 7: Range of Interest for High Enthalpy Tests

## Slide 8: Why NASA ARC uses Arc Jets

## Slide 9: How do Arc Jets Work
An arc jet produces an electrically heated, high speed gas flow onto a test article – matching key parameters of hypersonic entry from space into an atmosphere

## Slide 10: Standard arc jet process
Under vacuum, add argon gas; connect a hi-voltage D.C. source across electrodes to breakdown argon; and we have a flow of electrons inside the arc jet tube.
Air flow collides with electrons in this “lightning bolt”, dissociating air at high temperatures (> 9000º F)
Expand dissociated air out a nozzle to hypersonic conditions and into a chamber at altitude conditions matching peak heating
When conditions are correct, insert test sample and see what happens!

## Slide 11: Principle Types of Arc Jets
Huels or Linde (free length)
  high P
  H<20 MJ/kg
Segmented Constrictor (fixed length)
  low to high P
  H < 50 MJ/kg
Inductively Coupled Plasma devices
  P <= 1 bar
  H < 80 MJ/kg

## Slide 12: NASA Ames Arc Jet Complex
Facility Characteristics
High power, 5 operational arc jets ((1) x 10 MW, (3) x 20 MW, (1) x 60 MW)
Large test articles (up to 60 x 60 cm flat panel, 30.5 cm diameter stagnation)
Continuous high enthalpy flows (2 - 40 MJ/kg in air)
Combined heating with laser radiant source
Spectroscopic and LIF flow diagnostics available
Test times from seconds to over one hour
Laminar and turbulent flows
Instrumentation: pyrometers, IR camera, photogrammetric recession, HD video, scanning radiometer, LIF

## Slide 13: Ames Arc Jet Complex
Interaction Heating Facility (IHF) – 60 MW
Aerodynamic Heating Facility (AHF) (10 & 20 MW)
Panel Test Facility (PTF) – 20 MW
Turbulent Flow Duct (TFD) - ~15 MW

## Slide 14
NASA Ames Arc Jet Complex Neighborhood

## Slide 15: IHF now New and Improved with Combined Heating Capability
Combine IHF convective arc with 4 fiber optic IPG lasers of 50 kW each
λ= 1070nm ytterbium lasers
Produces 6x6” and 17 x 17” flat top and Gaussian distribution
Calibration plates, burn plates, 30 kW Ophir power meter

## Slide 16: LEAF-Lite
Laser Enhanced Arc-jet Facility (LEAF-Lite)
Interaction Heating Facility
LEAF-Lite allows for combined radiative and convective testing
LEAF-Lite Optics Enclosure (OE)
Beam Path Enclosure
IHF Test Box
Control Room
Convective Flow
North
Arc Jet Complex Combined Heating Layout

## Slide 17: Other Arc Heaters Worldwide
Facility | Location | Power Ranking (MW)
NASA ARC | USA | 60
NASA LaRC HYMETS |  | 0.5
AEDC |  | 70
Boeing LCAT |  | 6
Univ of Texas Austin |  | 1 .6
JAXA | Japan | 1
Chonbuk Nat’l Univ. | South Korea | 0.4 to 2.4
CIRA (SCIROCCO & Ghibli) | Italy | 70 & 2
ESA – Airbus | France | 6 - 20
DLR (L2K & L3K) | Germany | 5
IRS (PWK 1, 2, 4) |  | 6
Technion | Israel | 5
TsAGI | Russia | 10
Tsniimash |  | 50
CARDC | China | 20
CASC/BIA |  | Unk
VSSC | India | >0.25

## Slide 18: ICP Arc Facilities
Country | Institution | Facility | Power (kW) | Max Enthalpy (MJ/kg)
USA | U. Vermont | ICP Torch | 30 | 50
 | U of Texas Austin | ICP Torch | 50 | -
 | UI Urbana Champagne | ICP Torch | 80 | 30
Russia | IPM | IPG 3&4 | 100 - 750 | 50
China | CARDC | FD-31A | 1000 | 60
Japan | JAXA | ICP WT | 110 | 20
Germany | IRS | PWK 1,2,4 | 100 – 600 | 150
 |  | PWK-3 | 375 | 80
 |  | IPG6-B | 20 | -
France | CORIA | IPT-1 | 100 | 17
 | C. Supelec | ICP Torch | 50 | -
 | Airbus | Plasmatron | 150 | -
Belgium | VKI | Minitorch | 15 | -
 |  | Plasmatron | 1200 | 80

## Slide 19: Future Challenges
Higher enthalpy (Mars, comets, and asteroid returns)
Larger sample sizes, animated samples
Unusual gas mixes (gas giants, Venus, etc.)
The ability to use arc jets for validation would enhance their value significantly
Two approaches: improved in-situ diagnostics (instrumentation), improved modeling of arc column (simulation)
Will CFD replace the arc jets?

## Slide 20: Shock tubes and Tunnels
Brett A. Cruden
AMA Inc at NASA Ames Research Center
IPPW Short Course
Aug. 7, 2022

## Slide 21: Ground test facility types and uses
Kinetics and
Radiation
AEROHEATING
AND LOADS

## Slide 22: Shock Tube Similarity
Both Stagnation streamline and shock tubes are 1-D flows:
The equilibrium and non-equilibrium of the flow (on the stagnation line) is a function only of r∞ and vs
This 1D flow has similarity to a shock tube in terms of
  Chemical Kinetics
  (Volumetric) Radiance
The shock tube does not capture the time and length scales of flight
v=vs
= r∞
T= T∞
h = h0
22
Shock Tube
h = h0+ vs2/2
T=Ts
r = rs
v=vs
= r∞
T= T∞
h = h0
h = h0+ vs2/2
T=Ts
r = rs
Shock frame of reference
Notes: Note on radiation importance, relative magnitude and backshell

## Slide 23: Electric Arc Shock Wave Generation
Capacitor Bank
Delivers
0.2-1 MA
For 10-100 ms
Driven Section Filled with Test Gas
(0.01-2.0 Torr)
Driver Filled at
Higher pressure
(100 psi He)
Diaphragm Maintains
Pressure Differential
Pin charged
up to 10-25 kV (typical)
40 kV (Max)
Through 1.3 mF (1.2 MJ)
Capacitor Bank
Grounded
Wire is pulled in
1292 cc
Diaphragm Breaks
Shock
Front
Contact
Front
Compressed and
Dissociated Driven Gas
23

## Slide 24: Shock Wave Generation
Shock
Front
Contact
Front
Compressed and
Dissociated Driven Gas
Pressure
Transient
Emission
Transient
24

## Slide 25: The Shock x-t diagram
Shock tubes are often characterized in terms of an x-t diagram
The slope of the shock wave is the inverse of its velocity
The contact front separates test gas from driver gas
  The test gas is the region between the shock wave and contact front
Expansion waves will reflect off of the wall and other waves
Shock Wave
Contact Front
Expansion Head
Expansion Tail
Expansion Head
(Reflected)
Expansion Head
(Transmitted)
Expansion Head
(Reflected)

## Slide 26: Shock x-t and P vs. x Animation
Initial wave formation
  Shock, contact and expansion tail moves forward
  Expansion head moves backward
  Pressure drops from head to tail
Freestream Gas
Shocked Gas
Driver Gas
Shock Wave
Expansion Head
Expansion Fan

## Slide 27: Shock x-t and P vs. x Animation
Expansion head reflects off end wall
All waves move forward
Pressure is constant behind shock and contact front until expansion
Region between shock and contact (i.e. test time) grows as waves travel
Freestream Gas
Shocked Gas
Driver Gas
Shock Wave
Expansion Fan

## Slide 28: Shock Tunnels (Reflected)
Test Cabin
Driver Gas (He)
High Pressure
(N2)
Piston
Test Gas (Air)
Diaphragm
(Steel)
Diaphragm
(Mylar)
Test Article
Bow Shock
A shock tunnel is a shock tube with a test cabin at the end of it
Two types of shock tunnels: expansion and reflected
Primary use of shock tunnels is to study aeroheating on test articles in relevant environments
Similarity variables: H, pL (binary scaling)
Notes: 28

## Slide 29: Shock Tube Facilities around the World*
EAST
HET
T5
LENS
HIEST,
HEK-X
HVST
X2, X3
JF-12
HAST
ESTHER
T6
* Not exhaustive
HEG
HELM

## Slide 30: Super orbital expansion tube HEK-X
Free-piston driven expansion tube (Exit diameter of the conical nozzle is 200mm)
Over-driving operation: Up to 12km/s (H0=70MJ/kg) or higher. P0=130MPa. Test time 100-400 msec.
Short turn-round time: 4 or 5 shots a day
Credit: Dr. Hideyuki Tanno, JAXA
Notes: それでは実験の内容、主に設備と計測器の説明と実験の概要(流れですね)について説明します。

## Slide 31: Free-piston shock tunnel HIEST
90m
Compression tube : 42m, φ600mm
Shock tube : 17m,φ180mm
Piston : 220 ~ 780kg
Nozzle
  Conical : throat φ24~50mm exit φ1200mm
  Contoured : throat φ50mm exit φ800mm
Maximum stagnation enthalpy 25MJ/kg (V=8km/s)
Maximum stagnation pressure 150MPa
Test time 2~15ms
Credit: Dr. Hideyuki Tanno, JAXA
Notes: それでは実験の内容、主に設備と計測器の説明と実験の概要(流れですね)について説明します。

## Slide 32: Experimental Simulation
Medium size (Driver 21m, shock-tube 8-11m, nozzle diameter 0,7m)
Enthalpy range max. 20-25MJ/kg
Pressure sufficient for ρL, to generate turbulent flow conditions (max. 150-200 MPa)
Provides similarity in ρL=const. (binary scaling), velocity, gas, total enthalpy,
Re-number, compressibility effects
Recent research: Measurements of BL instability with ALTPs and of reservoir condition using LITA
Piston driven shock-tunnel HELM
Credit: Prof. Christian Mundt

## Slide 33
Caltech Hypervelocity Facilities
T5 Free Piston Reflected Shock Tunnel
Mach number 6
Re/m to 8 million
ho to 22 MJ/kg
1-2 ms test time
Hypervelocity Expansion Tube (HET)
Mach number 3.0 to 7.4
Re/m 0.4 million (Mach 7) - 5 million (Mach 4)
ho 2 to 9 MJ/kg
Thermochemically “clean” freestream
Both facilities recently characterized in collaboration
with RK Hanson (Stanford) via TDLAS Tr, Tv, U∞, ρNO measurements
(AFOSR FA9550-19-1-0219)
New facility planned: 17” Expansion Tube
Larger (150ft, 17” diam.) version of HET, Detonation-driven
Diagnostics: UV Emission Spectroscopy; MWIR Radiation; 1MHz schlieren; Focused Laser Differential Interferometry (FLDI); Surface heat flux, pressure; PSP
Credit: Prof. Joanna Austin

## Slide 34: Hypervelocity Spherically-Blunted Cone Flows in Mars Entry Ground Testing
Leibowitz and Austin, AIAA J., 2022.
Supported in part by the NASA Space Technology Research Fellowships NNX14AM59H and NASA awards NNX14AO97A and NNX16AO55G. Collaborations with NASA Ames & Langley gratefully acknowledged.
Comparison with cone/sphere behavior theory from Hornung, Martinez Schramm, Hannemann JFM 2019
Sphere-cone
T52892 & HET1459
T5 aft measurements
HET fore measurements
Credit: Prof. Joanna Austin

## Slide 35: Shock Tubes, in Perspective
Detonation Driver
Shock tube
Test section
Dump tank
CUBRC LENS XX
JAXA HIEST
CAS JF-12
EAST
HET

## Slide 36: Electric Arc Shock Tube (EAST)
The Electric Arc Shock Tube (EAST) is capable of simulating high speed flows relevant to entry problems
Two shock tubes are available:
  4” Aluminum Tube – most heavily used, velocities up to 46 km/s
  24” Stainless Steel Tube – presently under refurb, intended for Low Density Studies
Driver
Expansion Section
Test Section
4” Tube
24” Tube
7.5 m
23.5 m
36
Test section
VUV
Blue
Red
IR
Primary Instrumentation: 4 spectrometers measure full radiative spectrum of shock layer

## Slide 37: Radiance Obtained in Different Spectral Regions
VUV
UV
UV/Vis
Deep VUV
Visible
NIR
NIR
MWIR
37

## Slide 38: EAST operating envelope and Recent Tests
Chart: Shock Velocity (km/s)
| 17 | 23 | 29 | 46 | 46 | 27 | 17 | 17
10 cm dia., H2/He | 0.25 | 0.1 | 0.1 | 0.25 | 1 | 10 | 10 | 0.25
10 cm dia., Air, N2, CO2, etc | 760 | 760 | 100 | 2 | 0.25 | 0.25 | 0.1 | 0.1 | 1.55 | 760
60 cm dia., Air, CO2 | 0.01 | 0.01 | 5 | 5 | 1.5 | 0.01
38
Titan aerocapture (CH4/N2)
Mars aerocapture (CO2/N2)
Venus entry (CO2/N2)
Uranus/Saturn
Probes (H2/He)
Lunar return (Air)
Mars entry (CO2/N2)
Mars return (Air)

## Slide 39: EAST operating envelope and Recent Tests
Chart: Shock Velocity (km/s)
| 17 | 23 | 29 | 46 | 46 | 27 | 17 | 17
10 cm dia., H2/He | 0.25 | 0.1 | 0.1 | 0.25 | 1 | 10 | 10 | 0.25
10 cm dia., Air, N2, CO2, etc | 760 | 760 | 100 | 2 | 0.25 | 0.25 | 0.1 | 0.1 | 1.55 | 760
60 cm dia., Air, CO2 | 0.01 | 0.01 | 5 | 5 | 1.5 | 0.01
Shuttle | 331.8362 | 265.0303 | 89.4082 | 72.2552 | 30.0669 | 25.545 | 14.9684 | 12.0868 | 3.9282 | 3.2818 | 2.7581 | 1.5327 | 1.3063 | 0.90515 | 0.81938 | 0.6267 | 0.58276 | 0.45118 | 0.41652 | 0.34477 | 0.32198 | 0.27241 | 0.24671 | 0.17236 | 0.15585 | 0.11196 | 0.10904 | 0.075788 | 0.065323 | 0.043688 | 0.025894 | 0.010177 | 0.0036914 | 0.0011042 | 0.00033698
 | 0.0006556 | 0.023994 | 0.059015 | 0.14515 | 0.35702 | 0.55992 | 0.87813 | 1.3772 | 2.1599
 | 1e-05 | 0.0066111 | 0.042995 | 0.14704 | 0.31378 | 0.63024 | 0.7371 | 0.86253 | 1.0505 | 1.2804 | 1.6251 | 1.9061 | 2.2367 | 2.4232 | 2.4232
 | 5.9184e-05 | 0.00016622 | 0.00038456 | 0.0009676 | 0.002719 | 0.0085576 | 0.021855 | 0.057413 | 0.15118 | 0.31204 | 0.58578 | 0.98132
39
Orion Lunar
Hayabusa
Mars Return
Shuttle
MSL
Pioneer
Viking
Huygens
Galileo
Uranus Decadal
Saturn Decadal
Chelyabinsk

## Slide 40: EAST Upgrades: Low Density Shock Tube
Low Density Shock Tube (LDST) – 21.38” diameter (54.3 cm)
  Test time scaling (PD2) – 5x increase in diameter enables ~25x reduction in P
  Longer test times better for off-stagnation cases, thicker shocks with slower kinetics
  Investigation of Facility Artifacts
Expansion Cone
  Flows in expansion to simulate backshell heating
  mechanisms

## Slide 41: Voitenko shock tube (1969)
High-explosive, shaped-charge driver – record 88 km/s shock speed
Destroys itself with each run

## Slide 42: Conclusions – Shock Tubes
42
Shock tubes may be used to create flight-similar hypersonic flows
  Similarity in Radiation, Reaction Kinetics
Shock tunnels are generally used to quantify surface heating magnitudes and phenomena
  Binary scaling and enthalpy are similarity variables
Around a dozen shock tubes around the world may be used for quantifying hypersonic flow environments
  There are many more shock tubes that are used for, e.g. combustion studies
Most planetary entry environments have been replicated in the EAST facility (shock tube) with some other shock tubes providing comparable data
Questions about High Enthalpy Facilities at ARC?
https://www.nasa.gov/centers/ames/thermophysics-facilities-home