## Slide 1: MARS 2020 Backshell Radiative Heating Measurement and Shock Tube Verification
Brett A. Cruden(1), Ruth A. Miller(2), Aaron M. Brandis(2), Augustin C. Tibere-Inglesse(3), Christopher C. Jelloian(4), Mitchell Spearrin(4), Thomas K. West(5), Christopher O. Johnston(5), Dinesh K. Prabhu(1), Joshua Monk(2), Justin Clarke(6), Luca Di Mare(6), Matthew McGilvray(6)
Radiation in High Temperature Gases Workshop
Santa Maria, Portugal, Sep. 2022
(1)AMA Inc, NASA Ames Research Center
(2) NASA Ames Research Center
(3)ORAU, NASA Ames Research Center
(4)University of California, Los Angeles
(5) NASA Langley Research Center
(6) Oxford University

## Slide 2: Outline
MEDLI2 flight measurements
Shock Tube Informed Bias Methodology
EAST Test results
  Emission Spectroscopy
  Tunable Diode Laser Absorption Spectroscopy
  Resolution of Measurement Artifacts

## Slide 3: Mars2020 Entry Descent and Landing Instrumentation 2
Mars 2020 brought the Perseverance rover to the surface of Mars
MEDLI2 measured aerothermal environments during Mars 2020 entry
Forebody
Aftbody

## Slide 4: Backshell instrumentation
Sensors on Mars2020 Backshell detected heat fluxes and radiation during entry
Heatflux gauge measures convective heating (cold wall) and radiation (absorbed)
Radiometer measures radiation that passes through its view factor and spectral range
MTB08/09
MTB07
Heatflux Gauge
Radiometer
    qtotal = qconvective + aqradiative

## Slide 5: MEDLI2 Results – Initial Analysis
Heat Flux Sensors
  Reasonable agreement of predicted vs. measured total heat flux
  An inferred convective heating is deduced based on (measurement – predicted radiation)
    Agreement to predicted convective heating is reasonable (wall temperature must be considered)
  Leeside gauge is dominated by radiation
Radiometer
  Shows initial agreement to prediction, drops to 0.5x predicted radiation
  Believed to be due to coating of window by ablation products
MTB08/09
MTB07

## Slide 6: Revised MEDLI2 Analysis
Correction factors for temperature dependence of sensor increased measured heat flux by ~10%
Following entry, revised trajectory data became available
  OD58 – Orbital Determination 58 : based on entry state predicted while spacecraft in cruise
  MEADS – Trajectory Reconstruction using the MEADS (pressure) sensors on vehicle
  BET8 – ver. 8 of the Best Estimated Trajectory – updated atmospheric model
Sensitivity to flowfield inputs also observed
  “Cruden” model predicts higher heatflux with earlier peak than the “Johnston” model
Convective heat flux needs to be re-evaluated as cold wall
Chart: Time (s)
OD58 | 0.2245 | 0.4812 | 1.248 | 1.9332 | 2.7594 | 3.5445 | 4.5719 | 5.1222 | 5.4834 | 4.7921 | 2.5018 | 1.0744 | 0.3459 | 0.0862 | 0.0191
MEADS | 0.19109 | 0.26848 | 0.60017 | 1.5873 | 2.4377 | 3.1141 | 3.7741 | 4.1594 | 4.7196 | 5.0493 | 4.5979 | 2.3711 | 1.0088 | 0.32383 | 0.079224 | 0.01665
BET8 | 0.19659 | 0.26735 | 0.59162 | 1.5976 | 2.4273 | 3.1133 | 3.8056 | 4.1921 | 4.752 | 5.0273 | 4.3409 | 1.9938 | 0.79779 | 0.22892 | 0.069035 | 0.022169
Chart: Time (s)
DPLR/NEQAIR (Cruden) | 0.19659 | 0.26735 | 0.59162 | 1.5976 | 2.4273 | 3.1133 | 3.8056 | 4.1921 | 4.752 | 5.0273 | 4.3409 | 1.9938 | 0.79779 | 0.22892 | 0.069035 | 0.022169
LAURA/HARA (Johnston) | 0.15818 | 0.94027 | 2.4397 | 3.5502 | 4.1822 | 4.2585 | 4.1406 | 2.6199 | 1.2312 | 0.067115
Chart: Time (s)
| 43.358983039855957 | 51.483978033065796 | 57.858978033065796 | 62.858978033065796 | 68.983978033065796 | 73.233978033065796 | 77.358978033065796 | 79.858978033065796 | 83.858978033065796 | 88.608978033065796 | 92.858978033065796 | 99.608978033065796 | 104.9839780330658 | 111.6089780330658 | 119.8589780330658 | 129.9839780330658
Inferred (NEQAIR) | 0.02982 | 0.24699 | 0.38681 | -0.015177 | 0.087767 | 0.061428 | 0.17211 | 0.30396 | 0.31263 | 0.65067 | 1.2181 | 1.385 | 0.9381 | 0.61198 | 0.28784 | 0.17125
Inferred (HARA) | 0.047762 | 0.31072 | 0.80679 | 1.2407 | 1.3884 | 1.4523 | 1.4712 | 0.79644 | 0.53066 | 0.13064
Hot wall (LAURA) | 0.0571 | 0.0806 | 0.0789 | 0.0982 | 0.0815 | 0.0927 | 0.1309 | 0.1263 | 0.1401 | 0.0389
Hot wall (DPLR) | 0.072117 | 0.07019 | 0.041841 | 0.059115 | 0.1281 | 0.14289 | 0.20273 | 0.22285 | 0.26501 | 0.30503 | 0.23263 | 0.31112 | 0.19746 | 0.13114 | 0.067274 | 0.055906
qinferred=qmeasured-aqrad

## Slide 7: CO2 Chemistry (Simplified)
Chart: 1/Temperature (1/K)
| 1E-3 | 5.0000000000000001E-4 | 3.3333333333333332E-4 | 2.5000000000000001E-4 | 2.0000000000000001E-4 | 1.6666666666666666E-4 | 1.4285714285714287E-4 | 1.25E-4 | 1.1111111111111112E-4 | 1E-4 | 9.0909090909090904E-5 | 8.3333333333333331E-5
Streicher | 1.204e-09 | 2933.773 | 29348555.4942 | 2540671779.9617 | 33888797045.2528 | 180032581452.1483 | 569846713602.0968 | 1.3117e+12 | 2.45e+12 | 3.9629e+12 | 5.7832e+12 | 7.8227e+12
Park | 1.0503e-09 | 2881.5408 | 31053314.7318 | 2837983703.1088 | 39503074699.2157 | 217361711873.6275 | 708868583362.1008 | 1.6747e+12 | 3.2008e+12 | 5.2852e+12 | 7.8583e+12
Cruden | 1.3054e-09 | 4574.1837 | 46275188.559 | 3818603419.3368 | 47940482047.3212 | 239483468683.0186 | 714579500545.822 | 1.556e+12 | 2.759e+12 | 4.2511e+12 | 5.9278e+12
oops | 1.3054e-12 | 4.5742 | 46275.1886 | 3818603.4193 | 47940482.0473 | 239483468.683 | 714579500.5458 | 1555965960.2214 | 2759044152.5206 | 4251075775.234 | 5927750567.4449 | 7683149189.4945
CO2
CO
O
CO
O2
CO2
Chart: 1/Temperature (K-1)
| 1E-3 | 5.0000000000000001E-4 | 3.3333333333333332E-4 | 2.5000000000000001E-4 | 2.0000000000000001E-4 | 1.6666666666666666E-4 | 1.4285714285714287E-4 | 1.25E-4 | 1.1111111111111112E-4 | 1E-4 | 9.0909090909090904E-5
Park (molec) | 7.2255e-11 | 1403.8232 | 29051780.967 | 3679283629.6637 | 62287000256.9275 | 390503554582.8063 | 1.3979e+12 | 3.5417e+12 | 7.1475e+12 | 1.2327e+13 | 1.8992e+13
Park (atom) | 1.4379e-10 | 2800.6361 | 58006803.3187 | 7349374796.7392 | 124449488779.5841 | 780356541015.6849 | 2.7939e+12 | 7.079e+12 | 1.4287e+13 | 2.4641e+13 | 3.7968e+13
Ebrahim (CO2) | 4.4685e-09 | 1452.5024 | 10897093.247 | 984813795.4933 | 15064460502.1432 | 94400401484.0004 | 354379347542.1237 | 964340160848.595 | 2.1154e+12 | 3.988e+12 | 6.7302e+12
= “Johnston”
= “Cruden”
Chart: 1/Temperature (K-1)
| 1E-3 | 5.0000000000000001E-4 | 3.3333333333333332E-4 | 2.5000000000000001E-4 | 2.0000000000000001E-4 | 1.6666666666666666E-4 | 1.4285714285714287E-4 | 1.25E-4 | 1.1111111111111112E-4 | 1E-4 | 9.0909090909090904E-5
Ibragimova | 0.5673 | 12399168.0652 | 3466714908.151 | 57967012564.6363 | 314151106128.1443 | 969267630796.01 | 2.1674e+12 | 3.9635e+12 | 6.338e+12 | 9.2269e+12 | 1.2546e+13
Tsang | 54.5018 | 30368906.0746 | 2499012658.1466 | 22669299993.4204 | 85121624244.3898 | 205640079699.648 | 386124771758.9481 | 619359196278.4281 | 894446150649.6012 | 1.2002e+12 | 1.5266e+12
Thielen | 17.7351 | 19298608.5159 | 1984984389.8224 | 20131338227.5744 | 80824304349.8214 | 204168244803.8127 | 395776297082.3194 | 650198510286.7145 | 956603344825.1637 | 1.3028e+12 | 1.6774e+12
= Johnston/Cruden
= Park
= Johnston

## Slide 8: Shock Tube Informed Bias (Johnston 2019)
How can compressive shock measurements be used to validate predictions on oblique streamlines and the wake?
  The normal velocity of the oblique shock has similarity to the velocity of an incident shock in particle time
  Binary Scaling – for 2nd order collision processes, r∞,1d1 is similar to r∞,2d2
    A larger initial density will correspond to longer distances behind the shock
MTB07

## Slide 9: Selecting STI conditions for MEDLI2
Every point in the flowfield can be translated to a corresponding veff and deff
The contribution of the flowfield point to the radiative heat flux can then be evaluated
This maps the contributions of different velocities and particle times to the total radiative heat flux, at one point in time and one vehicle location
This was evaluated at 9 time points and 2 vehicle locations (MTB07, MTB08)
veff
deff
10% Lower Bound
90% Lower Bound

## Slide 10: EAST Test 64A Conditions
Densities were chosen corresponding to near peak heating, ½ of peak heating and at end of heat pulse
The velocity range is swept to cover most of the histogram
A follow up test in the low density EAST tube (64B) will study earlier time points
Chart: Time (s)
 | 2 | 3.25
 | 1.75 | 3
 | 1 | 2
 | 3.195 | 3.2466 | 3.0293 | 2.603 | 1.5178 | 2.3486 | 2.1937 | 2.8832 | 3.4033 | 3.0746 | 2.5085 | 2.9683 | 2.4718 | 2.9052 | 2.9911 | 1.9886 | 2.1913 | 3.0141 | 2.8787 | 2.696 | 2.9569 | 2.7927 | 2.5702 | 2.1748 | 1.9705 | 2.276 | 2.9109 | 2.64 | 2.5335 | 2.1782 | 2.0591 | 2.6385 | 2.83 | 1.846 | 2.3538 | 1.9951 | 2.0629 | 2.0438 | 1.3902 | 1.3023 | 3.2949 | 1.7035 | 2.133 | 4.647 | #N/A | 1.9554 | 3.1247 | 2.8823 | 3.2789 | 2.0235 | 2.3 | 3.75 | 1.48 | 2.49 | 1.25 | 2.0919 | 1.9366 | 1.1657 | 2.6791
Chart: Velocity (km/s)
| 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 1 | 1.5 | 2 | 1 | 1.5 | 2
Planned Test Points | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0046208 | 0.0046208 | 0.0046208 | 0.0046208 | 0.0046208 | 0.0046208
4.3 um band | 0.0025213 | 0.0025221 | 0.0025196 | 0.0025194 | 0.002518 | 0.0025226 | 0.0025158 | 0.0034485 | 0.0034519 | 0.0034445 | 0.0034445 | 0.0034361 | 0.003432 | 0.0045937 | 0.0045848 | 0.0045697 | 0.0045975 | 0.004603 | 0.002512 | 0.0025118 | 0.020561 | 0.0025089 | 0.020353 | 0.0046204 | 0.020792
2.7 um band | 0.0025239 | 0.0025243 | 0.0025177 | 0.0025263 | 0.0025265 | 0.0025292 | 0.0025146 | 0.0025195 | 0.0025297 | 0.0025218 | 0.0025151 | 0.0025142 | 0.0034365 | 0.0034375 | 0.0034347 | 0.0034347 | 0.0034336 | 0.0034295 | 0.0034382 | 0.0034365 | 0.0034331 | 0.0046088 | 0.0045809 | 0.020353 | 0.0044333 | 0.0046204

## Slide 11: EAST Facility
Low Density Shock Tube
High Velocity Tube
Expansion Cone
Driver
Vacuum Spectrometers

## Slide 12: EAST Set Up
Mid IR Spectrometer
UV Spectrometer
EAST Facility Test Section Equipped with
  3 Tunable Diode Lasers
    Measure CO and CO2 absorption
    Obtain number densities, temperature(s)
  Mid-infrared spectrometer
    Measure CO2 radiation
    Two bands must be measured separate shots
  UV absorption and radiation measurements attempted, but nothing interesting observed
Light Source
Absorption
Spectrometer

## Slide 13: Tests Completed
1.1 Torr
2.5-3.3 km/s
(Peak Heating)
1.5 Torr
1.9-3.0 km/s
(Mid Point)
2.0 Torr
1.3-2.1 km/s
(Close out)
Fun stuff
59 Shots completed
3 Pressure conditions
  Approx. 1 km/s sweep of velocity
2 Wavelength ranges in emission
  n3 fundamental (4.3 mm, DP=3)
  n3+2n2 and n3+n1 combination bands (2.7 mm, DP=5)
  2 high resolution shots
TDLAS utilized 4 lasers (3 simultaneous)
  ICL – CO2 v2”=0,1, J”=58/103-143 at 4.19 mm
  ICL – CO2 ground state, J”=110-134 at 4.17 mm
  QCL – CO at 4.98 mm, v”=0,2-3, J”=14-31
  ECQCL – CO2 at 4.24 mm (single line only)
Fun stuff
  Filling in some gaps in the previous sweeps
  High Pressure (9 Torr) shots – try to induce chemistry
  Low P & V (0.5 Torr, 1.5-2 km/s) – measure v-T relax
  Higher Velocity (3.3-4.7 km/s) – higher T chemistry

## Slide 14: Emission Data
V
Spectral data obtained in horizontal cross-section
Spatial dependence in vertical direction
dtest~10 cm => tlab ~ 30-50 ms tpart ~ 0.4-0.5 ms, deff~0.1 m
2.7 mm
4.3 mm
V

## Slide 15: Radiance vs. Distance
4.3 um
2.7 um

## Slide 16: Mid-infrared Spectra
4.3 mm
2.7 mm
3.2-3.4 km/s
2.5-2.6 km/s
2.0-2.2 km/s
~ 2 cm behind shock front

## Slide 17: Tunable Diode Laser Absorption Spectroscopy
Absorption lines measured vs. time from shock front
Fits obtain temperature and number density data
CO absorption not measured below ~2.7 km/s
17
4.19 μm
CO2
4.24 μm
CO2
4.19 μm
CO2
4.98 μm
CO
Shot # 10 Uis = 3.07 km/s
Shot # 11 Uis = 2.51 km/s
Shot # 16 Uis = 1.99 km/s
4.24 μm
CO2
4.19 μm
CO2

## Slide 18: TDLAS Analysis vs. Distance
Temperatures are reasonably close to CFD prediction vs. distance
Densities of CO2 tend to be low
No chemistry observed below 2.7 km/s
CO density well predicted when dissociation occurs
18
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary

## Slide 19: Emission Summary at 1.1 Torr
Shock appears frozen < 2.7 km/s – radiance exceeds frozen by up to 10%
At higher velocities is between two rate models

## Slide 20: Emission Summary at 1.5 Torr
Radiance exceeds frozen levels by ~10% below 2.7 km/s
Reaction rate mostly agrees better with Ebrahim above 2.8 km/s

## Slide 21: 1.5 Torr Spectra (~2 cm from shock front)
Higher velocity (~ 3 km/s)
v≈ 2.5 km/s
Lower velocity (< 2.2 km/s)
4.3 um
2.7 um

## Slide 22: Emission vs Distance from Shock (1.5 Torr)
4.3 um
2.7 um

## Slide 23: TDLAS Analysis vs. Distance at 1.5 torr condition
Temperatures are reasonably close to CFD prediction vs. distance
Densities of CO2 tend to be low
No chemistry observed below 2.7 km/s
CO density well predicted when dissociation occurs
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary
Preliminary

## Slide 24: TDLAS Summary
Temperatures measured by TDLAS within 5% of predictions
CO2 number densities deviate at higher velocity, tend low by ~10-20%
  Deviation at 2 Torr due to optical thickness

## Slide 25: CO Formation Data from TDLAS
CO formation rate at 1.1 Torr from TDLAS Measurements
The yield at 10 ms matches Park rate at low velocity, between two models at higher v
Characteristic formation time (exponential fit) is between the models

## Slide 26: 2 Torr Data
2 Torr data (below 2 km/s) appears chemically frozen
Radiance Magnitude exceeds frozen condition by as much as 20%
Comparison to measured radiation pulse close-out is reasonable (similarity not met)
EAST Emission data vs. MEDLI2 backshell data
(note densities and relaxation distances are not same)
2.7 mm
4.3 mm
Chart: Velocity (km/s)
| 1.9951157766450549 | 2.0629287184135188 | 2.0437809437346712 | 1.3902354264600219 | 1.3022906652784829 | 1.1656976701167081
4.3 um | 1.885 | 0.27583 | 0.21897 | 0.087965
2.7 um | 0.079482 | 0.00072257 | 0.1863

## Slide 27: Understanding Measurement Artifacts

## Slide 28: Shock History Artifacts
As shock wave decelerates, flight similarity assumption breaks down
  Positions further behind the shock were “created” at higher initial enthalpies upstream
Oxford’s LASTA code predicts the deceleration impact given a measured velocity vs. position in the tube
Different post-shock states are obtained versus distance behind the shock front
Post-shock state can be evaluated as either (chemical) equilibrium or frozen
A 0-D reactor is simulated starting from the frozen condition to get the post-shock state
Use similarity in Lagrangian time
Flow velocity
in the lab frame
Distance particle moved
Dx
Dt
nCO2
nCO
T
Reacting LASTA Sim

## Slide 29: Emission prediction corrected for shock history
Using LASTA frozen predictions matches the radiance measured at 2.3 km/s
LASTA correction does not substantially alter reacting case
Impact on TDLAS?
(Frozen)
(Reacting)

## Slide 30: Boundary Layer Impact on Absorption
Shock Location
(x = 0)
u2
Shot #14
Cold CO2 in the boundary layer may contribute to absorption signal
Boundary layer profile is calculated using similarity solution from Mirel’s theory.
Numerically solve in shock fixed coordinates
Including boundary layer did not alter emission data
Sum simulated absorbance along each x
LOS
Boundary
Layer
Core
The R(58) line of CO2 is primarily affected by the cooler boundary layer

## Slide 31: Frozen Case, Both Corrections
Fit of emission data yields temperature and density consistent with TDLAS and LASTA code
LASTA number density is within the uncertainty of TDLAS measurement

## Slide 32: Reacting Case, Both Corrections
Temperature from emission, TDLAS and LASTA are all consistent with DPLR (Ebrahim rate)
Density decreasing behind shock front observed in Emission and TDLAS, predicted by LASTA
Absorption density is increased with boundary layer correction, agrees within error
Corrections still need to be demonstrated on larger dataset

## Slide 33: Conclusions and Observations
MEDLI2 returned full data set of backshell and forebody heating
  Radiometer was blocked with ablation products but the lee-side heat flux gauge is a good indicator of radiation
  Predictions show sensitivity to chemistry, entry trajectory
Reconstruction of MEDLI2 backshell is attempted in EAST 4” (10 cm) Tube from 1.1-3.5 km/s
  Higher pressures (1.1-2.0 Torr) are representative of time after peak heating (92-140s)
  Particle time in EAST is ~0.5 ms, equivalent distance of 0.1 m is lower than flight scales for backshell radiation
Chemically frozen on experimental timescale < 2.7 km/s
  Emission data tends to exceed frozen result at shock front
  TDLAS agrees well with frozen temperature and number density
Reactions observed >2.7 km/s
  Emission lies between the two reaction models, but trends toward “Cruden” model at higher velocity and pressure
  TDLAS temperature/CO density agrees well with Johnston model initially, then falls between the two CO2 reaction models
  TDLAS CO2 number density lower than simulation in reacting regime
Measurement artifacts
  Emission underprediction may be explained by including deceleration in shock tube (LASTA code)
  Underestimate of core flow CO2 density in TDLAS is explained by boundary layer absorption
  Considering boundary layer absorption and shock deceleration together brings measurements into agreement
Data supports need for refinement of CO2 reaction model

## Slide 34: Backup

## Slide 35: High Pressure Tests
Shots at 9 Torr attempt to induce chemistry on experimental time scale
  Not accomplished at 2.3 km/s: Radiance increasing (probably deceleration effect)
  Not accomplished at 2.5 km/s: Radiance exceeds frozen by ~10%
  Chemistry observed at 2.7 km/s: Agrees with Ebrahim
TDLAS was optically thick, not useful for analysis

## Slide 36: High(er) Velocity Test
High(er) Velocity emission data appears consistent with Ebrahim/Cruden rate
High Velocity TDLAS temperature agrees wtith Park/Johnston
Two measurements show conflicting results

## Slide 37: Bonus Test #1 Low V/P
Tests to observe V-T relaxtion (<2 km/s, 0.5 Torr)
TDLAS shows reasonable agreement to Park v-T
  Note this is Tv of n2 (bending)
Emission still shows offset (higher intensity) than frozen or TDLAS data
  Emission depends on Tv of n3 (asymm. stretch)
High resolution emission measurement
*
* Number density was fixed to get good 2T fit

## Slide 38: Attempts to measure CO2 “Continuum”
TDLAS measurement at frozen condition shows good agreement to CDSD prediction
High-resolution emission detects something but mostly below detection limit
Shot #9, Uis = 3.4 km/s
Shot #11, Uis = 2.51 km/s
CO absorption
Vibrationally hot CO2
absorption