## Slide 1: Inherited items process 2.0
Dr. Jesse Leitner
Chief SMA Engineer
NASA GSFC
Jesse.Leitner@nasa.gov
321-352-7966

## Slide 2: Outline
Inherited items process overview
Phased approach
Comparison to traditional piece-part approach
Related items

## Slide 3: Inherited items process overview
Application: products that are inherited and currently built, COTS, to be built-to-print, or otherwise cannot be changed
Purpose of process: Most such items are built to to different standards and/or level of oversight is disruptive to the development
The reason for our traditional requirements:
  Based on one-of-a-kind developments
  Since there is no basis for reliability, reliability is assured as a by-product of quality measures, piece-part controls, and reliability analyses
Process has been based on an inherited item risk assessment (I2RA), which is linked to the established reliability of the item combined with what has changed
  Flight history of the item
  Changes in item or development process from prior flights
  Changes in the environment
  Lifetime comparisons
  Flight anomalies that affect lifetime
  Vendor performance and capabilities for the same or similar items

## Slide 4: Inherited Items Process 2.0 breakdown
Process will be divided into two phases
  Phase 1 is mandatory and is entirely handled within SMA
    SMA will determine promptly which items are inherited and determine which path will be used for the product based on Code 300 policy (designated products)
    Only (and all) SMA items in the project MAR are affected
      Project may choose to use the process for items outside of the MAR at their discretion, and we (300) will support as requested
    Phase 1 products will be based on basic principles (next chart)
      The Phase 1 SMA approach (contract items) will be delivered within 1 week of obtaining limited information (subsequent charts). This will be denoted the “Phase 1a” report.
      The Phase 1 final assessment (Phase 1b) will be delivered based on workload and priority, but does not affect contracts
    Any holdups will necessitate the inclusion of the Code 300 chief engineers (SMA CE, 370 CE, Asst Director/Technical)
  Phase 2 is optional and may include or require participation from engineering, with potential for multiple products
    Overall risks of using the product
    Identification of special operational considerations
    Those needed for compliance to COTS and inherited items elements of NPR 8735.2
Products used outside of their datasheets, qualification ranges, or known capabilities will prompt a special actions process involving systems engineering and will not be considered designated products
The SC CRAE is now the SMA technical authority (under the CSO) for all standard components, with overarching responsibility for SMA for the items

## Slide 5: Basic Phase 1 principles (apply to products used within their bounds and qualification ranges)
Changing processes for a proven product is unlikely to improve, but more likely to degrade the product
Changing processes for a proven product is most often not possible to do and doing so or attempting to do so will not only increase risk, but will substantially increase cost and development time
GMIPs inserted into a standard build only cause a distraction from the standard build process and should only be attempted if there is a history of quality escapes that have entailed mission risk that GMIPs have caught for the product. Review of records for common standard components has not revealed any such escapes.
Changing parts or part screening practices for a proven design or system will add both risk and cost to the system and likely will not be feasible
Reliability analyses are needed only if a design is unproven
The MAR requirements can be categorized as safety, quality, or reliability, but the purpose of quality requirements is to achieve reliability
  Established standard products are already proven reliable and thus should not be assessed from a piece-part, one-of-a-kind design perspective

## Slide 6: Determination of Applicability (Phase 1 is automatically applied as standard SMA policy)
Standard or reused product has history in multiple missions and/or indicates noncompliance(s) in MAR compliance matrix
The process is requested
Item built to print either to different standards or has inability to apply government surveillance
Item already existing
The SC CRAE as the TA over standard products has right to refusal upon initial review
Applicable items will be denoted designated products

## Slide 7: First steps
CSO or designee constructs product list based on applicability
  CSO will ask the following question to the developer SMA lead: “Do you have any products that either already exist or for which it is not reasonable to flow down requirements from the MAR because they are standardized, commercially procured on fixed price contracts, or are commercial-off-the-shelf?” Positive response items will be initially declared designated items.
CSO or applicable HQE verify product datasheet/spec sheet compliance to project application levels (will not hold up Phase 1 deliverables), e.g.
  38V limit on product and 32V +/- 3V application voltage
  max current 5A on product with application current 3A
  product used within temperature limits, product proven in same environment for comparable lifetime
  If there are violations, they must be addressed upon discovery, see “Special Cases”
Standard component CRAE is member of the project SMA team responsible for data collection by interface with contractor SMA representatives
  The role is analogous to that of a parts engineer, materials and processes engineer, or quality engineer

## Slide 8: Specific requests: Parts
Parts that have been changed from previous designs
Specialized or custom parts that have been historically produced by one manufacturer but changed to another. Examples:
  Custom Presidio M123-inspired capacitor now produced by AVX
  JANS Microsemi MOSFET replaced with Wolfspeed SiC MOSFET
  Very low ESL Kemet MLCCs replaced with Vishay very low ESL MLCCs
Any general, but major, changes in parts practices
  Changes in BGA or CGA approach
These do not affect Phase 1a product

## Slide 9: Short-term overall requests
On-orbit failure (catastrophic) time(s) and cause if known
Major environmental differential from past experience
Longest achieved lifetime in similar orbit
This is not intended to identify every anomaly that may have been tied to the component, but rather to address its overall reliability based largely on whether the item has failed or seriously degraded. Operational anomaly details are pertinent to the Phase 2 process, if selected. The results do not affect the Phase 1a product.

## Slide 10: Specific requests: Printed Circuit Boards and workmanship
Change in spec (other than moving to current rev)
  Switch from Class 3 to Space Addendum
  Changes in the board design
    Layout
    Routing
    Added or removed reference designators
Change to HDI design or changing HDI features
  Microvias or via-in-pad that weren’t present before
  Additional board layers
New major special restrictions on board materials
  Switch to halogen free
Major changes in soldering approach
  Switch to lead-free solder
These do not affect Phase 1a product

## Slide 11: Materials and Processes
Major materials approach changes
  Full switch to ROHS compliance
Switch to additive manufactured items
These do not affect Phase 1a product

## Slide 12: GMIP criteria (no vendor info needed except flight history)
For standard components with at least 10 past flights, minimum 1 at required mission lifetime and no prior instances of NASA catching quality escape that involved risk that vendor QA missed
  No GMIPs
For standard components that have had at least three prior NASA projects with no identified instances of NASA catching quality escape that involved risk that vendor QA missed
  No GMIPs
When standard component history is not sufficient or available, vendor history of 10 past similar products with similar lifetimes no identified instances of NASA catching quality escape that involved risk that vendor QA missed
  No GMIPs
COTS inherited items (not be confused with COTS parts inside): no GMIPs. Lack of past reliability history will be used to establish risk.
Other commercial fixed-price procurements: closeout photos on internal boards. Project decides if they want to wait for approval after review or not.
Cost plus contracts with limited prior history or quality escapes caught only by NASA, GMIPs as negotiated.
These are guidelines subject to SC CRAE interpretation and tailoring

## Slide 13: Reliability analyses
Reliability analyses are needed when a system does not have proven reliability
Reliability analyses are only required when
  There is no established history
  There is a major change in some element that has to be propagated through the system to characterize risk

## Slide 14: Special cases
An unestablished COTS (or otherwise unchangeable) product is in the system
  This will be common to have some in Class D, sub-Class-D, and in technology demonstration missions in general
  When such products are used, the risk should be characterized based on other products from the supplier and fault-tolerance in the system (This would apply only to Phase 2)
    For Class D and below, and tech demos, it will often mean flying with acknowledged elevated risk
    For Class A - C missions, such products should be avoided for critical components providing critical functions (i.e., no backup to maintain the function)
  If available, a reliability analysis of the product may be used to better characterize the risk
Use of product in a new and challenging environment that is outside of the datasheet/qualification bounds
  Primarily this would involve a new radiation environment or using the product at extremes (e.g. temperature) that it wasn’t designed for.
  In some sense, this is no longer an inherited item, it is a new item that requires qualification, although the phase 2 process can be used to determine to what extent a new qualification is required
Item will be no longer be a designated product upon discovery that either case applies

## Slide 15: Timeline
Phase 1 SMA approach (Phase 1a) memo must be complete before contracts are let by the government or the prime for the inherited items.
  Ideally, once designated items are identified, process should begin
  When possible, complete the bulk of the process before any contracts are awarded for items that are specifically identified in the proposal or existing in hand
  Goal - no more than one week for completion of Phase 1a SMA approach for any item, even when items are processed in parallel, but Phase 1a product completed before pertinent contracts are let
    Phase 1 complete assessment (1b) completed based on workload and priority (not needed for contracts)
Phase 2 process, when selected, will be on a longer and adjustable timeline, driven by needs, constraints, and information availability

## Slide 16: Inherited items process is an SMA implementation per Code 300 policy
Designated items fall under SC CRAE, all other items are covered by the other discipline areas
Does not require engineering inputs
  Identifying ”overall risk of using the item” would be an optional part only in Phase 2
Similar information needed for waivers, so waiver process will always be a much greater burden, with no value added
Entire Phase 1 process can be handled within Code 300
  If project SMA cannot obtain items such as flight history either internally or by requests to contractors, then the same risk would apply in a waiver process.
  Such items are needed to understand risk
If engineering would be involved in waiver process, then they have the option of being involved in inherited items process in the same way.

## Slide 17: In what instance is engineering involvement required?
When there is a major change in one of the key discipline areas such that circuit details are needed to characterize risk
  Reliability analyses may provide enough information to assess such risks
Such major changes will almost always entail a significant engineering change in the item that would not affect the implementation of SMA requirements, and thus would be resolved over time as part of a qualification or qualification by similarity process
  Thus, these types of changes would not affect the SMA approach (Phase 1a) memo (SMA relief recommendations)

## Slide 18: Phase 1 product
SMA approach memo (phase 1a) produced in about 1 week (prior to need for contracts), which includes
  GMIPs approach
  Parts approach
  Printed circuit boards approach
  Materials approach
  Workmanship approach
  Reliability analysis approach
Full Phase 1 assessment report (phase 1a and phase 1b) delivered based on priority and workload, which includes
  Any determinations of risk from the initially-provided data set
    Differences in environment or usage outside of datasheet or design limits, or proven lifetimes in comparable environments
  Any specific recommendations to the project for follow-up
  Possible recommendation for Phase 2

## Slide 19: Phase 2 product
Provides the full set of background information
  Select elements of the commodity usage guidelines
Might address some items outside of SMA-driven risks
Considers the most mature set of information
Can be used to address COTS/inherited elements of NPR 8735.2, Hardware Quality Assurance Program Requirements for Programs and Projects

## Slide 20: Externally performed I2RAs
We will work with partners and developers and encourage them to use or form their own process
Main points to agree upon:
  What are the thresholds required for processes such as GMIPs
  The content and construct of a risk statement, should be consistent with GPR 7120.4, Risk Management

## Slide 21: Technical authority
The standard components CRAE is the defined SMA technical authority (under the CSO) for all designated products.
  This includes all aspects of quality, reliability, parts, materials, and processes
  Similar to MPCB CRAE’s TA over bare printed circuit boards, lead parts engineer’s TA over EEE parts, or MPE’s TA over materials and processes that are not in designated items.

## Slide 22: Summary
Inherited items 2.0 is based on the principle that a manufacturer whose products have proven reliability can be trusted to deliver standard products without outside interference in their processes.
Standard and COTS components that are established as reliable are now called out as a specific commodity analogous to parts, materials, and printed circuit boards.
Standard and COTS components determined to be designated items will be under the Standard Components CRAE as the technical authority and the responsible SME within each project’s SMA program.
A designated item follows an alternative path within a project’s SMA program via the Inherited Items process.
Phase 1 of the process is mandatory. Phase 1a will provide all necessary input to establish basic SMA requirements in contracts.
Phase 2 of the process is optional and based on providing a holistic risk picture for the product and aid to obtain compliance to NPR 8735.2.