## Slide 1: SPACE ROS: ARCHITECTURE ROADMAP
Contributors:
Paul Tompkins, Blue Origin
Austin Probe, NASA
Amalaye Oyake, Blue Origin
Will Chambers

## Slide 2: Overview
Statement of Objectives
Driving Reference Applications
Technology Need
  NASA Taxonomy
  Community Input
Deployment Configurations
  Middleware Solutions
  Space ROS Deployment
Benchmarking
  Benchmarking Objectives
  Test Matrix Summary
Space ROS Development
  Governance
  License
  Pull Request Acceptance
  Community Guidelines

## Slide 3: Statement of Objectives
Develop a space-certifiable and reusable robotic framework
  Designed to meet flight software standards: Designed to be aligned with NASA so that it could be adopted for a Class A Mission
    Memory Safety
    Deterministic Performance
    Static analysis
    System Testing
Support characteristic space robotics applications
Enable rapid development of new robotic capabilities
Enable reuse of capabilities between missions

## Slide 4
Teleoperation
Autonomy
Mining & Excavation
ISRU
OSAM
Future Surface
Habitats
Distributed
Edge
Computing
Collaboration
Networks & Communications
Positioning Systems
Maintenance & Repair
Future Robotic Systems
Rovers
Toward a Common In-Space Command, Control, Communications and Compute Infrastructure
Human Controlled Robotics
Flying Robots
Spacecraft Autonomy
S/W Control
Framework

## Slide 5: Driving Reference Applications
A set of reference applications act as a litmus test for:
  Early assessment of existing (and missing) ROS features for space
  Identifying the driving attributes of Space ROS to achieve “typical” / projected space robotic systems
Objectives:
  Establish a systematic approach to specifying space robotics applications that motivate the definition of essential Space ROS features
  Identify a set of space robotics applications that collectively motivate the majority of features we hope Space ROS to embody
This package:
  Proposes an application spec template for uniform treatment of candidate applications
  Provides preliminary specifications for a number of space robotics applications
With a first round of feedback, we can expand concepts more thoroughly

## Slide 6: Surface: Cargo Offloading
Description
  Robotic lift, translation and placement of cargo from lander deck to surface
Key Elements
  Robotic Crane
  Lander
  Payload(s)
  Mission Control (Earth)
Technical Attributes
  Perception
    Payload location/segmentation
    Lander structure perception
    Surface characterization
  Planning
    Manipulator trajectory planning
    Payload surface placement planning
  Manipulation
    Payload grapple
    Payload translation under gravity and dynamics
    Payload surface placement amongst terrain features
  Control and Coordination
    Earth-based human supervision
    Interleaved lander and robotics tasks (e.g. payload umbilical and mechanical release)
    Possible payload health monitoring before/during/after crane operation
  Communication
    Crane-Lander: hardline (serial, Ethernet)
    Payload-Lander: hardline (via severable umbilical)
    Lander-Mission Control: RF
    EXTENSION: Payload-Crane (via grapple fixture?)

## Slide 7: Surface: Resource Prospecting
Description
  Mobile survey to characterize regions for amenability for later resource extraction
Key Elements:
  Mobile robotic resource prospector
  Instruments
  Drill
  Orbital (or surface) communications relay(s)
  Mission Control (Earth)
Technical Attributes
  Perception
    Natural terrain characterization (traversability) in low light (lunar)
    Detection of suitable drive paths and sampling sites
    Novel feature/signal detection
  Planning
    Traversal planning considering remote sensing (resource maps), lighting, communications
    Activity planning considering battery state of charge, intended activities and resource costs
  Mobility
    Control under rover kinematics and surface terramechanics
    Terrain obstacle avoidance
    Instrument, manipulator and/or drill placement
  Manipulation
    Possible active regolith interaction (scooping, scraping)
    Drilling / subsurface access
  Control and Coordination
    Earth-based human supervision
    Rover, instrument, manipulator and/or drill coordinated control
  Communications
    Prospector-Instruments: hardline (serial, Ethernet)
    Prospector-Drill: hardline (serial, Ethernet)
    Prospector-Mission Control: RF (direct-to-Earth)
    Prospector-Comm Relay: RF
    Comm Relay-Mission Control: RF

## Slide 8: Surface: Site Preparation
Description
  Terrain preparation and foundational construction in support of advanced surface operations, including:
    Landing
    Habitat emplacement
    In-situ resource utilization
Key Elements
  Robotic Regolith Movers (robot team; TBD composition and roles)
  Mission Control
Technical Attributes
  Perception
    Site characterization, including terrain volumetric assessments
    Terrain mechanical resistance, mass
    Other robot detection
  Planning
    Robot team-based excavation, deposition and leveling planning
    Local route planning
    Activity planning considering battery state of charge, intended activities and resource costs
  Mobility
    Control under rover kinematics and significant surface interactions
    Terrain obstacle avoidance
    Tool / manipulator placement and control under motion
  Control and Coordination
    Robot team coordination (loose and potentially tight coordination)
    Earth-based human supervision
  Communication
    Robot-Robot: RF / WiFi
    Robot-Mission Control: RF

## Slide 9: Surface: Orbital Station Unpressurized Robotics
Description
  External (unpressurized) service tasking in support of orbital space station operations
Key Elements
  Station Modules
  Visiting Vehicles
  Orbital Replacement Units
  Mission Control
  Crew Workstation
Technical Attributes
  Perception
    Proprioception (self-configuration)
    Obstacle detection (module hulls, visiting vehicles, external payloads and equipment, astronauts)
    Force/moment detection (contact)
  Planning
    Arm trajectory planning
    Task planning
  Mobility
    Control under arm kinematics, base contact and payload mass properties
    Station obstacle avoidance
  Manipulation
    Closed-chain grappling/initial contact, ungrappling
    Free-flyer grappling/initial contact, release
    Maneuvering “payloads” under arm kinematics and joint payload/station/arm contact avoidance, force and torque limits
    Emergency halt in face of unexpected contact or resistance
  Control and Coordination
    Earth-based human supervision
    Direct human control
    Station GNC coordination (collaborative mode switching, motion control, fault response)
    Visiting vehicle coordination (collaborative mode switching, motion control, fault response)
  Communications
    Station-Manipulator: hardline
    Station-Visiting Vehicle: RF and/or hardline (state-dependent)
    Station-Crew Workstation: hardline
    Station-ORU: hardline (via standard quick connect/disconnect interface)
    OPTIONAL: ORU-Manipulator (for health monitoring/status)
    Station-Mission Control: RF

## Slide 10: Technology Need

## Slide 11: NASA Technology Taxonomy - Overview
This taxonomy identifies, organizes, and communicates technology areas relevant to advancing the agency’s mission.
Provides a structure for articulating the technology development disciplines needed to enable future space missions
We identify several of the NASA Technology areas where Space ROS can have the most meaningful impact
https://www.nasa.gov/offices/oct/taxonomy/index.html

## Slide 12: NASA Technology Taxonomy - 04 Robotic Systems

## Slide 13: NASA Technology Taxonomy - 07 Exploration Destination Systems

## Slide 14: NASA Technology Taxonomy – 10 Autonomous Systems

## Slide 15: NASA Technology Taxonomy – 11 Software, Modeling, Simulation

## Slide 16: Community Feedback
NASA solicited feedback on the Space ROS concept from the space robotics and autonomy community
Responses were received from 30 companies, universities, and individuals
Chart: Country of Origin
| Australia | Belgium | India | Italy | Japan | Poland | Sweden | USA | (blank)
Total | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 26
Chart: Organization Type
| Comercial | Government | Individual | Non-Profit | University | (blank)
Total | 20 | 2 | 2 | 3 | 6

## Slide 17: RFI Takeaways: Statistics
Chart: 
| Single Robot | Multi Robot
Robotic Cardinality | 0.83333 | 0.55556
Chart: Mode of Locomotion/Mobility
| Wheel | Track | Prop | Aerial
Mode of Locomotion/Mobility | 0.44828 | 0.17241 | 0.2069 | 0.10345
Chart: 
| Vision | Lidar | Camera | GNSS | IMU
Mode of Perception | 0.48485 | 0.48485 | 0.30303 | 0.21212 | 0.24242
Chart: 
| LEO | Lunar | Surface | GEO
Operational Environment | 0.41935 | 0.41935 | 0.32258 | 0.29032

## Slide 18: RFI Takeaways: Statistics
Chart: 
| Single Arm | Muti Arm
Degree and Mode of Manipulation | 0.4 | 0.26667
Chart: 
| Autonomous | Teleoperation | Full | Semi
Degree of Autonomy | 0.60714 | 0.39286 | 0.25 | 0.071429
Chart: 
| Central | Distributed | Hierarchical
Control Topology | 0.48276 | 0.48276 | 0.17241
Chart: 
| Inter-Process | Inter-Robot | Ground
System Communication | 0.58621 | 0.44828 | 0.13793

## Slide 19: RFI Takeaways: Statistics
Chart: 
| Inter-Process | Inter-Robot | Ground
System Communication | 0.58621 | 0.44828 | 0.13793
Chart: 
| Real-time | Safety | Non-real-time | Mixed
Processor Considerations | 0.44118 | 0.35294 | 0.29412 | 0.26471
Chart: 
| Arm | GPU | FPGA | x86
Sensor Data processors | 0.5 | 0.5 | 0.28571 | 0.071429
Chart: 
| Camera | GNSS | Lidar | Force
Sensors and Actuator Drivers | 0.40741 | 0.18519 | 0.14815 | 0.14815

## Slide 20: RFI Takeaways: Statistics
Chart: 
| ROS2 | cFS
Software/Framework Interoperability | 0.6875 | 0.25
Chart: 
| Fusion | Planning | FDIR | SLAM | Machine Learning
Algorithms | 0.6 | 0.46667 | 0.26667 | 0.2 | 0.13333

## Slide 21: RFI Takeaways: Space ROS
There is significant interest in a version of ROS2 that is capable of supporting space systems and robotics
  Operating in a resource constrained environment is critical
  Interactions with embeded systems is a concern for many respondents
  Security is important to organizations working with the DoD
Documentation and examples are a key to adoption
A significant portion of respondents are interested in supporting the development community

## Slide 22: RFI Takeaways: ROS Packages
The RFI requested what ROS packages would be valuable to the community
The following packages were mentioned in two or more responses
Package | Votes | Package | Votes | Package | Votes
tf2 | 11 | ament_index_cpp | 2 | Rclcpp | 2
ros_control | 6 | rostopic | 2 | image_geometry | 2
MoveIt | 6 | Eigen | 2 | diagnostic_updater | 2
RViz | 5 | interactive_markers | 2 | Rclcpp_action | 2
urdf | 5 | angles | 2 | kdl | 2
xacro | 5 | Pluginlib | 2 | gazebo_ros_pkgs | 2
robot_localization | 4 | joint_state_publisher | 2 | gazebo_msgs | 2
Gazebo | 4 | Rosidl_default_generators | 2 | geometry_msgs | 2
image_transport | 4 | rtabmap | 2 | Nav_msgs | 2
cv_bridge | 3 | behavior_tree | 2 | Visualization_msgs | 2
Std_msgs | 3 | Builtin_interfaces | 2 |  | 
Sensor_msgs | 3 | rqt | 2 |  | 
Trajectory_msgs | 3 | tracetools_test | 2 |  | 
rosbag | 2 | PCL | 2 |  | 
Dynamic_reconfigure | 2 | Robot_state_publisher | 2 |  | 
Rcutils | 2 | camera_info_manager | 2 |  | 

## Slide 23: Architecture Concepts

## Slide 24: Space ROS App Definition
Executes one or more system functions
Multiple communications interfaces
Comprised of several packages
Apps can leverage support package to provide more standardized FSW app implementation (template)
Space ROS App
Space ROS App Packages
Space ROS Core
Domain Algorithms
Hardware Interface
Server Endpoints
Services
Actions
Client Connections
Pub/Sub Interface
Cmd/Tlm
Support
Space ROS Standard App Support
Hardware Interface
Domain Algorithms
Space ROS Core
Logging
Alerts /
FDIR
App
Lifecycle
Standard App Support
App Specific Functionality
Application Type | Description
Node App | Space ROS App that communicates solely with the message Space ROS message bus
Interface App | Provides a Space ROS compliant interface to an embedded sensor/system. Can be used to provide an abstraction to the underlying system
Bridge App | Bridges Space ROS to other middleware implementations Could be mission agnostic and auto-generated

## Slide 25: Standalone vs. Federated vs. IMA
Space ROS is a software framework designed to be deployed across a wide set of use cases.
There are a number of ways Space ROS could be deployed:
Standalone
Federated: Loosely coupled with another framework (such as cFS)
Integrate Modular Avionics (IMA) : Tightly integrated within the same computing using with another framework

## Slide 26: Standalone vs. Federated vs. IMA
Standalone: A single unit that encapsulates the entire system functionality and uses Space ROS may increase mass because it is its own physical payload but will require Space ROS to meet the validation requirements for the mission independently.
Federated: an independent unit encapsulates Space ROS communicates with the Avionics. This may increase mass because it is its own physical payload but reduces V&V from the flight software team.
IMA: a unit that is tightly integrated with the underlying Flight Software will impose some V&V work on the flight software team, but may save mass, because the compute capability lives in the centralized flight software computer.

## Slide 27: Deployment Configuration Types
Augmented System
Single Vehicle
Multi Vehicle
Integrated
Shared
Space ROS Deployment
Avionics

## Slide 28: Augmented System Overview
Integrated Avionics
Shared Avionics
Bus Avionics
Bus Middleware Apps
Space ROS System N Avionics
Space ROS Apps
Space ROS System 1 Avionics
Space ROS Apps
Bus Avionics
Bus Middleware Apps
Space ROS System N Apps
Space ROS System 1 Apps
Bridge App
Bridge App
App 1
App 2
App N
…
…
App 1
App 2
App N
…
App 1
App 2
App N
…
App 1
App 2
App N
…
…
App 1
App 2
App N
…
App 1
App 2
App N
…

## Slide 29: Augmented System App Architecture
Space ROS
Subsystem
Radio
App
Radio
Sensor /
System
Bus
Interface App
Mngt / Utility
Apps
Space ROS
Node
App
Space ROS
Bridge
App
Payload
App
Payload
Sensors / Systems
Sensors / Systems
Space ROS
Interface
App
Bus
App
Space ROS
Interface
App
Space ROS
Node
Apps
FSW Middleware Message Bus
Space ROS Message Bus
Ground Link
Payload
Interface
App
Payload
Bus
Interface App
Sensor /
System

## Slide 30: Single Vehicle System Overview
Integrated Avionics
Shared Avionics
Bus Avionics
Space ROS
Bus Apps
Space ROS System N Avionics
Space ROS Apps
Space ROS System 1 Avionics
Space ROS Apps
Bus Avionics
Space ROS
Bus Apps
Space ROS System N Apps
Space ROS System 1 Apps
App 1
App 2
App N
…
…
App 1
App 2
App N
…
App 1
App 2
App N
…
App 1
App 2
App N
…
…
App 1
App 2
App N
…
App 1
App 2
App N
…

## Slide 31: Single Vehicle System App Architecture
Space ROS
Subsystem
Radio
App
Radio
Mngt / Utility
Apps
Space ROS
Node
App
Sensors / Systems
Sensors / Systems
Space ROS
Interface
App
Space ROS
Bus Node
Apps
Space ROS
Interface
App
Space ROS
Node
Apps
Space ROS
Subsystem
Space ROS
Node
App
Sensors / Systems
Sensors / Systems
Space ROS
Interface
App
Space ROS
Interface
App
Space ROS
Node
Apps
Space ROS Message Bus
Subsystems include
Payloads
  i.e robot arm
Bus Interfaces
  i.e. Electrical Power System
Reusable, mission agnostic apps

## Slide 32: Multi Vehicle System Description
Peer to Peer comms via RF link
Use Cases
  Heterogenous middleware environment
    Intervehicle communications via Multi Agent Interface Language
    Space ROS message domain does not extend beyond single vehicle
  Space ROS only
    Space ROS message domain extends beyond single vehicle
  Mixed?

## Slide 33: Multi Vehicle System Description
Spacecraft 2
Augmented System
Bus Software
Apps
Space ROS Subsystem 1
Apps
Space ROS Subsystem N
Apps
Spacecraft N
Single Vehicle Space ROS
Space ROS Subsystem 1
Apps
Bus Apps
Spacecraft 1
No Space ROS Present
Bus Software
Apps
Ground Station
Intervehicle Comms via RF
Ground Comms
Radio App
Radio App
Radio App
…
…

## Slide 34: Ground-only Space ROS System Overview
Ground Subsystem
Flight Subsystem
Ground Data System
Ground Software Apps
Space ROS Ground Subsystem 2
Space ROS Apps
Space ROS Ground Subsystem 1
Space ROS Apps
Flight Subsystem
Middleware
Bus Apps
Middleware System N Apps
Middleware System 1 Apps
Radio
Telem and Cmd Server
Ground Station
App 1
Bridge App
App 2
App N
…
…
…
App 1
App 2
App N
App 1
App 2
App N
…
App 1
App 2
App N
Radio App
…
App 1
App 2
App N
…
App 1
App 2
App N
…

## Slide 35: Shared Space ROS Ground and Flight System Overview
Ground Subsystem
Flight Subsystem
Ground Data System
Ground Software Apps
Space ROS Ground Subsystem 2
Space ROS Apps
Space ROS Ground Subsystem 1
Space ROS Apps
Flight Subsystem
Space ROS
Bus Apps
Space ROS System N Apps
Space ROS System 1 Apps
Radio
Telem and Cmd Server
Ground Station
App 1
Bridge App
App 2
App N
…
…
…
App 1
App 2
App N
App 1
App 2
App N
…
App 1
App 2
App N
Radio App
…
App 1
App 2
App N
…
App 1
App 2
App N
…
…

## Slide 36: Shared Ground and Flight System App Architecture
Space ROS
Subsystem
Radio
App
Radio
Mngt / Utility
Apps
Space ROS
Node
App
Sensors / Systems
Sensors / Systems
Space ROS
Interface
App
Space ROS
Bus Node
Apps
Space ROS
Interface
App
Space ROS
Node
Apps
Space ROS
Flight System
Space ROS
Node
App
Sensors / Systems
Sensors / Systems
Space ROS
Interface
App
Space ROS
Interface
App
Space ROS
Node
Apps
Space ROS Message Bus
Reusable, mission agnostic apps
Tlm and Cmd Server
Mngt / Utility
Apps
Ground Software
Apps
Ground Software Message Bus
Space ROS
Bridge
App
Space ROS
Ground System
Sensors / Systems
Data Stores / Servers
Space ROS
Interface
App
Space ROS
Interface
App
Space ROS Message Bus
Mngt / Utility
Apps
Space ROS
Bus Node
Apps
Space ROS
Node
App
Space ROS
Node
Apps
Ground Station

## Slide 37: Space ROS used for Testing and Simulation
Ground Subsystem
Flight Subsystem
Ground Data System
Ground Software Apps
Ground System Testing and Simulation
Space ROS Apps
N
Flight Subsystem
Middleware
Bus Apps
Middleware System N Apps
Middleware System 1 Apps
Radio
Telem and Cmd Server
Ground Station
Flight System Testing and Simulation
Space ROS Apps
Bridge App
App 1
Bridge App
App 2
App N
…
…
…
App 1
App 2
App N
App 1
App 2
App N
…
App 1
App 2
App N
Radio App
…
App 1
App 2
App N
…
App 1
App 2
App N
…
…

## Slide 38: Space ROS Benchmarking

## Slide 39: Benchmarking Objectives
We are working to evaluate the build of Space ROS under development to:
Characterize Space ROS performance
  Processor Utilization
  Memory
  Network throughput
  QoS Metrics
Compare Performance to other frameworks using Ames Distributed Space Autonomy Suite
  Compare to NASA cFS with reimplemented applications for Autonomy and Navigation
Space-like targets
  X86 Architecture e.g. Unibap iX5-100
  ARM Architecture e.g. ZCU-102

## Slide 40: Benchmarking Test Matrix Summary
Test Description | Metric Recorded | Metric Details
Message passing tests using but a fully connected and linear mesh network with: Ideal, 10% loss, 50% loss, and 90% loss, 100 ms latency and 500 ms latency network configurations | Deployed Application Size | DSA Apps + SpaceROS Compiled File Size
 | CPU Utilization | SpaceROS CPU Utilization, max, min, mean, variance
 | Memory Usage | SpaceROS Memory Utilization, max, min, mean, variance
 | Topic Latency | Latency between nodes reward and assignment messages, max, min, mean, variance
 | Inter Container Latency | Latency between AUTO nodes Auto Sat State Message
 | Inter Container Packet Loss | Number of AUTO Sat State Messages not received.
 | Total State Messages Ignored | When a message is delayed to long it is just ignored so this combined both dropped packets and ones whose latency was too large.
A full test matrix has been developed for evaluating Space ROS in both a containerized development environment and in a processor-in-the-loop environment on target hardware including:

## Slide 41: Space ROS Community

## Slide 42: Space ROS Community Governance
Space ROS will seek to leverage ROS
  Space ROS trademarks being transferred to Open Robotics
  Following ROS2 Governance Guidelines: https://docs.ros.org/en/galactic/Governance.html
Space ROS will form a Technical Steering Committee (TSC) to prioritize feature selection
  Member slots available in exchange for TBD FTE support (e.g. 0.5 FTE-1 FTE)
  Membership is available to organizations and missions
Space ROS will attend relevant community events to advertise and seek community input
  e.g. ROS Con, FSW Workshop

## Slide 43: Governance and Post ACO Operations
Technical Steering Committee
Technical Steering Committee
  Volunteers to identify priorities and features
  Looking to identify members of government and industry groups to serve as members
Project Manager x1
  Interfaces with the community manages pull requests
Testing and Continuous Integration Management x2
  Maintains testing and V&V infrastructure
  Supports maintaining compatibility with ROS2
NASA
ESA
LSIC
etc.
Project Manager
Test/CI
Test/CI

## Slide 44: Space ROS Public Working Group
We are proposing a working group meeting separate from the ACO effort to integrate external partners into Space ROS development
  Companies and organizations who have expressed interest in supporting development
  Companies and organizations who responded to the RFI
  Allow for Will Chambers to maintain involvement
Open Questions?
  Meeting cadence
  How quickly to invite new people

## Slide 45: Space ROS Community Pull Request Acceptance Policy
TSC identifies pull requests for inclusion
Pull requests must Space ROS testing requirements
  Tooling for tests will be included in the repositories
  Static analysis testing
  Full DRM based scenario testing
TSC will identify what features from ROS2 can be incorporated into Space ROS and provide prioritization

## Slide 46: License
Space ROS will adopt ROS2 licenses
Largely Apache 2.0 and Space ROS will continue to
  Permissive
  Commercially Useable
Some Creative Commands and BSD licenses for tools and documentation

## Slide 47: Acknowledgments
This work was funded as a collaborative effort between NASA Goddard Space Flight Center, Ames Research Center, Johnson Space Center, and Blue Origin