## Slide 1: Discrete Roughness Boundary-Layer Transition at Hypersonic Conditions
Scott A. Berry
NASA Langley Research Center
UCAH Seminar Series
October 25, 2022
Cleared for Public Release
Notes: Provides a review of several examples of ground-based boundary layer transition studies completed in support of agency programs with comparison to flight results if available

## Slide 2
Presentation Focus
A review of ground-based experimental studies into discrete roughness hypersonic boundary layer transition with comparison to flight results
Presenation Outline
Background and motivation
Ground-based studies & results
Corresponding flight observations
Summary
Cleared for Public Release
Notes: This presentation will focus on a review of some of the ground-based studies I’ve conducted during my career on discrete roughness transition, along with observations from corresponding flight experiments.

## Slide 3
Background
Shouldn’t be a newsflash to anyone but: hypersonic = hot!
And hypersonic + turbulence = even hotter!
Economic impact:
Thermal management critical technology to enable hypersonic vehicle design
To counter high surface temperatures and sustained heat load
Traditionally done using thermal protection system (TPS) on Shuttle and X-43
Hot structures (X-15) including internal cooling passages (SR-71) also an option
Weight penalty associated with either using TPS or an active cooling system
Thus, BLT effects can have direct impact on vehicle size and cost (think NASP)
Mission Impact:
Vehicle aerodynamics also influenced by BLT effects
Increased drag directly reducing vehicle range
Transition location can alter control surface effectiveness
Roll/yaw increments due to asymmetric BLT (Shuttle experienced this)
Safety Impact:
Vehicle robustness could impact crew safety scenarios, for instance
Launch abort constraints (such as low AoA return to runway requirements)
Damage/repair constraints (how much surface damage is tolerable?)
Understanding boundary layer transition (BLT) is critical to hypersonic design
Cleared for Public Release
Notes: One can make the case for the criticality of boundary transition to hypersonic vehicles from many perspectives.
Despite the general pessimism of the role of wind tunnels for transition studies, useful information can be obtained in wind tunnels and applied to flight programs.

## Slide 4
Motivation
The problem:
Vehicle designers require reliable and timely methods for predicting when (and how) transition will occur during hypersonic flight in order to quantify its impact on the local and acreage heating environments for TPS design
A practical approach:
Until a comprehensive physics-based approach for predicting hypersonic boundary layer transition is available, vehicle designers will continue to rely heavily on empirical transition prediction strategies derived from ground-based measurements
Premise:
Present (and future) TPS technology continue to be roughness dominated
  “… roughness is such an overriding transition bypass that research can be conducted in conventional, noisy, tunnels” [Bushnell]
“Effective”
roughness
element
Trip
station
“Incipient”
roughness
element
Trip
station
Cleared for Public Release

## Slide 5
Empirically Derived Correlations
Basic Research Cone Study
Shuttle RTF Studies
Hyper-X Trip Screening Studies
Berry et al., NASA TM-2000-210315
Cleared for Public Release

## Slide 6: Examples of Experimental Hypersonic Transition Research at NASA LaRC
X-33
Phase I
Slender (Me > 4)
Moderately Blunt (1 < Me < 4)
X-38
X-33
X-34
Shuttle
NASP 201
NASP 202
Hyper-X
Missiles
X-37
Classified
Classified
Cleared for Public Release

## Slide 7: VG investigation during NASP
Using layers of tape built up to act as vortex generators (VG)
Heating data (classified) showed VGs worked to trip BL
Unpublished – circa 1993
Cleared for Public Release
Notes: Inspiration came during Morkovin workshop.

## Slide 8
Shuttle Orbiter Asymmetric BLT Study
Issue: Asymmetric BLT had resulted in excessive propellant usage to correct Orbiter yaw during entry
Impact: Surface roughness correlation developed to predict boundary layer transition from isolated surface protuberances
See AIAA 97-0273
STS-28 Mach 18 BLT
Gap filler
Discrete roughness correlation with BLIMP boundary layer properties
Incipient
Effective
Cleared for Public Release

## Slide 9
Issue: Proposed metallic TPS could deform (bow) during entry due to temperature gradients within individual panels
Impact: Transition correlation used by X-33 program for entry trajectory tailoring to constrain laminar heating rates to within the capability of the metallic TPS and distributed roughness (bowed panels) was found to be less effective than discrete roughness of equivalent height in promoting transition
X-33 Technology Demonstrator
Cast ceramic model with panel bowing
X-33 metallic TPS panel layout
Re∞ = 4x106/ft
Re∞ = 3.1x106/ft
Re∞ = 4x106/ft
Smooth
Discrete
k= 0.005-in
Bowed Panels
k= 0.008-in
Discrete roughness correlation based on LATCH code for boundary layer properties
Note only centerline results shown, but results applicable for attachment lines also
k
See AIAA 99-3560
Cleared for Public Release

## Slide 10
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
Normalized heating
X/L
Untripped
Tripped (k = 0.005-in)
0
0.05
0.1
0.15
0.2
0.25
0.3
Normalized heating
Nondimensional fin chord length
Fin/rudder
interface
0
1
0.5
Tripped
(Turbulent)
k = 0.005-in
Untripped
(Transitional)
Untripped
Tripped
k = 0.005 in.
Boundary Layer trips
Issue: Thermal margin of body flap based on fully turbulent flow which may not be representative of local peak heating.
Impact: Improvement in an engineering model used to assess the thermal margin of the X-38 body flap in the presence of a separating/reattaching transitional flow (nonlaminar but not fully turbulent).
X-38 Crew Return Vehicle
See AIAA 2000-2685
Cleared for Public Release

## Slide 11
Single Row of 17 Holes (0.020-in D) with 1/8-in Spacing
Run 78
No Blowing
P
2
= 0.08 psi
Run 83
P/P
2
= 20
Run 81
P/P
2
= 80
Bow shock
Shock induced by blowing
Closed-cowl
Issue: To improve inlet and engine performance and to provide data relevant for a full-scale scramjet powered vehicle, turbulent flow ahead of X-43 engine inlet was required
Impact: Trips for both X-43 flight vehicles were selected based on the passive results obtained (not shown, see AIAA 2000-4012) and active blowing was found to be equally effective while having smaller jet-induced shock and flow separation than corresponding discrete trips
Trip array
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Trip Screening for Hyper-X
See AIAA 2004-2246
a = 2 deg
Cleared for Public Release
Passive
Active

## Slide 12
Issue: Quantification of tunnel disturbance environment and assessment of discrete versus distributed roughness
Impact: First comparison of transition onset locations between conventional and low disturbance hypersonic tunnels using common model and transition detection technique (not shown, see AIAA 2002-2743) and determination of relative trip effectiveness
Roughness on Slender Cones
Sharp Nose 5-deg Flared Cone
Mach 6 α=0 deg Re=4.4 million/ft k/δ=0.7
Sharp Nose 5-deg Straight Cone
Mach 6 α=0 deg Re=4.4 million/ft
Cleared for Public Release

## Slide 13
Columbia Accident Investigation (CAI)
Issue: Could asymmetric BLT from a damaged “rough” wing affected the Orbiter aerodynamics and accelerated the erosion of Columbia’s TPS tiles?
Impact: Simultaneous aerodynamic and heating measurements refuted “rough” wing hypothesis.
Impact: Closure achieved through wind tunnel tests that identified leeside flow-field perturbations (separation and reattachment) which replicated the temperature anomalies observed in Columbia data
See AIAA 2004-1387
Cleared for Public Release

## Slide 14
Consistent Correlation Approach
1
10
100
1000
0.1
1
10
Centerline Effective Transition Results
Computed with LATCH
k/
δ
LAMINAR
TURBULENT
C
eff
= 70 ± 20%
Shuttle
α
= 40 deg
X-33
α
= 20 deg
X-33
α
= 40 deg
X-38
α
= 40 deg
X-33
α
= 30 deg
Reθ
/Me
Consistent Method:
Facility
Test Technique
Computations
Correlation shown
applicable for different:
Configurations
Model α
Locations on body
Comparison of existing Orbiter, X-33, and X-38 BLT correlations
based on edge conditions (published in AIAA 2002-2744)
Thus, for moderately-blunt vehicles, discrete roughness correlations can be used to predict transition when a consistent method is used between development and application
Cleared for Public Release

## Slide 15
Shuttle Orbiter Return-to Flight (RTF)
Issue: If transition occurs above Mach 18, the Shuttle may experience unacceptably high internal structural temperatures
Impact: Development, in time for the first RTF mission, of Shuttle tile damage/repair thresholds that could trigger corrective action
(see AIAA 2006-2917 through 2922)
Cleared for Public Release
Notes: For protuberances, a pretty good correlation was developed with cosideration of the flight data
For cavities, a well-behaved correlation could not be developed in time for RTF, so instead we had to rely upon conservative thresholds

## Slide 16: Summary of Ground-Test Observations
Observations of similar discrete roughness transition onset and effective results on several different moderately-blunt (supersonic edge conditions) configurations
When a consistent computational approach used to correlate results, prediction of discrete roughness heights required to “trip” BL is possible
Thus, for moderately-blunt vehicles, discrete roughness correlations can be used to predict transition when a consistent method is used between development and application
For sharp configurations (hypersonic edge conditions), large trips required (on par with BL edge) to “trip” BL
Cleared for Public Release

## Slide 17
Flight
(Where the rubber meets the road!)
Hyper-X
Shuttle
Cleared for Public Release

## Slide 18: Flight 2 Measurements
Mach 7
Final trips sized for Mach 7 flight
Reθ/Me ≈ 300 ± 4%
From AIAA 2008-3736
Cleared for Public Release

## Slide 19: Flight 3 Measurements
Mach 10
Reθ/Me ≈ 280 ± 6%
From AIAA 2008-3736
Cleared for Public Release

## Slide 20: Return-to-Flight Overview
Columbia Accident Investigation directive to develop on-orbit TPS inspection and repair capabilities as part of the RTF effort
  Suite of tools developed/integrated to allow rapid assessment of TPS health (more on next chart)
BLT prediction based on physical mechanism approach would be ideal
  For Shuttle RTF, not ready for prime time
Most hypersonic vehicles have surfaces that by-pass natural instabilities, such as roughness (like Shuttle)
Shuttle BLT Tool developed with this in mind
  Utilized discrete roughness correlation approach
  Previously shown to capture WT trends for a variety of configurations (JSR 45.2 2008)
STS-114 exposed uncertainties with prediction of high Mach BLT, led to unprecedented repair
Shuttle BLT Flight Experiment (FE) developed to address high Mach BLT Tool uncertainties
STS-114 Repair
~24,000 Black Tiles
~20,000 Gap fillers
Shuttle offers wealth of hypersonic BLT data, with 135 missions flown
Next few charts taken from AIAA-2016-3533
Cleared for Public Release

## Slide 21: Mission Support Timeline
BLT Tool required to:
  Set proper aeroheating environment for subsequent thermal & structural analysis
  Rapidly determine time of transition onset for each and every damage site (~5-20 sites)
Within a typical 2-week mission:
  Photos of TPS damage from RPM by FD3
  Initial TPS assessment by FD4
  Further analysis, as required, using the OBSS starting on FD4
  Flight cleared to continue mission by FD7 (ideal)
Material
Temperatures
Bond Factor
of Safety
Structural
Margin and
Deflections
Damage
information
Trajectory
information
3D Thermal
Math Model
RTV Bond
Line Tool
Stress
Assessor
Tool
Cavity
Heating
Tool
XF0002
(Legacy Body-Point
Analysis Code)
Input
Tools
Output
BLT Tool
Damage Assessment Flowchart:
BLT Tool V1 ready before STS-114 (AIAA-2006-2918)
BLT Tool V2 update after STS-114 (AIAA-2010-0246)
Cleared for Public Release

## Slide 22: BLT Tool V2 Protuberance Correlations
All Shuttle high-Mach BLT experience has been due to gap filler protrusions
  Historical earliest was at Mach 18 during STS-28 and STS-73
Use of 2 correlations during mission intended to provide method to assess uncertainty
Note, bias observed between mean of WT & flight, tool utilized flight for BLT estimation
BLT FE developed to explore protuberance correlation bias using envelope expansion:
  Incremental increase in protuberance height over 5 flights
  Is there a limit to how early BLT can occur at hypersonic (& nonequilibrium) conditions?
Protuberance Correlation #1 (Req approach):
Protuberance Correlation #2 (Rek approach):
Cleared for Public Release

## Slide 23: BLT Flight Experiment
Protuberance designed integral to TPS tile and to minimize slumping
Location on port wing selected based on:
  Consideration of TPS thermal/structural margins
  Suitability for new instrument wiring
  Regions of minimal historical debris damage
New thermocouples added/moved, as shown per flight
k = 0.25” for STS-119
= 0.35” for STS-128 & STS-131
= 0.50” for STS-133 & STS-134
Cleared for Public Release

## Slide 24: HYTHIRM Shuttle Support
Missions Supported by HYTHIRM:
On Ground
At Sea
In Air
Hypersonic Thermodynamic Infrared Measurements (HYTHIRM)
Capabilities:
KSC 248
Observation
~Mach 16-13
STS-134 Reentry 6-01-11
Observation
~Mach 11-5
KSC 249
Mission Planning:
Weather Briefings
Sensor Upgrades:
Wider dynamic range
Improved signal-to-noise
Integration time controls
Mission success through rigorous planning and enhanced capabilities
Now SCIFLI
Cleared for Public Release

## Slide 25: STS-119
3D Mapped HYTHIRM Image @ Mach 8.4
Flown on Discovery
HYTHIRM image @ Mach 8.4 reveals 2 BLT wedges, one from an unknown source, the other from FE
Asymmetric wedge thought to be from GF about 0.18” high, but not found (assumed fell out on runway)
BLT FE TCs reveal extent and timing of transition from 0.25” protrusion:
  Onset at t=969s (or Mach 15.6)
  Fully effective at roughly t=1045s (or Mach 13.1)
  Wedge half-angle of roughly 7 deg
Cleared for Public Release

## Slide 26: STS-128
3D Mapped HYTHIRM Image @ Mach 14.7
Flown on Discovery
HYTHIRM image @ Mach 14.7 shows BLT FE wedge
TCs reveals port-side BLT at t=1040s, or Mach 13.6, thought to be from a noted forward-facing step found between tiles (~0.15” high)
BLT FE TCs reveal extent and timing of transition from 0.35” protrusion:
  Onset at t=916s (or Mach 17.3)
  Fully effective at roughly t=970s (or Mach 15.8)
  Wedge half-angle of roughly 5 deg
Cleared for Public Release

## Slide 27: STS-131
Flown on Discovery
HYTHIRM image @ Mach 15 shows BLT FE wedge
TCs reveals late BLT at ~t=1320s, or Mach 6.4
BLT FE TCs reveal extent and timing of transition from 0.35” protrusion (a repeat):
  Onset at t=932s (or Mach 17.3)
  Fully effective at roughly t=996s (or Mach 15.6)
  Wedge half-angle of roughly 5 deg
3D Mapped HYTHIRM Image @ Mach 15
Cleared for Public Release

## Slide 28: STS-133
3D Mapped HYTHIRM Image @ Mach 18.1
Flown on Discovery
HYTHIRM image @ Mach 18 shows BLT FE wedge
  Highest Mach observation
TCs reveals late BLT at ~t=1220s, or Mach 8.5
BLT FE TCs reveal extent and timing of transition from 0.5” protrusion:
  Onset at t=829s (or Mach 19.6)
  Fully effective at roughly t=930s (or Mach 16.9)
  Wedge half-angle of roughly 3 deg
Cleared for Public Release

## Slide 29: STS-134
Flown on Endeavour
HYTHIRM image @ Mach 6.2 shows BLT FE wedge
TCs reveals late & asymmetric BLT at ~t=1270s, or Mach 6.8
BLT FE TCs show transition onset from 0.5” protrusion (a repeat):
  Onset at t=840s (or Mach 19.4)
3D Mapped HYTHIRM Image @ Mach 6.2
Cleared for Public Release

## Slide 30: STS-134
Series of HYTHIRM Images showing evolution of hypersonic BLT during reentry
M=6.9 a = 33.4 deg
L = 6-in, W = 1-in, D = ~ 0.15-in
Streamlines from CFD
Unprecedented detail showing flow features not observed with on-board TCs
For instance, take cavity case shown at left, based on the IR video data only:
  Onset at t=1261s (or Mach 7.1)
  Fully effective at t=1269s (or Mach 6.9)
  Wedge half-angle of ~8 deg
BLT Tool V2 prediction of Mach 8.4 based on cavity volume
(c)
(e)
~16 deg
Other damage sites
Cleared for Public Release

## Slide 31: Comparison of TC Traces
Some TC traces reveal anomalous behavior due to high-Mach roll maneuvers
  Roll-reversal anomaly previously discussed in AIAA-2010-240, not well understood
Looking past anomalies, BLT onset times change systematically with trip height
  BLT onset based on TC#1 critical for comparison to correlations
  TC#2 provides similar (but delayed) trends
BLT earlier than Mach 18 (& at nonequilibrium conditions) shown possible with STS-133 and STS-134 results
TC#1
TC#2
Incipient
Critical
Cleared for Public Release

## Slide 32: Correlation Comparison
Both protuberance correlations shown to compare well against BLT FE data
  Corr#1 (Req-based): within 15% of accepted correlation used for flight
  Corr#2 (Rek-based): within 30% of accepted correlation used for flight
Combined analysis uncertainty of 9% based on RSS of:
  Experimental: trip height & location (<1%) and BLT onset determination (~4%)
  Computational: error of interpolating BL properties from existing database (<8%)
WT to flight bias shown to be real phenomenon, no longer attributable to uncertainties with the quality of the historical data
Correlation#1
Correlation#2
Cleared for Public Release

## Slide 33: Shuttle Summary
Hypersonic BLT an enabling technology for future high-speed systems
Shuttle required a reliable & quick method to predict BLT
  Discrete roughness approach utilized
  Uncertainty with WT to flight bias unexplained during RTF development
BLT FE proposed to reduce uncertainties with tool predictions and improve technological “state-of-the-art”
  Limit to how early BLT can occur?
  Is WT to flight bias real?
Incremental trip height expansion resulted in systematic (& predictable) change in BLT onset times
  BLT shown to occur at Mach 19.5 (nonequilibrium conditions)
  New flight cases shown in agreement with historical calibration cases based on comparison to correlations
  WT to flight bias maintained for these well controlled results
Cleared for Public Release

## Slide 34: Next Steps
Work continues to extend discrete roughness correlations shown applicable to moderately blunt (supersonic conditions at BL edge) to sharp configurations
  Recent BOLT II flight included discrete BL trips
    Flight data analysis underway with early results to be reported at SciTech23
  Wind tunnel testing completed to provide ground-based data for examinations of correlations
    Intend to look back at X-43 data as well
BOLT II @ WFF
March 21st, 2022
Test 7071 in 20” M6
July 2022
Cleared for Public Release

## Slide 35
Summary
Measurement technique advancements have permitted the experimental hypersonic aerothermodynamicist to have a practical and significant impact on the design process of several space transportation vehicles
  Screening of different trip concepts for promoting turbulence ahead of scramjet inlets and down select to the Hyper-X trips for both flight vehicles
  Development of empirical hypersonic surface roughness boundary layer transition criteria shown to be applicable over a range of angle of attack and surface location for a class of Shuttle-like (moderately blunt) vehicles
  Establishment of Shuttle Orbiter TPS damage and repair threshold for prevention of high Mach number boundary layer transition
Comparison of flight measurements to the ground-based results have thus far shown reasonable but qualitative agreement
Further reduction of uncertainties with flight boundary layer prediction methodologies can be accomplished through additional flight experiments
Cleared for Public Release

## Slide 36: Bibliography
AIAA 97-0273 - Boundary Layer Transition Due to Isolated Roughness: Shuttle Results From the LaRC 20-Inch Mach 6 Tunnel by Berry, Bouslog, Brauckmann & Caram
AIAA 99-3560 - X-33 Hypersonic Boundary Layer Transition by Berry, Horvath, Hollis, Thompson & Hamilton
NASA TM-2000-210315 - Forced Boundary-Layer Transition on X-43 (Hyper-X) in NASA LaRC 31-Inch Mach 10 Air Tunnel by Berry, DiFulvio & Kowalkowski
AIAA 2000-2685 - X-38 Experimental Aerothermodynamics by Horvath, Berry, Merski & Fitzgerald
AIAA 2000-4012 - Hypersonic Boundary-Layer Trip Development for Hyper-X by Berry, Auslender, Dilley & Calleja
AIAA 2002-2743 - Boundary Layer Transition on Slender Cones in Conventional and Low Disturbance Mach 6 Wind Tunnels by Horvath, Berry, Hollis, Chang & Singer
AIAA 2002-2744 - Discrete Roughness Effects on Shuttle Orbiter at Mach 6 by Berry & Hamilton
AIAA 2004-1387 - Experimental Aerothermodynamics in Support of the Columbia Accident Investigation by Horvath
AIAA 2004-2246 - Boundary Layer Control for Hypersonic Airbreathing Vehicles by Berry, Nowak & Horvath
AIAA 2006-2917 - Orbiter Return-To-Flight Entry Aeroheating by Campbell, Bourland, Bouslog, Horvath, Berry, Gnoffo, Reuther, Chao, Anderson & Picetti
AIAA-2006-2918 - Overview of Boundary Layer Transition Research in Support of Orbiter Return To Flight by Berry, Horvath, Greene, Kinder & Wang
AIAA-2006-2919 - Shuttle Damage/Repair from the Perspective of Hypersonic Boundary Layer Transition - Experimental Results by Horvath, Berry, Merski, Berger, Leichty & Schneider
AIAA-2006-2921 - Review of Orbiter Flight Boundary Layer Transition Data by McGinley, Berry, Kinder, Barnwell, Wang & Kirk
AIAA-2006-2922 - Boundary Layer Transition Results From STS-114 by Berry, Horvath, Cassady, Kirk, Wang & Hyatt
AIAA 2008-3736 - Boundary Layer Transition on X-43A by Berry, Daryabeigi, Wurster & Bittner
AIAA-2010-0246 - Orbiter Boundary Layer Transition Prediction Tool Enhancements by Berry, King, Kegerise, Wood, McGinley, Berger & Anderson
AIAA-2016-3533 - Flight Experiment Verification of Shuttle Boundary Layer Transition Prediction Tool by Berry, Berger & Horvath
Cleared for Public Release