## Slide 1
Sampling Functions from Gaussian Processes and Structured Covariance Gaussian Networks
1Flight Dynamics Branch 2Aerothermodynamics Branch
NASA Langley Research Center
NASA Data Science Summit
15 November 2022
Tenavi Nakamura-Zimmerer1 and J.B. Scoggins2

## Slide 2: Outline
Aerodynamic modeling and UQ
  Motivating stochastic process models
Gaussian process regression
  Efficiently sampling consistent functions
Structured covariance Gaussian NNs
  Converting conditional distributions to stochastic processes
Conclusions

## Slide 3: Orion crew module
Image credits: Liam Yanulis, NASA

## Slide 4: Orion crew module aerodynamics
Airflow
Center of mass
Angle of attack
Lift force
Drag Force
Pitching moment
(static, longitudinal aero only)
Velocity

## Slide 5: Aerodynamic modeling
DATA
ENGINEERING & MISSION DESIGN
AERO-DATABASE
1
3
2
Image credits. 1: Chun Tang, NASA. 2: Sandra Gibbs, NASA. 3: Karen Bibb, NASA.

## Slide 6: Aerodynamic uncertainty quantification
State of the practice: “UQ by inspection”
Development of the Orion crew module static aerodynamic database, part I: Hypersonic & part II: Subsonic/supersonic (Bibb et al., AIAA SciTech Forum, 2011a,b)
1. Nominal aero
2. Uncertainty buildup
Data is noisy, can deviate from true physics, can reflect different stages of vehicle design process – need UQ!

## Slide 7: Machine learning for aerodynamic UQ
From data, learn a surrogate conditional probability distribution
AeroFusion Early Career Initiative:
Tailor and apply modern ML for streamlined & repeatable aerodynamic UQ
Many possible methods…
Gaussian process regression
Structured covariance Gaussian NNs
Bayesian NNs
Dropout NNs
Sliced normal regression
Random predictor models
Polynomial regression
Conditional generative NNs

## Slide 8: Atmospheric reentry simulation
Monte Carlo simulation of atmospheric reentry of Orion crew module
  Aerodynamic model trained on data used to build v0.60 Orion aerodatabase*
3-DoF longitudinal dynamics
Flight control system adjusts angle of attack to maintain trim
altitude
velocity
flight path angle
angle of attack
Image credit: Liam Yanulis, NASA. *Bibb et al. SciTech 2011a,b

## Slide 9: Stochastic process models
Sampling naïvely leads to
  inconsistent predictions for the same
  uncorrelated predictions for nearby
Inconsistent with physics! Aerodynamics are uncertain but not random
Don’t know a priori want to sample functions that preserve
Stochastic process:

## Slide 10: Gaussian process regression (GPR)
Generalization of Gaussian distribution to functions using kernel function to model covariance (Rasmussen & Williams, 2006)
Kernel hyperparameters learned by maximizing the log marginal likelihood of seeing data given model
Function values at input points are jointly Gaussian with predictive mean and variance obtained by conditioning on training data

## Slide 11: Inconsistent GPR function sampling
Cholesky factorization used to sample from joint Gaussian distribution with order
Repeat samples generate inconsistent functions
  Each new sample forgets history (correlation) with previously sampled points
For trajectory sims, function inputs unknown a priori
Possible solution: sample lookup tables
  Interpolation errors
  Costly for input dimensions > 2

## Slide 12: Consistent GPR function sampling
Adding new points (2) to previously sampled points (1)
Solving for block Cholesky components leads to reduced system, that can be updated by performing Cholesky decomposition only on new points
For single point updates, computational complexity reduced to
Additional book-keeping to maintain list of unique input points and intermediate results
previous samples
new samples
updated Cholesky
updated normal samples
updated mean
updated Cholesky obtained from block covariance matrix

## Slide 13: GPR function sampling for trajectory simulation
Continuous aero coefficient function sampled along trajectory that is not known a priori
Integrated trajectories account for uncertainties in aero coefficient database
time
time

## Slide 14: Structured Covariance Gaussian Networks (SCGN)*
* Dorta et al., IEEE/CVF Conference on Computer Vision and Pattern Recognition, 2018.
Nakamura-Zimmerer et al. AIAA SciTech Forum, 2023 (to appear).
Mean network
Covariance network
is triangular with positive diagonal
Cholesky decomposition of inverse covariance
Guarantee positive definite covariance
Efficiently compute log-likelihood for training
Conditional Gaussian

## Slide 15: Sampling the conditional distribution
To sample with covariance , sample standard normal and compute
We learn , so we could sample as
For same , different yields different
Even if we keep track of , nearby samples uncorrelated

## Slide 16: Towards smooth function samples
To generate a smooth, deterministic function, sample and fix single
Triangular structure of in introduces unwanted dependence on arbitrary order of
2D example:
No dependence on cross-covariance!
has fixed sign

## Slide 17: Spectral decomposition sampling
To sample , we don’t have to pick …
Any matrix satisfying works
SVD:
Choose
Each sample yields a function
Can cross

## Slide 18: Why spectral decomposition?
Identical to Cholesky
Cannot cross
For this model, variables in (arbitrary) order
Setting removes cross-covariance influence from

## Slide 19: Effect on reentry trajectory simulations
Both sample methods: 3.6ms / function call
Aero less important in ballistic entry, but noise causes problems for control system model and numerical integration
For clarity, only 1 white noise trajectory shown
time
time
Notes: White noise: 3.9e-03
Spectral: 4.0e-03

## Slide 20: Concluding remarks
Deterministic function samples required for variety of ML/UQ tasks
GPR and SCGN present unique challenges for function sampling
  GPR: consistent function sampling algorithm based on block updates of the Cholesky decomposition of the covariance matrix
  SCGN: spectral decomposition sampling strategy removes variable order dependencies
Trajectory simulations provide an important testbed / motivation for function sampling algorithms
GPR and SCGN function sampling demonstrated on 3-DoF trajectory simulation for models trained on Orion aerodynamic coefficient data

## Slide 21: Appendix: GPR function sample updates