## Slide 1: SPEED – Stratospheric Projectile Experiment of Entry Dynamics
Ben Libben, Cole Kazemba, Roshan Jagani, Hannah Alpert

## Slide 2: Problem
Mach Number
2
4+
0
3
1
Ballistic Range
Drone Drop Testing
VST
Free or Forced Oscillation
Potential instabilities in blunt-body dynamics pose a significant burden on the design of entry missions
Dynamic stability characterization methodologies have drawbacks and do not cover a full Mach range of interest in any given facility
No existing test methodology can provide:
  … Full 6 DOF motion,
  … With instrumentation,
  … Across continuum of Mach numbers from 2 to 0.5,
  … While matching dynamic scaling laws
SPEED
Notes: Our project is centered around the dynamic stability characteristics of entry vehicles.
Instabilities in entry vehicle dynamics pose a significant burden on entry mission design.
You can see here a Genesis capsule tumbling due to these instabilities.
Methodologies for characterizing dynamic stability exist. However, no method captures 6-DOF motion with instrumentation across a Mach range from 2 to 0.5 that matches dynamic scaling laws.
This leads to our project SPEED.

## Slide 3: Stratospheric Projectile Experiment of Entry Dynamics (SPEED)
Ballistically accelerated payload dropped from a stratospheric balloon ejects a scaled entry capsule
Heavily instrumented capsule recording free-flight 6-DOF state, stagnation, and aft body pressures in-situ
80 kg total mass delivered to 40 km (6 – 8 payloads)
Tailorable to different:
  3D printed capsule geometries (OMLs, surface features)
  Initial angles of attack
  Dynamically scaled flight profiles (Titan, Earth, Mars)
Low-cost payload:
  All primary components are 3D printed (~ $500 total per payload)
  Expense is concentrated in avionics
Objective: Develop a test methodology to characterize the dynamic stability of entry vehicles across a Mach range representative of a full-scale mission
Notes: SPEED stands for Stratospheric Projectile Experiment of Entry Dynamics.
Our objective is to develop a test methodology to characterize the dynamic stability of entry vehicles across a Mach range representative of a full-scale mission.
We achieve this by dropping a payload via stratospheric balloon.
The payload is ballistically accelerated to an altitude and Mach number dependent on dynamic scaling parameters before ejecting a scaled entry capsule.
This capsule is instrumented to record its 6 degrees of freedom trajectory and pressures along the aft body to understand how those forces play into stability.
We can bring 80 kg up to 40 km, which translates to 6-8 payloads per flight.
One of our primary goals is to be tailorable to different mission profiles. 3D printing helps us out here to accommodate different capsule geometries. This means we can tailor the capsule to whatever OML the customer wants, along with added surface features, initial angles of attack, and dynamically scaled flight profiles.
Another goal is to create a cost-competitive architecture. 3D printing the structural components brings our manufacturing cost per payload to around $500.
Our avionics can cost between one and five thousand dollars, depending on customer need.
And our balloon cost to drop all payloads is $300K

## Slide 4: Driving Requirements
The flight system shall enable data collection required to reconstruct the 6-degree of freedom (DOF) trajectory of an entry vehicle.
The flight system shall deliver an entry vehicle matching dynamic similitude to a full-scale reentry mission, with a minimum initial Mach number of 1.5.
Data to be collected
X, Y, Z Translation
X, Y, Z Rotation
Pressure Altitude
Stagnation Pressure
Aft body pressure (if applicable)
Dynamic Scaling to Dragonfly Capsule
Mass: 1.859 kg
Iyy: 2.52e-3 kg-m2
Release Altitude: 20 km
Notes: Here are the driving requirements for the system.
Two big ones are L2-1 and L2-2, which specify the data we are after and what is being dropped.
You can see the angle of attack oscillation we are looking to characterize with 6 DOF trajectory in addition to altitude, stagnation, and Aft body pressure measurements.
The capsule is dynamically scaled to an actual entry mission. We are using the Genesis shaped Dragonfly capsule, scaled to a diameter of 15cm, as our point design.

## Slide 5: ConOps
Notes: Here is a video of our ConOps to help visualize what an experiment will look like:
First, perform our system check out…
before our flight system ascends, suspended below the balloon until reaching an altitude of 40 km…
After reaching our float altitude, we sequentially release our 6-8 payloads
The payload accelerates to a speed of around Mach 2 due to its ballistic shape
The scaled capsule is jettisoned from the payload at an altitude of 20km
Our capsule enters free flight and decelerates until reaching a terminal descent velocity. This period of deceleration through the transonic range is where we are most interested in collecting data.
Lastly, our capsule touches down, and we recover the data

## Slide 6: Avionics ConOps
Chart: Altitude [m]
 | 40000 | 40000
 | 20000 | 20000
Balloon | 40000 | 39200 | 38400 | 37600 | 36800 | 36000 | 35200 | 34400 | 33600 | 32800 | 32000 | 31200 | 30400 | 29600 | 28800 | 28000 | 27200 | 26400 | 25600 | 24800 | 24000 | 23200 | 22400 | 21600 | 20800 | 20000 | 19200 | 18400 | 17600 | 16800 | 16000 | 15200 | 14400 | 13600 | 12800 | 12000 | 11200 | 10400 | 9600 | 8800 | 8000 | 7200 | 6400 | 5600 | 4800 | 4000 | 3200 | 2400 | 1600 | 800 | 0
35 – 40 km
15 – 20 km
5 – 10 km
Terminal Descent (Mach ~0.15)
Capsule Touchdown & Recovery
Payload Freefall
Payload Release
Launch
Ascent
July 26th, 2022
6
Capsule Free flight
1. Detect high altitude with barometer
2. Detect decreasing altitude with barometer
3. Detect jettison of capsule with G trigger
4. Stop recording data before impact
Data Recording
Ballast and capsule avionics do the same actions
Ballast avionics trigger jettison of capsule and they fall separately

## Slide 7: Data Acquisition
60
5
40
90
17
Avionics box
+Z
+Y
+X
Battery
Avionics Box
Attenuation rubber
SD writer and card
Pressure transducers on the forebody and aft body (if applicable)
  ADC measurements for pressure transducers give very low quantization noise with a ±1% error band from sensor error
IMU with integrated sensor fusion algorithm
  Accelerometer range: ±100 g
  Gyroscope range: ±2000 °/s
SD card is surrounded in attenuation rubber to prevent excessive G loading

## Slide 8: Data Recovery
Protect it | Find it
SD card embedded in attenuation rubber Drop Testing | Placing a Bluetooth tracking device in one or more capsules (range ~200 feet) Filling compartment with colorful powder Distance between capsules largely determined by the distance the balloon travels between release due to stratospheric winds A detailed wind profile will be available directly before launch
1
2
3
4
5
6
7
8
~800 m
Capsule Landing Dispersion
We only care about the data, everything else is expendable
Notes: The last requirement we will examine is our data recovery requirement levied on the capsule. The only thing we care about surviving this experiment is the data we collect.
To recover the data, there are two things we need to do: protect it and find it.
We will sandwich our SD card between rubber attenuation material to protect it. We were fortunate enough to test this design in the Engineering Evaluation Laboratory, which I’ll discuss in the following slides.
For finding the data, the current plan is to equip the capsules with Bluetooth devices which have a range of a couple hundred feet. We are also considering filling a compartment with colorful holi powder so that when it hits the ground there is an explosion of color (think over the top gender reveal style) and that will act as a visual cue as well.
We think we can get away with one GPS because we expect the distance between capsules at landing to be driven mainly by the distance the balloon travels between drops. This assumes the capsules will experience the same wind profiles during descent because of how closely they will be dropped to each other.
Also, we will have a detailed wind profile provided directly before launch to reduce uncertainty in capsules’ landing locations.

## Slide 9: Avionics Prototype
Prototype uses system architecture that is capable of:
  All 6 degrees of freedom measurement
  Reading 4 pressure transducers
  Keeping itself above a critically low temperature
  Reading and writing all measurements listed above at 800 Hz
800 hz Accelerometer Data
Gyroscope
Accelerometer
ARM Cortex M0 Computer
SD Writer
Voltage Regulator
Resistive Heater
Notes: We had an intern over the summer build a prototype of the avionics system. We are in the process of refining this, potentially with more off the shelf parts, but it was great to get an idea for which sensors and components to use.

## Slide 10
Capsule
+
Sabot
Ejection Mechanism
Ballast Mass
Capsule Ejection
Three major parts: Ballast mass, ejection mechanism, and capsule + sabot.
Ballast mass is stacked ½ in steel plates, brings vehicle mass up to 8kg for Mach 1.9 flight
Energy for the ejection is provided by 3 springs
Uses a 4-piece discarding sabot to guide the capsule straight out of the aerodynamic shell
All parts 3D printed, laser cut, or COTS – cost < $500
Vehicle OML is two 3D printed shells combined with a lap joint and fasteners
Sabot section and ballast mass sections are modular to allow for different capsules, sensor packages, and flight profiles
Mechanical Overview
Height = 0.486m

## Slide 11
Sabots
Battery
Avionics Box
Attenuation Rubber
Pressure Sensors
Ballast Mass
Delrin Piston Rings
Printed Prototypes
Sabots can be printed in less than a day for any capsule shape
Some size margin to scale up capsule for different dynamic scaling
Dragonfly |  | 
Diameter (m) | Mass (kg) | Iyy (kg-m2)
4.5 | 2256 | 2757
Current Design |  | 
Diameter (m) | Mass (kg) | Iyy (kg-m2)
0.15 | 1.86 | 2.52E-03
Capsule and Sabot
Magnetic Lid
Sizing of capsule and ballast largely driven by matching dynamic similitude of mass and MOI for Dragonfly
Diameter = 0.15m

## Slide 12
Steel Ballast Mass
3D Printed Shell
Carrying Handle
OML Lap Joint
Ballast Mass
Modular ballast mass section holds up to 4.4 kg of mass
Inexpensive water-jet cut steel plates of varying diameters provide reasonable packing density, push CG low enough
Carrying handle and bayonet-mount retention provides easy installation and removal
Plates can be omitted/drilled out to tune mass/CG

## Slide 13
Ballast Mass

## Slide 14
Three springs provide combined 140lbs of force to eject capsule at 5m/s
3D printed cup pushes against sabots during ejection. Motion is fully constrained in every degree of freedom except +z axis with steel guide shafts and Delrin bushings
Before release, spring force is reacted into a ¼ aluminum plate via polypropylene rope, which is cut with a burn rope mechanism to trigger ejection
All parts waterjet, 3D printed, or COTS  <$50 per unit. Springs swappable for increased/decreased force
Cup pushes against sabot
Tensioned hot nichrome wire cuts polypropene rope to trigger ejection
Guiding shaft and printed pieces keep cup constrained in all DOF except axial push
Ejection Mechanism
COTS toggle clamp actuates gripping plates to cinch rope, hold mechanism in “cocked” position
Avionics placeholder
Notes: Purely a mechanical system, in that there’s no pyrotechnics, stored high pressure cold gas, and therefore no serious range safety concerns which should make operations a lot easier. With this mechanism, a constant 2.5A current through a single wire is all it takes to trigger the ejection

## Slide 15: Ejection Mechanism
Spring applies ~6 pounds of force pulling a nichrome wire through a polypropylene rope.
Several types of rope, wire lengths, applied electrical currents tested to produce reliable cuts.
Design details based on 2012 paper for CubeSat deployment. Redesigned to be entirely 3D printed or COTS, <1/20 cost with comparable reliability.

## Slide 16: Conclusion and Development Timeline
Preliminary Design
Development (Current State)
Flight Demonstrations
Mission Use
4 Interns
~ 3 months of work
~ $2000 budget
Working prototype by end of summer
Concept maturation
Awarded Ames Center Innovation Fund
Flight Opportunities Program letter of recommendation
Flight test ready in 1 year
New test methodology ready in ~2 years with current timeline
Notes: This has been the project's concept development and preliminary design.
This has been the work of 4 interns in about ~ 3 months with > $2000 in materials taking a back of the napkin concept to prototype by the end of Summer.
Next is to finalize a design through component and integration testing ending with a helicopter test.
We have the development framework set; we just need funding to execute it, and we have submitted a proposal to the AMEs CIF fund.
After development, we have a flight opportunities program letter of recommendation for a system test from a stratospheric balloon. With funding for our development, will we have the flight ready for us in about 12 months.
After refinement, we will have a new dynamic stability characterization test that will be used to influence future entry mission design ready in about two years.

## Slide 18: Phase 1 – Conceptual Design / Prototype Outline
CAD Work
  Launch Platform – early dev
  Payload – Update to EES OML, Avionics black box, and ballast mass update
  Ballast – Size update, ballast mass update, connection to launch platform
  Avionics Chip – doesn’t exist currently
Design Work
  Launch Platform
  Ejection Mechanism – increase fidelity
  Avionics Box / Instrumentation Suite – update from new trajectory and payload OML
  Recovery System
ConOps Work
  Recovery System
  Ground Ops
Systems Engineering Work
  Requirements Update
  MEL, PAL Update
Objective: Close an MSR-EES based point design and validate each system through prototyping. Hold design review with independent expert panel before CY23 start.
Notes: SPEED stands for Stratospheric Projectile Experiment of Entry Dynamics.
Our objective is to develop a test methodology to characterize the dynamic stability of entry vehicles across a Mach range representative of a full-scale mission.
We achieve this by dropping a payload via stratospheric balloon.
The payload is ballistically accelerated to an altitude and Mach number dependent on dynamic scaling parameters before ejecting a scaled entry capsule.
This capsule is instrumented to record its 6 degrees of freedom trajectory and pressures along the aft body to understand how those forces play into stability.
We can bring 80 kg up to 40 km, which translates to 6-8 payloads per flight.
One of our primary goals is to be tailorable to different mission profiles. 3D printing helps us out here to accommodate different capsule geometries. This means we can tailor the capsule to whatever OML the customer wants, along with added surface features, initial angles of attack, and dynamically scaled flight profiles.
Another goal is to create a cost-competitive architecture. 3D printing the structural components brings our manufacturing cost per payload to around $500.
Our avionics can cost between one and five thousand dollars, depending on customer need.
And our balloon cost to drop all payloads is $300K

## Slide 19: Phase 2 – Test Campaign
Subsystem Testing (Jan – Mar)
  Launch Platform Testing
  Ejection Mechanism Testing
  Fit Tests
  Manufacturing Procedures and Drawings
Integrated System Testing (Mar – Apr)
  Assembly Procedures
  Command simulation testing
  Power testing and simulated ConOps
Drone Drop Test (Apr – May)
  Payload data retention drop test
  Ejection Mechanism test
Helicopter Drop Test (May – Jul)
  End-to-end full system test
  Recovery System/Ground-Ops test
Sabot separation testing
  Ballistic Range?
Objective: Provide Verification and Validation proof for the fully integrated flight system and ConOps to meet FOP balloon flight requirements.

## Slide 20: Phase 2 – Drone Drop Test
Units: 3 EDU-2
  Only QTY 2 units with instrumented payload
  Multiple dummy mass payloads
  No Launch Platform testing
  Need drone with lift capability between 2kg (Payload only) and 10 kg (full fidelity Flight Unit)
  Follow-me mini-drone
    Something we can drop repeatedly
System Success Criteria:
  One successful payload ejection during free-fall
  Data recovered from landed memory chip
Data Success Criteria:
  Avionics data recorded and recovered after hard landing
  Impact data parameters quantified
    Standalone impact accelerometer sys?
    Tumbling and off-nominal impacts
  HD Video of ejection and landing
  Soil data for future LS-DYNA run correlation?
Objective: Perform low-altitude (~500ft) drop test of Payload and Ballast systems to test data recovery capability and ejection mechanism
Dev needed:
Arming detection for ejection
auto timed release and ejection

## Slide 21: Phase 2 – Helicopter Drop Test
Units: QTY 8 Flight Units, QTY 1 Launch Platform
  Only QTY 3 units with instrumented payload
  Recovery System/Ground-Ops Hardware
  Any necessary safety hardware
System Success Criteria:
  Successful release of Capsules from Launch Platform
  At least one successful Payload ejection from Ballast during free-fall
  Recovery System enables landed system location
Data Success Criteria:
  HD Video of Release, Ejection, and Landing
  Recover recorded flight data
Objective: Use simulated commands and flight profiles to test the end-to-end baselined flight ConOps on all systems from pre-flight gound-ops to post-flight recovery-ops. Test landed payload dispersion and recovery system.
Capsule
Ejection
Qty scope can be driven by left over cif funds
Ask about bulk printing