## Slide 1: Multiphase Simulations of the SLS Launch Environment
Travis Rivord – CFD Research Corporation, Jacobs Space Exploration Group, NASA MSFC-ER42
Brandon Williams – ER42, NASA MSFC-ER42

## Slide 2: SLS Background
NASA’s Space Launch System (SLS) will soon send astronauts back to the Moon
  The two solid rocket boosters (SRBs) provide 75% of the total thrust at launch
  Ignition of the powerful SRBs generate significant ignition overpressure (IOP) waves
The unmitigated launch environment can damage the vehicle
  During the first Space Shuttle launch, IOP waves caused structural damage to the vehicle
    Resulted in an effort to mitigate the SRB IOP by modifying the existing water sound suppression system
  Based on Shuttle experience, the SLS design includes a sound suppression water system to protect against IOP waves and acoustics
Notes: 46 s

## Slide 3: SLS Water System
To maximize the ignition overpressure/ sound suppression (IOP/SS) water system’s effectiveness, water is injected very close to the nozzle exit planes
  The water forms a dense and chaotic layer inches from the SLS rocket nozzles
Results in a complex multiphase environment during the SRB ignition transient
  Consists of the SRB plumes, IOP/SS water, and the RS-25 engine plumes at full power
The IOP/SS design creates challenges related to
  water spray into/onto nozzles
  potential debris transport
  strong plume-water interaction
Test of the SLS IOP/SS water System
Notes: 38 s

## Slide 4: Shuttle and SLS Differences
Configuration differences limit use of historical Shuttle data
Vehicle/ML configuration
  Shuttle RS-25 engines located far from the SRB nozzles
    Enables separate holes for plumes
  SLS RS-25 engines located close to the SRB nozzles
    Requires one large hole for all plumes
    RS-25 plume entrainment has a strong effect on the SRB IOP/SS water
IOP/SS water system design (SRB specific)
  Shuttle water was split into multiple levels
    The densest layer furthest from the SRB
  SLS water injected at one level a short distance from the SRB
    Results in a dense, chaotic, layer of water close to the nozzle
    Splashing may project water upwards into the nozzle
    At ignition, this water can result in large side loads that the SRB hardware must withstand
Shuttle
SLS
Single Hole for All Nozzles
Notes: 1:36 s

## Slide 5: SRB Operational Environment
Currently, the SRB operational environment is uncertain
  Shuttle experience inapplicable or limited due to configuration differences
Some data is available from tests of individual systems
  Water system operation data obtained from the ISVV-14 test series
  RS-25 plume-water interaction insight from SLS Green Run
  Nozzle side load data obtained from FSB-1 booster static test fire
All tests lack key physics of the full SLS launch configuration
  No integrated testing will be available prior to the Artemis I launch
The only means of gaining insight is computational fluid dynamics (CFD) modeling
ISVV-14 Water System Test
FSB-1 Test
Green Run Test
Notes: 1:29 s

## Slide 6: Modeling Challenges
Modeling the SLS launch environment involves tightly-coupled physics which are incredibly challenging to simulate
  Multiple, hot, supersonic rocket plumes
  Multiphase flow (gas and liquid) + phase change
  Large length scales (heavy launch vehicle)
  Small length scales (droplet formation/break-up, turbulence)
  Long time scales (~10s for vehicle ignition sequence)
  Small time scales (~10𝜇s for droplet break-up in supersonic plumes)
NASA engineers at MSFC have conducted state-of-the-art CFD simulations to better understand these physics
  Use the Loci/STREAM-Volume of Fluid (VoF) multiphase CFD solver
  Initial efforts focused on validating CFD predictions against tests
  Currently conducting more complex simulations of the integrated vehicle
These simulations
  Are conducted on thousands of processors
  Take weeks to months to execute
  Require terabytes of storage
Hot Plume
Sound Suppression
Water
Notes: 60 s
4.5 min

## Slide 7: SLS Ignition Sequence
The SLS ignition sequence occurs in 3 steps
  T0-14 s: IOP/SS activation
270,000 gallons of water is fed into the IOP/SS system
IOP/SS Water System Test

## Slide 8: SLS Ignition Sequence
The SLS ignition sequence occurs in 3 steps
  T0-14 s: IOP/SS activation
  T0- 6 s: RS-25 ignition
The RS-25 engines active in a staggered sequence
  Takes ~4 seconds to reach 100% rated power level
  Held at 100% power for 2 seconds
Core Stage Green Run Test[1]

## Slide 9: SLS Ignition Sequence
The SLS ignition sequence occurs in 3 steps
  T0-14 s: IOP/SS activation
  T0- 6 s: RS-25 ignition
  T0+ 0 s: SRB ignition
SRB ignition initiated at T0
  3.6 million lb of thrust per SRB
  Liftoff occurs shortly after ignition
Flight Support Booster-1 SRB Test[2]

## Slide 10: SLS Ignition Simulation: RS-25 Plumes
The SLS ignition simulation occurs in 3 steps, mimicking the actual ignition sequence
  IOP/SS water-only to quasi-steady state
  RS-25 transient
  SRB transient
The rapid RS-25 transient disturbs the Core Stage water
  The water eventually recovers to a quasi-steady state
Water splashing under the SRB nozzle visibly reduces
The unsteadiness of the RS-25 Mach disks appears physical
RS-25 Ignition
Simulation
image credit Patrick Moran

## Slide 11: SLS Ignition Simulation: SRB-Plumes
The SRB plume ignition simulation is conducted from the end state of the RS-25 simulation
The plume emerging from the nozzle displaces the water and pushes through the duct
This simulation will be used for post-flight analysis of Artemis I including
  Plume-water induced side loads
  Throat plug debris transport
  Acoustic environment
  Unexpected phenomenon witnessed at launch
Artemis I flight data will also be used to validate the simulation
SRB Ignition
Simulation
image credit Patrick Moran

## Slide 12: SLS Ignition Simulation: Pseudo-Schlieren
CFD can provide a deep understanding of the physics
Still frame of the SRB simulation
  Planar slice through RS-25 and SRB centerlines
  Greyscale pseudo-Schlieren contour
    Dark regions represent shocks and other waves
  Blue represents water on this plane
  Velocity vectors colored by velocity magnitude

## Slide 13: SLS Ignition Simulation: Pseudo-Schlieren
CFD can provide a deep understanding of the physics
Still frame of the SRB simulation
  Planar slice through RS-25 and SRB centerlines
  Greyscale pseudo-Schlieren contour
    Dark regions represent shocks and other waves
  Blue represents water on this plane
  Velocity vectors colored by velocity magnitude
Time just after igniter shock shown
  Igniter shock (IS) is the pressure wave resulting from SRB ignition
SRB Ignition
Simulation
Igniter shock
Igniter shock

## Slide 14: SLS Ignition Simulation: Pseudo-Schlieren
CFD can provide a deep understanding of the physics
Still frame of the SRB simulation
  Planar slice through RS-25 and SRB centerlines
  Greyscale pseudo-Schlieren contour
    Dark regions represent shocks and other waves
  Blue represents water on this plane
  Velocity vectors colored by velocity magnitude
Time just after igniter shock shown
  Igniter shock (IS) is the pressure wave resulting from SRB ignition
  Igniter shock reflects off the water sheets
SRB Ignition
Simulation
Igniter shock
Igniter shock
Reflection
Igniter shock

## Slide 15: SLS Ignition Simulation: Pseudo-Schlieren
CFD can provide a deep understanding of the physics
Still frame of the SRB simulation
  Planar slice through RS-25 and SRB centerlines
  Greyscale pseudo-Schlieren contour
    Dark regions represent shocks and other waves
  Blue represents water on this plane
  Velocity vectors colored by velocity magnitude
Time just after igniter shock shown
  Igniter shock (IS) is the pressure wave resulting from SRB ignition
  Igniter shock reflects off the water sheets
  The flow from IS and the plume mushrooms outwards from the booster centerline
SRB Ignition
Simulation
Igniter shock
Igniter shock
Reflection
Igniter shock
Outward flow

## Slide 16: Conclusions and Forward Work
Initial efforts to apply state of the art simulation tools for the SLS launch environment focused on validating Loci/STREAM-VoF CFD predictions
Simulations are currently being executed of the entire SLS ignition sequence that will
  provide deeper understanding into the SLS multiphase launch environment
  provide insight for decision making for the first crewed SLS flight, Artemis II
  be validated against Artemis I flight data
Future simulations will
  target new configurations of the SLS IOP/SS water required to support more powerful variants of the SLS vehicle
  investigate launch environments for vehicles other than the SLS to support other agency space missions
image credit Patrick Moran

## Slide 17: References
[1] SLS Core Stage Green Run Testing Media Resources: https://images.nasa.gov/details-NHQ_2021_0106_NASA%20Conducts%20Test%20of%20SLS%20Rocket%20Core%20Stage%20for%20Artemis%20I%20Moon%20Mission
[2] Media Resources: Flight Support Booster Test: https://images.nasa.gov/details-MSFC_XP01_V_0133_FSB1_BROLL
[3] SLS-4091 August 2022 Artemis I Resource Reel 081922: https://images.nasa.gov/details-SLS-4091%20August%202022%20Artemis%20I%20Resource%20Reel%20081922
[4] KSC-20190913-RV-CMS01_0001-Nominal_Wet_Flow_Test_at_Pad_39B-3229665: https://images.nasa.gov/details-KSC-20190913-RV-CMS01_0001-Nominal_Wet_Flow_Test_at_Pad_39B-[4] 3229665
[5] NASA's Second Hot Fire Test for the Artemis Moon Rocket: https://images.nasa.gov/details-NASA%E2%80%99s%20Green%20Run%20Hot%20Fire%20Test%20of%20the%20Space%20Launch%20System%20Core%20Stage