## Slide 1: ANOPP2 Mission Analysis Tool (AMAT)
Leonard V. Lopes and Stephen A. Rizzi
NASA Langley Research Center

## Slide 2: Outline
UAM Noise-Power-Distance Prediction Process
  Prediction of single source noise hemisphere
  Collecting source noise hemispheres to define flight event
  Modification of hemispheres for V&V
  Propagation of noise to ground and metric calculation
ANOPP2 Toolchain: AARON, ARMIT, ASOFT, AMPIT, AMAT
AMAT Examples
  Calculation of NPD during level flyover (Mode L)
  Calculation of OASPL (dBA) during approach (Mode A)
  Calculation of 1/3rd Octave SPL along line on ground (Mode L)
Conclusion

## Slide 3: UAM NPD Prediction Process
UAM source noise prediction requires mid- to high-fidelity aerodynamics
  Aerodynamics affects blade dynamics and rotor performance
  Blade dynamics and rotor performance affect aerodynamics
The aerodynamics are affected by flight condition and trim state
Similar flight conditions may result in significantly different aerodynamics
There may exist many trim states capable of the same flight condition
Vehicle Concept
Flight Conditions
Aerodynamic
Computation
Aerodynamic Assessment
Trim State

## Slide 4: Single Source Noise Hemisphere
Many different sound sources on vehicle
  Tonal noise source: deterministic (from rotating/moving blade volume and surface pressures)
  Broadband self-noise source: stochastic (from turbulent boundary layer and related phenomena)
  Blade vortex interaction (BVI) : included in tonal noise sources
  Blade wake interaction (BWI): stochastic (from turbulent self wake ingested by rotor or from rotor-rotor interaction)
  Turbulence ingestion noise (TIN) : surrounding turbulence environment ingested (e.g. nearby buildings)
  Electric motor noise: significant tonal noise in the mid-frequency range (annoying for listeners)
Each flight condition and trim state results in a unique aerodynamic assessment
Capability of aerodynamics and acoustics is evolving, multiple iterations of same assessment as tools improve
Leads to a large database of aerodynamic assessments and source noise hemispheres that is ever-evolving
Aerodynamic Assessment
Source Noise Hemispheres
Aerodynamic Assessments
Source Noise Hemispheres
Version 1, 2, 3…. of
Currently Available
Not Yet Available

## Slide 5: Flight Event
Flight event is defined as one or more flight conditions at emission times
Start with a database of source noise hemispheres for each flight condition and trim state
Flight event can be a simple flyover, climb, or approach at many altitudes (h)
  Each hemisphere run at many different altitudes
  Each hemisphere run at level flyover, approach, and takeoff
Can also be a complex vehicle maneuver
  Several hemispheres selected to coincide with flight path’s required flight conditions
Level Flyover
Approach
Takeoff
Maneuver
Source Noise Hemispheres for
Flight Condition and Trim State
h

## Slide 6: V&V
Modification of the source noise hemisphere is critical for analysis
  Replace entire hemisphere with noise at a single point (eliminates source interpolation)
  Eliminate all azimuthal angles other than 0°
    Eliminates azimuthal interpolation and simulates fixed wing source flyover event
  Select on azimuthal angles of -45°, 0°, 45°
    Simulates rotorcraft source flyover event
Modified ‘hemisphere’ is used in propagation as if full noise hemisphere
0°
45°
-45°

## Slide 7: Propagation
Each combination of hemisphere, flight path, and observer
  Given time history of noise hemisphere, calculate noise at one or more ground observer positions
  Source noise hemisphere may be 1/3rd octave band SPL, NBS, or PSD
  Account for spherical spreading
  Account for atmospheric absorption (several models)
  Account for ground effects
  Account for different emission angles (due to ground)
  Layered atmosphere (not required for NPD generation)
Called many times for each vehicle NPD database
Also leveraged for certification assessment

## Slide 8: Outline
UAM Noise-Power-Distance Prediction Process
  Prediction of single source noise hemisphere
  Collecting source noise hemispheres to define flight event
  Modification of hemispheres for V&V
  Propagation of noise to ground and metric calculation
ANOPP2 Toolchain: AARON, ARMIT, ASOFT, AMPIT, AMAT
AMAT Examples
  Calculation of NPD during level flyover (Mode L)
  Calculation of OASPL (dBA) during approach (Mode A)
  Calculation of 1/3rd Octave SPL along line on ground (Mode L)
Conclusion

## Slide 9: ANOPP2
ANOPP2
ANOPP2 is a multifaceted program used to perform noise calculations
ANOPP2 is composed of three components
  Common framework that can be used for fine-grained control
    Does require writing a user code in Fortran, C++, or Python
    Because of its complexity, using the framework directly has steep learning curve
  Functional modules perform a specific acoustic calculation and require the framework
  Tools focus on the user’s application by reducing available capability are reducing the learning curve
Framework
Functional Modules
Tools

## Slide 10: AARON
ANOPP2 Aeroacoustic ROtor Noise (AARON)
  Comprehensive analysis using CAMRAD II for vehicle trim and lifting-line motion and forces
  The ANOPP2 Farassat Formulation 1A Internal Functional Module (AF1AIFM) for tonal noise
  The ANOPP2 Self-Noise Internal Functional Module (ASNIFM) for broadband noise
  Exports ANOPP2 restart file containing single source noise hemisphere (all noise sources)
Tonal Noise
Broadband Self Noise
Optional
CFD coupled aerodynamics

## Slide 11: ARMIT, ASOFT, AMPIT
ANOPP2 Restart Metadata Insertion Tool (ARMIT)
  Metadata are additional information (other than noise) on hemisphere
  Attaching metadata allows for organization and hemisphere selection
  ARMIT allows for including any type of metadata to source noise hemispheres
ANOPP2 Source Observer Filtering Tool (ASOFT)
  V&V for source noise hemispheres is important in order to trust results
  We can limit the noise hemisphere to a particular azimuth angle(s)
  Examples 0° (fixed-wing mode) or -45°, 0°, 45° (helicopter mode)
  ASOFT allows the study of directionality on far-field noise
ANOPP2 Message Passing Interface (MPI) Tool (AMPIT)
  Source noise and propagation computations can take a long time
  Leveraging computational resources reduced the time significantly
  AARON and AMAT leverage AMPIT to significantly reduce computation time on the order of the number of processors available
Not To Scale

## Slide 12: AMAT
Single vehicle noise predictions feed into community noise impact assessment
  Source noise hemispheres of various vehicles under various flight conditions are fed into design tool
  Environment impact (AEDT) simulates many different flight paths and accumulates to assess noise over large area
  Noise from entire airport is simulated and community impact assessed
ANOPP2’s Mission Analysis Tool (AMAT)
  Command line tool that wraps the ANOPP2 Straight Ray Propagation Internal Functional Module (ASRPIFM)
  Takes a source noise hemisphere and flies under various flight conditions
  Doppler shift, spherical spreading, atmospheric absorption, ground effects
  Records data required by AEDT for community impact assessment
Source Noise
SPL [dB]
Integrated Acoustic Metric Data
AEDT
AMAT
Source Noise Prediction
OVERFLOW
ANOPP2
CAMRAD II

## Slide 13: Outline
UAM Noise-Power-Distance Prediction Process
  Prediction of single source noise hemisphere
  Collecting source noise hemispheres to define flight event
  Modification of hemispheres for V&V
  Propagation of noise to ground and metric calculation
ANOPP2 Toolchain: AARON, ARMIT, ASOFT, AMPIT, AMAT
AMAT Examples
  Calculation of NPD during level flyover (Mode L)
  Calculation of OASPL (dBA) during approach (Mode A)
  Calculation of 1/3rd Octave SPL along line (Mode L)
Conclusion

## Slide 14: Namelist Input File
AMAT input file includes 2 parts
  Single namelist: short list of settings/options
  Flight path and source specifications: source selection, mode, velocity, source hemisphere files
&AmatConfiguration
Absorption flag (on/off, model)
Ground settings (on/off, model)
Flight path and simulation settings
Metadata settings
Frequency filter settings
/
Noise source selection (F1A only, etc.)
Mode
Velocity and source hemisphere file
lossless (no absorption)
SAE ARP 866a
ANSI S1 26 1978
ANSI S1 26 2014
ICAO6 1978
Hard/Soft/No Ground
Flow Resistance
Duration of flight event
Tonal Noise
Broadband Self Noise
Level Flyover
Approach
Takeoff
Maneuver
h

## Slide 15: Command Line Output
+ Series of Tecplot formatted files of metadata and predictions

## Slide 16: 1) Calculation of NPD during level flyover (Mode L)

## Slide 17: 2) Calculation of OASPL (dBA) during approach (Mode A)

## Slide 18: 3) Calculation of 1/3rd Octave SPL along line (Mode L)

## Slide 19: Conclusion
UAM vehicle noise requires suite of tools chained together
ANOPP2 provides suite of tools for different pieces of the noise assessment puzzle
Examples have been demonstrated showcasing the ANOPP2 Mission Analysis Tool (AMAT), which provides the far-field propagation portion of the tool chain